TSENG ET4000 DRIVER INSTALLATION
                FOR MICROSOFT WINDOWS 3.0 and 3.0a

The instructions which follow are applicable to users of 
Microsoft Windows and Tseng ET4000 VGA based adapters. Note 
that, to use 800x600 and 1024x768 modes, an ANALOG color display 
capable of these high resolutions is required.

The "Tseng ET4000 - Windows 3.0 Driver Disk" contains 256-color 
and high-resolution drivers, as well as a file called SETUP.INF 
that replaces the file of the same name on the Microsoft Windows 
3.0 or 3.0a Setup "DISK 1" diskette. Follow the instructions listed
below carefully to install the drivers.

Instructions:

1. Make a DISKCOPY of the Setup "Disk 1" diskette.  
   Example (for systems with a single floppy and hard drive):

         C:>DISKCOPY A: A:

   The system will use drive A: for both the original and the 
   copy as the source and target diskettes are inserted 
   alternately for the copy.

2. After the copy is made, return the original to its jacket and 
   store safely.

3. Copy the SETUP file from the Tseng ET4000 - Windows 3.0 
   Driver Disk to the newly-created copy of the Setup "Disk 1" 
   diskette. Example (for systems with a single floppy and hard 
   drive):

   For Windows 3.0:
         C:>COPY A:SETUP.W30 B:SETUP.INF

   For Windows 3.0a:
         C:>COPY A:SETUP.W3A B:SETUP.INF

   The system will use drive A: as drive B: also. After the copy 
   is finished, type A: [ENTER].

4. Type SETUP [ENTER] to begin installation of Windows.

5. Review the configuration list when it is shown. If you wish to 
   change Display type, move the cursor (highlighted line) to the 
   "Display:" line and press [ENTER] to select from the available 
   list. 

6. The program will ask you to insert the Tseng ET4000 VGA - 
   Windows 3.0 Driver Disk in order to install the drivers as 
   required. After this is done, the installation program will 
   continue normally.

After you complete the above steps you can begin using Windows.

Note: If you wish to change the display type after completing the 
installation, click on the Windows Setup icon found in the Main 
desktop window.