OPERATION INSTRUCTIONS

The enclosed ADI printer driver PPFUJIE.COM has been developed
for FUJITSU 24-wire printers of the DL series in DPL24C emulation 
with a maximum resolution of 360 * 180 dots per inch.

ADI provides the same functionality and performance as the standard 
device drivers used for AutoCAD. 
As opposed to other common AutoCAD drivers the ADI drivers have 
to be loaded before starting AutoCAD. 
They are residing in the main memory.

1. Printer Installation

Before starting with the printing set the printer to the following values:

EMULATE:		DPL24I  	for black-and-white printer
			DPL24C  	for 8-color printers
COLOR:		AUTOSEL  (only for 8-color printers)
LF-Code:		LF only
CR-Code:		CR only



2. Driver Installation

Copy the driver via the following command onto your harddisk:

	COPY A:PPFUJIE.COM C:

3. Usage of the Driver with AutoCAD

Before starting AutoCAD you first have to load the driver 
PPFUJIE.COM for FUJITSU 24 pin dot matrix printers, which 
are driven by the DPL 24C command set.
 
Proceed according to the following syntax:

C:\ACAD>PPFUJIE /M			- monochrome printout
C:\ACAD>PPFUJIE /C			- color printout
C:\ACAD>PPFUJIE /F			- output into a file


If you want to delete the driver that is loaded residentially 
from your main memory, enter the filename PPFUJIE.

If the driver is to be loaded automatically then PPFUJIE.COM  
has to be entered together with the right parameter in the 
AUTOEXEC.BAT batch file.

If ADI is used for the first time together with AutoCAD the 
program must be configured. Thus, select the option 
"Configure AutoCAD" from the AutoCAD main menu. In case
AutoCAD is already configured you are automatically set 
into the configuration mode when starting the program. 
Regarding the item "Configure PRINTER PLOTTER" the ADI 
printer plotter must be selected.If this option is not 
available in the program, in any case you must check 
whether your AutoCAD version comprises all drivers 
(files with the extension .DRV) and whether they have been 
installed into your program.
An UPDATE diskette can be obtained from your AutoCAD dealer,
if necessary.

After selection of the ADI printer plotter the following 
setting ought to be taken into account when using the 
FUJITSU 24-wire printers of the DL series.

Programming Text                                       Your Choise
__________________________________________________________________

Do you want to specify plot size in millimeter? <N>         RETURN
Maximum horizontal (X) plot size in inches <11.0000>:       13.599
Dots per inch in horizontal direction <100.0>:                 360
Maximum vertical (Y) plot size in inches <8.5000>:              12
Dots per inch in vertical (Y) direction <360.0>:               180
.
.
.
Output format, 0 to 2:                                           2
Hexadecimal Interrupt Code (ADI 0XXh)  <7B>:                RETURN
.
.
.
Do you want to calibrate the printer plotter? <N>           RETURN
Format Units (inch or millimeter)  <Z>:                          M
Plot origin in millimeter <0.00,0.00>:                      RETURN
Standard values for plot format
.
.
.
.
Specify format, width and height                   (siehe Punkt A)
in millimeter <MAX>:

Rotate 2-dimensional plots clockwise by 90 ø? <N>           RETURN
Remove hidden lines? <N>                                    RETURN


Specification of the rule by entering:
plotted millimeters=drawing units or adaptation or? <A>          A

__________________________________________________________________


When entering the format you have the following input 
possibilities:

	- A4, if your printer is to proceed A4 paper
	- MAX, if you want to make use of the entire width of the
	  printer

After the installation you have to abandon the configuration menu. 
In doing so, the changed setting is saved.

5. General Hints for Usage

Due to the limited capacity of the main memory the color printers
can only be selected with 8 pins. This cannot be changed because 
of programming reasons. We hope you understand our situation. 
The result is a slower printout than in the case of a 
white-and-black printout, but the print quality is the same.

If you should have any problems with the configuration or the 
work with AutoCAD under the ADI-driver, please call the hotline
of your country specific subsidiary of Autodesk or FUJITSU.  

We hope that these operation instructions will help you and 
hope you enjoy working with AutoCAD and your Fujitsu printer.