ELF


                            EXTENDED LISP FUNCTION LIBRARY
                                     for AutoLISP


                              Version 1.0 Documentation
                                 and Reference Manual

                                   December 1, 1992



                                   _______
                              ____|__     |               (R)
                           --|       |    |-------------------
                             |   ____|__  |  Association of
                             |  |       |_|  Shareware
                             |__|   o   |    Professionals
                           -----|   |   |---------------------
                                |___|___|    MEMBER






                                Mountain Software


                          Autodesk Registered Developer



                               1579 Nottingham Road
                               Charleston, WV 25314

                                 CIS 70717,3564 
                              Orders: 1-800-2424-PsL













                      Copyright 1992 Jerome Lee Workman, jr.
                               all rights reserved



                          EXTENDED LISP FUNCTION LIBRARY

                                Table of Contents



        Using ELF
          Introduction  . . . . . . . . . . . . . . . . . . . . . . .   1
          ELF Features  . . . . . . . . . . . . . . . . . . . . . . .   1
          Installation  . . . . . . . . . . . . . . . . . . . . . . .   3
          ACAD.ADS  . . . . . . . . . . . . . . . . . . . . . . . . .   3
          ACAD.LSP  . . . . . . . . . . . . . . . . . . . . . . . . .   4
          Sample Programs . . . . . . . . . . . . . . . . . . . . . .   4

        ELFDOS Commands
          cd  . . . . . . . . . . . . . . . . . . . . . . . . . . . .   5
             change directories; chdir, dcd
          cls . . . . . . . . . . . . . . . . . . . . . . . . . . . .   5
             clear (erase) the text screen; 
          c:  . . . . . . . . . . . . . . . . . . . . . . . . . . . .   5
             logs to C: drive; 
          dcopy . . . . . . . . . . . . . . . . . . . . . . . . . . .   6
             copy DOS file(s); 
          derase  . . . . . . . . . . . . . . . . . . . . . . . . . .   6
             erase / delete DOS file(s); ddel
          dir . . . . . . . . . . . . . . . . . . . . . . . . . . . .   6
             prints a file directory list; ddir
          drename . . . . . . . . . . . . . . . . . . . . . . . . . .   6
             rename / move file(s); dmove
          elf . . . . . . . . . . . . . . . . . . . . . . . . . . . .   7
             displays a list of all ELF commands and functions; 
          ff  . . . . . . . . . . . . . . . . . . . . . . . . . . . .   7
             find file(s) on the AutoCAD library path and DOS path; 
          look  . . . . . . . . . . . . . . . . . . . . . . . . . . .   7
             display ASCII file(s) to the screen using the ELF browser;

          mkdir . . . . . . . . . . . . . . . . . . . . . . . . . . .   8
             create a directory; md, dmd
          password  . . . . . . . . . . . . . . . . . . . . . . . . .   8
             register  ELF  with  your password  (obtain  from Mountain
             Software); 
          rmdir . . . . . . . . . . . . . . . . . . . . . . . . . . .   8
             remove (delete) a directory; rd, drd
          sd  . . . . . . . . . . . . . . . . . . . . . . . . . . . .   9
             set default disk drive; dsd
          symbol  . . . . . . . . . . . . . . . . . . . . . . . . . .   9
             displays the value of an AutoLISP symbol; 
          ver . . . . . . . . . . . . . . . . . . . . . . . . . . . .   9
             prints ELF, DOS and AutoCAD version numbers; 

        AutoLISP Functions
          Optional Parameters . . . . . . . . . . . . . . . . . . . .  10
          Variable Parameters . . . . . . . . . . . . . . . . . . . .  10
          Data Types  . . . . . . . . . . . . . . . . . . . . . . . .  10
          Return Values . . . . . . . . . . . . . . . . . . . . . . .  11



        ELF Documentation                      Table of Contents, Page ii


        Video Functions
          box . . . . . . . . . . . . . . . . . . . . . . . . . . . .  12
             draws a  box (rectangle) on the  text screen using graphic
             ascii characters.; (box col row ecol erow attr btype)
          cls . . . . . . . . . . . . . . . . . . . . . . . . . . . .  12
             clear text screen to optional color attribute; (cls attr)
          get_video . . . . . . . . . . . . . . . . . . . . . . . . .  12
             get current text screen video parameters; (get_video)
          printf  . . . . . . . . . . . . . . . . . . . . . . . . . .  13
             formatted  "C"  type print  to  text  screen  or  graphics
             command prompt area; (printf format ...)
          prts  . . . . . . . . . . . . . . . . . . . . . . . . . . .  13
             fast  write  to  text screen  at  col,  row  position with
             optional attribute; (prts col row string attr)
          puts  . . . . . . . . . . . . . . . . . . . . . . . . . . .  13
             fast write to text screen at cursor position with optional
             attribute; (puts string attr)
          restore_screen  . . . . . . . . . . . . . . . . . . . . . .  14
             restores    a    previously    captured    text    screen;
             (restore_screen)
          save_screen . . . . . . . . . . . . . . . . . . . . . . . .  14
             captures the  contents of  the  text  screen to  a  memory
             buffer; (save_screen)
          scr_fill  . . . . . . . . . . . . . . . . . . . . . . . . .  14
             fill a rectangle  of the text screen  with a character and
             color attribute; (scr_fill col row cols rows ch attr)
          scr_printf  . . . . . . . . . . . . . . . . . . . . . . . .  15
             formatted "C" type print to text screen using direct video
             buffer write; (scr_printf format ...)
          set_color . . . . . . . . . . . . . . . . . . . . . . . . .  15
             sets the internal  "color" variable for use  by subsequent
             uses  of routines which can  use the default  color (r11);
             (set_color attr)

        Cursor Functions
          get_cursor  . . . . . . . . . . . . . . . . . . . . . . . .  16
             get cursor size / shape; (get_cursor)
          getxy . . . . . . . . . . . . . . . . . . . . . . . . . . .  16
             get cursor screen coordinates; (getxy)
          gotoxy  . . . . . . . . . . . . . . . . . . . . . . . . . .  16
             position the screen cursor; (gotoxy col row)
          set_cursor  . . . . . . . . . . . . . . . . . . . . . . . .  16
             set  cursor size;  start  to end  scan lines;  (set_cursor
             start end)

        Window Functions
          set_menu_help . . . . . . . . . . . . . . . . . . . . . . .  17
             sets the user  help string list for  wmenu; (set_menu_help
             <slist>)
          wclose  . . . . . . . . . . . . . . . . . . . . . . . . . .  18
             closes  the  top  window  restoring the  screen  under the
             window; (wclose)
          wcloseall . . . . . . . . . . . . . . . . . . . . . . . . .  18
             closes all windows; (wcloseall)



        ELF Documentation                     Table of Contents, Page iii


          wclreol . . . . . . . . . . . . . . . . . . . . . . . . . .  18
             erase from window cursor to end of line; (wclreol)
          wcls  . . . . . . . . . . . . . . . . . . . . . . . . . . .  18
             clear window to optional color attribute; (wcls attr)
          werase_line . . . . . . . . . . . . . . . . . . . . . . . .  19
             erase a line of text from a window; (werase_line line)
          wgetstr . . . . . . . . . . . . . . . . . . . . . . . . . .  19
             open a window centered on the text screen, prints a prompt
             on the top border and gets  string input.; (wgetstr prompt
             default length wattr battr btype)
          wgetdrive . . . . . . . . . . . . . . . . . . . . . . . . .  19
             select  a disk  drive from  a menu,  all valid  drives are
             listed   with    their   respective    drive   type    (eg
             removable/floppy, fixed, network, and redirected devices);
             (wgetdrive col row wattr battr hattr btype)
          wgetfile  . . . . . . . . . . . . . . . . . . . . . . . . .  20
             select a file from  a menu of  DOS files from the  current
             directory.  The user can change directories and access all
             available disk  drives.; (wgetfile  filespec fileattr  col
             row wattr battr hattr btype)
          wgetxy  . . . . . . . . . . . . . . . . . . . . . . . . . .  21
             get window screen position; (wgetxy)
          wgotoxy . . . . . . . . . . . . . . . . . . . . . . . . . .  21
             move window cursor; (wgotoxy col row)
          winfo . . . . . . . . . . . . . . . . . . . . . . . . . . .  21
             gets the top window size and position; (winfo)
          wmenu . . . . . . . . . . . . . . . . . . . . . . . . . . .  22
             opens a centered window  and displays a menu. The user can
             then  select one  of  the displayed  items.; (wmenu  slist
             wattr battr hattr btype shadow title)
          wmsg  . . . . . . . . . . . . . . . . . . . . . . . . . . .  23
             opens a centered window, displays a message and optionally
             waits for  a keystroke  and closes the  window; (wmsg  str
             wait attr battr btype)
          wopen . . . . . . . . . . . . . . . . . . . . . . . . . . .  24
             open a window on the text  screen with specified location,
             size,  border,  and colors;  saving  the  area  under  the
             window; (wopen col row cols rows wattr battr btype)
          wpopup  . . . . . . . . . . . . . . . . . . . . . . . . . .  24
             open a window  centered on the  text screen;  (wpopup cols
             rows wattr battr)
          wprintf . . . . . . . . . . . . . . . . . . . . . . . . . .  25
             printf  to  window at  window  cursor  position;  (wprintf
             format ...)
          wprts . . . . . . . . . . . . . . . . . . . . . . . . . . .  25
             write  to  window  at  col,  row  position  with  optional
             attribute; (wprts col row string attr)
          wputcen . . . . . . . . . . . . . . . . . . . . . . . . . .  25
             write a centered  string to  window at  window cursor  row
             position; (wputcen str)
          wputs . . . . . . . . . . . . . . . . . . . . . . . . . . .  26
             write  to window at  window cursor position  with optional
             attribute; (puts string attr)
          wscroll . . . . . . . . . . . . . . . . . . . . . . . . . .  26



        ELF Documentation                      Table of Contents, Page iv


             scroll window text; (wscroll dir start end lines)
          wshadow . . . . . . . . . . . . . . . . . . . . . . . . . .  26
             adds  a  drop shadow  to  the  top  (last opened)  window;
             (wshadow attr)
          wtitle  . . . . . . . . . . . . . . . . . . . . . . . . . .  27
             prints on the border  of a window  in one of 6  positions;
             (wtitle <str> [<pos>])

        Keyboard Functions
          getch . . . . . . . . . . . . . . . . . . . . . . . . . . .  27
             get a character from the keyboard; (getch)
          getche  . . . . . . . . . . . . . . . . . . . . . . . . . .  28
             get a character from the keyboard with echo; (getche)
          getkey  . . . . . . . . . . . . . . . . . . . . . . . . . .  28
             get a keystroke from the keyboard; (getkey)
          kbhit . . . . . . . . . . . . . . . . . . . . . . . . . . .  28
             checks  the  keyboard  buffer  for  a  waiting  keystroke;
             (kbhit)
          key_clear . . . . . . . . . . . . . . . . . . . . . . . . .  29
             clears  the  keyboard buffer  of  any pending  keystrokes;
             (key_clear)
          key_ready . . . . . . . . . . . . . . . . . . . . . . . . .  29
             returns immediately with a waiting key; (key_ready)
          key_stat  . . . . . . . . . . . . . . . . . . . . . . . . .  29
             gets the state of  keyboard shift and other special  keys;
             (key_stat)
          key_stuff . . . . . . . . . . . . . . . . . . . . . . . . .  29
             "pushes" keys into the keyboard buffer; (key_stuff str)

        Directory Functions
          access  . . . . . . . . . . . . . . . . . . . . . . . . . .  30
             determines if a  file exists and can  be accessed by mode;
             (access path mode)
          chdir . . . . . . . . . . . . . . . . . . . . . . . . . . .  30
             change disk directory; (chdir path)
          chpath  . . . . . . . . . . . . . . . . . . . . . . . . . .  31
             change current disk drive and directory; (chpath path)
          disk_ready  . . . . . . . . . . . . . . . . . . . . . . . .  31
             verifies  that a  removable  (floppy) drive  is ready  and
             readable; (disk_ready drive)
          disk_type . . . . . . . . . . . . . . . . . . . . . . . . .  31
             ; (disk_type drive)
          disk_valid  . . . . . . . . . . . . . . . . . . . . . . . .  31
             verifies  that a  disk drive  is a  valid device  (but not
             necessarily   ready    if   a   removable/floppy   drive);
             (disk_valid drive)
          erasefile . . . . . . . . . . . . . . . . . . . . . . . . .  32
             erase file(s); (erasefile filename)
          file_exists . . . . . . . . . . . . . . . . . . . . . . . .  32
             determines if a file exists; (file_exists path)
          findfirst . . . . . . . . . . . . . . . . . . . . . . . . .  32
             finds  the  first  instance  of  a  file  who's  name  and
             directory  attributes  match  the  arguments.;  (findfirst
             filespec attribute)



        ELF Documentation                       Table of Contents, Page v


          findnext  . . . . . . . . . . . . . . . . . . . . . . . . .  33
             finds  the next occurrence  of the file  specification and
             attribute after a findfirst call; (findnext)
          fullpath  . . . . . . . . . . . . . . . . . . . . . . . . .  34
             expands  a partial  path  into  a full  DOS  path  string;
             (fullpath path)
          getdir  . . . . . . . . . . . . . . . . . . . . . . . . . .  34
             returns a string with the current drive:\path; (getdir)
          getdiskfree . . . . . . . . . . . . . . . . . . . . . . . .  34
             returns size statistics in the specified drive number as a
             list; (getdiskfree 3)
          getdisk . . . . . . . . . . . . . . . . . . . . . . . . . .  35
             returns the  current drive  number (A=1,  B=2, C=3,  etc);
             (getdisk)
          load_dirs . . . . . . . . . . . . . . . . . . . . . . . . .  35
             returns a list of strings containing file directories from
             the current directory; (load_dirs)
          load_drives . . . . . . . . . . . . . . . . . . . . . . . .  35
             returns  a  list of  strings  containing  all  valid  disk
             drives; (load_drives)
          load_files  . . . . . . . . . . . . . . . . . . . . . . . .  35
             returns  a list  of  strings containing  files matching  a
             filespec  and  directory  attribute; (load_files  filespec
             attribute)
          makepath  . . . . . . . . . . . . . . . . . . . . . . . . .  36
             Combines the four components  into a full DOS path string;
             (makepath drive dir name ext)
          mkdir . . . . . . . . . . . . . . . . . . . . . . . . . . .  36
             creates a new directory; (mkdir dirname)
          rmdir . . . . . . . . . . . . . . . . . . . . . . . . . . .  36
             removes (deletes) a directory; (rmdir dirname)
          setdisk . . . . . . . . . . . . . . . . . . . . . . . . . .  36
             logs to the specified disk drive; (setdisk drive)
          splitpath . . . . . . . . . . . . . . . . . . . . . . . . .  37
             splits  a  DOS  path  string  into  its  four  components;
             (splitpath path)
          unlink  . . . . . . . . . . . . . . . . . . . . . . . . . .  37
             erase file(s); (unlink filename)

        File Functions
          copyfile  . . . . . . . . . . . . . . . . . . . . . . . . .  38
             copies file(s); (copyfile source destination)
          look  . . . . . . . . . . . . . . . . . . . . . . . . . . .  38
             displays  an  ASCII file  to  screen  using the  ELF  file
             viewer; (look filespec)
          movefile  . . . . . . . . . . . . . . . . . . . . . . . . .  38
             moves / renames file(s); (movefile source destination)
          read_file . . . . . . . . . . . . . . . . . . . . . . . . .  38
             reads an  ASCII file and  returns a string  list from file
             records.  Each line  in  the text  file is  parsed  into a
             string  and appended  to  the returned  list.;  (read_file
             filespec mode)



        ELF Documentation                      Table of Contents, Page vi


          write_file  . . . . . . . . . . . . . . . . . . . . . . . .  39
             opens an  ASCII file and writes a string  list to the file
             and then  closes the  file. Each  string is placed  in the
             text file as a line of text.; (write_file filespec type)

        Math Functions
          | . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  39
             returns the  result of a  bitwise OR of  the arguments; (|
             ...)
          ||  . . . . . . . . . . . . . . . . . . . . . . . . . . . .  40
             returns the result  of a logical OR  of the arguments; (||
             ...)
          & . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  40
             returns the result  of a bitwise AND  of the arguments; (&
             ...)
          &&  . . . . . . . . . . . . . . . . . . . . . . . . . . . .  40
             returns the result of  a logical AND of the arguments; (&&
             ...)
          acos  . . . . . . . . . . . . . . . . . . . . . . . . . . .  40
             returns the inverse cosine of the argument; (acos rad)
          asin  . . . . . . . . . . . . . . . . . . . . . . . . . . .  40
             returns the inverse sine of the argument; (asin rad)
          ceil  . . . . . . . . . . . . . . . . . . . . . . . . . . .  41
             returns  the  smallest  integer  greater or  equal  to the
             argument; (ceil rval)
          cosh  . . . . . . . . . . . . . . . . . . . . . . . . . . .  41
             returns the hyperbolic cosine of the argument; (cosh rad)
          dtr . . . . . . . . . . . . . . . . . . . . . . . . . . . .  41
             converts an angle in degrees to radians; (dtr ang)
          floor . . . . . . . . . . . . . . . . . . . . . . . . . . .  41
             returns the largest integer not greater than the argument;
             (floor rval)
          hibyte  . . . . . . . . . . . . . . . . . . . . . . . . . .  42
             returns the upper  (most significant) byte of  an integer;
             (hibyte val)
          lobyte  . . . . . . . . . . . . . . . . . . . . . . . . . .  42
             returns  the lower (least significant) byte of an integer;
             (lobyte val)
          log10 . . . . . . . . . . . . . . . . . . . . . . . . . . .  42
             returns the  logarithm to  the base  10  of the  argument;
             (log10 x)
          rand  . . . . . . . . . . . . . . . . . . . . . . . . . . .  42
             generates a pseudo random number; (rand)
          round . . . . . . . . . . . . . . . . . . . . . . . . . . .  42
             rounds a real value; (round val places)
          rtd . . . . . . . . . . . . . . . . . . . . . . . . . . . .  43
             converts an angle in radians to degrees; (rtd ang)
          sinh  . . . . . . . . . . . . . . . . . . . . . . . . . . .  43
             returns the hyperbolic sine of the argument; (sinh rad)
          srand . . . . . . . . . . . . . . . . . . . . . . . . . . .  43
             seeds the random number generator; (srand i)
          tan . . . . . . . . . . . . . . . . . . . . . . . . . . . .  43
             returns  the trigonometric tangent  of the  argument; (tan
             rad)



        ELF Documentation                     Table of Contents, Page vii


          tanh  . . . . . . . . . . . . . . . . . . . . . . . . . . .  44
             returns the hyperbolic tangent of the argument; (tanh rad)

        List Handling Functions
          bsearch . . . . . . . . . . . . . . . . . . . . . . . . . .  44
             located a value in  a sorted string, integer or real value
             list; (bsearch vlist key)
          delete  . . . . . . . . . . . . . . . . . . . . . . . . . .  44
             deletes  a list or  atom from  another list;  (delete list
             pos)
          insert  . . . . . . . . . . . . . . . . . . . . . . . . . .  45
             inserts a list or atom into another list; (insert list pos
             item)
          lfind . . . . . . . . . . . . . . . . . . . . . . . . . . .  45
             located a  value in  an unsorted string,  integer or  real
             value list; (lfind vlist key)
          lsearch . . . . . . . . . . . . . . . . . . . . . . . . . .  45
             located a value  in a string, integer  or real value list;
             (lsearch vlist key)
          qsort . . . . . . . . . . . . . . . . . . . . . . . . . . .  46
             sorts a string, integer or real value list; (qsort lst)
          replace . . . . . . . . . . . . . . . . . . . . . . . . . .  46
             replace a  list or atom  in a list  with another; (replace
             list pos item)
          symbol  . . . . . . . . . . . . . . . . . . . . . . . . . .  46
             Displays the contents of  a symbol to the screen using the
             ELF file/symbol viewer.; (symbol sym)

        String Handling Functions
          field . . . . . . . . . . . . . . . . . . . . . . . . . . .  47
             returns a substring of str1  from token delimiters in str2
             and position.; (field str1 str2 pos)
          set_edit_help . . . . . . . . . . . . . . . . . . . . . . .  47
             sets the  user help string list for the function (strget);
             (set_edit_help <slist>)
          sprintf . . . . . . . . . . . . . . . . . . . . . . . . . .  47
             same as printf except that nothing is printed,  the string
             is returned; (sprintf format ...)
          strchr  . . . . . . . . . . . . . . . . . . . . . . . . . .  48
             finds  the first  occurrence of  ch in  str and  returns a
             substring starting at that character; (strchr str ch)
          strcmp  . . . . . . . . . . . . . . . . . . . . . . . . . .  48
             compares  two  strings  for   equality  (case  sensitive);
             (strcmp str1 str2)
          strcspn . . . . . . . . . . . . . . . . . . . . . . . . . .  48
             determine  the length of the prefix  of str1 made entirely
             of chars not in str2; (strcspn str1 str2)
          strdate . . . . . . . . . . . . . . . . . . . . . . . . . .  49
             returns the  current date  from the  internal  clock as  a
             formatted string; (strdate)
          strdela . . . . . . . . . . . . . . . . . . . . . . . . . .  49
             delete  all  occurrences  of  chars  in  str2  from  str1;
             (strdela str1 str2)
          strget  . . . . . . . . . . . . . . . . . . . . . . . . . .  49



        ELF Documentation                    Table of Contents, Page viii


             edit  a string on the text  screen with cursor positioning
             and editing, background mask, color attribute control, and
             on line help.; (strget str len curpos mask attr ...)
          stricmp . . . . . . . . . . . . . . . . . . . . . . . . . .  50
             compares  two strings  for  equality  (case  insensitive);
             (stricmp str1 str2)
          strncpy . . . . . . . . . . . . . . . . . . . . . . . . . .  51
             copies the first n characters of a string; (strncpy str n)
          strnset . . . . . . . . . . . . . . . . . . . . . . . . . .  51
             fills a string; (strnset char len)
          strpbrk . . . . . . . . . . . . . . . . . . . . . . . . . .  51
             returns  a  substring  of  the  first  occurrence  of  any
             character of str2 in str1; (strstr str1 str2)
          strrchr . . . . . . . . . . . . . . . . . . . . . . . . . .  51
             finds  the last  occurrence  of ch  in str  and  returns a
             substring starting at that character; (strrchr str ch)
          strrev  . . . . . . . . . . . . . . . . . . . . . . . . . .  52
             returns the  string  argument  with  the  character  order
             reversed; (strrev str)
          strspn  . . . . . . . . . . . . . . . . . . . . . . . . . .  52
             determine the  length of the prefix  of str1 made entirely
             of chars in str2; (strspn str1 str2)
          strstr  . . . . . . . . . . . . . . . . . . . . . . . . . .  52
             returns a  substring of  the first occurrence  of str2  in
             str1; (strstr str1 str2)
          strswap . . . . . . . . . . . . . . . . . . . . . . . . . .  52
             swaps all occurrences of char1 with char2 in str; (strswap
             str char1 char2)
          strtime . . . . . . . . . . . . . . . . . . . . . . . . . .  53
             returns  the current  time from  the  internal clock  as a
             formatted string; (strtime)
          strtok  . . . . . . . . . . . . . . . . . . . . . . . . . .  53
             returns  the first substring of str1 from token delimiters
             in   str2.  subsequent  calls  after  the  first  with  no
             arguments  will   return  the   second  and   any  further
             substrings; (strtok str1 str2)
          strtrim . . . . . . . . . . . . . . . . . . . . . . . . . .  53
             trim  white  space  (all  char  values  <  '!')  from  the
             beginning (left side) and end (right side); and compresses
             white space  within a  string to  a  single space  between
             words; (strtrim str)
          strtriml  . . . . . . . . . . . . . . . . . . . . . . . . .  54
             trim  white  space  from the  beginning  (left side)  of a
             string; (strtriml str)
          strtrimr  . . . . . . . . . . . . . . . . . . . . . . . . .  54
             trim white  space from the  end (right side)  of a string;
             (strtrimr str)
          tolower . . . . . . . . . . . . . . . . . . . . . . . . . .  54
             ; (tolower char)
          toupper . . . . . . . . . . . . . . . . . . . . . . . . . .  54
             ; (toupper char)

        Character Classification Functions
          isalnum . . . . . . . . . . . . . . . . . . . . . . . . . .  55



        ELF Documentation                      Table of Contents, Page ix


             returns a non-zero value if argument is a letter or digit;
             (isalnum char)
          isascii . . . . . . . . . . . . . . . . . . . . . . . . . .  55
             returns  a  non-zero   value  if  argument  is   an  ASCII
             character; (isascii char)
          iscntl  . . . . . . . . . . . . . . . . . . . . . . . . . .  55
             returns   a  non-zero  value  if  argument  is  a  control
             character; (iscntl char)
          isdigit . . . . . . . . . . . . . . . . . . . . . . . . . .  55
             returns  a non-zero value if argument  is a numeric digit;
             (isdigit char)
          isgraph . . . . . . . . . . . . . . . . . . . . . . . . . .  56
             returns   a  non-zero  value  if  argument  is  a  visible
             printable character; (isgraph char)
          islower . . . . . . . . . . . . . . . . . . . . . . . . . .  56
             returns  a  non-zero  value if  argument  is a  lower case
             letter; (islower char)
          isodigit  . . . . . . . . . . . . . . . . . . . . . . . . .  56
             returns a non-zero value if argument is an octal digit (0-
             7); (isodigit char)
          isprint . . . . . . . . . . . . . . . . . . . . . . . . . .  56
             returns  a  non-zero value  if  argument  is  a  printable
             character; (isprint char)
          ispunct . . . . . . . . . . . . . . . . . . . . . . . . . .  57
             returns  a non-zero  value  if argument  is a  punctuation
             character; (ispunct char)
          isspace . . . . . . . . . . . . . . . . . . . . . . . . . .  57
             returns  a non-zero  value  if argument  is a  white-space
             character (space, tab, newline, etc); (isspace char)
          isupper . . . . . . . . . . . . . . . . . . . . . . . . . .  57
             returns a  non-zero value  if argument  is  an upper  case
             letter; (isupper char)
          isxdigit  . . . . . . . . . . . . . . . . . . . . . . . . .  57
             returns  a non-zero  value  if argument  is a  hexadecimal
             digit (0-F); (isxdigit char)

        Utility / Miscellaneous Functions
          adsdump . . . . . . . . . . . . . . . . . . . . . . . . . .  58
             prints  the data  type and  value  of an  AutoLISP symbol;
             (adsdump sym)
          beep  . . . . . . . . . . . . . . . . . . . . . . . . . . .  58
             sound a beep on  the PC speaker for optional frequency and
             duration; (beep freq duration)
          clock . . . . . . . . . . . . . . . . . . . . . . . . . . .  58
             reads the current internal clock; (clock)
          exit  . . . . . . . . . . . . . . . . . . . . . . . . . . .  58
             cancels  execution  and returns  to  the  Command: prompt;
             (exit)
          getdosver . . . . . . . . . . . . . . . . . . . . . . . . .  59
             returns the DOS version; (getdosver)
          last_error  . . . . . . . . . . . . . . . . . . . . . . . .  59
             returns the last internal error message; (last_error)
          nosound . . . . . . . . . . . . . . . . . . . . . . . . . .  59
             turns off the PC speaker after a sound function; (nosound)



        ELF Documentation                       Table of Contents, Page x


          pause_key . . . . . . . . . . . . . . . . . . . . . . . . .  59
             prints "press  any  key to  continue..." and  waits for  a
             keystroke; (pause_key)
          sound . . . . . . . . . . . . . . . . . . . . . . . . . . .  59
             turns on  the PC speaker  at a  specified tone  frequency;
             (sound freq)
          system  . . . . . . . . . . . . . . . . . . . . . . . . . .  60
             executes a DOS command; (system cmd)
          wait  . . . . . . . . . . . . . . . . . . . . . . . . . . .  60
             suspend execution for a specified time duration; (wait ti)

        Symbols
          *last_error*  . . . . . . . . . . . . . . . . . . . . . . .  60
             the last error message string
          color . . . . . . . . . . . . . . . . . . . . . . . . . . .  60
             default color attribute
          edit_help . . . . . . . . . . . . . . . . . . . . . . . . .  60
             string  list  with user  defined  help  for  the  (strget)
             function
          menu_help . . . . . . . . . . . . . . . . . . . . . . . . .  60
             string  list  with  user  defined  help  for  the  (wmenu)
             function
          Copyright . . . . . . . . . . . . . . . . . . . . . . . . .  62
          Trademark . . . . . . . . . . . . . . . . . . . . . . . . .  62



        Elf Documentation                                          Page 1



        Using ELF

        Introduction

        ELF is  a library of  commands and functions designed  to enhance
        AutoCAD and  AutoLISP. The  ELF library  contains 15 utility  and
        file management commands, and over 150 functions for AutoLISP all
        contained in a single EXP file.

        ELF gives  the  AutoLISP programmer  a  professional  programming
        language  rivaling many  commercial compiled  language libraries.
        The range  of functions include  those for text screen  video and
        window control; popup menus and  data entry with a build  in help
        system; sound; keyboard;  string manipulation; math;  sorting and
        searching;  list  handling; file  and directory  handling; entity
        creation; and several utility functions.

        Non-programmers  will   also  appreciate   the  mini-applications
        (ELFapps), including  the ELF  notepad; and  the several  utility
        commands.

        In  addition,  ELF  contains ELFDOS,  which  implements  many DOS
        commands  within AutoCAD for  file management, a  file and symbol
        browser, and integrated help.

        ELF is designed  to operate with AutoCAD 386  (release 10-386 and
        above) on  IBM PC  and  compatible computers  under the  MS/PCDOS
        operating system.


        ELF Features

        *  Over 150 new functions for AutoLISP programmers:
             + Video
                  -    fast direct video writes to the text screen
                  -    printf for C programmers
                  -    color attribute control
                  -    screen save, fill, and restore
             + Text screen windowing
                  -    22 functions for full window management
                  -    multiple overlapping  windows with  shaded borders
                       and drop shadows      
                  -    menus and line editor with integrated user defined
                       help system      
                  -    a file dialogue
             + Cursor
                  -    cursor positioning
                  -    cursor size shape
             + Keyboard
                  -    getkey, getch, getche, and kbhit functions
                  -    keyboard status
                  -    stuff keyboard buffer with keystrokes
             + Directory



        Elf Documentation                                          Page 2


                  -    create / remove / change directories
                  -    read / verify / log to all disk drives
                  -    read disk directory and disk statistics
                  -    copy, move, erase, and rename files.
                  -    file path manipulation
             + File
                  -    fast one step ASCII file read and write
             + Math
                  -    expanded trig, logical, and bit manipulation
             + List Handling
                  -    insert, delete, and replace items in a list
                  -    sort and search a string, integer, or real list
                  -    view a string list using the internal browser
             + String Handling
                  -    full C library string scanning and manipulation
                  -    a  full  featured line  editor  for  flexible data
                       entry
             + Entity Creation
                  -    fast basic entity creation  in one statement using
                       entmake    + Utility / Misc
                  -    sound routines
                  -    dump a list for debugging
                  -    run other programs under program control
                  -    clock and timer routines

        *    an ASCII file browser (like the shareware program LIST)

        *    ELFDOS  - "DOS-like"  file management  commands from  within
             AutoCAD,  no more  shelling out  to copy  a file  or perform
             other DOS functions.

        *    Three   useful  "ELFapps"  that   utilize  the  ELF  library
             including:    

             +    NotePad -  a windowed /  full screen ASCII  file editor
                  written in AutoLISP using ELF
             +    Etables - an  AutoCAD "stock"  application modified  to
                  utilize the ELF menus and symbol browser to display all
                  tables within a drawing.
             +    Demo - a program the demonstrates many of the functions
                  of the ELF library



        Elf Documentation                                          Page 3


        Installation

        Copy the  ELF files  from the  distribution diskette  (or extract
        them from  the archive file)  to any subdirectory on  the AutoCAD
        library  path.  You  may  place   the  ELF  files  in  their  own
        subdirectory (eg C:\ELF)  and add that directory to  your AutoCAD
        Library Path. To insure that AutoCAD can the find files,  add the
        ELF  directory  to   your  ACAD  environment  variable   in  your
        AUTOEXEC.BAT or ACAD386.BAT file:

        Example:

        SET ACAD=C:\ACAD386\SUPPORT;C:\ELF


        ACAD.ADS

        If you have an  ACAD.ADS file, then add ELF to that  file with an
        ASCII editor, or create  a file named ACAD.ADS to  a directory on
        the library path.

        Example contents release 12 ACAD.ADS file:

        ACADAPP
        ELF

        If ELF  does not load with your ACAD.ADS  file then you must load
        it manually:

        eg: (XLOAD"ELF")

        Once  loaded, ELF  will  display the  following message,  and ELF
        commands and functions will be available for use:

        ELF vX.XX - <compile date>, Registered to: Your Name
        Copyright 1992 Mountain Software. - Enter "ELF" for help:

        You may add the following code to any AutoLISP program which uses
        ELF to automatically xload ELF.EXP:

        (if(not(member(findfile "ELF.EXP") (ADS)))
          (if(not(xload"ELF" nil)) (progn
            (princ "\nERROR: Unable to xload ELF.EXP")
            (princ\nThis program requires ELF to operate!\007")))
        )

        or you can simply add (load"ELF") to your program to load ELF.EXP
        and define color and key symbols.



        Elf Documentation                                          Page 4


        ACAD.LSP

        ELF functions can not be  executed until ELF initializes. AutoCAD
        does not initialize ADS programs until  after ACAD.LSP loads. You
        can  include ELF  functions  in  any function  that  you wish  to
        (defun) in ACAD.LSP, but they can not execute during the load.

        Therefore, if you wish to execute an ELF function at entry to the
        drawing  editor, you can  place that  function into  the function
        (S::STARTUP)  which  will  execute  automatically  after  AutoCAD
        initialized ELF.


        Sample Programs

        The  following files contain  "ELFapps" that demonstrate  many of
        the  ELF functions.  You may  run  these programs  to test  ELF's
        features  and  copy portions  of  the code  for  use in  your own
        programs.


        Filename       Description

        DEMO.LSP       A demonstration of many of ELF's functions
        NOTEPAD.LSP    An ASCII file editor written in AutoLISP and ELF.
        ETABLES.LSP    A  program   which  demonstrates  how   a  "stock"
                       AutoLISP  program   (here  TABLES.LSP,   a  sample
                       program included with other  AutoCAD sample files)
                       can  be easily  modified using functions  from ELF
                       and greatly improved from it's original form.
        ELF.LSP        defines  symbols  for  screen  attributes,  border
                       types,  keycode values, and  xloads ELF.EXP if not
                       already loaded.



        Elf Documentation                                          Page 5



        ELFDOS Commands

        ELF  contains many file  manipulation commands equivalent  to the
        same commands in DOS. Many of  the command names are the same  as
        the DOS command except that the letter "D" is added as  the first
        letter  of  the  command to  differentiate  from  similarly named
        AutoCAD command (eg DCOPY for COPY).

        Why not just shell to DOS?

        The  ELF  replacements  for  DOS commands  are  faster  and  more
        convenient. It takes time  to shell to  DOS and return after  the
        command has completed.

        ELF  also adds  ASCII file  and  AutoLISP symbol  viewers, and  a
        filefind command.

                     ----------------------------------------

        Function:   cd                                       ELF Commands

        Synopsis:   change directories
        Aliases:    chdir, dcd
        Arguments:  directory name
        Notes:      works just like the DOS chdir command except a space
                    or Enter is required between CD and the directory
                    name
        Example:    CD \ACAD

                     ----------------------------------------

        Function:   cls                                      ELF Commands

        Synopsis:   clear (erase) the text screen
        Aliases:
        Arguments:
        Notes:
        Example:

                     ----------------------------------------

        Function:   c:                                       ELF Commands

        Synopsis:   logs to C: drive
        Aliases:
        Arguments:



        Elf Documentation                                          Page 6


        Notes:      Similar to DOS, ELF creates a command for each valid
                    disk drive, therefore, if drives A:,B:,C:, and D: are
                    valid drives, then any of those drives can be logged
                    by entering its drive letter and a colon. Elf will
                    not log to a drive that is not ready (eg floppy drive
                    door open)
        Example:

                     ----------------------------------------

        Function:   dcopy                                    ELF Commands

        Synopsis:   copy DOS file(s)
        Aliases:
        Arguments:  from      filespec to copy from (can be a wildcard)
                    to        filename or directory to copy to
        Notes:      dcopy performs a "double buffered" (eg fast) file
                    copy and prints from and to filenames as they are
                    copied
        Example:    dcopy c:\acad\*.doc d:\temp

                     ----------------------------------------

        Function:   derase                                   ELF Commands

        Synopsis:   erase / delete DOS file(s)
        Aliases:    ddel
        Arguments:  filespec  filespec to erase (can be a wildcard)
        Notes:      prints filenames as they are deleted
        Example:    derase c:\acad\*.bak

                     ----------------------------------------

        Function:   dir                                      ELF Commands

        Synopsis:   prints a file directory list
        Aliases:    ddir
        Arguments:  filespec  optional wildcard filespec (eg *.DWG)
                    /W        optional switch, prints wide (five
                              filenames per line)
        Notes:
        Example:    ddir *.doc

                     ----------------------------------------

        Function:   drename                                  ELF Commands

        Synopsis:   rename / move file(s)
        Aliases:    dmove
        Arguments:  from      filespec to move from (can be a wildcard)
                    to        filename or directory to move to



        Elf Documentation                                          Page 7


        Notes:      destination must be the same device
        Example:    dmove c:\acad\*.doc c:\temp

                     ----------------------------------------

        Function:   elf                                      ELF Commands

        Synopsis:   displays a list of all ELF commands and functions
        Aliases:
        Arguments:
        Notes:      uses the ELF browser to display help for all ELF
                    commands and functions (see look).
        Example:

                     ----------------------------------------

        Function:   ff                                       ELF Commands

        Synopsis:   find file(s) on the AutoCAD library path and DOS path
        Aliases:
        Arguments:
        Notes:      searches for file(s) in the following sequence:
                    1 -       The current directory, the real current
                              directory, which may not be on the AutoCAD
                              library path if you have changed
                              directories after starting AutoCAD.
                    2 -       the AutoCAD library path using AutoCAD's
                              (findfile) function.
                    3 -       the DOS path
        Example:    ff *.sty

                     ----------------------------------------

        Function:   look                                     ELF Commands

        Synopsis:   display ASCII file(s) to the screen using the ELF
                    browser
        Aliases:
        Arguments:  filespec  file(s) to display



        Elf Documentation                                          Page 8


        Notes:      look loads each file matching the filespec into a
                    memory buffer and displays each using the internal
                    full screen browser. The cursor keys can be used to
                    view the file contents. The file can also be printed.
                    If no filename is specified, look will call
                    (wgetfile) where the user can select a file. Key
                    assignments in the browser are as follows:
                    Key       Function        
                    F1        Help
                    F2        text search (case insensitive)
                    Esc       Quit all files
                    Q/X/E     Quit / Exit file
                    Alt-P     print the entire contents of the buffer to
                              PRN
                    Home      Top of file
                    End       Bottom of file
                    Up        Up one line
                    Dn        Down one line
                    PgUp      Up one page
                    PgDn and
                    other keys  Down one page
        Example:    look c:\acad\*.doc

                     ----------------------------------------

        Function:   mkdir                                    ELF Commands

        Synopsis:   create a directory
        Aliases:    md, dmd
        Arguments:  directory name
        Notes:
        Example:    MD C:\ACAD\TEMPDIR

                     ----------------------------------------

        Function:   password                                 ELF Commands

        Synopsis:   register ELF with your password (obtain from Mountain
                    Software)
        Aliases:
        Arguments:
        Notes:      Once the elf password is entered, the delay messages
                    will not appear. Passwords are provided to those who
                    purchase ELF.
        Example:

                     ----------------------------------------

        Function:   rmdir                                    ELF Commands

        Synopsis:   remove (delete) a directory
        Aliases:    rd, drd
        Arguments:



        Elf Documentation                                          Page 9


        Notes:      the directory must be empty
        Example:    RD C:\ACAD\TEMPDIR

                     ----------------------------------------

        Function:   sd                                       ELF Commands

        Synopsis:   set default disk drive
        Aliases:    dsd
        Arguments:
        Notes:      ELF also defines all valid drives as commands (eg A:,
                    B:, C:, D:, etc).
        Example:

                     ----------------------------------------

        Function:   symbol                                   ELF Commands

        Synopsis:   displays the value of an AutoLISP symbol
        Aliases:
        Arguments:  sym       symbol name
        Notes:      (release 12 only) Symbol name can not be an AutoLISP
                    expression. Symbols of type Subr or Exsubr can not be
                    displayed. See the command "look" for a description
                    of the ELF browser.
        Example:    (setq symlist (qsort(atoms-family 1)))
                    symbol symlist

                     ----------------------------------------

        Function:   ver                                      ELF Commands

        Synopsis:   prints ELF, DOS and AutoCAD version numbers
        Aliases:
        Arguments:
        Notes:
        Example:

                     ----------------------------------------



        Elf Documentation                                         Page 10



        AutoLISP Functions

        Optional Parameters

        The  ELF library  utilizes optional  parameters  for many  of its
        functions. Optional  parameters assume  a default  value when  no
        specific value  is specified in  the function call.  For example,
        the  ELF function  (beep) with  no parameters  will sound  the PC
        speaker at a  frequency of 440 hertz for 0.5  seconds by default.
        Or,  you  can specify  the  frequency  alone  (beep 800)  or  the
        frequency and time, (beep 800 1.0). You can not, however, specify
        the second parameter without specifying the first.

        Variable Parameters

        Some functions also  accept a variable number  of parameters. For
        example,  the  function  (printf format  ...)  requires  a format
        parameter, but  additional parameters  are required  only if  the
        format contains  variable  specifier.  (printf  "\nHello  World")
        requires  only the format  parameter but (printf  "Name: %10.10s,
        Age: %2d" name age) requires two  additional parameters to supply
        the required values.

        Data Types

        The following  pneumonics are  used to denote  data types  in ELF
        functions.

        Pneumonic Data Type       Description
        -------------------------------------------------------------
        <int>     integer         signed short Integer
        <real>    real            double precision float
        <str>     string          character string
        <char>    integer         a character ascii value
        <list>    list            AutoLISP list
        <slist>   string list     list of strings
        <fspec)   string          filespec string
        <path>    string          directory path
        <drive>   string          single character string drive letter
        <dir>     string          directory
        <fn>      string          file name
        <ext>     string          file extension
        <disk>    integer         integer disk number (A=1)
        <col>     integer         screen column (X) position
        <row>     integer         screen row (Y) position
        <attr>    integer         screen color attribute
        <pt>      point           a list of two or three reals
        <cen>     point           "
        <rad>     real            radius units
        <ang>     real            angle in radians
        <layer>   string          an AutoCAD layer
        <symbol>  symbol          an AutoLISP symbol (atom or list)



        ELF Functions                                             page 11


        Return Values

        ELF  functions can return any of the  primary data types (eg int,
        real, string, and nil) and lists.  AutoCAD 386 does not support a
        long integer data  type, therefore some ELF  functions that would
        return  a long  will  return a  real value.  The  function (rand)
        returns real values from a long integer result.

        Many functions return lists of values. The values of the list can
        be retrieved using (nth) as well as  (car), (cdr), and up to four
        levels of concatenations of (car) and (cadr) as follows:

        (nth 0 lst)    (car list)     ;first element
        (nth 1 lst)    (cadr list)    ;second element
        (nth 2 lst)    (caddr list)   ;third element
        (nth 3 lst)    (cadddr list)  ;fourth element
        (nth 4 lst)    (caddddr list) ;fifth element
        (nth 5 lst)                   ;fifth element, etc

        Many functions  that are converted  C functions  will return  nil
        instead of 0 to indicate a False  result. This allows testing for
        falsity in one step. For example:

        (if(isascii ch)(doit)) 

        is much simpler than:

        (if(/= 0 (isascii ch))(doit))


        Video Functions

        The ELF  video  system  is  a collection  of  fast  and  flexible
        functions  that write  directly to the  text screen  video screen
        buffer.

        The function printf, from of the C function  library, is included
        in  two forms.  The  first, (printf)  uses  the AutoCAD  internal
        printf  function. Text printed with this function will "stick" if
        the user  presses <F1> to  flipscreen to the  graphics screen and
        back to the text screen. AutoCAD uses it's own text screen buffer
        to save the screen on a single monitor setup. 

        The function  (scr_printf), as well  as many of  the other screen
        write functions, writes directly to the video buffer,  and is not
        saved  to AutoCAD's internal buffer. It  is much faster, but will
        disappear  when the user flips screen  to the graphics screen and
        then returns to the text screen. (scr_printf) also prints using a
        color attribute. 

        The  color attribute is set with  the (set_color) function or, in
        release 12 the  symbol "color" can be  set to the  selected color
        attribute. The internal color variable is also used  by the other



        ELF Functions                                             page 12


        screen write functions if no color attribute is  specified in the
        optional  attribute  function  parameter.  The  file   COLORS.LSP
        contains symbolic  names  for the  color  attributes and  can  be
        loaded within any AutoLISP program to define the color symbols.

                     ----------------------------------------

        Function:   box                                             Video

        Synopsis:   draws a box (rectangle) on the text screen using
                    graphic ascii characters.
        Prototype:  (box col row ecol erow attr btype)
        Arguments:  <int>     col  upper left corner column position
                    <int>     row  upper left corner row position
                    <int>     ecol                lower right corner
                                                  column position
                    <int>     erow                lower right corner row
                                                  position
                    <int>     attr                optional color
                                                  attribute [default
                                                  color symbol]
                    <int>     btype               optional border type
                                                  [default single line]
        Returns:    none
        Notes:      does not erase the area inside the box
        Example:    (box 10 2 70 18 23 1)

                     ----------------------------------------

        Function:   cls                                             Video

        Synopsis:   clear text screen to optional color attribute
        Prototype:  (cls attr)
        Arguments:  <int>     attr                optional color
                                                  attribute
        Returns:    none
        Notes:
        Example:    (cls 23) ;;; clear screen using light grey on blue
                    attribute

                     ----------------------------------------

        Function:   get_video                                       Video

        Synopsis:   get current text screen video parameters
        Prototype:  (get_video)
        Arguments:  none



        ELF Functions                                             page 13


        Returns:    <list>
                    cols      <int>               width of text screen
                                                  (usually 80)
                    rows      <int>               height of text screen
                                                  (usually 25)
                    mode      <int>               video mode
                    page      <int>               video page
        Notes:
        Example:    (setq vid      (get_video)
                              cols                (car vid)
                              rows                (cadr vid))

                     ----------------------------------------

        Function:   printf                                          Video

        Synopsis:   formatted "C" type print to text screen or graphics
                    command prompt area
        Prototype:  (printf format ...)
        Arguments:  format    <string>            conversion
                                                  specification string
        Returns:    ...                           a <string>, <int> or
                                                  <float> arguments for
                                                  each format specifier
                                                  in the format parameter
        Notes:      see a "C" language text or compiler library
                    documentation
        Example:    (printf "%-10s%10.2f  %d" strvar floatvar intvar)

                     ----------------------------------------

        Function:   prts                                            Video

        Synopsis:   fast write to text screen at col, row position with
                    optional attribute
        Prototype:  (prts col row string attr)
        Arguments:  col       <int>               screen column position
                    row       <int>               screen row position
                    string    <str>               text string
                    attr      <int>               optional color
                                                  attribute
        Returns:    none
        Notes:      uses direct video buffer write for speed
        Example:    (prts 40 10 "Hello World" 23)

                     ----------------------------------------

        Function:   puts                                            Video

        Synopsis:   fast write to text screen at cursor position with
                    optional attribute
        Prototype:  (puts string attr)



        ELF Functions                                             page 14


        Arguments:  string    <str>               text string
                    attr      <int>               optional color
                                                  attribute
        Returns:    none
        Notes:      uses direct video buffer write for speed
        Example:    (puts "Hello World" 23)

                     ----------------------------------------

        Function:   restore_screen                                  Video

        Synopsis:   restores a previously captured text screen
        Prototype:  (restore_screen)
        Arguments:  none
        Returns:    1 if successful, nil otherwise
        Notes:      the cursor position and size are not restored (use
                    get_cursor/set_cursor)
        Example:    see save_screen

                     ----------------------------------------

        Function:   save_screen                                     Video

        Synopsis:   captures the contents of the text screen to a memory
                    buffer
        Prototype:  (save_screen)
        Arguments:  none
        Returns:    1 if successful, nil otherwise
        Notes:      only one buffer is allocated, subsequent use will
                    overwrite any previous contents of the buffer
        Example:    (save_screen)                 ;;; take a picture of
                                                  the screen
                    ;;; do something that messes up the screen
                    (restore_screen)              ;;; put it back the way
                                                  that it was

                     ----------------------------------------

        Function:   scr_fill                                        Video

        Synopsis:   fill a rectangle of the text screen with a character
                    and color attribute
        Prototype:  (scr_fill col row cols rows ch attr)
        Arguments:  col       <int>               upper left column
                                                  position
                    row       <int>               upper left row position
                    cols      <int>               lower right column
                                                  position
                    rows      <int>               lower right row
                                                  position
                    ch        <int>               character as an integer
                    attr      <int>               color attribute
        Returns:    none



        ELF Functions                                             page 15


        Notes:
        Example:    (setq vid (get_video) vcols (car vid) vrows (cadr
                    vid))
                    (scr_fill 0 0 vcols vrows (ascii "°") 23) ;;;
                              fill entire screen with patterned
                              lightgrey on blue

                     ----------------------------------------

        Function:   scr_printf                                      Video

        Synopsis:   formatted "C" type print to text screen using direct
                    video buffer write
        Prototype:  (scr_printf format ...)
        Arguments:  format    <string>            conversion
                                                  specification string
        Returns:    ...                           any number of <string>,
                                                  <int> or <float>
                                                  arguments
        Notes:      see a "C" language text or compiler library
                    documentation
        Example:    see printf

                     ----------------------------------------

        Function:   set_color                                       Video

        Synopsis:   sets the internal "color" variable for use by
                    subsequent uses of routines which can use the default
                    color (r11)
        Prototype:  (set_color attr)
        Arguments:  attr      <int>               color attribute
        Returns:    for release 12 the AutoLISP symbol COLOR is used to
                    set the default color
        Notes:      (set_color 23)
        Example:

                     ----------------------------------------

        Cursor Functions

        The cursor functions provide a means to control  the location and
        appearance of  the screen  cursor.  Several of  the video  screen
        write  functions print at the cursor location, (gotoxy) positions
        the  cursor  and  (getxy) returns  the  current  cursor location.
        (get_cursor) returns the  cursor shape and (set_cursor)  sets the
        cursor shape  (start and ending  scan lines).  (set_cursor 32  0)
        will also hide the cursor.

                     ----------------------------------------



        ELF Functions                                             page 16


        Function:   get_cursor                                     Cursor

        Synopsis:   get cursor size / shape
        Prototype:  (get_cursor)
        Arguments:
        Returns:    <list>
                    start     <int>               start scan line
                    end       <int>               end scan line
        Notes:
        Example:    (setq save_cur (get_cursor)) ;;; save cursor shape

                     ----------------------------------------

        Function:   getxy                                          Cursor

        Synopsis:   get cursor screen coordinates
        Prototype:  (getxy)
        Arguments:
        Returns:    <list>
                    col       <int>               screen column position
                    row       <int>               screen row position
        Notes:
        Example:    (setq pos (getxy) col (car pos) row (cadr pos))

                     ----------------------------------------

        Function:   gotoxy                                         Cursor

        Synopsis:   position the screen cursor
        Prototype:  (gotoxy col row)
        Arguments:  col       <int>               screen column (x)
                                                  position
                    row       <int>               screen row (y) position
        Returns:
        Notes:
        Example:    (gotoxy 0 0) ;;; home cursor

                     ----------------------------------------

        Function:   set_cursor                                     Cursor

        Synopsis:   set cursor size; start to end scan lines
        Prototype:  (set_cursor start end)
        Arguments:  start     <int>               start scan line
                    end       <int>               end scan line
        Returns:



        ELF Functions                                             page 17


        Notes:      full cursor size is different depending on video
                    mode, the CGA cursor is 8 scan lines high, the
                    monochrome ,EGA, and VGA cursors are 14 scan lines
                    high. Specifying 32 as the start scan line will hide
                    the cursor.
        Example:    (set_cursor 0 13)  ;;; full block cursor
                    (set_cursor 12 13) ;;; normal cursor
                    (set_cursor 32 0)  ;;; hide cursor

                     ----------------------------------------

        Window Functions

        The ELF text screen window system rivals many commercial compiled
        language  function libraries. It provides the programmer with the
        tools  to  produce a  professional  "look and  feel"  to AutoLISP
        programs.

        When a window is opened, the screen text under the window and its
        border and shadow are saved. When the window is closed the screen
        is restored to its previous state. There is no practical limit to
        the number of windows open at on time.

        Only  the topmost  window  can be  written  to  using the  window
        writing routines (eg wputs,  wprts, etc). If you wish to write to
        a window other  than the topmost window,  you can do so,  but you
        must  use the screen writing routines, calculate cursor position,
        and otherwise maintain the window yourself.

        When no color attribute is specified in a  window write function,
        the window  attribute will  be used  by default,  not the  symbol
        "color" as used by screen writing functions.

                     ----------------------------------------

        Function:   set_menu_help                                  Window

        Synopsis:   sets the user help string list for wmenu
        Prototype:  (set_menu_help <slist>)
        Arguments:  <slist>   a string list to be displayed when the F1
                              key is pressed while in (wmenu). The first
                              item in the list will be the help window
                              title.
        Returns:



        ELF Functions                                             page 18


        Notes:      In release 12 or higher the symbol MENU_HELP can be
                    used to set the help string. In release 12
                    (set_menu_help) will also set this symbol. The symbol
                    MENU_HELP can be local to a particular function or
                    global in scope.

                    The user can display the default help screen by
                    pressing F1 the second time.
        Example:    (set_menu_help '("[ My Help Screen ]" "" "This is my
                    help message"))

                     ----------------------------------------

        Function:   wclose                                         Window

        Synopsis:   closes the top window restoring the screen under the
                    window
        Prototype:  (wclose)
        Arguments:  none
        Returns:    number of remaining open windows if successful or nil
        Notes:
        Example:

                     ----------------------------------------

        Function:   wcloseall                                      Window

        Synopsis:   closes all windows
        Prototype:  (wcloseall)
        Arguments:  none
        Returns:
        Notes:      use at the end of programs to close any remaining
                    open windows
        Example:

                     ----------------------------------------

        Function:   wclreol                                        Window

        Synopsis:   erase from window cursor to end of line
        Prototype:  (wclreol)
        Arguments:
        Returns:    none
        Notes:
        Example:

                     ----------------------------------------

        Function:   wcls                                           Window

        Synopsis:   clear window to optional color attribute
        Prototype:  (wcls attr)



        ELF Functions                                             page 19


        Arguments:  <int>     attr                optional color
                                                  attribute
        Returns:    none
        Notes:
        Example:    (wcls 23) ;;; clear window using light grey on blue
                    attribute

                     ----------------------------------------

        Function:   werase_line                                    Window

        Synopsis:   erase a line of text from a window
        Prototype:  (werase_line line)
        Arguments:  line      <int>               window row to erase
        Returns:    none
        Notes:
        Example:    (werase_line 2) ;;; erase line 2

                     ----------------------------------------

        Function:   wgetstr                                        Window

        Synopsis:   open a window centered on the text screen, prints a
                    prompt on the top border and gets string input.
        Prototype:  (wgetstr prompt default length wattr battr btype)
        Arguments:  prompt    <string>            prompt string
                    default   <string>            optional default string
                                                  / string to edit
                    len       <int>               optional string length
                                                  (default = 78)
                    wattr     <int>               optional window
                                                  attribute (default =
                                                  color symbol)
                    battr     <int>               optional border
                                                  attribute (optional =
                                                  wattr)
                    btype     <int>               optional border type
                                                  (default = double)
        Returns:    the edited string or nil if the string is empty
        Notes:      see strget and wpopup
        Example:    (wgetstr "Enter text" "Hello World" 60 23 23 33)

                     ----------------------------------------

        Function:   wgetdrive                                      Window

        Synopsis:   select a disk drive from a menu, all valid drives are
                    listed with their respective drive type (eg
                    removable/floppy, fixed, network, and redirected
                    devices)
        Prototype:  (wgetdrive col row wattr battr hattr btype)



        ELF Functions                                             page 20


        Arguments:  col       <int>               optional upper left
                                                  column position
                                                  (default = centered)
                    row       <int>               optional upper left row
                                                  position (default =
                                                  centered)
                    wattr     <int>               optional window
                                                  attribute (default =
                                                  color variable)
                    battr     <int>               optional border
                                                  attribute
                    hattr     <int>               optional highlight
                                                  (cursor) bar attribute
                    btype     <int>               optional border type
        Returns:    the disk drive as an integer (A:=1, B:=2, etc)
        Notes:
        Example:    (setq drive (wgetdrive 10 5))

                     ----------------------------------------

        Function:   wgetfile                                       Window

        Synopsis:   select a file from a menu of DOS files from the
                    current directory. The user can change directories
                    and access all available disk drives.
        Prototype:  (wgetfile filespec fileattr col row wattr battr hattr
                    btype)
        Arguments:  filespec  <string>            wildcard filespec (eq
                                                  *.DAT)
                    fileattr  <int>               file attribute mask
                                                  (see findfirst)
                    col       <int>               optional upper left
                                                  column position
                                                  (default = -1 centered)
                    row       <int>               optional upper left row
                                                  position (default = -1
                                                  centered)
                    wattr     <int>               optional window
                                                  attribute (default =
                                                  color variable)
                    battr     <int>               optional border
                                                  attribute
                    hattr     <int>               optional highlight
                                                  (cursor) bar attribute
                    btype     <int>               optional border type
        Returns:    the full qualified pathname of the selected file or
                    nil if <Esc> is pressed.
        Notes:      The drive select menu is activated by pressing <Alt-
                    D>.
        Example:    (setq filename (wgetfile "*.TXT" 33 -1 -1 23 23 70
                    17)

                     ----------------------------------------



        ELF Functions                                             page 21


        Function:   wgetxy                                         Window

        Synopsis:   get window screen position
        Prototype:  (wgetxy)
        Arguments:  none
        Returns:    <list>
                    col       <int>               window column position
                    row       <int>               window row position
        Notes:
        Example:    (setq 
                      wcur (getxy)
                      wcol (car wcur)             ;;; cursor column
                      wrow (cadr wcur)            ;;; cursor row
                    )

                     ----------------------------------------

        Function:   wgotoxy                                        Window

        Synopsis:   move window cursor
        Prototype:  (wgotoxy col row)
        Arguments:  col       <int>               window column position
                    row       <int>               window row position
        Returns:    none
        Notes:
        Example:    (wgotoxy 0 0) ;;; home cursor in window

                     ----------------------------------------

        Function:   winfo                                          Window

        Synopsis:   gets the top window size and position
        Prototype:  (winfo)
        Arguments:  none
        Returns:    <list>
                    col       <int>               upper left column
                                                  position
                    row       <int>               upper left row position
                    cols      <int>               lower right column
                                                  position
                    rows      <int>               lower right row
                                                  position
        Notes:
        Example:    (setq     w    (winfo)
                              wcol                (car w)
                              wrow                (cadr w)
                              wcols               (caddr w)
                              wrows               (cadddr w))

                     ----------------------------------------



        ELF Functions                                             page 22


        Function:   wmenu                                          Window

        Synopsis:   opens a centered window and displays a menu. The user
                    can then select one of the displayed items.
        Prototype:  (wmenu slist wattr battr hattr btype shadow title)
        Arguments:  slist     <list>              list of strings to
                                                  display in the menu
                    col       <int>               optional upper left
                                                  column position
                                                  (default = centered)
                    row       <int>               optional upper left row
                                                  position (default =
                                                  centered)
                    wattr     <int>               optional window color
                                                  attribute (default =
                                                  "color" symbol)
                    battr     <int>               optional border
                                                  attribute (default =
                                                  wattr)
                    hattr     <int>               optional highlight bar
                                                  attribute (default =
                                                  reversed wattr)
                    btype     <int>               optional border type
                                                  (default = double line)
                    title     <string>            optional window title
        Returns:    <list>
                    <int>     0 based item number selected
                    <int>     keycode of key pressed to exit menu



        ELF Functions                                             page 23


        Notes:      If the list of items is longer that can be displayed
                    in one window then the user can page through the list
                    with the cursor keys. Keys are as follows:
                    Key       Meaning             
                    <Up>      move cursor up
                    <Down>    move cursor down
                    <PgUp>    move up one page
                    <PgDn>    move down one page
                    <Enter>   exit
                    <Ctrl-Enter>   exit
                    <Esc>     exit
                    <F1>      Display help screen. If the symbol
                              MENU_HELP is defined, its contents will be
                              displayed. The function (set_menu_help)
                              can be used to set MENU_HELP in release 10
                              or 11. The user can press F1 the second
                              time to display the default help text.
                    <End>     move to last item
                    <Home>    move to first item
                    <char>    any alphanumeric key will move the cursor
                              to the next item starting in that
                              character
        Example:    (setq 
                      item (wmenu '("Yes" "No") 23 23 1 1 "?"))
                      yn (car item)
                      key (cadr item)
                    )
                    (if(/= key EscKey) (doit) (exit))

                     ----------------------------------------

        Function:   wmsg                                           Window

        Synopsis:   opens a centered window, displays a message and
                    optionally waits for a keystroke and closes the
                    window
        Prototype:  (wmsg str wait attr battr btype)
        Arguments:  str       <string>            the message string
                    wait      <int>               optional, 1 = wait for
                                                  a keystroke then close
                                                  window (default) else
                                                  leave window open
                    wattr     <int>               optional window color
                                                  attribute (default =
                                                  color symbol)
                    wattr     <int>               optional border color
                                                  attribute (default =
                                                  wattr)
                    btype     <int>               optional border type
                                                  (default = double line
                                                  with drop shadow)
        Returns:    if wait=1 then keycode entered to close window is
                    returned



        ELF Functions                                             page 24


        Notes:
        Example:    (setq key (wmsg "Continue ?[Y/N]" 1 23 23 1))

                     ----------------------------------------

        Function:   wopen                                          Window

        Synopsis:   open a window on the text screen with specified
                    location, size, border, and colors; saving the area
                    under the window
        Prototype:  (wopen col row cols rows wattr battr btype)
        Arguments:  col       <int>               upper left column
                                                  position (-1 =
                                                  centered)
                    row       <int>               upper left row position
                                                  (-1 = centered)
                    cols      <int>               number of columns
                                                  (including border)
                    rows      <int>               number of rows
                                                  (including border)
                    wattr     <int>               optional window
                                                  attribute (default =
                                                  color variable)
                    battr     <int>               optional border
                                                  attribute
                    btype     <int>               optional border type:
                    Type      Meaning             
                    0         no border
                    1         single line
                    2         double line
                    3         double vertical
                    4         double horizontal
                    5         solid
                    btype + 8  = hilight upper left sides of border for
                    raised effect
                    btype + 16 = hilight lower right sides of border
                    btype + 32 = add drop shadow to right and lower sides
                    of window

        Returns:    <int>     the number of windows currently open
        Notes:      flips screen to the text screen
        Example:    (wopen 20 5 40 10 23 23 2)

                     ----------------------------------------

        Function:   wpopup                                         Window

        Synopsis:   open a window centered on the text screen
        Prototype:  (wpopup cols rows wattr battr)



        ELF Functions                                             page 25


        Arguments:  cols      <int>               number of column wide
                                                  (including border)
                    rows      <int>               number of rows high
                                                  (including border)
                    wattr     <int>               optional window
                                                  attribute (default =
                                                  color symbol)
                    battr     <int>               optional border
                                                  attribute (optional =
                                                  wattr)
                    btype     <int>               optional border type
                                                  (default = double)
        Returns:    the number of windows currently open
        Notes:
        Example:    (wpopup 40 10 23 23)

                     ----------------------------------------

        Function:   wprintf                                        Window

        Synopsis:   printf to window at window cursor position
        Prototype:  (wprintf format ...)
        Arguments:  see printf
        Returns:
        Notes:      see printf
        Example:

                     ----------------------------------------

        Function:   wprts                                          Window

        Synopsis:   write to window at col, row position with optional
                    attribute
        Prototype:  (wprts col row string attr)
        Arguments:  col       <int>               window column position
                    row       <int>               window row position
                    string    <str>               text string
                    attr      <int>               optional color
                                                  attribute
        Returns:    none
        Notes:
        Example:    (wprts 0 3 "Hello World" 23)

                     ----------------------------------------

        Function:   wputcen                                        Window

        Synopsis:   write a centered string to window at window cursor
                    row position
        Prototype:  (wputcen str)
        Arguments:  str       <string>            the string to print
        Returns:



        ELF Functions                                             page 26


        Notes:      cursor column position is ignored and the string is
                    centered within the window
        Example:

                     ----------------------------------------

        Function:   wputs                                          Window

        Synopsis:   write to window at window cursor position with
                    optional attribute
        Prototype:  (puts string attr)
        Arguments:  string    <str>               text string
                    attr      <int>               optional color
                                                  attribute
        Returns:    none
        Notes:
        Example:    (wputs "Hello World" 23)

                     ----------------------------------------

        Function:   wscroll                                        Window

        Synopsis:   scroll window text
        Prototype:  (wscroll dir start end lines)
        Arguments:  dir       <int>               direction; 0 = up
                                                  (default), 1 = down
                    start     <int>               start row to scroll
                                                  (default = 0)
                    end       <int>               end row  (default =
                                                  last window row)
                    line      <int>               optional number of
                                                  lines to scroll
                                                  (default = 1)
        Returns:    none
        Notes:
        Example:    (wscroll) ;;; scroll entire window up 1 line
                    (wscroll 1 0 2 1) ;;; scroll first 3 window rows up 1
                    line


                     ----------------------------------------

        Function:   wshadow                                        Window

        Synopsis:   adds a drop shadow to the top (last opened) window
        Prototype:  (wshadow attr)
        Arguments:  attr      <int>               color attribute
                                                  (default lightgrey on
                                                  black)
        Returns:



        ELF Functions                                             page 27


        Notes:
        Example:    (wshadow 23)

                     ----------------------------------------

        Function:   wtitle                                         Window

        Synopsis:   prints on the border of a window in one of 6
                    positions
        Prototype:  (wtitle <str> [<pos>])
        Arguments:  str       <string>            title message
                    pos       <int>               optional position to
                                                  place string
                    Value     Meaning             
                    0         top left (default)
                    1         top center
                    2         top right
                    3         bottom left
                    4         bottom center
                    5         bottom right
        Returns:
        Notes:      If no windows are open wtitle has no effect. Titles
                    will be trimmed to fit available space on the border.
        Example:    (wtitle "My Window" 1)

                     ----------------------------------------

        Keyboard Functions

        The ELF keyboard functions add both C library functions to read a
        character from the  keyboard and functions  to read the  keyboard
        directly. The function  (getkey) returns a unique  value for each
        key on  the PC keyboard.  The file  ELF.LSP contains symbols  for
        many (but not all)  of the PC function and control  keys. You can
        determine  the value  of  any key  by  entering  (getkey) at  the
        Command: prompt and then pressing the desired key.

        The  function (key_stuff)  provides  a  means  to  control  other
        programs when no other means exists to execute a command  or feed
        data to another command or program. The function is limited to 15
        characters unless  you have installed  a TSR keyboard  handler or
        driver which expands the size of the PC keyboard buffer.

                     ----------------------------------------

        Function:   getch                                             Key

        Synopsis:   get a character from the keyboard
        Prototype:  (getch)
        Arguments:
        Returns:    <int>     key character as an integer



        ELF Functions                                             page 28


        Notes:
        Example:    (setq char (chr(getch))) ;;; character as a string

                     ----------------------------------------

        Function:   getche                                            Key

        Synopsis:   get a character from the keyboard with echo
        Prototype:  (getche)
        Arguments:
        Returns:    <int>     key character as an integer
        Notes:      see getch
        Example:

                     ----------------------------------------

        Function:   getkey                                            Key

        Synopsis:   get a keystroke from the keyboard
        Prototype:  (getkey)
        Arguments:
        Returns:    <int>     keycode             The lower byte of
                                                  keycode contains the
                                                  key character and the
                                                  upper byte contains the
                                                  keyboard scancode.
        Notes:      The value returned by getkey is unique for (nearly)
                    every key on the PC keyboard. The file KEYS.LSP
                    contains a list of keycodes of cursor movement and
                    function keys. The keycode of any key can be
                    determined by executing (getkey) interactively.
        Example:    (setq 
                      c       (getkey)            ;;; the keycode
                      char    (chr(lobyte c))     ;;; key character as a
                                                  string
                      scode   (hibyte c)          ;;; keyboard scan code
                    )

                     ----------------------------------------

        Function:   kbhit                                             Key

        Synopsis:   checks the keyboard buffer for a waiting keystroke
        Prototype:  (kbhit)
        Arguments:
        Returns:    a non-zero value if a key is waiting
        Notes:
        Example:    (while (not(kbhit)))

                     ----------------------------------------



        ELF Functions                                             page 29


        Function:   key_clear                                         Key

        Synopsis:   clears the keyboard buffer of any pending keystrokes
        Prototype:  (key_clear)
        Arguments:
        Returns:
        Notes:
        Example:    (key_clear)    ;;; clear the keyboard
                    (setq key (getkey))           ;;; get a keystroke

                     ----------------------------------------

        Function:   key_ready                                         Key

        Synopsis:   returns immediately with a waiting key
        Prototype:  (key_ready)
        Arguments:
        Returns:    <int>     key                 or nil
        Notes:      key_ready checks the keyboard buffer and immediately
                    returns the next keycode (leaving it in the buffer)
                    or nil if no key is waiting
        Example:    (while (not(key_ready)))

                     ----------------------------------------

        Function:   key_stat                                          Key

        Synopsis:   gets the state of keyboard shift and other special
                    keys
        Prototype:  (key_stat)
        Arguments:
        Returns:    <int>     a bit coded field as follows:
                    Bit       Mask                Meaning
                                                  
                    0         1    Right shift key pressed
                    1         2    Left shift key presses
                    2         4    Ctrl key pressed
                    3         8    Alt key pressed
                    4         16   ScrollLock On
                    5         32   NumLock On
                    6         64   Capslock On
                    7         128  Insert On
        Notes:
        Example:

                     ----------------------------------------

        Function:   key_stuff                                         Key

        Synopsis:   "pushes" keys into the keyboard buffer
        Prototype:  (key_stuff str)
        Arguments:  str       <string>            up to 15 characters
        Returns:



        ELF Functions                                             page 30


        Notes:      stuffs the keyboard buffer to control "ill behaved"
                    programs. The DOS keyboard buffer can hold a maximum
                    of 15 keys, additional keys are ignored.
        Example:    (key_stuff ".QUIT\nY\n")

                     ----------------------------------------

        Directory Functions

        Elf contains a full suite of functions to read and manipulate the
        DOS file  directory system. In  addition to C  library functions,
        ELF  provides macro  functions  to return  a list  of  valid disk
        drives, directories, and files.

                     ----------------------------------------

        Function:   access                                      Directory

        Synopsis:   determines if a file exists and can be accessed by
                    mode
        Prototype:  (access path mode)
        Arguments:  <string> path
                    <int> mode:
                    Value     Test For            
                    0         existence only
                    1         read permission
                    2         write permission
                    3         read and write permission
        Returns:    1 if true, nil otherwise
        Notes:
        Example:    (access "C:\ACAD\FOO.DAT" 2)  ;;;checks for the
                                                  existence and write
                                                  permission

                     ----------------------------------------

        Function:   chdir                                       Directory

        Synopsis:   change disk directory
        Prototype:  (chdir path)
        Arguments:  path      <string>            DOS path
        Returns:    <string>  current directory after successful
                              execution or nil otherwise.
        Notes:      If a drive different from the current drive is
                    specified, the directory on the specified drive will
                    be changed. Does not log to a different drive.
        Example:    (chdir "\acad\dwgs")

                     ----------------------------------------



        ELF Functions                                             page 31


        Function:   chpath                                      Directory

        Synopsis:   change current disk drive and directory
        Prototype:  (chpath path)
        Arguments:  path      <string>            DOS path including
                                                  drive letter
        Returns:    <string> current directory after successful execution
                    or nil otherwise.
        Notes:
        Example:    (chpath "d:\dwgs")

                     ----------------------------------------

        Function:   disk_ready                                  Directory

        Synopsis:   verifies that a removable (floppy) drive is ready and
                    readable
        Prototype:  (disk_ready drive)
        Arguments:  drive     <int>               drive to check (1=A:,
                                                  2=B:, etc)
        Returns:    1 if true or nil otherwise
        Notes:
        Example:    (disk_ready 1) ;;; verify that drive A: is ready

                     ----------------------------------------

        Function:   disk_type                                   Directory

        Synopsis:
        Prototype:  (disk_type drive)
        Arguments:  drive     <int>               drive to check (1=A:,
                                                  2=B:, etc)
        Returns:    0         removable (floppy) disk
                    1         fixed (hard) disk
                    2         network drive
                    3         redirected device
                    nil       invalid drive
        Notes:
        Example:

                     ----------------------------------------

        Function:   disk_valid                                  Directory

        Synopsis:   verifies that a disk drive is a valid device (but not
                    necessarily ready if a removable/floppy drive)
        Prototype:  (disk_valid drive)
        Arguments:  drive     <int>               drive to check (1=A:,
                                                  2=B:, etc)
        Returns:    1 if true or nil otherwise



        ELF Functions                                             page 32


        Notes:
        Example:    (disk_valid 6) ;;; verify that drive F: is valid

                     ----------------------------------------

        Function:   erasefile                                   Directory

        Synopsis:   erase file(s)
        Prototype:  (erasefile filename)
        Arguments:  filename <string> - file to erase
        Returns:    1 - success
                    0 - fail
        Notes:
        Example:    (erasefile "thisfile.dat")

                     ----------------------------------------

        Function:   file_exists                                 Directory

        Synopsis:   determines if a file exists
        Prototype:  (file_exists path)
        Arguments:  <string> path
        Returns:    1 if true, nil otherwise
        Notes:
        Example:    (file_exists "C:\ACAD\FOO.DAT")

                     ----------------------------------------

        Function:   findfirst                                   Directory

        Synopsis:   finds the first instance of a file who's name and
                    directory attributes match the arguments.
        Prototype:  (findfirst filespec attribute)



        ELF Functions                                             page 33


        Arguments:  filespec <string>             optional - a filespec
                                                  which can include
                                                  wildcard characters in
                                                  the file specification
                                                  (default *.*)
                    attribute <integer>           optional - a value
                                                  between 0 and 255.
                                                  (default 33) The
                                                  following values can be
                                                  ORed or added to
                                                  produce the needed
                                                  attribute.

                    Value     Attribute           
                    1         Archive file
                    4         Hidden file
                    8         Normal file
                    16        Read only file
                    32        System file
                    64        Subdirectory
                    128       Volume ID
        Returns:    an AutoLISP list if successful or nil otherwise.
                    filename  <string> includes file extension
                    filesize  <string> size of the file in bytes.
                    date      <string> the file date
                    time      <string> the file time
                    attribute <int> the files' attribute

                    Example: ("FILENAME.EXT" "134562" "3/31/92" "11:21a"
                    9)
        Notes:      Findfirst allows you to use the * and ? wildcard
                    characters to search the file system directory
                    structure. If the file is found then the function
                    returns information about the file in an AutoLISP
                    list. If the attribute parameter is 255 then all
                    files and directories will match the attribute. The
                    combination of attribute = 255 and wildcard = "*.*"
                    will match all files, all directories, and the volume
                    id if it exists from the current subdirectory.

                    Files with no attributes will always be returned.
                    Therefore in order to retrieve only directories then
                    files with an attribute value of 0 must be filtered
                    out.
        Example:    (findfirst "*.DWG" 1+8+16)

                     ----------------------------------------

        Function:   findnext                                    Directory

        Synopsis:   finds the next occurrence of the file specification
                    and attribute after a findfirst call
        Prototype:  (findnext)



        ELF Functions                                             page 34


        Arguments:  none
        Returns:    AutoLISP list for the file. (see findfirst)
        Notes:
        Example:    (setq fn (findfirst 33 "*.DAT"))
                    (while (boundp 'fn))
                      (printf "\n%s" (car fn)))
                      (setq fn (findnext)
                    )

                     ----------------------------------------

        Function:   fullpath                                    Directory

        Synopsis:   expands a partial path into a full DOS path string
        Prototype:  (fullpath path)
        Arguments:  path <string> a relative or partial path string (eg
                    "c:filename.ext"
        Returns:    <string> the full path string (eg
                    "C:\ACAD\FILENAME.EXT")
        Notes:      the file does not have to exist
        Example:    (fullpath "D:FILE.DAT") ;;; might return
                    "D:\DIR1\FILE.DAT

                     ----------------------------------------

        Function:   getdir                                      Directory

        Synopsis:   returns a string with the current drive:\path
        Prototype:  (getdir)
        Arguments:  none
        Returns:    <string>  current directory path
        Notes:
        Example:    (setq curdir (getdir))

                     ----------------------------------------

        Function:   getdiskfree                                 Directory

        Synopsis:   returns size statistics in the specified drive number
                    as a list
        Prototype:  (getdiskfree 3)
        Arguments:  <int> drive number (Current=0, A=1, B=2, C=3, etc)
        Returns:    <list>(<int> total bytes <int> free bytes <int>
                    sector size <int> sectors per cluster)
        Notes:
        Example:    (setq     dstat       (getdiskfree 0)
                              sector      (cadddr dstat)
                              cluster     (* sector (caddr dstat))
                              drive_bytes (* cluster (car dstat))
                              free_bytes  (* cluster (cadr dstat))
                    )

                     ----------------------------------------



        ELF Functions                                             page 35


        Function:   getdisk                                     Directory

        Synopsis:   returns the current drive number (A=1, B=2, C=3, etc)
        Prototype:  (getdisk)
        Arguments:  none
        Returns:    <int> current drive
        Notes:
        Example:    (setq DriveStr (sprintf "%c:" (+(getdisk)(1-(ascii
                    "A"))))

                     ----------------------------------------

        Function:   load_dirs                                   Directory

        Synopsis:   returns a list of strings containing file directories
                    from the current directory
        Prototype:  (load_dirs)
        Arguments:  none
        Returns:    <list> A list of directories if successful or nil
                    otherwise
        Notes:      uses DOS findfirst and findnext
        Example:    (setq dirs (load_dirs))

                     ----------------------------------------

        Function:   load_drives                                 Directory

        Synopsis:   returns a list of strings containing all valid disk
                    drives
        Prototype:  (load_drives)
        Arguments:  none
        Returns:    <list> A list of drives if successful or nil
                    otherwise
        Notes:
        Example:    (setq drives (load_drives))

                     ----------------------------------------

        Function:   load_files                                  Directory

        Synopsis:   returns a list of strings containing files matching a
                    filespec and directory attribute
        Prototype:  (load_files filespec attribute)
        Arguments:  <string>  filespec            optional path and file
                                                  specification, default:
                                                  "*.*"
        Returns:    <int>     attribute           optional bit coded file
                                                  attributes (see
                                                  findfirst), default: 33
                    <list> A list of files if successful or nil otherwise



        ELF Functions                                             page 36


        Notes:
        Example:    (setq files (qsort(load_files "D:\DWGS\*.DWG")))

                     ----------------------------------------

        Function:   makepath                                    Directory

        Synopsis:   Combines the four components into a full DOS path
                    string
        Prototype:  (makepath drive dir name ext)
        Arguments:  see (splitpath)
        Returns:    <string> full path string
        Notes:
        Example:    (makepath "D:" "\ACAD\SUPPORT\" "ACAD" ".LSP")

                     ----------------------------------------

        Function:   mkdir                                       Directory

        Synopsis:   creates a new directory
        Prototype:  (mkdir dirname)
                    directory <string> directory to create
        Arguments:  <string>  directory name if successful or nil
                              otherwise
        Returns:
        Notes:      (mkdir "\newdir")
        Example:

                     ----------------------------------------

        Function:   rmdir                                       Directory

        Synopsis:   removes (deletes) a directory
        Prototype:  (rmdir dirname)
        Arguments:  directory      <string> directory to remove
        Returns:    <string> current directory if successful or nil
                    otherwise
        Notes:
        Example:    (rmdir "\olddir")

                     ----------------------------------------

        Function:   setdisk                                     Directory

        Synopsis:   logs to the specified disk drive
        Prototype:  (setdisk drive)
        Arguments:  drive     <int>               drive number (A=1, B=2,
                                                  C=3, etc)
        Returns:    <int>     current drive if successful or nil
        Notes:
        Example:    (setdisk 3) ;;; make drive C: current

                     ----------------------------------------



        ELF Functions                                             page 37


        Function:   splitpath                                   Directory

        Synopsis:   splits a DOS path string into its four components
        Prototype:  (splitpath path)
        Arguments:  path      <string> full DOS path to a file
        Returns:    a <list> containing four strings:
                    drive     the drive character followed by a ':' (eg
                              "C:")
                    dir       the directory (eg "\ACAD\SUPPORT"
                    name      the name of the file (eg "ACAD")
                    ext       a period followed by the file extension
                              (eg ".LSP")
        Notes:
        Example:    (setq
                      plist (splitpath "D:\ACAD\SUPPORT\ACAD.LSP")
                      drive (car plist)           ;;; "D:"
  dir (cadr plist)            ;;; "\ACAD\SUPPORT\"
                      name (caddr plist)          ;;; "ACAD"
                      ext (cadddr plist)          ;;; ".LSP"
                    )

                     ----------------------------------------

        Function:   unlink                                      Directory

        Synopsis:   erase file(s)
        Prototype:  (unlink filename)
        Arguments:  filename <string> - file to erase
        Returns:    1 - success
                    0 - fail
        Notes:      unlink and erasefile are identical
        Example:    (unlink "thisfile.dat")

                     ----------------------------------------

        File Functions

        ELF  contains file  handling functions  to  speed file  handling.
        AutoLISP provides  functions to read  and write  to text files  a
        character and a  line at a time.  ELF adds functions to  read and
        write the entire file in one step. 

        The function (read_file)  will return the  contents of an  entire
        file and  can be used  to quickly load  the contents of  the file
        into  an AutoLISP symbol.  (write_file) inverses the  process and
        will write  the entire contents of  an AutoLISP string  list to a
        file. These functions are much faster than looping through a list
        and reading/writing a line at a time with AutoLISP.

                     ----------------------------------------



        ELF Functions                                             page 38


        Function:   copyfile                                         File

        Synopsis:   copies file(s)
        Prototype:  (copyfile source destination)
        Arguments:  <string>  source path
                    <string>  destination path
        Returns:    number of files copied if successful, nil otherwise
        Notes:      The destination can be a either a file or directory.
                    Both input and output streams are buffered to improve
                    copy speed.
        Example:    (copyfile "C:\ACAD\*.DAT" "D:")

                     ----------------------------------------

        Function:   look                                             File

        Synopsis:   displays an ASCII file to screen using the ELF file
                    viewer
        Prototype:  (look filespec)
        Arguments:  <filespec>     filename or wildcard filespec to view
        Returns:    1 if successful, nil otherwise
        Notes:
        Example:    (look "C:\ACAD\*.DOC"

                     ----------------------------------------

        Function:   movefile                                         File

        Synopsis:   moves / renames file(s)
        Prototype:  (movefile source destination)
        Arguments:  <string>  source path
                    <string>  destination path
        Returns:    number of files moved if successful, nil otherwise
        Notes:      destination must be on the same drive
        Example:    (movefile "C:\ACAD\*.DAT" "C:\DATDIR")

                     ----------------------------------------

        Function:   read_file                                        File

        Synopsis:   reads an ASCII file and returns a string list from
                    file records. Each line in the text file is parsed
                    into a string and appended to the returned list.
        Prototype:  (read_file filespec mode)
        Arguments:  <string>  filespec            file specification of
                                                  the file to read
                    <int>     mode                type of list to create
                                                  (see return value)



        ELF Functions                                             page 39


        Returns:    <list>    A list whose contents are dependant on
                              mode
                    Value     Meaning             
                    0 or nil  A list of strings
                    1         A list of dotted pairs containing a 0
                              based sequential value and a string
        Notes:      The dotted pair list can be accessed randomly using
                    the (assoc) function.
        Example:    (read_file "FOO.BAR" 1)

                     ----------------------------------------

        Function:   write_file                                       File

        Synopsis:   opens an ASCII file and writes a string list to the
                    file and then closes the file. Each string is placed
                    in the text file as a line of text.
        Prototype:  (write_file filespec type)
        Arguments:  <string>  filespec            file specification of
                                                  the file to write
                    <string>  type                how the file will be
                                                  opened, "a" appends to
                                                  the end of the file,
                                                  otherwise a new file
                                                  will be created and any
                                                  other character is
                                                  ignored.
                    <list>    A list of strings
        Returns:    <int>     the number of lines written
        Notes:
        Example:    (write_file "FOO.BAR" "a" "This is data") ;;; appends
                    a line to file FOO.BAR

                     ----------------------------------------

        Math Functions

        ELF expands the AutoLISP math library with additional math, trig,
        and logical functions.

                     ----------------------------------------

        Function:   |                                              Math

        Synopsis:   returns the result of a bitwise OR of the arguments
        Prototype:  (| ...)
        Arguments:  ...       <int>               any number of integer
                                                  values
        Returns:    <int>     the result of the bitwise OR
        Notes:
        Example:    (setq color (| lgrey blue_bg))

                     ----------------------------------------



        ELF Functions                                             page 40


        Function:   ||                                               Math

        Synopsis:   returns the result of a logical OR of the arguments
        Prototype:  (|| ...)
        Arguments:  ...       <int>               any number of integer
                                                  values
        Returns:    <int>     the result of the logical OR
        Notes:
        Example:

                     ----------------------------------------

        Function:   &                                                Math

        Synopsis:   returns the result of a bitwise AND of the arguments
        Prototype:  (& ...)
        Arguments:  ...       <int>               any number of integer
                                                  values
        Returns:    <int>     the result of the bitwise AND
        Notes:
        Example:

                     ----------------------------------------

        Function:   &&                                               Math

        Synopsis:   returns the result of a logical AND of the arguments
        Prototype:  (&& ...)
        Arguments:  ...       <int>               any number of integer
                                                  values
        Returns:    <int>     the result of the logical AND
        Notes:
        Example:

                     ----------------------------------------

        Function:   acos                                             Math

        Synopsis:   returns the inverse cosine of the argument
        Prototype:  (acos rad)
        Arguments:  rad       <real>              angle in radians
        Returns:    <real>
        Notes:
        Example:

                     ----------------------------------------

        Function:   asin                                             Math

        Synopsis:   returns the inverse sine of the argument
        Prototype:  (asin rad)
        Arguments:  rad       <real>              angle in radians
        Returns:    <real>



        ELF Functions                                             page 41


        Notes:
        Example:

                     ----------------------------------------

        Function:   ceil                                             Math

        Synopsis:   returns the smallest integer greater or equal to the
                    argument
        Prototype:  (ceil rval)
        Arguments:  rval      <real>
        Returns:    <real>
        Notes:
        Example:    (ceil 7.5)     ;;; returns 8.0
                    (ceil -7.5)    ;;; returns -7.0

                     ----------------------------------------

        Function:   cosh                                             Math

        Synopsis:   returns the hyperbolic cosine of the argument
        Prototype:  (cosh rad)
        Arguments:  rad       <real>              angle in radians
        Returns:    <real>
        Notes:
        Example:

                     ----------------------------------------

        Function:   dtr                                              Math

        Synopsis:   converts an angle in degrees to radians
        Prototype:  (dtr ang)
        Arguments:  ang       <real>              angle in degrees
        Returns:    <real>    the angle in radians
        Notes:
        Example:    (setq rad (dtr deg))

                     ----------------------------------------

        Function:   floor                                            Math

        Synopsis:   returns the largest integer not greater than the
                    argument
        Prototype:  (floor rval)
        Arguments:  rval      <real>
        Returns:    <real>
        Notes:
        Example:    (floor 7.5)  ;;; returns 7.0
                    (floor -7.5) ;;; returns -8.0

                     ----------------------------------------



        ELF Functions                                             page 42


        Function:   hibyte                                           Math

        Synopsis:   returns the upper (most significant) byte of an
                    integer
        Prototype:  (hibyte val)
        Arguments:  val       <int>               an integer value
        Returns:    <int>     an integer value containing the MSB
        Notes:
        Example:    (setq keycode (getkey) ;;; get a keypress
                      char (lobyte keycode) ;;;the character value
                      scancode (hibyte keycode) ;;; the keyboard scancode
                    )

                     ----------------------------------------

        Function:   lobyte                                           Math

        Synopsis:   returns the lower (least significant) byte of an
                    integer
        Prototype:  (lobyte val)
        Arguments:  val       <int>               an integer value
        Returns:    <int>     an integer value containing the LSB
        Notes:
        Example:    see hibyte

                     ----------------------------------------

        Function:   log10                                            Math

        Synopsis:   returns the logarithm to the base 10 of the argument
        Prototype:  (log10 x)
        Arguments:  x         <real>
        Returns:    <real>    or nil of x <= 0.0
        Notes:
        Example:

                     ----------------------------------------

        Function:   rand                                             Math

        Synopsis:   generates a pseudo random number
        Prototype:  (rand)
        Arguments:
        Returns:    <real>    a random value (actually a long integer)
        Notes:      the sequence has a period of 2^32
        Example:    (setq x (fix(rem(rand 10))))

                     ----------------------------------------

        Function:   round                                            Math

        Synopsis:   rounds a real value
        Prototype:  (round val places)



        ELF Functions                                             page 43


        Arguments:  val       <real>              the value to round
                    places    <int>               the number of places to
                                                  the right of the
                                                  decimal
        Returns:    <real>    the rounded value
        Notes:
        Example:    (setq pct (round val 2))

                     ----------------------------------------

        Function:   rtd                                              Math

        Synopsis:   converts an angle in radians to degrees
        Prototype:  (rtd ang)
        Arguments:  ang       <real>              angle in radians
        Returns:    <real>    the angle in degrees
        Notes:
        Example:    (setq deg (rtd rad))

                     ----------------------------------------

        Function:   sinh                                             Math

        Synopsis:   returns the hyperbolic sine of the argument
        Prototype:  (sinh rad)
        Arguments:  rad       <real>              angle in radians
        Returns:    <real>
        Notes:
        Example:

                     ----------------------------------------

        Function:   srand                                            Math

        Synopsis:   seeds the random number generator
        Prototype:  (srand i)
        Arguments:  i         <int>               optional seed value
                                                  (default = 1)
        Returns:
        Notes:
        Example:    (srand pi)

                     ----------------------------------------

        Function:   tan                                              Math

        Synopsis:   returns the trigonometric tangent of the argument
        Prototype:  (tan rad)
        Arguments:  rad       <real>              angle in radians
        Returns:    <real>



        ELF Functions                                             page 44


        Notes:
        Example:

                     ----------------------------------------

        Function:   tanh                                             Math

        Synopsis:   returns the hyperbolic tangent of the argument
        Prototype:  (tanh rad)
        Arguments:  rad       <real>              angle in radians
        Returns:    <real>
        Notes:
        Example:

                     ----------------------------------------

        List Handling Functions

        The list  data structure  is a  central part  of  LISP. ELF  adds
        functions to manipulate single dimension AutoLISP arrays. You can
        sort, insert, delete, replace, and find elements in a list.

                     ----------------------------------------

        Function:   bsearch                                          List

        Synopsis:   located a value in a sorted string, integer or real
                    value list
        Prototype:  (bsearch vlist key)
        Arguments:  vlist     <list>              list of string,
                                                  integer, or real values
                    key       <atom>              string, integer, or
                                                  real value to locate
        Returns:    <int>     0 based index if found or nil if not found
        Notes:      the list must be sorted and of type string, integer,
                    or real
        Example:    (setq sl (qsort '("CC" "BB" "AA")) ;;; returns ("AA"
                    "BB" "CC")
                    (bsearch sl "AA") ;;; returns 0

                     ----------------------------------------

        Function:   delete                                           List

        Synopsis:   deletes a list or atom from another list
        Prototype:  (delete list pos)
        Arguments:  list      <list>              list
                                                  a list
                    pso       <int>               0 based position to
                                                  insert
        Returns:    new list



        ELF Functions                                             page 45


        Notes:
        Example:    (setq new_list(delete old_list 3)) ;;; deletes 4th
                    element

                     ----------------------------------------

        Function:   insert                                           List

        Synopsis:   inserts a list or atom into another list
        Prototype:  (insert list pos item)
        Arguments:  list      <list>              a list
                    pos       <int>               0 based position to
                                                  insert
                    <list> or <atom>              val
                                                  the list or value to
                                                  insert
        Returns:    new list
        Notes:
        Example:    (setq new_list (insert old_list 3 '("XX" "YY" 123)))

                     ----------------------------------------

        Function:   lfind                                            List

        Synopsis:   located a value in an unsorted string, integer or
                    real value list
        Prototype:  (lfind vlist key)
        Arguments:  vlist     <list>              list of string,
                                                  integer, or real values
                    key       <atom>              string, integer, or
                                                  real value to find
        Returns:    <int>     0 based index if found or nil if not found
        Notes:      the list must be of type string, integer, or real
        Example:    (setq sl '("CC" "BB" "AA"))
                    (lfind sl "AA") ;;; returns 2

                     ----------------------------------------

        Function:   lsearch                                          List

        Synopsis:   located a value in a string, integer or real value
                    list
        Prototype:  (lsearch vlist key)
        Arguments:  vlist     <list>              list of string,
                                                  integer, or real values
                    key       <atom>              string, integer, or
                                                  real value to locate
        Returns:    <int>     vlist if found or vlist with key appended
                              if not found



        ELF Functions                                             page 46


        Notes:      the list must be of type string, integer, or real
        Example:    (setq sl '("CC" "BB" "AA"))
                    (lsearch sl "XX") ;;; returns ("CC "BB" "AA" "XX")

                     ----------------------------------------

        Function:   qsort                                            List

        Synopsis:   sorts a string, integer or real value list
        Prototype:  (qsort lst)
        Arguments:  lst       <list>              list of string,
                                                  integer, or real values
        Returns:    <list>    sorted list
        Notes:
        Example:    (qsort '("CC" "BB "AA")) ;;; returns ("AA" "BB" "CC")
                    (qsort '(3 2 1) ;;; returns (1 2 3)

                     ----------------------------------------

        Function:   replace                                          List

        Synopsis:   replace a list or atom in a list with another
        Prototype:  (replace list pos item)
        Arguments:  list      <list>              a list
                    pos       <int>               0 based position to
                                                  insert
                    <list> or <atom>              val
                                                  the new list or value
                                                  to substitute
        Returns:    new list
        Notes:
        Example:    (replace old_list 3 "XX")

                     ----------------------------------------

        Function:   symbol                                           List

        Synopsis:   Displays the contents of a symbol to the screen using
                    the ELF file/symbol viewer.
        Prototype:  (symbol sym)
        Arguments:  sym       an AutoLISP symbol / list / function
        Returns:
        Notes:      release 12 only
        Example:    (symbol (qsort(atoms-family 1))) ;;; displays a list
                    of all symbols

                     ----------------------------------------

        String Handling Functions

        The ELF string library contains functions to scan and modify text
        strings. In addition, the function (strget) adds a flexible  line
        editor with an integrated help system.



        ELF Functions                                             page 47


                     ----------------------------------------

        Function:   field                                          String

        Synopsis:   returns a substring of str1 from token delimiters in
                    str2 and position.
        Prototype:  (field str1 str2 pos)
        Arguments:  str1      <string>            the string to search
                    str2      <string>            the string containing
                                                  delimiters
        Returns:    pos       <int>               the 1 based position in
                                                  the string
                    <string>  the nth pos substring of str1 delimited by
                              chars in str2 or nil
        Notes:
        Example:    (field "AA;BB;CC;DD;EE" ";" 2) ;;; returns "BB"

                     ----------------------------------------

        Function:   set_edit_help                                  String

        Synopsis:   sets the user help string list for the function
                    (strget)
        Prototype:  (set_edit_help <slist>)
        Arguments:  <slist>   a string list to be displayed when the F1
                              key is pressed while in (strget). The
                              first item in the list will be the help
                              window title.
        Returns:
        Notes:      In release 12 or higher the symbol EDIT_HELP can be
                    used to set the help string. In release 12
                    (set_edit_help) will also set this symbol. The symbol
                    EDIT_HELP can be local to a particular function or
                    global in scope.

                    The user can display the default help screen by
                    pressing F1 the second time.
        Example:    (set_edit_help '("[ My Help Screen ]" "" "This is my
                    help message"))

                     ----------------------------------------

        Function:   sprintf                                        String

        Synopsis:   same as printf except that nothing is printed, the
                    string is returned
        Prototype:  (sprintf format ...)
        Arguments:  see printf
        Returns:    <string>  formatted string



        ELF Functions                                             page 48


        Notes:      printf to string
        Example:    (write-line (sprintf "\n%-10s%10.3g%10d" name salary
                    age) fp)

                     ----------------------------------------

        Function:   strchr                                         String

        Synopsis:   finds the first occurrence of ch in str and returns a
                    substring starting at that character
        Prototype:  (strchr str ch)
        Arguments:  str       <string>            the string to search
                    ch        <int>               the character to search
                                                  for
        Returns:    <string>  the substring starting in ch
        Notes:
        Example:    (strchr "AABBCC" (ascii "B")) ;;; returns "BBCC"

                     ----------------------------------------

        Function:   strcmp                                         String

        Synopsis:   compares two strings for equality (case sensitive)
        Prototype:  (strcmp str1 str2)
        Arguments:  str1      <string>            the string compare
                    str2      <string>            the string compare
        Returns:    Value     Meaning             
                    -1        str1 < str2
                    0         str1 = str2
                    1         str1 > str2
        Notes:
        Example:    (strcmp "Hello World" "HELLO WORLD") returns 1

                     ----------------------------------------

        Function:   strcspn                                        String

        Synopsis:   determine the length of the prefix of str1 made
                    entirely of chars not in str2
        Prototype:  (strcspn str1 str2)
        Arguments:  str1      <string>            the main string
                    str2      <string>            the string of chars to
                                                  test
        Returns:    <string>  the length of the segment of str1 that
                              begins in the beginning of the string and
                              is made up entirely of characters that do
                              not occur in str2
        Notes:
        Example:    (strcspn "AABBCCDDEE" "AB") ;;; returns 0
                    (strcspn "AABBCCDDEE" "D") ;;; returns 6

                     ----------------------------------------



        ELF Functions                                             page 49


        Function:   strdate                                        String

        Synopsis:   returns the current date from the internal clock as a
                    formatted string
        Prototype:  (strdate)
        Arguments:  none
        Returns:    date string as MM-DD-YY
        Notes:
        Example:    (printf "\nToday is %s" (strdate))

                     ----------------------------------------

        Function:   strdela                                        String

        Synopsis:   delete all occurrences of chars in str2 from str1
        Prototype:  (strdela str1 str2)
        Arguments:  str1      <string>            string containing chars
                                                  to be deleted
                    str2      <string>            string containing chars
                                                  to delete
        Returns:    <string>  str1 with chars from str2 deleted
        Notes:
        Example:    (setq str (strdela "This\t is a test;;::///"
                    "\t;:/"))

                     ----------------------------------------

        Function:   strget                                         String

        Synopsis:   edit a string on the text screen with cursor
                    positioning and editing, background mask, color
                    attribute control, and on line help.
        Prototype:  (strget str len curpos mask attr ...)
        Arguments:  str       <string>            optional string to edit
                                                  (default - "")
                    curpos    <int>               optional starting
                                                  cursor position within
                                                  string (default - 0)
                    len       <int>               optional edit field
                                                  length (default 80)
                    mask      <int>               optional background
                                                  mask character (default
                                                  - " ")
                    attr      <int>               optional color
                                                  attribute (default -
                                                  "color: symbol)
                    ...       <int>               optional keycodes which
                                                  will cause strget to
                                                  exit (in addition to
                                                  <Esc>, <Up>, <Down>,
                                                  <Enter>, and <Ctrl-
                                                  Enter>



        ELF Functions                                             page 50


        Returns:    <list>
                    <string>  the edited string
                    <int>     keycode of key causing function to exit
                    <int>     cursor position within string at exit
        Notes:      strget prints the string and mask at the cursor
                    position then waits for user input. The cursor is
                    placed at <curpos> within the string.
                    Insert/overwrite mode is saved between calls to
                    strget. If a string longer than <len> is edited the
                    string will "ticker tape", the maximum string length
                    is 255 characters. Response to keystrokes is as
                    follows:
                    Key       Action              
                    <Left>    move cursor left
                    <Right>   move cursor right
                    <Up>      exit
                    <Down>    exit
                    <Enter>   exit
                    <Ctrl-Enter>   exit
                    <F1>      Display help screen, if the symbol
                              EDIT_HELP is defined, then the contants of
                              that symbol is displayed. In versions
                              prior to release 12, the function
                              (set_edit_help) can be used to set the
                              user defined help. 

                              If the user presses F1 the second time,
                              then the default help screen is displayed.
                    <Ctrl-Rt> word right
                    <Ctrl-Lt> word left
                    <Ctrl-Y>  delete from cursor to end of line
                    <End>     move to end
                    <Home>    move to start
                    <Ins>     toggle insert / overwrite mode
        Example:    (setq name (strget name 25 0 (ascii "_") 23 15360);;;
                    <F2> will cause strget to exit strget also

                     ----------------------------------------

        Function:   stricmp                                        String

        Synopsis:   compares two strings for equality (case insensitive)
        Prototype:  (stricmp str1 str2)
        Arguments:  str1      <string>            the string compare
                    str2      <string>            the string compare
        Returns:    Value     Meaning             
                    -1        str1 < str2
                    0         str1 = str2
                    1         str1 > str2
        Notes:
        Example:    (stricmp "Hello World" "HELLO WORLD") returns 0

                     ----------------------------------------



        ELF Functions                                             page 51


        Function:   strncpy                                        String

        Synopsis:   copies the first n characters of a string
        Prototype:  (strncpy str n)
        Arguments:  str       <string>            the string to copy
                    n         <int>               the number of
                                                  characters to copy
        Returns:    <string>  the copied string
        Notes:
        Example:    (strncpy "Hello World" 8) ;;; returns "Hello Wo"

                     ----------------------------------------

        Function:   strnset                                        String

        Synopsis:   fills a string
        Prototype:  (strnset char len)
        Arguments:  char      <int>               character to use to
                                                  fill string
                    len       <int>               number of characters
        Returns:    <string>  the filled string
        Notes:
        Example:    (strnset (ascii " ") 40) ;;; returns a string of 40
                    spaces

                     ----------------------------------------

        Function:   strpbrk                                        String

        Synopsis:   returns a substring of the first occurrence of any
                    character of str2 in str1
        Prototype:  (strstr str1 str2)
        Arguments:  str1      <string>            the string to search
                    str2      <string>            the substring
        Returns:    <string>  the substring starting in any char in str2
        Notes:
        Example:    (strpbrk "AABBCCDDEE" "CCBB") ;;; returns "BBCCDDEE"

                     ----------------------------------------

        Function:   strrchr                                        String

        Synopsis:   finds the last occurrence of ch in str and returns a
                    substring starting at that character
        Prototype:  (strrchr str ch)
        Arguments:  str       <string>            the string to search
                    ch        <int>               the character to search
                                                  for
        Returns:    <string>  the substring starting in ch
        Notes:
        Example:    (strrchr "AABBCC" (ascii "B")) ;;; returns "BCC"

                     ----------------------------------------



        ELF Functions                                             page 52


        Function:   strrev                                         String

        Synopsis:   returns the string argument with the character order
                    reversed
        Prototype:  (strrev str)
        Arguments:  str       <string>            string to be reverses
        Returns:    <string>  the reverses string
        Notes:
        Example:    (setq revs (strrev "ABCDE"));;; returns "EDCBA"

                     ----------------------------------------

        Function:   strspn                                         String

        Synopsis:   determine the length of the prefix of str1 made
                    entirely of chars in str2
        Prototype:  (strspn str1 str2)
        Arguments:  str1      <string>            the main string
                    str2      <string>            the string of chars to
                                                  test
        Returns:    <string>  the length of the segment of str1 that
                              begins in the beginning of the string and
                              is made up entirely of characters that
                              occur in str2
        Notes:
        Example:    (strspn "AABBCCDDEE" "AB") ;;; returns 4

                     ----------------------------------------

        Function:   strstr                                         String

        Synopsis:   returns a substring of the first occurrence of str2
                    in str1
        Prototype:  (strstr str1 str2)
        Arguments:  str1      <string>            the string to search
                    str2      <string>            the substring
        Returns:    <string>  the substring starting in str2
        Notes:
        Example:    (strstr "AABBCCDDEE" "CC") ;;; returns "CCDDEE"

                     ----------------------------------------

        Function:   strswap                                        String

        Synopsis:   swaps all occurrences of char1 with char2 in str
        Prototype:  (strswap str char1 char2)
        Arguments:  str       <string>            string to search
                    char1     <int>               character to search for
        Returns:    char2     <int>               character to substitute
                                                  for char1



        ELF Functions                                             page 53


        Notes:      <string>  the string with swapped chars
        Example:

                     ----------------------------------------

        Function:   strtime                                        String

        Synopsis:   returns the current time from the internal clock as a
                    formatted string
        Prototype:  (strtime)
        Arguments:  none
        Returns:    time string as HH:MM:SS
        Notes:
        Example:    (printf "\nThe current time is %s" (strtime))

                     ----------------------------------------

        Function:   strtok                                         String

        Synopsis:   returns the first substring of str1 from token
                    delimiters in str2. subsequent calls after the first
                    with no arguments will return the second and any
                    further substrings
        Prototype:  (strtok str1 str2)
        Arguments:  str1      <string>            the string to search
                    str2      <string>            the string containing
                                                  tokens delimiters
        Returns:    <string>  the substring of str1 up but not including
                              any chars in str2
        Notes:
        Example:    (setq s2 (strtok "AA;BB;CC;DD;EE" ";"))
                              ;;; returns "AA" and saves "BB;CC;DD;EE"
                              internally
                    (while (boundp 's2)
                      (print s2)
                      (setq s2 (strtok)) ;; then returns "BB", etc
                    )

                     ----------------------------------------

        Function:   strtrim                                        String

        Synopsis:   trim white space (all char values < '!') from the
                    beginning (left side) and end (right side); and
                    compresses white space within a string to a single
                    space between words
        Prototype:  (strtrim str)
        Arguments:  str       <string> the string to be trimmed
        Returns:    <string>  trimmed string if success or nil if error



        ELF Functions                                             page 54


        Notes:
        Example:    (strtrim "\t\t     Hello   \t  world\t     ")
                    returns: "Hello World"

                     ----------------------------------------

        Function:   strtriml                                       String

        Synopsis:   trim white space from the beginning (left side) of a
                    string
        Prototype:  (strtriml str)
        Arguments:  str       <string> the string to be trimmed
        Returns:    <string>  trimmed string if success or nil if error
        Notes:
        Example:    (strtriml "\t\t     Hello world")
                    returns: "Hello World"

                     ----------------------------------------

        Function:   strtrimr                                       String

        Synopsis:   trim white space from the end (right side) of a
                    string
        Prototype:  (strtrimr str)
        Arguments:  str       <string> the string to be trimmed
        Returns:    <string>  trimmed string if success or nil if error
        Notes:
        Example:    (strtrimr "Hello world\t     ")
                    returns: "Hello World"

                     ----------------------------------------

        Function:   tolower                                        String

        Synopsis:
        Prototype:  (tolower char)
        Arguments:  char      <int>
        Returns:    <char>    character converted to lower case
        Notes:
        Example:    (chr(tolower(ascii "A"))) ;;; returns: "a"

                     ----------------------------------------

        Function:   toupper                                        String

        Synopsis:
        Prototype:  (toupper char)
        Arguments:  char      <int>
        Returns:    <char>    character converted to upper case
        Notes:
        Example:    (chr(toupper(ascii "a"))) ;;; returns: "A"

                     ----------------------------------------



        ELF Functions                                             page 55


        Character Classification Functions

        The character classification  functions are  equivalent to  those
        from the "C" function library except that they return nil instead
        of 0  to indicate  a FALSE  condition. This  allows the  AutoLISP
        programmer to test the expression directly with an (if) function.

        eg.       (If(IsUpper ch) (do something))

                     ----------------------------------------

        Function:   isalnum                                     Character

        Synopsis:   returns a non-zero value if argument is a letter or
                    digit
        Prototype:  (isalnum char)
        Arguments:  char      <int>
        Returns:    <int>     non-zero if true, nil otherwise
        Notes:
        Example:

                     ----------------------------------------

        Function:   isascii                                     Character

        Synopsis:   returns a non-zero value if argument is an ASCII
                    character
        Prototype:  (isascii char)
        Arguments:  char      <int>
        Returns:    <int>     non-zero if true, nil otherwise
        Notes:
        Example:

                     ----------------------------------------

        Function:   iscntl                                      Character

        Synopsis:   returns a non-zero value if argument is a control
                    character
        Prototype:  (iscntl char)
        Arguments:  char      <int>
        Returns:    <int>     non-zero if true, nil otherwise
        Notes:
        Example:

                     ----------------------------------------

        Function:   isdigit                                     Character

        Synopsis:   returns a non-zero value if argument is a numeric
                    digit
        Prototype:  (isdigit char)
        Arguments:  char      <int>



        ELF Functions                                             page 56


        Returns:    <int>     non-zero if true, nil otherwise
        Notes:
        Example:

                     ----------------------------------------

        Function:   isgraph                                     Character

        Synopsis:   returns a non-zero value if argument is a visible
                    printable character
        Prototype:  (isgraph char)
        Arguments:  char      <int>
        Returns:    <int>     non-zero if true, nil otherwise
        Notes:
        Example:

                     ----------------------------------------

        Function:   islower                                     Character

        Synopsis:   returns a non-zero value if argument is a lower case
                    letter
        Prototype:  (islower char)
        Arguments:  char      <int>
        Returns:    <int>     non-zero if true, nil otherwise
        Notes:
        Example:

                     ----------------------------------------

        Function:   isodigit                                    Character

        Synopsis:   returns a non-zero value if argument is an octal
                    digit (0-7)
        Prototype:  (isodigit char)
        Arguments:  char      <int>
        Returns:    <int>     non-zero if true, nil otherwise
        Notes:
        Example:

                     ----------------------------------------

        Function:   isprint                                     Character

        Synopsis:   returns a non-zero value if argument is a printable
                    character
        Prototype:  (isprint char)
        Arguments:  char      <int>
        Returns:    <int>     non-zero if true, nil otherwise
        Notes:
        Example:

                     ----------------------------------------



        ELF Functions                                             page 57


        Function:   ispunct                                     Character

        Synopsis:   returns a non-zero value if argument is a punctuation
                    character
        Prototype:  (ispunct char)
        Arguments:  char      <int>
        Returns:    <int>     non-zero if true, nil otherwise
        Notes:
        Example:

                     ----------------------------------------

        Function:   isspace                                     Character

        Synopsis:   returns a non-zero value if argument is a white-space
                    character (space, tab, newline, etc)
        Prototype:  (isspace char)
        Arguments:  char      <int>
        Returns:    <int>     non-zero if true, nil otherwise
        Notes:
        Example:

                     ----------------------------------------

        Function:   isupper                                     Character

        Synopsis:   returns a non-zero value if argument is an upper case
                    letter
        Prototype:  (isupper char)
        Arguments:  char      <int>
        Returns:    <int>     non-zero if true, nil otherwise
        Notes:
        Example:

                     ----------------------------------------

        Function:   isxdigit                                    Character

        Synopsis:   returns a non-zero value if argument is a hexadecimal
                    digit (0-F)
        Prototype:  (isxdigit char)
        Arguments:  char      <int>
        Returns:    <int>     non-zero if true, nil otherwise
        Notes:
        Example:

                     ----------------------------------------

        Utility / Miscellaneous Functions

        Utility functions include those to  control the PC speaker,  read
        the PC  system clock, for  program debugging, and  to execute DOS
        programs under program control.



        ELF Functions                                             page 58


                     ----------------------------------------

        Function:   adsdump                                       Utility

        Synopsis:   prints the data type and value of an AutoLISP symbol
        Prototype:  (adsdump sym)
        Arguments:  sym       <symbol>            an AutoLISP symbol
        Returns:
        Notes:
        Example:    (setq x (load_dirs))
                    (adsdump x)

                     ----------------------------------------

        Function:   beep                                          Utility

        Synopsis:   sound a beep on the PC speaker for optional frequency
                    and duration
        Prototype:  (beep freq duration)
        Arguments:  freq      <int>               frequency in hertz
                    duration  <real>              length/duration of the
                                                  beep in decimal seconds
        Returns:
        Notes:
        Example:    (beep 440 1.0) ;;; beep middle A for one second

                     ----------------------------------------

        Function:   clock                                         Utility

        Synopsis:   reads the current internal clock
        Prototype:  (clock)
        Arguments:  none
        Returns:    <real>    the current internal clock register
                              reading in seconds (0.01 second precision)
        Notes:
        Example:    (setq end (+(clock) 2.5)) ;;; delay for 2.5 seconds
                    (while (> end (clock)))

                     ----------------------------------------

        Function:   exit                                          Utility

        Synopsis:   cancels execution and returns to the Command: prompt
        Prototype:  (exit)
        Arguments:
        Returns:
        Notes:      duplicates the (exit) function available in release
                    12 for pre-release 12 versions
        Example:

                     ----------------------------------------



        ELF Functions                                             page 59


        Function:   getdosver                                     Utility

        Synopsis:   returns the DOS version
        Prototype:  (getdosver)
        Arguments:
        Returns:    <list>
                    <int>     major version number
                    <int>     minor version number
        Notes:
        Example:    (set ver (getdosver))
                    (printf "DOS Version %d.%d" (car ver) (cadr ver))

                     ----------------------------------------

        Function:   last_error                                    Utility

        Synopsis:   returns the last internal error message
        Prototype:  (last_error)
        Arguments:
        Returns:    <string>  the error message
        Notes:      with release 12 the symbol *LAST_ERROR* also contains
                    this message
        Example:    (printf "\nThe last ELF error was %s" (last_error))

                     ----------------------------------------

        Function:   nosound                                       Utility

        Synopsis:   turns off the PC speaker after a sound function
        Prototype:  (nosound)
        Arguments:
        Returns:
        Notes:
        Example:    see sound

                     ----------------------------------------

        Function:   pause_key                                     Utility

        Synopsis:   prints "press any key to continue..." and waits for a
                    keystroke
        Prototype:  (pause_key)
        Arguments:
        Returns:
        Notes:
        Example:

                     ----------------------------------------

        Function:   sound                                         Utility

        Synopsis:   turns on the PC speaker at a specified tone frequency
        Prototype:  (sound freq)



        ELF Functions                                             page 60


        Arguments:  freq      <int>               frequency in hertz
        Returns:
        Notes:      see beep
        Example:    (defun play(freq time)
                      (sound freq) ;;; turn on note
                      (wait time)  ;;; wait time seconds
                      (nosound) ;;; turn it off
                    )
                    (play 440 0.5);;; sounds middle A for 1/2 second

                     ----------------------------------------

        Function:   system                                        Utility

        Synopsis:   executes a DOS command
        Prototype:  (system cmd)
        Arguments:  cmd       <string>            DOS command or program
        Returns:    <int>     DOS errorlevel if successful or -1 on
                              error
        Notes:      You MUST run "cfig386 acad -maxreal FFFFh" to
                    configure the PharLap DOS extender to allow realmode
                    programs to run (select a value large enough to run
                    the desired programs). This function is preferable to
                    SH or SHELL, or executing some programs from an
                    ACAD.PGP entry, when the return value must be known.
                    It's also a little faster.
        Example:    (keystuff "/FRmyfile\n/FSY/QY")
                    (if(>= (system "123") 0)
                      (princ "Lotus 123 executed successfully"))

                     ----------------------------------------

        Function:   wait                                          Utility

        Synopsis:   suspend execution for a specified time duration
        Prototype:  (wait ti)
        Arguments:  ti        <real>              time in decimal seconds
        Returns:
        Notes:
        Example:    (wait 2.5) ;;; delays for 2.5 seconds

                     ----------------------------------------

        Symbols
        (release 12 or later only)

        Symbol          Description
        *last_error*    the last error message string
        color           default color attribute
        edit_help       string  list  with   user  defined  help  for  the
                        (strget) function
        menu_help       string  list  with  user   defined  help  for  the
                        (wmenu) function



        ELF Functions                                             page 61



        ELF Functions                                             page 62


        Copyright

        The  ELF program code and documentation are copyrighted material,
        registered with the  US Copyright office  and protected under  US
        and International copyright laws. All rights are reserved.


        Trademark

        Mountain  Software and ELF  are trademarks of  Mountain Software.
        MS-DOS is a registered trademark of Microsoft Corporation. PC-DOS
        is  a  registered  trademark  of  IBM  Corporation.  AutoCAD  and
        AutoLISP are registered trademarks of AutoDesk.



                                      Index

        *last_error* . . . . . 59, 60      elf  1-11, 17, 27, 30, 37-39,
        & . . . . . . . . . . . . . 40                     44, 46, 59, 62
        &&  . . . . . . . . . . . . 40     elfapps . . . . . . .  1, 2, 4
        | . . . . . . . . .  1, 39, 40     elfdos  . . . . . . .  1, 2, 5
        ||  . . . . . . . . . . . . 40     entity  . . . . . . . . . 1, 2
        acad  3-9, 30, 32, 34, 36-38,      erasefile . . . . . . . 32, 37
                                    60     esc . . . . . .  8, 20, 23, 49
        acadapp . . . . . . . . . .  3     exit  .  8, 22, 23, 49, 50, 58
        access  . . . . . . . . 20, 30     exp . . . . . . . . .  1, 3, 4
        acos  . . . . . . . . . . . 40     exsubr  . . . . . . . . . .  9
        ads . . . . . . . . . . . 3, 4     f1   8, 11, 17, 18, 23, 47, 50
        adsdump . . . . . . . . . . 58     ff  . . . . . . . . . . . .  7
        asin  . . . . . . . . . . . 40     field . . . . . . . 29, 47, 49
        attr  10, 12-15, 18, 19, 23, 2     file_exists . . . . . . . . 32
                             5, 26, 49     findfile  . . . . . . . . 3, 7
        attribute  1, 10-15, 17-20, 22     findfirst . . . . .  20, 32-35
                  -26, 32, 33, 35, 49,     findnext  . . . . . . .  33-35
                                    60     flipscreen  . . . . . . . . 11
        autocad . . . 1-5, 7, 9-11, 62     floor . . . . . . . . . . . 41
        autodesk  . . . . . . .  1, 62     floppy  . . . . . .  6, 19, 31
        autolisp  1-5, 9, 10, 12, 15,      fullpath  . . . . . . . . . 34
                  17, 33, 34, 37, 39,      get_cursor  . . . . . .  14-16
                    44, 46, 55, 58, 62     get_video . . . . . 12, 13, 15
        beep  . . . . . . . 10, 58, 60     getch . . . . . . .  1, 27, 28
        boundp  . . . . . . . . 34, 53     getche  . . . . . . . .  1, 28
        box . . . . . . . . . . . . 12     getdir  . . . . . . . . . . 34
        bsearch . . . . . . . . . . 44     getdisk . . . . . . . . . . 35
        capslock  . . . . . . . . . 29     getdiskfree . . . . . . . . 34
        cd  . . . . . . . . . . . .  5     getdosver . . . . . . . . . 59
        ceil  . . . . . . . . . . . 41     getkey  . . . . . 1, 27-29, 42
        chdir . . . . . . . . .  5, 30     getxy . . . . . . . 15, 16, 21
        chpath  . . . . . . . . . . 31     gotoxy  . . . . . . . . 15, 16
        clock . . .  2, 49, 53, 57, 58     hibyte  . . . . . . . . 28, 42
        cls . . . . . . . . . .  5, 12     insert  . . . 2, 29, 44-46, 50
        color  1, 3, 10-15, 17-20, 22-     isalnum . . . . . . . . . . 55
                        26, 39, 49, 60     isascii . . . . . . . . 11, 55
        commands  . . . . . . 1-3, 5-9     iscntl  . . . . . . . . . . 55
        copyfile  . . . . . . . . . 38     isdigit . . . . . . . . . . 55
        cosh  . . . . . . . . . . . 41     isgraph . . . . . . . . . . 56
        dcd . . . . . . . . . . . .  5     islower . . . . . . . . . . 56
        dcopy . . . . . . . . . . 5, 6     isodigit  . . . . . . . . . 56
        ddel  . . . . . . . . . . .  6     isprint . . . . . . . . . . 56
        ddir  . . . . . . . . . . .  6     ispunct . . . . . . . . . . 57
        delete  2, 6, 8, 44, 45, 49, 5     isspace . . . . . . . . . . 57
                                     0     isupper . . . . . . . . 55, 57
        derase  . . . . . . . . . .  6     isxdigit  . . . . . . . . . 57
        dir . . . .  6, 10, 26, 36, 37     kbhit . . . . . . . . .  1, 28
        dmd . . . . . . . . . . . .  8     key_clear . . . . . . . . . 29
        dmove . . . . . . . . . . 6, 7     key_ready . . . . . . . . . 29
        drd . . . . . . . . . . . .  8     key_stat  . . . . . . . . . 29
        drename . . . . . . . . . .  6     key_stuff . . . . . 27, 29, 30
        dsd . . . . . . . . . . . .  9     keycode  4, 22, 23, 28, 29, 42
        dtr . . . . . . . . . . . . 41                               , 50
        edit_help . . . . . 47, 50, 60     keycodes  . . . . . . . 28, 49



        keystuff  . . . . . . . . . 60     shareware . . . . . . . . 1, 2
        last_error  . . . . . . 59, 60     sinh  . . . . . . . . . . . 43
        len . . . . . . . .  19, 49-51     solid . . . . . . . . . . . 24
        lfind . . . . . . . . . . . 45     sound . . . .  1, 2, 10, 58-60
        line  1, 2, 6, 8, 16-19, 22-24     splitpath . . . . . . . 36, 37
                  , 26, 37, 38, 39, 46     sprintf . . . . . . 35, 47, 48
                               , 48-50     srand . . . . . . . . . . . 43
        list  1, 2, 6, 7, 10-12, 16, 1     strchr  . . . . . . . . . . 48
                  7, 21, 22, 23, 28, 3     strcmp  . . . . . . . . . . 48
                  0, 33-35, 37-39, 44-     strcspn . . . . . . . . . . 48
                        47, 50, 59, 60     strdate . . . . . . . . . . 49
        load_dirs . . . . . . . 35, 58     strdela . . . . . . . . . . 49
        load_files  . . . . . . 35, 36     strget  19, 46, 47, 49, 50, 60
        lobyte  . . . . . . . . 28, 42     stricmp . . . . . . . . . . 50
        log10 . . . . . . . . . . . 42     string  1, 2, 10, 11, 13-15, 1
        look  . . . . . .  7-9, 17, 38               7-20, 22, 23, 25-39,
        lsearch . . . . . . . . 45, 46                      44-54, 59, 60
        lsp . .  4, 12, 27, 28, 36, 37     strncpy . . . . . . . . . . 51
        makepath  . . . . . . . . . 36     strnset . . . . . . . . . . 51
        md  . . . . . . . . . . . .  8     strpbrk . . . . . . . . . . 51
        menu_help . . . 17, 18, 23, 60     strrchr . . . . . . . . . . 51
        mkdir . . . . . . . . .  8, 36     strrev  . . . . . . . . . . 52
        movefile  . . . . . . . . . 38     strspn  . . . . . . . . . . 52
        nosound . . . . . . . . 59, 60     strstr  . . . . . . . . 51, 52
        numlock . . . . . . . . . . 29     strswap . . . . . . . . . . 52
        password  . . . . . . . . .  8     strtime . . . . . . . . . . 53
        pause_key . . . . . . . . . 59     strtok  . . . . . . . . . . 53
        pgdn  . . . . . . . . .  8, 23     strtrim . . . . . . . . 53, 54
        pgp . . . . . . . . . . . . 60     strtriml  . . . . . . . . . 54
        pgup  . . . . . . . . .  8, 23     strtrimr  . . . . . . . . . 54
        pharlap . . . . . . . . . . 60     subr  . . . . . . . . . . .  9
        point . . . . . . . . . . . 10     substring . . .  47, 48, 51-53
        popup . . . . . . . . . . .  1     substrings  . . . . . . . . 53
        printf  1, 10, 11, 13, 15, 25,     symbol  1, 2, 5, 9-11, 15, 17-
                   34, 47, 48, 49, 53,               19, 22, 23, 25, 37,
                                    59               46, 47, 49, 50, 58,
        prts  . . . . . . . . . . . 13                             59, 60
        puts  . . . . . . . 13, 14, 26     system  1, 11, 17, 30, 33, 46,
        qsort . . . . .  9, 36, 44, 46                             57, 60
        radians . . 10, 40, 41, 43, 44     tan . . . . . . . . . . . . 43
        rand  . . . . . . . . . 11, 42     tanh  . . . . . . . . . . . 44
        rd  . . . . . . . . . . . 8, 9     text  1, 5, 8, 11-15, 17, 19,
        read_file . . . . . . .  37-39               23-26, 37-39, 46, 49
        replace . . . . . .  2, 44, 46     tolower . . . . . . . . . . 54
        rmdir . . . . . . . . .  8, 36     toupper . . . . . . . . . . 54
        round . . . . . . . . . 42, 43     unlink  . . . . . . . . . . 37
        rtd . . . . . . . . . . . . 43     utility . . . . .  1, 2, 57-60
        scancode  . . . . . . . 28, 42     ver . . . . . . . . . .  9, 59
        scr_fill  . . . . . . . 14, 15     wait  . . . . . . . . . 23, 60
        scr_printf  . . . . . . 11, 15     wclose  . . . . . . . . . . 18
        sd  . . . . . . . . . . . .  9     wcloseall . . . . . . . . . 18
        set_cursor  . . . . . .  14-17     wclreol . . . . . . . . . . 18
        setdisk . . . . . . . . . . 36     wcls  . . . . . . . . . 18, 19
        setq  9, 13, 15, 16, 20, 21, 2     wgetdrive . . . . . . . 19, 20
                  3, 24, 28, 29, 34-37     wgetfile  . . . . . . .  8, 20
                  , 39, 41-46, 49, 50,     wgetstr . . . . . . . . . . 19
                            52, 53, 58     wgetxy  . . . . . . . . . . 21



        wgotoxy . . . . . . . . . . 21
        winfo . . . . . . . . . . . 21
        wmenu . . . . . 17, 22, 23, 60
        wmsg  . . . . . . . . . 23, 24
        wopen . . . . . . . . . . . 24
        wpopup  . . . . . . 19, 24, 25
        wprintf . . . . . . . . . . 25
        wprts . . . . . . . . . 17, 25
        wputcen . . . . . . . . . . 25
        wputs . . . . . . . . . 17, 26
        write_file  . . . . . . 37, 39
        wscroll . . . . . . . . . . 26
        wshadow . . . . . . . . 26, 27
        wtitle  . . . . . . . . . . 27
        xload . . . . . . . . . . .  3