TRAJECTORY MAKER

                        A Trajectory Simulation Tool
                        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ























                        
                                    ALGORITHM SUPPLEMENT

                        









                        



                                                             ORBIT HORIZONS
                                                               94 Promenade
                                                   Irvine, California 92715
                                                                     U.S.A.





                                COPYRIGHT NOTICE

     This document and software package  consisting of the Trajectory Maker
     and Trajectory Scape computer programs  are copyrighted (C) 1991, 1992
     by H.B. Reynolds, President, ORBIT HORIZONS.  All rights are reserved.
     No  part   of  this   publication  may   be  reproduced,  transmitted,
     transcribed, stored  in any retrieval  system, or  translated into any
     language by any means without  the express written permission of ORBIT
     HORIZONS, 94 Promenade, Irvine California 92715, USA.


























                          FIRST EDITION/FIRST PRINTING

                                    July 1992








                                                                         ii





                                LIMITED WARRANTY

     THIS  ALGORITHM  SUPPLEMENT,  THE  USER'S  GUIDE,  AND  THE  PROGRAMS,
     "TRAJECTORY MAKER" AND  "TRAJECTORY SCAPE" ARE  SOLD "AS IS",  WITHOUT
     WARRANTY  AS  TO  THEIR PERFORMANCE,  OR  FITNESS  FOR  ANY PARTICULAR
     PURPOSE.  THE  ENTIRE RISK  AS TO THE  RESULTS AND  PERFORMANCE OF THE
     PROGRAMS IS ASSUMED BY THE USER.

     HOWEVER, ORBIT HORIZONS WARRANTS THE MAGNETIC DISKETTE(S) ON WHICH THE
     PROGRAM IS RECORDED  TO BE FREE  FROM DEFECTS IN  MATERIALS AND FAULTY
     WORKMANSHIP UNDER NORMAL USE FOR A PERIOD OF NINETY DAYS FROM THE DATE
     OF PURCHASE.   IF DURING  THIS NINETY  DAY PERIOD  THE DISKETTE SHOULD
     BECOME  DEFECTIVE,  IT  MAY  BE  RETURNED  TO  ORBIT  HORIZONS  FOR  A
     REPLACEMENT WITHOUT CHARGE, PROVIDED YOU SEND PROOF OF PURCHASE OF THE
     PROGRAM.

     YOUR SOLE AND EXCLUSIVE  REMEDY IN THE EVENT  OF A DEFECT IS EXPRESSLY
     LIMITED TO REPLACEMENT OF THE  DISKETTE AS PROVIDED ABOVE.  IF FAILURE
     OF  A DISKETTE  HAS RESULTED  FROM ACCIDENT  OR ABUSE,  ORBIT HORIZONS
     SHALL HAVE NO  RESPONSIBILITY TO REPLACE THE  DISKETTE UNDER THE TERMS
     OF THIS LIMITED WARRANTY.

     IN NO  EVENT SHALL ORBIT  HORIZONS BE  LIABLE TO YOU  FOR ANY DAMAGES,
     INCLUDING BUT NOT LIMITED TO ANY  LOST PROFITS, LOST SAVINGS, OR OTHER
     CONSEQUENTIAL DAMAGES ARISING OUT OF THE USE OR INABILITY TO USE THESE
     PROGRAMS AND  ACCOMPANYING MATERIALS EVEN  IF ORBIT  HORIZONS HAS BEEN
     ADVISED OF THE  POSSIBILITY OF SUCH  DAMAGES, OR FOR  ANY CLAIM BY ANY
     OTHER PARTY.

     SOME STATES DO NOT ALLOW THE  LIMITATION OR EXCLUSION OF LIABILITY FOR
     INCIDENTAL  OR  CONSEQUENTIAL  DAMAGES,  SO  THE  ABOVE  LIMITATION OR
     EXCLUSION  MAY NOT  APPLY TO  YOU.  THIS  WARRANTY GIVES  YOU SPECIFIC
     LEGAL RIGHTS, AND YOU MAY ALSO HAVE OTHER RIGHTS WHICH VARY FROM STATE
     TO STATE.

     THIS WARRANTY SHALL BE CONSTRUED,  INTERPRETED AND GOVERNED BY LAWS OF
     THE STATE OF CALIFORNIA.

     YOU AGREE TO THESE TERMS BY YOUR DECISION TO USE THIS SOFTWARE.










                                                                              iii






                                                                       iii








                                   TABLE OF CONTENTS


               1  INTRODUCTION ...................................... 1-1

               2  EQUATIONS OF MOTION ............................... 2-1

               3  GRAVITY PERTURBATION MODEL ........................ 3-1

               4  DRAG PERTURBATION MODEL ........................... 4-1
                   4.1  Density Profile ............................. 4-4
                   4.2  Wind Profile ............................... 4-14

               5  NUMERICAL INTEGRATION SCHEME ...................... 5-1

               6  COORDINATE SYSTEMS AND TRANSFORMATIONS ............ 6-1

                   6.1  Time Considerations ......................... 6-1
                   6.2  Orbital Elements ............................ 6-2
                   6.3  Geospherical Inertial Coordinates ........... 6-6
                   6.4  Earth-Fixed-Geocentric Coordinates .......... 6-6
                   6.5  Local Topocentric Coordinates ............... 6-7
                   6.6  Common Radar Coordinates ................... 6-10
                   6.7  Geodetic Coordinates ....................... 6-10

               7 BIBLIOGRAPHY ....................................... 7-1



                                    LIST OF TABLES


               Table                                                Page

                3-1  WGS-72 Earth Constants ........................ 3-1

                3-2  Smithsonian Zonal Harmonic Coefficients ....... 3-2

                4-1  Drag Coefficient vs. Mach Number .............. 4-3

                4-2  Molecular Scale Temperature ................... 4-4

                4-3  Atmospheric Density Profile ................... 4-6

                5-1  Shanks 8-12 Numerical Integration Constants ... 5-3







                                                                       iv





                                    LIST OF FIGURES


               Figure                                                Page

                3-1  Magnitude of Vector Differences Between the
                     23rd and 2nd, 3rd, 4th and 5th Order Gravity
                     Models ......................................... 3-7

                3-2  Magnitude of Vector Differences Between the
                     23rd and 6th, 7th, 8th and 9th Order Gravity
                     Models ......................................... 3-8

                3-3  Magnitude of Vector Differences Between the
                     23rd and 10th, 11th, 12th and 13th Order
                     Gravity Models ................................. 3-9

                3-4  Magnitude of Vector Differences Between the
                     23rd and 14th, 15th, 16th and 17th Order Gravity
                     Models ........................................ 3-10

                3-5  Magnitude of Vector Differences Between the
                     23rd and 18th, 19th, 20th and 21st Order
                     Gravity Models ................................ 3-11

                3-6  Magnitude of Vector Differences Between the
                     23rd and 19th, 20th, 21st and 22nd Order
                     Gravity Models ................................ 3-12

                3-7  Magnitude of Vector Differences Between the
                     23rd and 2nd, 4th, 6th and 8th Order (Even)
                     Gravity Models ................................ 3-13

                3-8  Magnitude of Vector Differences Between the
                     23rd and 3rd, 5th, 7th and 9th Order (Odd)
                     Gravity Models ................................ 3-14

                3-9  Magnitude of Vector Differences Between the
                     23rd and 2nd, 6th, 10th and 14th Order
                     Gravity Models ................................ 3-15

                3-10 Magnitude of Vector Differences Between the
                     23rd and 5th, 10th, 15th and 20th Order
                     Gravity Models ................................ 3-16

                4-1  1976 U. S. Standard Atmosphere Density
                     Profile ........................................ 4-7

                4-2  Abbreviated 1976 U. S. Standard Atmosphere
                     Density Profile ................................ 4-8


                                                                        v





                                    LIST OF FIGURES


               Figure                                                Page

                4-3  Trajectory Maker Density Profile Model ......... 4-9

                4-4  Cubic Spline Interpolation Error for 21 and
                     48 Point Tables ............................... 4-10

                4-5  Cubic Spline Interpolation Error for 21 and
                     48 Point Tables ............................... 4-11

                4-6  Cubic Spline and Linear Interpolation Error
                     for 48 Point Table ............................ 4-12

                4-7  Cubic Spline Interpolation Error for 48 Point
                     Table ......................................... 4-13

                4-8  East/North Wind velocity Components
                     (Example 1) ................................... 4-15

                4-9  East/North Wind velocity Components
                     (Example 2) ................................... 4-16

                5-1  Numerical Integration Error .................... 5-6



























                                                                       vi





               Trajectory Maker                              Introduction
               Algorithm Supplement                                  1-1
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               1.  INTRODUCTION

               The Trajectory Maker/Trajectory Scape software system is a
               state of the art simulation and design tool for use on IBM
               compatible personal computers.  Within minutes it predicts
               precision trajectory ephemerides and displays their ground
               traces on world map projections.

               The shapes  of various  orbit ground  traces can  be quite
               bizarre, unexpected and difficult  to visualize because of
               two motion  processes; namely  the Earth's  rotation about
               its axis, coupled with the  motion of the orbiting object.
               With  Trajectory  Maker,  visualization  of  this  complex
               interaction is a breeze.

               But Trajectory Maker  gives much more  than this graphics'
               visualization capability.  It  also creates high-precision
               numerical  output  data,  in  several  formats,  for those
               wanting more comprehensive analysis capabilities.

               Major  features of  the  software and  how  to use  it are
               described in detail in the User's Guide.  The User's Guide
               also  contains  some  historical  background  material,  a
               glossary of  terms, definitions  and illustrations  to aid
               the user with the external interface to the system.

               Transparent  to the  user is  an underlying  foundation of
               sophisticated mathematical algorithms  and techniques that
               are  employed  by  the  system  in  order  to  perform the
               relevant  numerical  computations,   in  an  accurate  and
               expedient manner.

               The user of  the system need  not necessarily be concerned
               with  its  inner workings;  however,  an  understanding of
               theory is sometimes helpful in understanding its practice.

               This paper presents a detailed description of mathematical
               algorithms and  techniques used  by the  Trajectory Maker/
               Trajectory Scape software system.

               In  addition to  presenting the  mathematical core  of the
               software system, the  merits and limitations  of the algo-
               rithms  are  discussed.  Illustrations  are  provided that
               will aid in selecting various  aspects of the models, such
               as truncation error, integration  step-size, etc., for the
               particular application under consideration.

               The equations  of motion  that govern  the trajectories of





               Trajectory Maker                              Introduction
               Algorithm Supplement                                  1-2
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               Earth  orbiting  satellites  and  ballistic  missiles  are
               summarized.

               The force models include perturbation effects due to Earth
               oblateness, aerodynamic drag and atmospheric winds.  These
               forces are developed and investigated.

               Explicit  closed-form  expressions  for  the gravitational
               acceleration components  are derived  for an axi-symmetric
               oblate  Earth  model.   The  model  contains  an arbitrary
               number of zonal harmonic coefficients.  Effects of various
               orders of the coefficients  on certain mission ephemerides
               are investigated.

               The  aerodynamic drag  force  is defined,  the atmospheric
               density profile is  modeled as a  function of altitude and
               its relative  error is analyzed.   An innovative algorithm
               for computing altitude is presented that is very fast, yet
               produces highly accurate values.

               A numerical scheme for integrating the equations of motion
               is presented, relevant coordinate  systems are defined and
               algorithms for  transforming the various  input and output
               parameters are summarized.

               All physical constants used by the software are included.

               The  algorithms  presented herein  support  the trajectory
               mechanics  functions  in  the  program  source  code  with
               examples that demonstrate their integrity.  A bibliography
               is  provided  for  algorithm  extensions,  map  projection
               related processes and routine mathematical processes.





               Trajectory Maker                       Equations of Motion
               Algorithm Supplement                                  2-1
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               2.  EQUATIONS OF MOTION

               The equations  of motion for  propagating trajectories are
               modeled  in rectangular,  geocentric  inertial coordinates
               with fundamental  plane coplanar with  the Earth's equator
               and principle axis in the direction of the vernal equinox.

               Let x, y,  z denote these  coordinates with z-axis coinci-
               dent with the Earth's  spin-axis, positive northwards; the
               x-axis in the equatorial  plane, positive in the direction
               of  the  vernal  equinox;  and  the  y-axis  lying  in the
               equatorial  plane  in such  a  manner that  the  system is
               right-handed.

               Further, let  i, j, k  be unit  vectors along the  x, y, z
               axes, respectively.  Then, the position  of a point mass m
               may be represented in vector form

                   r = xi + yj + zk

               and according  to  Newton's  second law,  the differential
               equations of motion may be written

                     d2r
                   m ÄÄÄ =  ä F
                     dt2

               where ä F is the sum  of the external forces acting on the
               mass m.

               In this paper the forces  due to the Earth's gravitational
               potential  function   and  its   atmosphere  are  treated.
               Letting G and D denote these  forces per unit mass, we may
               write

                   d2r
                   ÄÄÄ = G + D
                   dt2

               By  substitution  of  variables,   this  equation  may  be
               decomposed  into  the following  first  order differential
               equations,

                   dr
                   ÄÄ = v
                   dt





               Trajectory Maker                       Equations of Motion
               Algorithm Supplement                                  2-2
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               



                   dv
                   ÄÄ = G + D
                   dt

               where,  using  Newtonian   differentiation,  the  velocity
               vector is
                       .    .    .
                   v = xi + yj + zk

               Expressed in component form, these two vector differential
               equations become

                   dx   .            dy   .            dz   .
                   ÄÄ = x ,          ÄÄ = y  ,         ÄÄ = z
                   dt                dt                dt

                    .                 .                 .
                   dx                dy                dz
                   ÄÄ = Gx + Dx ,    ÄÄ = Gy + Dy ,    ÄÄ = Gz + Dz
                   dt                dt                dt

               A  solution to  these  six differential  equations  may be
               obtained,  once the  components  of the  gravity  and drag
               acceleration components  are expressed  as known functions
               of x, y,  z.  A time  series solution is  called an ephem-
               eris.  The actual path of the mass m is its trajectory.





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-1
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               3.  GRAVITY PERTURBATION MODEL

               We suppose that the Earth's  figure is an oblate spheroid,
               and let P be point at a distance r from its center of mass
               and let í'  be the declination of  P.  Then, the potential
               at P may  be expressed as a  series of spherical harmonics
               of the form

                          æ ÚÄ     ì                        Ä¿
                   V = - ÄÄ ³ 1 -  ä  Jn ( R/r)n  Pn(sin í') ³
                          r ÀÄ    n=2                       ÄÙ

               where æ is the Earth's  gravitational mass constant, R its
               equatorial radius, Jn the  zonal harmonic coefficients and
               Pn the associated  Legendre polynomials of  order n.  This
               form of  the Earth's  potential function  is known  as the
               Vinti potential function [1].

               The gravitational  mass constant  and Earth  radii used in
               this  paper are  from the  WGS-72  constants [3]  shown in
               Table 3-1.


                         Table 3-1.  WGS-72 Earth Constants

                 ÕÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                 ³   ³      English          ³      Metric         ³
                 ÃÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
                 ³ æ ³ 62750.16789 nm3/sec2  ³ 398600.50 km3/sec2  ³
                 ÃÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
                 ³ R ³  3443.91739 nm        ³   6378.135 km       ³
                 ÃÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
                 ³ ê ³  0.7292115147 (10)-4  rad/sec               ³
                 ÃÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
                 ³ f ³  1/298.26  Dimensionless                    ³
                 ÀÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


               The  harmonic  coefficients are  the  Smithsonian  1973 II
               coefficients [2] tabulated in Table 3-2.





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-2
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                 Table 3-2.  Smithsonian Zonal Harmonic Coefficients

                 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                 ³    J2 = 1082.636e-6    º    J13 =  -0.336e-6    ³
                 ³    J3 =   -2.540e-6    º    J14 =   0.101e-6    ³
                 ³    J4 =   -1.619e-6    º    J15 =   0.104e-6    ³
                 ³    J5 =   -0.230e-6    º    J16 =   0.043e-6    ³
                 ³    J6 =    0.552e-6    º    J17 =  -0.227e-6    ³
                 ³    J7 =   -0.345e-6    º    J18 =  -0.077e-6    ³
                 ³    J8 =   -0.204e-6    º    J19 =   0.083e-6    ³
                 ³    J9 =   -0.162e-6    º    J20 =  -0.108e-6    ³
                 ³    J10 =  -0.232e-6    º    J21 =  -0.070e-6    ³
                 ³    J11 =   0.317e-6    º    J22 =   0.075e-6    ³
                 ³    J12 =  -0.196e-6    º    J23 =   0.111e-6    ³
                 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÐÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


               Now, the distance  from the Earth's center  to the mass m,
               coincident with the point P,  is the magnitude of r, given
               by

                  r = û(x2 + y2 + z2)

               and the sine of its declination is

                   sin í' = z/r

               Since  the gravitational  force  is conservative,  the net
               gravitational  acceleration G  acting on  the mass  is the
               negative gradient of V

                   G = -   V

               which can be decomposed, by differentiating, into the form

                   G = -(æ/r3)r -   U

               The first term in  this expression represents the dominant
               attraction the  Earth would  exhibit if  it were  a sphere
               comprised  of  homogeneous concentric  shells.   This term
               accounts for the non-perturbed conic motion of m.

               The function U  is the disturbing  function whose gradient
               represents  the  gravity  perturbation  acceleration which
               causes  deviations  from  the  conic  motion  of  m.  This
               function is given by





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-3
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                          ì
                   U = æ  ä  Jn Rn r-(n+1) Pn(sin í')
                         n=2

               It follows from the  gradient operator that the components
               of the gravitational perturbation acceleration are

                   ëGx ð -   U/  x = (æx)/r3 ä Jn(R/r)n fn(í')

                   ëGy ð -   U/  y = (æy)/r3 ä Jn(R/r)n fn(í')

                   ëGz ð -   U/  z = (æz)/r3 ä Jn(R/r)n gn(í')

               where

                fn(sin í') = (n + 1)Pn(sin í') + sin í Pn'(sin í')

                gn(sin í') = (n + 1)Pn(sin í') - cos í cot í Pn'(sin í')

               Whittaker  and  Watson  [5]   derive  the  following  four
               recurrence formulas for the complex variable u:

                   Pn+1'(u) - uPn'(u) = (n + 1)Pn(u)                  (1)

                   (u2 - 1)Pn'(u) = nuPn(u) - nPn-1(u)                (2)

                   (n + 1)Pn+1(u) - (2n + 1)uPn(u) + nPn-1(u) = 0     (3)

                   Pn+1'(u) - Pn-1'(u) = (2n + 1)Pn(u)                (4)

               Using the first recurrence formula yields

                   fn(sin í') = Pn+1'(sin í')

               and the second and third formulas yield

                   gn(sin í') = (n + 1)Pn+1(sin í')/sin í'

               Therefore, the components of the perturbation acceleration
               become

                   ëGx = (æx)/r3 ä Jn(R/r)n Pn+1'(sin í')

                   ëGy = (æy)/r3 ä Jn(R/r)n Pn+1'(sin í')

                   ëGz = (æ)/r2  ä Jn(R/r)n(n + 1)Pn+1(sin í')

               In order to numerically  evaluate these expressions it is,





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-4
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               of  course, necessary  to limit  the  series' to  a finite
               number of  terms.  Suppose, then,  that the  degree of the
               polynomials in R/r is specified, say  M ò 2.  Then, with a
               shift of indices we have

                                        M-1
                   ëGx = (æx)/r3 (R/r)2  ä  ai(R/r)i-1
                                        i=1

                                        M-1
                   ëGy = (æy)/r3 (R/r)2  ä  ai(R/r)i-1
                                        i=1

                                        M-1
                   ëGz = (æ)/r2  (R/r)2  ä  bi(R/r)i-1
                                        i=1

               where

                   ai = Ji+1 Pi+2'(sin í')

                   bi = Ji+1(i + 2)Pi+2(sin í')

               The Legendre polynomials  and their derivatives  for n ò 3
               may  be respectively  computed from  the third  and fourth
               recurrence formulas once it is noted that [5]

                   P1(u) = u

                   P2(u) = 1/2 (3u2 - 1)

               and consequently

                   P1'(u) = 1

                   P2'(u) = 3u

               In order to illustrate the effects of various combinations
               of gravity  harmonic coefficients,  we consider  a nominal
               Defense Meteorological Satellite Program mission.

               Its state  vector, at  orbit insertion,  is represented in
               the following Earth-centered-inertial coordinates:





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-5
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                                            .
                   x =   442.151588 nm      x =  0.512255 nm/sec
                                            .
                   y =  1387.396376 nm      y = -3.732104 nm/sec
                                            .
                   z = -3611.173591 nm      z = -1.373147 nm/sec

               The  satellite's  near circular  orbit  is sun-synchronous
               with altitude of about 450 nm.

               The orbit ephemerides were propagated from orbit insertion
               for a duration of 25000 seconds, in increments of 100 sec.
               This step-size is optimal, in this case, since any smaller
               step  does not  significantly  improve the  solution.  The
               trajectory ephemeris spans eight orbits.

               Various gravity  models with reduced  orders (less coeffi-
               cients)  were compared  with  the model  of  highest order
               having the 22 coefficients listed in Table 2 above.

               The state vector  of the highest  order model was compared
               with the lower order  models by differencing their respec-
               tive  position   vector  components,   and  computing  the
               magnitude  of  the resulting  difference  vector.   In the
               figures the difference between a trajectory generated with
               a gravity model of order M and one of order N is indicated
               in the legend by the symbol DJMJN.

               The first group of the  figures, namely, Figures 3-1, 3-2,
               3-3, 3-4, 3-5, 3-6, illustrate differences in ephemerides,
               sequentially beginning with the  J2 coefficient and ending
               with coefficients up to J23.   It is seen that this family
               of curves has  a secular growth over  the time span, while
               exhibiting a  tendency towards  convergence; however, that
               is not to say that  any given order gravity model produces
               more accurate trajectories than a lower order model, as
               for  example, comparison  of the  sixth and  seventh order
               models  in   Figure  3-2.   Figure   3-3  illustrates  the
               beginning  of  the  loss of  data  integrity  as round-off
               accumulates, becoming  more pronounced in  Figures 3-4 and
               3-5.

               The scales in  the above group of  figures vary across the
               figures by  two orders of  magnitude.  In  order to illus-
               trate variations across scales, the next group of figures,
               namely,  Figures 3-7,  3-8, 3-9,  and 3-10  were composed.
               Not all differences are illustrated, but enough to get the
               idea.





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-6
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               The  gravitational effects  on  other orbit  parameters is
               given in detail in Reynolds [4].





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-7
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               














































               Figure 3-1.  Magnitude of Vector Differences Between the
                            23rd and 2nd, 3rd, 4th and 5th Order Gravity
                            Models.





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-8
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               














































               Figure 3-2.  Magnitude of Vector Differences Between the
                            23rd and 6th, 7th, 8th and 9th Order Gravity
                            Models.





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-9
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               














































               Figure 3-3.  Magnitude of Vector Differences Between the
                            23rd and 10th, 11th, 12th and 13th Order
                            Gravity Models.





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-10
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               







































               






               Figure 3-4.   Magnitude of Vector  Differences Between the
                            23rd  and  14th, 15th,  16th  and  17th Order
                            Gravity Models.





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-11
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               






































               
               





               
               Figure 3-5.   Magnitude of Vector  Differences Between the
                            23rd  and  18th, 19th,  20th  and  21st Order
                            Gravity Models.





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-12
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


































               
               







               
               
               
               Figure 3-6.   Magnitude of Vector  Differences Between the
                            23rd  and  19th, 20th,  21st  and  22nd Order
                            Gravity Models.





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-13
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               











































               
               
               
               Figure 3-7.   Magnitude of Vector  Differences Between the
                            23rd and 2nd,  4th, 6th and  8th Order (Even)
                            Gravity Models.





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-14
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               














































               Figure 3-8.   Magnitude of Vector  Differences Between the
                            23rd and  3rd, 5th,  7th and  9th Order (Odd)
                            Gravity Models.





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-15
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               














































               Figure 3-9.   Magnitude of Vector  Differences Between the
                            23rd  and  2nd,  6th,  10th  and  14th  Order
                            Gravity Models.




               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-16
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               














































               Figure 3-10.  Magnitude of  Vector Differences Between the
                             23rd  and  5th, 10th,  15th  and  20th Order
                             Gravity Models.





               Trajectory Maker                             Gravity Model
               Algorithm Supplement                                  3-17
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                                       References

               1.  Anon., Space Flight Handbooks, Volume I, NASA SP-33
                   Part 1, Office of Scientific and Technical Inform-
                   ation, NASA, Washington D. C., 1963.

               2.  Gaposchkin, F. M., ed., 1973 Smithsonian Standard
                   Earth (III), Smithsonian Astrophysical Observatory,
                   Special Report 353, Cambridge, Ma., November 28, 1973.

               3.  Hieb, H., Western Test Range Geodetic Coordinate
                   Manual, Part 1, Federal Electric Corporation, Feb.
                   1980.

               4.  Reynolds, H. B., High-Order Gravitational Perturbation
                   Effects On DMSP Extended Mission Ephemerides, OAO
                   Corporation, Technical Operating Report, El Segundo,
                   Ca., Jan. 3, 1985.

               5.  Whittaker, F. and G. Watson, A Course in Modern
                   Analysis, Cambridge University Press, Fourth Ed. 1963.

               



               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-1
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               4.  DRAG PERTURBATION MODEL

               The  aerodynamic drag  force  acting on  an  object varies
               jointly with  the atmospheric  density å,  the object drag
               coefficient CD,  the projected  cross sectional  area A of
               the object (normal to the  velocity vector), the square of
               its  speed relative  to  the rotating  atmosphere  va, and
               inversely  with its  mass  m.  The  drag  force acts  in a
               direction opposite that of the relative velocity vector.

               In vector form this force per unit mass may be written

                           CD A
                   D = - å ÄÄÄÄ  va va
                            2m

               justifiably, since the object  imparts a velocity of order
               va  to a  mass of  air Aåva  in each  second; the  rate of
               change of momentum, equal to the drag force on the object,
               is thus Aåvaý.  The empirical drag coefficient is based on
               such  things  as  the object's  shape,  altitude  and Mach
               number.

               Taking into account local  wind conditions with the vector
               q, the velocity relative to the rotating air mass is

                   va = v - ê x r - q

               where ê  = êk is  the Earth's rotation  rate vector having
               magnitude 0.7292115147 (10)-4  rad/sec.

               It is usual to define a ballistic coefficient á by

                        m
                   á = ÄÄÄÄ
                       CD A

               and write the drag force as

                           1
                   D = -  ÄÄÄ å va va
                          2 á

               which in component form,  after expanding the above vector
               product, becomes





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-2
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                              .
                   Dx = -åva[(x + êy) - q1]/(2á)
                              .
                   Dy = -åva[(y - êx) - q2]/(2á)
                              .
                   Dz = -åva[ z - q3 ]/(2á)

               where
                           .                  .                 .
                  va = û{[(x + êy) - q1]2 + [(y - êx) - q2]2 + (z - q3)2}

               and  q1,  q2,  q3  denote  the  wind  velocity  components
               relative to the rotating atmosphere.

               Ballistic  coefficients  have  an  intuitive  appeal since
               their units,  measured in  kg/mý,  resemble density units.
               When working with English units, the ballistic coefficient
               is usually expressed in mean  sea level weight rather than
               mass, that is lb/ftý.   The following are typical examples
               that may be encountered:

                   o A space based radar antenna: 0.144, to 0.448 lb/ftý
                   o Space Shuttle Discovery: 42 lb/ftý
                   o Ballistic missiles: 25, 75, 2150 lb/ftý

               When  computing  a  ballistic  coefficients  for  orbiting
               objects,  the  parameter  with  the  most  uncertainty  is
               usually the drag coefficient.  Although this is not always
               the  case.  For  example, Reynolds  [2] considers  a space
               based radar system  having a rotating  antenna whose shape
               is an arbitrary surface of revolution.

               Wertz  [5] suggests  that  in the  absence  of aposteriori
               knowledge of the  drag coefficient that a  value of 2.0 be
               used.   Waison [4]  reports that  it should  be consistent
               with the value  used to derive  the atmospheric model, and
               that for the 1959  ARDC model one should  use 2.0; for the
               1964 Jacchia model, a value of 2.2 should be used.

               For reentry vehicles, the drag coefficient may be provided
               as  a function  of Mach  number  M, as  in the  Table 4-1,
               together with the vehicle's mass and effective area.





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-3
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                     Table 4-1.  Drag Coefficient vs. Mach Number

                        Mass = 35.8365 slugs,   Area = 19.8 ftý
                ÚÄÄÄÄÒÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄ¿
                ³ M  º 0   ³ .25 ³ .50 ³ .75 ³ 1.0 ³ 1.25 ³ 1.5 ³ 100 ³
                ÃÄÄÄÄ×ÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄ´
                ³ CD º .38 ³ .40 ³ .44 ³ .55 ³ .72 ³ .76  ³ .77 ³ .77 ³
                ÀÄÄÄÄÐÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÙ


               Mach number  is function of  the speed of  sound, which in
               turn is a function of temperature.  The expression adopted
               for the speed of sound in Reference [1] is

                   Cs = û(  R* TM/M0)

               where   is the  ratio of specific heat  of air at constant
               pressure to that  at constant volume, and  taken to be 1.4
               (dimensionless) exactly, R*  the gas constant  taken to be
               8314.32  N.m/(kmol.K),  M0  the  sea-level  mean molecular
               weight  of  the  mixture of  gasses  taken  to  be 28.9644
               kg/kmol,  and  TM  is  the  molecular  scale  temperature,
               modeled as a linear, segmental arc.

               Putting all these things together results in

                   Cs = 20.04680276 ûTM    (meters/sec)

               and the Mach number is

                   M = va/Cs

               The  concept of  speed of  sound progressively  looses its
               range  of applicability  at  high altitudes  and  for this
               reason the values  of speed of sound  are not computed for
               heights above 86 km.

               Table 4-2 is extracted from Table  9 of the U. S. Standard
               1976 abbreviated tables.





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-4
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                                  Table 4-2

                           Molecular Scale Temperature

                      ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                      ³ Geometric     ³ Molecular Scale  ³
                      ³ Altitude (km) ³ Temperature (K)  ³
                      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
                      ³     0.0000    ³     288.150      ³
                      ³    11.0190    ³     216.650      ³
                      ³    20.0631    ³     216.650      ³
                      ³    32.1619    ³     288.650      ³
                      ³    47.3500    ³     270.650      ³
                      ³    51.4124    ³     270.650      ³
                      ³    71.8019    ³     214.650      ³
                      ³    86.0000    ³     186.946      ³
                      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


               Since the U. S. STandard  models the temperature as linear
               segments, it is only  necessary to interpolate linearly in
               this  table  to  obtain  TM  for  arbitrary  altitude, and
               substitute the result  into the above  equation to compute
               the speed of sound.


               4.1  Atmospheric Density Profile

               Another complication  is that  density varies  in a fairly
               irregular  manner  with factors  such  as  solar activity,
               yearly  seasons, time  of  day, geographical  location and
               altitude.   Fortunately,   extensive  research   has  been
               performed  by various  agencies to  define models  for the
               principle atmospheric parameters.

               The 1976  U. S. Standard  Atmosphere [1]  is an idealized,
               steady state representation of the Earth's atmosphere from
               its surface  to 1000 km,  as it  is assumed to  exist in a
               period of moderate solar activity.  It consists of compre-
               hensive  tables  (approximately  1000  points)  of various
               atmospheric parameters, including  density, tabulated as a
               function of altitude.  The  density profile is illustrated
               in Figure 4-1 on a common logarithm scale.

               Since 1000 pairs is a lot  of data to handle, subsets were
               extracted and modeled  with the goal  of obtaining a rela-
               tively small subset that would yield sufficient accuracy.





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-5
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               In effort to obtain  the smoothest possible representation
               for density, cubic spline functions were used to model the
               common logarithm of the density profile, with the realiza-
               tion  that,   during  orbit   propagation,  density  would
               necessarily  be  obtained from  the  logarithm  profile by
               exponentiation.

               Several  subsets were  extracted  from the  Standard Atmo-
               sphere, starting  with the  abbreviated tables, consisting
               of  21 pairs,  from the   Standard Atmosphere  [1].  These
               points are illustrated in Figure 4-2.

               The final set selected for the model, herein, was obtained
               by judiciously  selecting points from  the idealized model
               until the percent relative error in density was reduced to
               less than 1%.  The resulting set consisted of 48 altitude-
               density pairs illustrated in  Figure 4-3.  Note that these
               data are not equally spaced.  However,  besides being very
               fast, Thompson's  algorithm [3]  accounts for  this situa-
               tion.

               Figure 4-4 illustrates the percent relative error obtained
               when  using  these  two  density  profiles  to  model  the
               idealized atmosphere.  The dashed  curve shows that in the
               critical altitude  region (less  than 200  km) for reentry
               trajectories, the 21 point set  produces errors as high as
               6%.  On the  other hand, for  the 48 point  set the errors
               are less  than 1%.  This  is shown more  clearly in Figure
               4-5.

               Figure  4-6 compares  linear interpolation  (dashed curve)
               with spline interpolation (solid  curve).  It is seen that
               linear interpolation  produces errors  as high  as 4%.  It
               should be emphasized  that these error  curves are density
               errors rather than the logarithm of the density errors.

               Figure 4-7  isolates the error  for the 48-point  set on a
               magnified scale.   The figure shows  that the  error to be
               less than 1% on the entire altitude range.  It is this set
               that  comprises  the  density  profile  used  herein.  The
               actual values for this set are tabulated in Table 4-3.

               This study also found that the endpoint derivatives played
               a  significant  role  towards  achieving  the  1% accuracy
               criterion.   Thus, rather  than computing  the derivatives
               with  values from  Table  4-3, the  following  values were
               computed  using  a  finer  resolution  from  data  in  the
               comprehensive table:





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-6
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               



                   (log å(0))' = -0.041934

                   (log å(1000))' = -0.001834

               where we  recall that the  splines were fit  to the common
               logarithm of the density values.


                       Table 4-3.  Atmospheric Density Profile

                ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                ³ Altitude   Density     º Altitude   Density      ³
                ³  (km)      (kg/m3)     º (km)       (kg/m3)      ³
                ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ×ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
                ³   0       1.2250       º    90      3.416e-6     ³
                ³   2       1.0066       º   100      5.604e-7     ³
                ³   4       8.1935e-1    º   110      9.708e-8     ³
                ³   6       6.6011e-1    º   120      2.222e-8     ³
                ³   8       5.2579e-1    º   130      8.152e-9     ³
                ³   10      4.1351e-1    º   140      3.831e-9     ³
                ³   12      3.1194e-1    º   150      2.076e-9     ³
                ³   14      2.2786e-1    º   160      1.233e-9     ³
                ³   16      1.6647e-1    º   170      7.815e-10    ³
                ³   18      1.2165e-1    º   180      5.194e-10    ³
                ³   20      8.8910e-2    º   190      3.581e-10    ³
                ³   25      4.0084e-2    º   200      2.541e-10    ³
                ³   30      1.8410e-2    º   220      1.367e-10    ³
                ³   35      8.4634e-3    º   240      7.858e-11    ³
                ³   40      3.9957e-3    º   260      4.742e-11    ³
                ³   45      1.9663e-3    º   280      2.971e-11    ³
                ³   50      1.0269e-3    º   300      1.916e-11    ³
                ³   45      1.9663e-3    º   400      2.802e-12    ³
                ³   60      3.0968e-4    º   500      5.215e-13    ³
                ³   65      1.6321e-4    º   600      1.137e-13    ³
                ³   70      8.2829e-5    º   700      3.069e-14    ³
                ³   75      3.9921e-5    º   800      1.136e-14    ³
                ³   80      1.8458e-5    º   900      5.759e-15    ³
                ³   85      8.2196e-6    º  1000      3.561e-15    ³
                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÐÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-7
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               
















































               Fig. 4-1.  1976 U. S. Standard Atmosphere Density Profile.





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-8
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               











































               

               

               Fig. 4-2.  Abbreviated 1976 U. S. Standard Atmosphere
                          Density Profile.





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-9
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               













































               
               
               
               Fig. 4-3.  Trajectory Maker Density Profile Model.





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-10
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               















































               Fig. 4-4.  Cubic Spline Interpolation Error for the 21 and
                          48 Point Tables.





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-11
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               











































               

               

               Fig. 4-5.  Cubic Spline Interpolation Error for the 21 and
                          48 Point Tables.





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-12
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               












































               


               Fig. 4-6.  Cubic Spline and Linear Interpolation Error
                          for the 48 Point Table.





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-13
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               










































               

               

               
               Fig.  4-7.  Cubic  Spline Interpolation  Error for  the 48
                          Point Table.





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-14
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               4.2  Wind Profile

               Local atmospheric winds are typically supplied in the form
               of a table which contains the wind velocity magnitude q(h)
               and direction é(h)  as functions of  altitude.  The direc-
               tion of the wind is defined as the true bearing from which
               it is blowing.   The east, north and  up components of the
               wind velocity are, respectively,

                   qe = -q(h) sin é(h)

                   qn = -q(h) cos é(h)

                   qu = 0

               For the purpose of illustration,  a couple of typical wind
               profiles from the Lompoc region are illustrated in Figures
               4-8  and   4-9.   The  symbols   represent  observed  wind
               velocities that were mapped into east and north components
               by the above equations.   Cubic spline functions were used
               to model these  data and several  values were computed and
               plotted at  intermediate values  of altitude.   Two things
               are noteworthy - that  splines provide a smooth represent-
               ation of the data, and that Lompoc is a windy place.

               The above components can  be transformed into Earth-fixed-
               geocentric coordinates with the aid of a rotation matrix R
               which  shall  be  defined,  subsequently,  when coordinate
               systems and transformations are treated.  At that time, an
               innovative algorithm  for computing altitude  will also be
               developed.  For now, it suffices to write

                   ÚÄ  Ä¿      ÚÄ  Ä¿
                   ³ q1 ³      ³ qe ³
                   ³ q2 ³ =  R ³ qn ³
                   ³ q3 ³      ³ qu ³
                   ÀÄ  ÄÙ      ÀÄ  ÄÙ





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-15
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               
















































               Fig. 4-8.  East-North Wind Velocity Components, Example 1.





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-16
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               
















































               Fig. 4-9.  East-North Wind Velocity Components, Example 2.





               Trajectory Maker                                Drag Model
               Algorithm Supplement                                  4-17
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                                       References

               1.  Menzner, et. al., Defining Constants, Equations,
                   and Abbreviated Tables of the 1975 U. S. Standard
                   Atmosphere, National Aeronautics and Space
                   Administration, Technical Report NASA TR R-459,
                   Washington D. C., May 1976.

               2.  Reynolds, H. B., Atmospheric Drag Effects on a Space
                   Based Radar Antenna, TRW Technical Memorandum,
                   January, 1991.

               3.  Thompson, R. F., Spline Interpolation on  a Digital
                   Computer, Goddard Space Flight Center, Technical
                   Report X-692-70-261, Greenbelt, Md., July 1970.

               4.  Waison, G. R., Prediction of Orbital Decay Rates Due
                   to Atmospheric Drag, TRW Program Technical Report,
                   3150-6020-RO-000, January 7, 1966.

               5.  Wertz, J. R., ed., Spacecraft Attitude Determination
                   and Control, D. Reidel Publishing Company, Boston,
                   1985.






               Trajectory Maker                        Integration Scheme
               Algorithm Supplement                                  5-1
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               5.  NUMERICAL INTEGRATION SCHEME

               Substituting  the   atmospheric  drag   and  gravitational
               perturbation acceleration  components, into  the component
               form of the  first order vector  differential equations of
               motion, results  in the  following explicit  system of six
               first-order ordinary differential equations:

                   dx   .
                   ÄÄ = x
                   dt

                   dy   .
                   ÄÄ = y
                   dt

                   dz   .
                   ÄÄ = z
                   dt
                    .
                   dx     æx
                   ÄÄ = - ÄÄ + ëGx + Dx
                   dt     r3
                    .
                   dy     æy
                   ÄÄ = - ÄÄ + ëGy + Dy
                   dt     r3
                    .
                   dz     æz
                   ÄÄ = - ÄÄ + ëGz + Dz
                   dt     r3

               If  the  perturbation  components  are  set  to  zero, the
               resulting equations are clearly recognizable as describing
               classical two-body motion.

               By defining the system state as the vector
                               . . .
                   x = [ x y z x y z ]T

               where the superscript T  denotes matrix transposition, the
               differential  equations   may  now   be  brought   into  a
               computational convenient vector form

                   dx
                   ÄÄ = f(x)
                   dt





               Trajectory Maker                        Integration Scheme
               Algorithm Supplement                                  5-2
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               where f represents the vector-valued function of the state
               vector defined by the  right-hand-side of the differential
               equations.

               The differential  equations of motion  comprise an initial
               value system,  which may be  written in  more generally in
               the vector form including time,

                   dx
                   ÄÄ = f(t, x),   x(t0) = x0
                   dt
                                                              .  .  .
               where x = (x1, x2, x3, x4, x5, x6) ð (x, y, z, x, y, z).

               A numerical  scheme for integrating  initial value systems
               that  is  of  very  high-precision,  generally  stable and
               relatively  easy  to implement  is  Shanks'  explicit 8-12
               formulation  for  solutions to  differential  equations by
               evaluations of functions [1].

               This method is based on the classical Runge-Kutta formulas
               found in most textbooks on numerical analysis.

               The 8-12 means that the order of the integration scheme is
               eight (that  is, the truncation  error is  order nine) and
               twelve  evaluations (that  is,  stages) of  the right-hand
               side of the differential equations are performed.

               This scheme is a fixed  step integrator which is preferred
               for  trajectory  animation   graphics.   For  example,  an
               orbiting object may move farther  in its present time step
               than its preceding  time step. To  an observer, the object
               appears to move faster.

               An  advantage of  employing  a high-order  scheme  is that
               accuracy  may be  maintained  in considerable  fewer steps
               than the classical formulations.

               Given the state x = x(t) of the system at time t, then the
               state of the system at t + ët is given by

                   x(t + ët) = x(t) + ëx

               where

                   ëx ÷ ( 41 k1 + 216 k6 + 272 k7 + 27 k8 +  27 k9

                        + 36 k10 + 180 k11 + 41 k12 ) / 840 + O(ët9)





               Trajectory Maker                        Integration Scheme
               Algorithm Supplement                                  5-3
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               Using the Einstein  summation convention with  å = 1, ...,
               12 and æ ó å, the coefficients may be defined by

                   kå = f(t + tå ët, x + såæ kæ ) ët

               The  non-zero  constants  tå  and  såæ  appearing  in this
               expression are defined in Table 5-1 below.


                Table 5-1. Shanks' 8-12 Numerical Integration Constants.

               ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
               ³ t2 = 1/9     t3 = 1/6   t4 = 1/4    t5 = 1/10          ³
               ³ t6 = 1/6     t7 = 1/2   t8 = 2/3    t9 = 1/3           ³
               ³ t10= 5/6     t11= 5/6   t12= 1                         ³
               ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
               ³ s11 = 1/9                                              ³
               ³ s21 = 1/24         s22 = 1/8                           ³
               ³ s31 = 1/16         s33 = 3/16                          ³
               ³ s41 = 29/500       s43 = 33/500      s44 = -3/125      ³
               ³ s51 = 11/324       s54 = 1/243       s55 = 125/972     ³
               ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
               ³ s61 = -7/12        s64 = 19/9        s65 = 125/36      ³
               ³ s66 = -9/2                                             ³
               ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
               ³ s71 = -10/81       s74 = -32/243     s75 = 125/243     ³
               ³ s77 = 11/27                                            ³
               ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
               ³ s81 = 1175/324     s84 = -32/3        s85 = -3125/162  ³
               ³ s86 = 26           s87 = 121/162      s88 = -1/12      ³
               ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
               ³ s91 = 293/324      s94 = -71/27       s95 = -1375/324  ³
               ³ s96 = 51/9         s97 = -59/162      s98 = 1/2        ³
               ³ s99 = 1                                                ³
               ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
               ³ s101 = 1303/1620   s104 = -71/27      s105 = -1375/324 ³
               ³ s106 = 37/6        s107 = 103/162     s1010= 1/10      ³
               ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
               ³ s111 = -955/492    s114 = 2560/369    s115 = 8125/738  ³
               ³ s116 = -612/41     s117 = 7/82        s118 = -27/164   ³
               ³ s119 = -18/41      s1110= -12/41      s1111=  30/41    ³
               ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


               Then, given the initial state x0 of the system at time t0,
               the time increment ët and  the final time tf, the solution
               may  be  generated  (or  propagated)  with  the  following
               recursion scheme:





               Trajectory Maker                        Integration Scheme
               Algorithm Supplement                                  5-4
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                   x(tm) = x(t0 + m ët);   m = 0, 1, ..., (tf - t0)/ët

               A  numerical  scheme   that  integrates  the  differential
               equations of motion  directly, such as  this one, is known
               as a Cowell integration scheme.  The scheme doesn't really
               care  what kind  of  orbit it  is  generating, and  it can
               handle   deviations   from   classical   two-body  motion.
               Moreover,  the user  has  complete control  concerning its
               accuracy with his choice of propagation step-size.

               Figure  5-1  illustrates  the   common  logarithm  of  the
               relative  error  in  Shanks'  8-12  numerical  integration
               scheme.

               The error is based on a 200 nm unperturbed orbit.  In this
               instance, the  Earth is  modeled as  a sphere  so that, at
               least theoretically,  the altitude  is a  constant 200 nm.
               The  computed altitude  will, of  course, differ  from the
               true altitude  depending on the  integration step-size and
               the number of integration steps.

               The  figure illustrates  the error  as  a function  of the
               final time  in days of  86400 seconds.  (Equivalent to the
               duration of the orbit since the initial time was zero.)

               The relative error is shown because of its connection with
               the number  of significant  figures and  independence from
               any particular units  employed.  From elementary numerical
               analysis, it  is known that  if the relative  error in any
               number  is not  greater  than 0.5  X  10-N, the  number is
               certainly correct to N significant figures.

               It is  seen, for example,  that if an  orbit is propagated
               with a step size of 300 seconds (5 minutes) for a duration
               of  7 days  (2016 steps),  the  logarithm of  the relative
               error is about -5.5.  Since

                   log(0.5 X 10-N) ÷ -(0.301 + N)

               and  -5.5  <  -5.301, the  computation  is  accurate  to 5
               significant figures, which is  equivalent to about 0.01 nm
               for a 200.00 nm orbit.

               It is emphasized that the results obtained from the figure
               are  based on  an unperturbed  orbit.  However,  they will
               generally be valid for gravity perturbed orbits as well.





               Trajectory Maker                        Integration Scheme
               Algorithm Supplement                                  5-5
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               Things  are  quite  different  for  objects  entering  the
               Earth's atmosphere.  Such an object  experiences a violent
               transient in  its acceleration  profile that  can tax most
               any integrator's numerical integrity.

               Several factors are  involved. The speed  of the object is
               squared in the drag force  equation, the density varies by
               orders of  magnitude becoming large  in the  100 km region
               and the drag force is sensitive to the ballistic coeffi-
               cient. (Small ballistic coefficients result in larger drag
               forces than large ballistic coefficients.)





               Trajectory Maker                        Integration Scheme
               Algorithm Supplement                                  5-6
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               
















































               Figure 5-1.  Numerical Integration Error





               Trajectory Maker                        Integration Scheme
               Algorithm Supplement                                  5-7
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                                       References

               1.  Shanks, B. F., Solutions of Differential Equations by
                   Evaluations of Functions, Math. Comp. 20 (1966) pp.
                   21-38.





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-1
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               6.  COORDINATE SYSTEMS AND TRANSFORMATIONS

               We have seen  that in order to  propagate the equations of
               motion  with  a  Cowell integration  scheme,  all  that is
               required  is  an  initial state  vector  given  in  Earth-
               centered-inertial coordinates,
                            .  .  .
                   [x, y, z, x, y, z]T

               at some epoch  t0.  Rectangular coordinates  such as these
               are  difficult  to visualize.   Nevertheless,  the program
               should  include the  option for   specifying input  in the
               form of ECI coordinates, because these coordinates will be
               known for  many applications; in  particular for ballistic
               missile trajectories.

               However, there  exist other coordinate  systems which will
               simplify  our  visualization  process  when  it  comes  to
               describing  an  initial trajectory  with  input  data, and
               interpreting various characteristics with output data.


               6.1  Time Considerations

               A  fundamental  parameter  that  is  needed  to  define an
               inertial reference system  is the Greenwich  hour angle of
               the  vernal equinox  at  epoch or  orbit  insertion.  This
               angle is  equivalent to  Greenwich sidereal  time at epoch
               and serves to fix a satellite ground trace relative to the
               rotating earth.

               We suppose that  the initial time,  or epoch, is specified
               by the year,  I, month, J,  day, K, and  universal time in
               hours, minutes, and seconds  (past midnight).  These units
               may  be converted  to the  Julian  date JD,  measured from
               January 0.0 by the clever expression in Wertz [4],

                JD = K - 32075 + 1461*( I + 4800 + (J - 14)/12)/4
                                + 367*( J -    2 - (J - 14)/12*12)/12
                                  - 3*((I + 4900 + (J - 14)/12)/100)/4
                                  - 0.50

               where  I,  J,  K  are  defined  to  be  integers  and  the
               arithmetic  is  performed  in   integer  mode.   That  is,
               floating point  numbers are truncated  at each  stage of a
               computation, such as done by a computer language such as C
               or FORTRAN.





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-2
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               The right ascension of the Sun is obtained using Newcomb's
               equation [1]

                   Ru = 279.6910 + 36000.7689 T + 0.0004 T2   (degrees)

               where T  is the number  of Julian centuries  of 36525 days
               elapsed since noon Greenwich mean time on January 0, 1900.
               This value is computed from

                   T = (JD - JD0)/36525

               where JD0  is the Julian  day from Greenwich  mean noon on
               January 0.5, 1900 which is 2,415,020.0.

               Universal time in degrees is

                   UT = 15*(hours + minutes/60 + seconds/3600)

               So that the Greenwich sidereal time is

                   GST = Ru + UT - 180   (degrees)


               6.2  Orbital Elements

               A  convenient method  for defining  an  orbit is  with its
               orbital elements.  These elements describe its size, shape
               and orientation.   They are:  semimajor  axis a, eccentri-
               city e,  inclination i, longitude of the ascending node ê,
               argument of  perigee w,  and some  time when  the orbiting
               object passes perigee ç.

               This latter element is also  equivalent to mean anomaly M,
               but  when  specifying non-elliptical  orbits,  it  is more
               convenient to specify  time past perigee  and compute mean
               anomaly from the formula

                   M = nç

               where n is the mean motion given by

                   n = (æ a3)1/2

               This parameter  is the  same as  2ã/P for  elliptic orbits
               having period P.

               It is a  known from two-body  theory that orbital elements
               at an  instant in  time, in  particular at  the epoch, are





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-3
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               integration  constants  of the  differential  equations of
               motion,  and   these  constants  are   equivalent  to  the
               instantaneous   rectangular   coordinates   by   a   given
               coordinate  transformation.  This  transformation  is from
               Roy [3].

               A geocentric, inertial coordinate system is defined in the
               orbit plane  with principle axis  x* along  the major axis
               positive  in the  direction  of perigee,  another  axis z*
               normal to  the orbit  plane in  the direction  of positive
               angular momentum and  a third axis y*  defined so that the
               system is right handed.

               From the orientation angles ê, w, i, the direction cosines
               of the  x*, y*,  z* two  planar axes  relative to  the ECI
               system may be obtained.  They are

                   l1 = cos ê cos w - sin ê sin w cos i
                   m1 = sin ê cos w + cos ê sin w cos i
                   n1 = sin w sin i

                   l2 = -cos ê cos w - sin ê sin w cos i
                   m2 = -sin ê cos w + cos ê sin w cos i
                   n2 = cos w sin i

               These  cosines are  independent  of the  specific  type of
               orbit be it elliptic, hyperbolic or parabolic.


               Elliptical Case
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               
               The ECI state vector for the elliptical case is given by

                   x = al1 cos E + bl2 sin E - ael1

                   y = am1 cos E + bm2 sin E - aem1

                   z = an1 cos E + bn2 sin E - aen1
                   .
                   x = (bl2 cos E - al1 sin E)(na/r)
                   .
                   y = (bm2 cos E - am1 sin E)(na/r)
                   .
                   z = (bn2 cos E - an1 sin E)(na/r)

               where b is the orbit's semiminor axis given by





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-4
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                   b = a(1 - e2)1/2

               and r is objects' radius vector magnitude given by

                   r = a(1 - e cos E)

               The  parameter   E  is  the   object's  eccentric  anomaly
               obtainable from Kepler equation

                   E - e sin E = M

               by employing Newton's method for finding roots.


               Hyperbolic Case
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               
               The ECI state vector for the hyperbolic case is given by

                   x = -al1 cosh F + bl2 sinh F + ael1

                   y = -am1 cosh F + bm2 sinh F + aem1

                   z = -an1 cosh F + bn2 sinh F + aen1
                   .
                   x = (bl2 cosh F - al1 sinh F)(na/r)
                   .
                   y = (bm2 cosh F - am1 sinh F)(na/r)
                   .
                   z = (bn2 cosh F - an1 sinh F)(na/r)


               where b is the orbit's semiminor axis given by

                   b = a(e2 - 1)1/2

               and r is objects' radius vector magnitude given by

                   r = a(F cosh F - 1)

               The parameter F is the objects' hyperbolic areal parameter
               obtainable from the hyperbolic analog of Kepler's equation

                   F sinh F - F = M

               also, by employing Newton's method for finding roots.





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-5
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               Parabolic Case
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               The ECI state vector for the parabolic case is given by

                   x = l1r x* + l2r y*

                   y = m1r x* + m2r y*

                   z = n1r x* + n2r y*
                   .
                   x = l1 x* + l2 y*
                   .
                   y = m1 x* + m2 y*
                   .
                   z = n1 x* + n2 y*

               where

                   x* = û(æp) ( sin f* cos f* /p - sin f* /r)

                   y* = û(æp) ( sin f* sin f* /p - cos f* /r)

               For the parabolic  case, the semimajor  axis a is defined,
               herein,  as the  object's perigee  distance and  the conic
               parameter is computed from

                   p = 2a

               The parameter f*  is the object's true  anomaly and may be
               found by solving Barker's cubic equation
                                 _
                   D + 1/3 D3 = 2n(t - ç)

               where

                   D = tan (f*/2)

               and
                   _
                   n2 p3 = æ

               Details of the solution are given in Roy [3].





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-6
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               6.3  Geospherical Inertial Coordinates

               Geospherical    inertial    coordinates    are   spherical
               coordinates  having their  origin  at the  Earth's center.
               These  coordinates consist  of an  objects range  r, right
               ascension à and declination  ë.  Declination is equivalent
               to geocentric latitude, until now, denoted by í'.

               These coordinates are defined by

                   r = û(x2 + y2 + z2)

                   ë = arcsin(z/r)

                   à = arctan(y/x)

               In addition, the following flight parameters are computed:

               Inertial velocity

                         .    .    .
                   v = û(x2 + y2 + z2)

               Flight path angle

                   â = arcsin(x'/v)

               Velocity azimuth angle

                   å = arctan(y'/z')

               where

                ÚÄ  Ä¿   ÚÄ                                   Ä¿ ÚÄ Ä¿
                ³ x' ³   ³  cos ë cos à    cos ë sin à   sin ë ³ ³ x ³
                ³    ³   ³                                     ³ ³   ³
                ³ y' ³ = ³    -sin à          cos à        0   ³ ³ y ³
                ³    ³   ³                                     ³ ³   ³
                ³ z' ³   ³ -sin ë cos à   -sin ë sin à   cos ë ³ ³ z ³
                ÀÄ  ÄÙ   ÀÄ                                   ÄÙ ÀÄ ÄÙ

               All the remaining coordinates used for the software system
               are relative to the rotating Earth.


               6.4  Earth-Fixed-Geocentric Coordinates

               Earth-fixed-geocentric  (EFG) coordinates  have  origin at





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-7
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               the Earth's  geocenter, fundamental  plane coincident with
               the equatorial plane  and principle axis  in the direction
               of the Greenwich meridian.   This coordinate system, being
               fixed  relative  to  the  Earth  is  actually  a  rotating
               coordinate system.

               Letting e, f, g denote  these coordinates, the e-axis lies
               in the equatorial  plane and is  positive in the direction
               of Greenwich;  the g-axis  is coincident  with the Earth's
               polar axis, i.e.,  its spin axis; and  the f-axis lying in
               the equatorial plane such that the system is right-handed.

               This coordinate system is related to the inertial frame by
               the transformation

                   e =  x cos(gst) + y sin(gst)

                   f = -x sin(gst) + y cos(gst)

                   g =  z

               where gst is the current  Greenwich sidereal time.  If gha
               is the Greenwich sidereal time at epoch, then

                   gst= gha + êt  (mod 360)

               where t is the time past epoch.


               6.5  Local Topocentric Coordinates

               Local topocentric  coordinates (UVW)  have origin  at some
               local site  on the surface  of the  Earth, and fundamental
               plane tangent to the surface  at the site.  This reference
               system is also a rotating coordinate system.

               Letting u, v, w denote these coordinates, where the w-axis
               is  normal  to the  tangent  plane at  the  site, positive
               upwards;  the  principle  u-axis is  lies  in  the tangent
               plane, positive at  in an azimuthal  direction   ; and the
               v-axis lies in  the tangent plane such  that the system is
               right-handed.

               It is shown in O'Connor  [2], that the transformation from
               earth-fixed-geocentric  coordinates  to  local topocentric
               coordinates is given by the transformation





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-8
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                   ÚÄ Ä¿       ÚÄ      Ä¿
                   ³ u ³       ³ e - e0 ³
                   ³ v ³ =  ABC³ f - f0 ³
                   ³ w ³       ³ g - g0 ³
                   ÀÄ ÄÙ       ÀÄ      ÄÙ

               where the rotation matrices are

                         ÚÄ                    Ä¿
                         ³  sin      cos      0 ³
                   A =   ³ -cos      sin      0 ³
                         ³    0        0      1 ³
                         ÀÄ                    ÄÙ

                         ÚÄ                    Ä¿
                         ³ 1      0        0    ³
                   B =   ³ 0    sin í    cos í  ³
                         ³ 0   -cos í    sin í  ³
                         ÀÄ                    ÄÙ

                         ÚÄ                    Ä¿
                         ³ -sin      cos      0 ³
                   C =   ³ -cos     -sin      0 ³
                         ³    0        0      1 ³
                         ÀÄ                    ÄÙ

               where í,   denote the latitude  and longitude of the site,
               respectively, and e0, f0, g0, are its EFG coordinates.

               These latter coordinates may be computed directly from

                        ÚÄ                     Ä¿
                        ³        a              ³
                   e0 = ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ  + h ³ cos í cos *
                        ³ û(1 - e2 sin2 í)      ³
                        ÀÄ                     ÄÙ

                        ÚÄ                     Ä¿
                        ³        a              ³
                   f0 = ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ  + h ³ cos í sin *
                        ³ û(1 - e2 sin2 í)      ³
                        ÀÄ                     ÄÙ

                        ÚÄ                     Ä¿
                        ³    a(1 - e2)          ³
                   g0 = ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ  + h ³ sin í
                        ³ û(1 - e2 sin2 í)      ³
                        ÀÄ                     ÄÙ





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-9
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               If the azimuth angle is 90ø, this system is referred to as
               the  East-North-Up coordinate  system.   In this  case the
               azimuthal matrix is the unit matrix

                        ÚÄ           Ä¿
                        ³ 1    0    0 ³
                   A =  ³ 0    1    0 ³
                        ³ 0    0    1 ³
                        ÀÄ           ÄÙ

               and the transformation becomes

                   ÚÄ  Ä¿      ÚÄ      Ä¿
                   ³ ue ³      ³ e - e0 ³
                   ³ vn ³ =  BC³ f - f0 ³
                   ³ wu ³      ³ g - g0 ³
                   ÀÄ  ÄÙ      ÀÄ      ÄÙ

               where

                         ÚÄ                                      Ä¿
                         ³        -sin            cos        0    ³
                   BC=   ³  -sin í cos     -sin í sin        0    ³
                         ³   cos í cos      cos í sin      sin í  ³
                         ÀÄ                                      ÄÙ

               By differentiating  and solving for  the e,  f, g velocity
               components, we find that

                    .  .  .                .  .  .
                  [ e  f  g ]T =   (BC)T [ u  v  w ]T

               These  components   may  be   identified  with   the  wind
               components in Section 4.  That is  R= (BC)T so that

                  Ú   Ä¿      ÚÄ  Ä¿
                  ³ q1 ³      ³ qe ³
                  ³ q2 ³ =  R ³ qn ³
                  ³ q3 ³      ³ qu ³
                  À   ÄÙ      ÀÄ  ÄÙ

               Carrying out the matrix operations, we have

                   q1 = -[qe sin   + qn cos * sin í]

                   q2 =  [qe cos   - qn sin * sin í]

                   q3 =  qn cos í





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-10
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               which are  the inertial wind  velocity components required
               for the equations of motion.


               6.6  Common Radar Coordinates

               Radar coordinates  (RAE) are  used for  measurements of at
               some particular geographic location or site.  They consist
               of an object's  range, azimuth and  elevation.  Range R is
               the distance from the site to the object; azimuth A is the
               angle between  the object  and the  radar site's meridian,
               measured  clockwise  from   the  northern  direction;  and
               elevation  E  is the  angle  above or  below  the horizon.
               These coordinates are given by the following expressions

                   R = û(ue2 +vn2 + wu2)

                   A = arctan(ue/vn)

                   E = arcsin(wn/R)

               where the subscripts e, n, u denote the east, north and up
               components, respectively.

               In  addition  range rate  is  obtained  by differentiating
               range.  We have,

                   .      .      .       .
                   R = (ueue + vnvn +  wuwu)/R


               6.7  Geodetic Coordinates and Computation of Altitude

               Altitude of  an orbiting  object is  its height  above the
               Earth's surface.  If the Earth  were a sphere of radius of
               radius a, then the  altitude of an object  at a distance r
               from the geocenter would be

                   h = r - a

               But the equatorial and polar radii differ by nearly 12 nm;
               The  polar  radius  being  the  smaller  of  the  two.   A
               parameter  commonly used  for measuring  the shape  of the
               Earth is its flattening defined by

                   f = (a - b)/a

               where,  in  this  section, a   and  b  denote  the Earth's





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-11
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               equatorial and  polar radii,  respectively.  Flattening is
               usually provided  as a  reciprocal, for  example the value
               used herein, is the WGS-72 value of 1/298.26.

               An improved altitude model is

                   h = r - a(1 - f sin í')

               where,  as  before  í',  denotes  the  declination  of the
               object.  The  declination   is  equivalent  to  geocentric
               latitude.

               Both  of  these  expressions are  used  by  the trajectory
               software, but  are principally  used for  estimates in the
               computer graphics.

               A great deal of effort was expended in order to accurately
               model the density profile, so we should expect an accurate
               altitude model from which density is obtained during orbit
               propagation.

               An altitude model that will  achieve any desired degree of
               precision that is also extremely fast; indeed the one used
               in this paper, is an unpublished algorithm conceived by L.
               H. Ivy.   A by-product of  his algorithm  are the trigono-
               metric functions  required to construct  the geocentric to
               topocentric rotation matrix, R sited in previous sections.

               Consider  an  instantaneous  cross-section  of  the  Earth
               defined by  the plane  containing its  polar axis  and the
               mass m.   Define a two-dimensional  coordinate system with
               u-axis formed by  the intersection of  this plane with the
               equatorial  plane, and  v-axis  coincident with  the polar
               axis.

               The cross-section is bounded  by an ellipse whose equation
               is

                   u2   v2
                   ÄÄ +  ÄÄ = 1
                   a2   b2

               Since the eccentricity of the ellipse is given by

                   b2 = a2(1 - e2)

               the its equation may be written





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-12
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                   u2(1 - e2) + v2 = a2(1 - e2)

               Now, the tangent of the geodetic  latitude í of a point on
               the ellipse is the negative reciprocal of the slope of the
               line tangent to the ellipse  at that point.  It follows by
               differentiation that

                               1      v
                   tan í =  ÄÄÄÄÄÄÄÄ ÄÄÄ
                            (1 - e2)  u

               Consequently,

                             a cos í
                   u =  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                        û(1 - e2 sin2 í)

                         a(1 - e2) sin í
                   v =  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                        û(1 - e2 sin2 í)

               These coordinates  are the coordinates  of a  point on the
               ellipse whose geodetic latitude is í.

               On  the  other hand,  the  coordinates  of a  point  at an
               altitude h whose geodetic latitude is í are

                   uh= u + h cos í

                   vh= v + h sin í

               The geocentric latitude í' of this point is given by

                            ÚÄ                                Ä¿
                            ³                   e2             ³
                   tan í' = ³ 1 -  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³ tan í
                            ³      1 + (h/a) û(1 - e2 sin2 í ) ³
                            ÀÄ                                ÄÙ

               One can also find the following expression for altitude

                   h= uh cos í  + vh sin í - aû(1 - e2 sin2 í)

               These two equations form the basis of Ivy's algorithm.

               In essence,  the algorithm  is an  iterative process which
               uses these equations starting  with geocentric latitude as
               an estimate for geodetic latitude.





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-13
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               To complete the algorithm, Ivy  defines a miss distance as
               the  distance between  the  current estimate  for geodetic
               latitude íi and the line normal to the reference ellipsoid
               corresponding to the true geodetic coordinates.

               Let ui, vi be  a point on the  ellipsoid whose latitude is
               íi.  Then the equation of the line normal to the ellipsoid
               at this point, expressed in normal form, is

                  (v - vi)cos íi - (u - ui)sin íi = 0

               The distance from the line to the point u, v is

                   p = ³ (u - ui)sin íi - (v - vi)cos íi ³

               Using (3) and (4) with u = ui, v = vi, we have the
               convergence criterion,


                       ³                          ae2sin íi cos íi ³
                   p = ³ uh sin íi - vh cos íi - ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
                       ³                          û(1 - e2 sin2 í) ³


               The algorithm can now be summarized.


               Algorithm Summary
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               
               1. Input the coordinates of the object: x, y, z

               2. Compute:  û(x2 + y2)

               3. Compute:  tan í' = z/û(x2 + y2)

               4. Replace:  tan í = tan í'

               5. Compute:  cos2 í = 1/(1 + tan2 í)

               6. Compute:  sin2 í = 1 - cos2 í

               7. Compute:  rdcl = û(1 - e2 sin2 í)

               8. Compute:  cos í = ûcos2 í

               9. Compute:  sin í = cos í tan í





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-14
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               10. Compute: h = x cos í + y sin í - a rdcl

               11. Compute: p = ³x sin í - y cos í - ae2sin í cos í/rdcl³

               12. Test: If p is less than some error criterion, end
                   algorithm.  Otherwise,

               13. Compute: D = 1 + (h/a) rdcl

               14. Compute: tan í = tan í '/(1 - e2/D)

               15. Repeat Steps 5 through Step 14.

               Optional computations:

               Compute geocentric and geodetic latitudes:

                   í' = arctan(tan í'),    í = arctan(tan í)

               Compute right ascension:

                   cos à = x/û(x2 + y2),    sin à = y/û(x2 + y2)

                   à = arctan(sin à /cos à)

               It is worthy  to note that  no trigonometric functions are
               actually  computed  with  this  algorithm,  yet  it  makes
               available the  sine and  cosine of  the geodetic latitude.
               Thus  the  rotation matrix,  required  for  computing wind
               velocity components, may readily  be constructed.  This is
               a great savings in  computer resources because this matrix
               must be computed for each integration step.

               The algorithm was tested  with latitudes ranging from -90ø
               to 90ø, and altitude ranging from -300 to 5 X 1012 feet at
               each latitude.  Miss distances of 10-1, 10-4 and 10-5 feet
               were used as  convergence criteria.  In  no case were more
               than three iterations required, and  no more than two were
               required for miss distances of 10-4 feet.





               Trajectory Maker                        Coordinate Systems
               Algorithm Supplement                                  6-15
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


                                       References

               1.  Anon., United States Navel Observatory and Royal
                   Greenwich Observatory, Explanatory Supplement to the
                   American Ephemeris and Nautical Almanac, Her Majesty's
                   Stationary Office, London, 1961.

               2.  O'Conner, J. J., Transformations Applicable to Missile
                   and Satellite Trajectory Computations, RCA
                   International Service Corporation, Technical Report
                   AFETR-TR-75_29, Patrick Air Force Base, Florida, July
                   1975.

               3.  Roy,A. E.,  The Foundations of Astrodynamics, The
                   Macmillan Company, New York, 1965.

               4.  Wertz, J. R., ed., Spacecraft Attitude Determination
                   and Control, D. Reidel Publishing Company, Boston,
                   1985.





               Trajectory Maker                              Bibliography
               Algorithms Supplement                                  7-1
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               7.  BIBLIOGRAPHY

               Abell, G.,   Exploration of  the Universe,  Holt, Reinhart
               and Winston, New York, 1964.

               Anon., Space Flight  Handbooks, Volume I,  NASA SP-33 Part
               1, Office  of Scientific and  Technical Information, NASA,
               Washington D. C., 1963.

               Anon., United States Navel Observatory and Royal Greenwich
               observatory,  Explanatory   Supplement  to   the  American
               Ephemeris and  Nautical Almanac,  Her Majesty's Stationary
               Office, London, 1961.

               Anon., Orbital  Flight Handbook, Office  of Scientific and
               Technical  Information,  National  Aeronautics  and  Space
               Administration, Washington D.C., 1963.

               Bates,  R.,  and  D. Mueller,  J.  White,  Fundamentals of
               Astrodynamics, Dover Publications, Inc., New York, 1971.

               Battin,  B.,   An  Introduction  to  the  Mathematics  and
               Methods   of   Astrodynamics,    American   Institute   of
               Aeronautics and Astronautics, Inc., New York, 1987.

               Deetz,  C.  and  O. Adams,  Elements  of  Map Projections,
               Greenwood Press, New York, 1969.

               Felberg,  F., New  One-Step  Integration Methods  of High-
               -Order  Accuracy  Applied to  Some  Problems  in Celestial
               Mechanics, NASA Technical Report  NASA TR R-248, George C.
               Marshall Space Flight Center, Huntsville, Alabama, October
               1966, pp. 32-33.

               Gaposchkin, F.  M., ed.,  1973 Smithsonian  Standard Earth
               (III),  Smithsonian   Astrophysical  Observatory,  Special
               Report 353, Cambridge, Massachusetts, November 28, 1973.

               Hieb, H.,  Western Test Range  Geodetic Coordinate Manual,
               Part 1, Federal Electric Corporation, Feb. 1980.

               Ivy  L.  and H.  Reynolds,  On the  Sensitivity  of Impact
               Prediction   to  Methods   of   Interpolating  Atmospheric
               Density,  ITT Technical  Note, TN-76-1463,  Vandenberg Air
               Force Base, 1976.

               Maling,  D.,   Coordinate  Systems  and  Map  Projections,
               George Phillip and Son Limited, London, 1973.





               Trajectory Maker                              Bibliography
               Algorithms Supplement                                  7-2
               ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
               


               Mc  Cuskey,  S.,   Introduction  to  Celestial  Mechanics,
               Addison Wesley Publishing Company, Inc., Palo Alto,  1963.

               Menzner,  et.  al.,  Defining  Constants,  Equations,  and
               Abbreviated Tables of the  1975 U. S. Standard Atmosphere,
               National Aeronautics  and Space  Administration, Technical
               Report NASA TR R-459, Washington D. C., May 1976.

               O'Connor, J. J., Transformations Applicable to Missile and
               Satellite   Trajectory  Computations,   RCA  International
               Service  Corporation,   Technical  Report  AFETR-TR-75-29,
               Patrick Air Force Base, Florida, July 1975.

               Pearson,  F.,  Map  Projections: Theory  and Applications,
               CRC Press, Inc., Boca Raton, 1990.

               Ratcliffe, J., A.,  An Introduction to  the Ionosphere and
               Magnetosphere, Cambridge Univ. Press., 1972, p.31.

               Ridpath, I.,  Longman Illustrated  Dictionary of Astronomy
               and Astronautics, York Press, Essex, 1988.

               Roy, R.,  The Foundations of  Astrodynamics, The Macmillan
               Company, New York, 1965.

               Shanks,  B.  F., Solutions  of  Differential  Equations by
               evaluations of Functions, Math. Comp. 20 (1966) pp. 21-38.

               Steers,  D.,   An  Introduction   to  the   Study  of  Map
               Projections,  University  of  London  Press  Ltd., London,
               1962.

               Struick, D., Lectures  on Classical Differential Geometry,
               Addison-Wesley Publishing Company, Inc., Reading, 1961.

               Thompson,  R.  F.,  Spline   Interpolation  on  a  Digital
               Computer,  Goddard Space  Flight Center,  Technical Report
               X-692-70-261, Greenbelt, Md., July 1970.

               Waison, G.  R., Prediction of  Orbital Decay  Rates Due to
               Atmospheric Drag, TRW  Program Technical Report 3150-6020-
               RO-000, January 7, 1966.

               Wertz, J.  R., ed., Spacecraft  Attitude Determination and
               Control, D. Reidel Publishing Company, Boston, 1985.

               Whittaker, F. and G. Watson,  A Course in Modern Analysis,
               Cambridge University Press, Fourth Ed. 1963.