440 MINI-SPOILER MANUAL
                                  VERSION 2.0

     The Kenwood TS-440S is a full-feature amateur-radio transceiver capable of
transmission on  all ham  bands and  reception on  all frequencies  between  30
KiloHertz and  30 MegaHertz.   It is a beautifully designed radio with a single
exception: its  front panel.   All  of the powerful features of the transceiver
must be  accessed through a very small and complex set of bounce-prone switches
and a  miniscule display.   Operating the TS-440S to take full advantage of its
features from  the front  panel  takes  extraordinary  dexterity,  memory,  and
patience.  Such is the problem.

     The solution  to the  problem is as easy as controlling the TS-440S from a
Tandy Model  100 or  102 laptop  computer.   The 440  Mini-Spoiler opens up the
full-featured insides  of the  TS-440S so that they are available for efficient
and convenient  use.   In addition,  it makes  remote  operation  (changing  of
frequencies, modes,  memories, split  operation, and  the like)  possible  over
distances of up to 100 feet by hardwire connection and up to thousands of miles
by modem connection.

     We at the QS02000 Project hope that you find your amateur-radio operations
more pleasant and productive because of the 440 Mini-Spoiler.

     The 440  Mini-Spoiler is  brought to you through shareware marketing.  You
may try  the package  for up  to one  month at  no cost  whatsoever, and if you
during that  time find the package to be of sufficient value to you to continue
its use, we ask you to remit the $16.50 registration cost.

     The QSO2000 Project sponsors amateur-radio software development to provide
operators with  the latest  in excellent operating tools.  You help the project
to develop  more high-quality  software at  a more  rapid pace when you support
software from  the project that you are using.  Your contribution also helps to
ensure that  the 440  Mini-Spoiler will  be maintained and further improved for
your use in the future (see the Release Notes at the end of this document).

440 MINI-SPOILER: A SHAREWARE PACKAGE

     Version  2  of  the  440  Mini-Spoiler  has  cost  hundreds  of  hours  of
development and  testing efforts, but it is yours for one month to try for your
own purposes.   If  you use  it for more than a month, the QSO2000 Project asks
you to share in the development costs by registering your copy of the 440 Mini-
Spoiler for  the nominal  fee of  $16.50.  Your contribution to the maintenance
and further  development of  the software  package does, on average, determines
whether the  package continues to be developed as a useful product for years to
come.

     When you  register the  package, you  may, for  a $2.50 media and handling
charge, receive  the latest  version of  the  440  Mini-Spoiler  on  Model  100
cassette tape, portable-drive 3-1/2 inch disk, or Disk/Video Interface (DVI) 5-
1/4 inch  disk.   This version  includes advanced  features  such  as  Transmit
control and  memory-file save  and  load  provisions,  features  that  are  not
available in the shareware examination copy.

     The advanced  features that  are not included in the shareware examination
copy of  version 2  of the 440 Mini-Spoiler are the file commands (function key
6) and  the transmit  command (function  key 7).   These features are available
only to  owners of  registered copies  who remit  an additional $2.50 media and
handling charger for tape or diskette of their registered copy.

     Shareware marketing  provides a  way for the QSO2000 Project to distribute
high-quality amateur-radio  software at a minimal cost to operators who use the
package.   When you  register your copy, you provide for further development of
the 440 Mini-Spoiler and other amateur-radio packages written by members of the
QSO2000 project.

LOADING THE 440 MINI-SPOILER INTO THE MODEL 100/102

     The 440  Mini-Spoiler is  a Model  100/102 BASIC program in ASCII (text or
.DO) format.   You  may import  it into  your Model  100/102 by connecting your
Model 100/102  and the  computer you  downloaded the  file with together with a
"null-modem" cable  that reverses  the signals on pins 2 and 3 (and maintains a
ground on  pin 7  on both ends) of a standard 25-pin "D" connecter.  Set up the
Model 100/102's  TELCOM program  to download,  and initialize a program in your
other computer to upload.

     The 440 Mini-Spoiler program (4MS200.BAS) is a Model 100/102 BASIC program
in ASCII  format.  You may import it into your Model 100/102 by connecting your
Model 100/102  and the  computer you  downloaded the  file with together with a
"null-modem" cable  that reverses  the signals on pins 2 and 3 (and maintains a
ground on  pin 7  on both ends) of a standard 25-pin "D" connecter.  Set up the
Model 100/102's  TELCOM program  to download, and initialize a program (such as
QMODEM) in  your other computer to upload.  Transfer speeds up to 9600-baud may
be achieved  if you  enable XON/XOFF handshaking in both TELCOM and your MS-DOS
program.  When you upload it to your Model 100/102, you must set up your MS-DOS
program to  cancel line-feeds as it sends the file.  At the TELCOM end, specify
the download-file name as MS4200.DO.

     When you  have the  program downloaded into Model 100/102 memory, you must
load it into Model 100/102 BASIC.

     One of  the most  frustrating features  of Model  100/102 BASIC is that it
will not  run a program which has not been converted into internal, "tokenized"
(slightly compressed)  format.   Therefore the  computer must  convert the  440
Mini-Spoiler to  tokenized  format  before  the  Model  100/102  will  run  it.
Unfortunately, Model  100/102 BASIC  converts the entire file while retaining a
copy of  the ASCII  file in  memory.   This means  that you  must have  a Model
100/102 with  32 kilobytes  of memory  to perform  the conversion.  (Disk Video
Interface--DVI--users have  the memory  requirement relaxed,  because they  can
convert a  text file  stored on  disk into  a tokenized  file in memory without
incurring the huge memory overhead.)

     Once you  have MS4200.DO  in memory,  simply enter  "LOAD MS4200.DO"  from
BASIC and  you're ready to run the program.  You will likely find it convenient
to save  the program as a memory file by entering "SAVE MS4200" while BASIC has
the MS4200.DO  program loaded  in tokenized  format.  The program is saved as a
memory file with the name MS4200.BA, and you may use the KILL command to delete
the MS4200.DO file in order to conserve memory.

     The simplest  solution to  the loading  problem is  to obtain a registered
copy of  the 440  Mini-Spoiler in BASIC (MS4200.BA) format which has been saved
on cassette tape, 3-1/2 inch portable-drive disk, or 5-1/4 inch DVM disk by the
QSO2000 Project.

HARDWARE

     The 440  Mini-Spoiler, written  in optimized BASIC-language code, will run
in a  Model 100/102  with as little as 16 Kilobytes of RAM installed, if you in
accordance with  the cautions  given above can get it loaded in .BA format from
an outside device.

     You must  have your  TS-440S completely  outfitted for the standard RS-232
interface;  Kenwood   left  a   couple  of   empty  integrated-circuit  sockets
unpopulated behind  the front  panel,  and  you  need  an  external  RS-232/TTL
converter.   Both Kenwood  and at  least two  independent suppliers market both
items.

     Kenwood designates  its pair of IC chips the IC-10 and its external RS-232
level converter the IF-232C product models.

     Phil Whitehouse, W1GEE, offers a much more economical alternative in a kit
that includes  both the  TS-440S chip set and an RS-232/TTL level converter for
$50 (assembled  price $60).   Phil's  level  converter  draws  power  from  the
transceiver in  order to  minimize wiring clutter.  You may contact Phil at the
following address.

                         Mr. Phil Whithouse, W1GEE
                         P. O. Box 527
                         Hampden, Maine 04444

     Lawrence Anderson,  KA6FQN, offers  a chip  set and  level converter  in a
small package  in assembled  form for  $59.   The level  converter, cables, and
instructions alone  (without the  internal chip set) is priced at $49.  You may
contact Lawrence at the following address

                         Mr. Lawrence R. Anderson, KA6FQN
                         35615 Avenue D
                         Aucaipa, CA 92399

     The QSO2000  project has  tested both  Phil's and  Larry's assembled level
converters and found found them both to be extremely reliable, easy-to-install,
and attractive.

STARTING UP THE 440 MINI-SPOILER

     When you  have the 440 Mini-Spoiler stored as a .BA file in memory and the
cables connecting  your Model  100/102 to  the RS-232/TTL  converter  and  your
fully-chipped TS-440S,  all you  need to  do is  run  the  program.    It  will
interrogate your  transceiver for frequencies and modes stored in both VFOs and
the 90  non-split memories.   During  your initial installation, you'll have to
wait approximately  30 seconds  amid entertaining beeps from your Model 100/102
for the  memories to  be loaded  and the  data to  be converted  to displayable
format.   After your  initial installation, you have no such wait to be patient
with.  The 440 Mini-Spoiler will assume that you have not altered your memories
manually, and it will load in the previously stored memories from a file called
MEMFLE.DO in Model 100/102 in RAM.

NOTE:     To test  your hardware  link if  you find  that the  440 Mini-Spoiler
          fails to  work for  you, break  (ctl-pause) out of the spoiler.  Exit
          BASIC and  enter TELCOM.    Choose  communication  parameters  (STAT)
          78N2E,  giving   you  the   4800-baud,  8-bit-character,   2-stop-bit
          convention that the TS-440S requires.  Enter TERM, and type "IF;" (no
          ENTER,  please:   it  will   only  interfere,   because  the  TS-440S
          understands the  semicolon to  be an  enter signal).  If your TS-440S
          doesn't immediately  respond to  the Model  100/102  screen  with  38
          characters beginning with "IF", continuing through many numbers and a
          few spaces,  and ending  with ";",  you do have some misconnection or
          malfunction in  your hardware.   If  you get the right response, your
          communication link  is working  properly and you've may have gotten a
          corrupted copy  of the  440 Mini-Spoiler.   Obtain  another copy post
          haste.

DATA DISPLAY AND DATA ENTRY

     The 440  Mini-Spoiler is  designed to  provide totally separate data-entry
and data-display  tasks.   You may  use either  the TS-440S  front panel or the
Model 100/102  keyboard for  entry at  any time,  and the resulting changes are
reflected on both the transceiver display and the 440 Mini-Spoiler screen.

     At least  some TS-440S  transceivers include  front-panel keypads that are
extremely prone  to contact bounce.  An annoying result of erroneous data entry
is that  the transceiver  receives multiple  number entries  from its own front
panel when  you press  a button  only once.   A more serious result is that the
transceiver can  send out  status-update packets  at such  a rapid pace that it
overloads the  440 Mini-Spoiler.   Such  a jam  occurs most often with entry of
memory frequency data on the transceiver's numeric keypad.  If your transceiver
has such  switch-bounce difficulty,  you can  avoid the problem by entering new
VFO and  memory data  through the  440 Mini-Spoiler  keyboard (it's  much  more
convenient and less troublesome to enter it that way otherwise too).

THE 440 MINI-SPOILER SCREENS

     The 440  Mini-Spoiler initializes  your Model  100/102 while it displays a
title screen; it reads data from your TS-440S.  It also dallies a little bit to
thoroughly display  the copyright notice to remind you that much work and other
resources have gone into development of the program.

     After the  title and  copyright screen  disappears, the  440  Mini-Spoiler
operating display  appears.   The display  contains three areas: (1) an area to
the left  of the  screen for  display of  the VFOs  and the  currently selected
memory, (2)  an area  to the right of the screen for displaying any five of the
90 simplex  memories, and (3) a line across the bottom of the screen to display
command prompts.  Figure 1 shows a typical operating display upon startup.

                 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                 ºÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿º
                 º³FQ 28.718.87 USB VA³³00  3.933.00 LSB U³º
                 ºÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³01 21.023.00 CW  U³º
                 ºÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³02 14.300.00 USB U³º
                 º³    7.213.02 LSB VB³³03 28.454.00 USB U³º
                 º³   14.300.00 USB 02³³04  7.085.00 FSK U³º
                 ºÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙº
                 ºSlct Freq Mode Copy Wndw File TRtg  Quit º
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                  [1]  [2]  [3]  [4]  [5]  [6]  [7]   [8]

                     Figure 1.- Typical operating display

VFO and Current Memory Area

     Your current  operating frequency (or frequencies) and mode (or modes) are
shown at  the top of the VFO and Current Memory Area.  The top box displays the
currently selected  transmission and  reception source(s).   From figure 1, the
source for both reception and transmission (indicated by "FQ" for frequency) is
VFO A at a frequency of 27.71887 MegaHertz in upper-sideband mode.

     For single-source,  non-split operation,  the top box contains information
about VFO A, VFO B, or the currently selected memory.  For example, if memory 2
is selected as the source, the display changes to that shown in figure 2.

                 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                 ºÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿º
                 º³FQ 14.300.00 USB 02³³00  3.933.00 LSB U³º
                 ºÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³01 21.023.00 CW  U³º
                 ºÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³02 14.300.00 USB U³º
                 º³   28.718.87 USB VA³³03 28.454.00 USB U³º
                 º³    7.213.02 LSB VB³³04  7.085.00 FSK U³º
                 ºÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙº
                 ºSlct Freq Mode Copy Wndw File TRtg  Quit º
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                  [1]  [2]  [3]  [4]  [5]  [6]  [7]   [8]

                  Figure 2.- Typical memory-selected display

     The 440 Mini-Spoiler supports split-VFO operation, but it does not support
split-memory operation  (memories 90  through 99 only).  During a period when a
memory is  selected, the  top box will contain a single line with memory number
appended to  indicate the  frequency (FQ) and mode of the memory that currently
controls the transceiver.

     When a  VFO is  selected, it will contain one or two lines to respectively
indicate the  VFO controlling  the transmit-and-receive frequencies or both the
VFO controlling  the receive  frequency and  the VFO  controlling the  transmit
frequency.

     When you  have set  up the  transmitter for split-frequency operation from
the VFOs,  the receive VFO information is always shown on the top line of the a
two-line box  (with an  "RX" prefix).  The transmit VFO is shown on the bottom,
with a  "TX" prefix.   One  of the  advantages of using the 440 Mini-Spoiler is
that you  always be  able to  see your  transmit frequency  before you  press a
microphone button  or tap  a key.   Figure 3 shows a typical display in the VFO
and Current  Memory Area  when the  TS-440S  is  set  for  splif-frequency  VFO
operation.

                 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                 ºÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿º
                 º³RX  7.075.00 LSB VA³³00  3.933.00 LSB U³º
                 º³TX  7.213.00 LSB VB³³01 21.023.00 CW  U³º
                 ºÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³02 14.300.00 USB U³º
                 ºÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³03 28.454.00 USB U³º
                 º³   14.300.00 USB 02³³04  7.085.00 FSK U³º
                 ºÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙº
                 ºSlct Freq Mode Copy Wndw File TRtg Quit  º
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                  [1]  [2]  [3]  [4]  [5]  [6]  [7]  [8]

                         Figure 3.- Split-VFO display

     The frequencies  shown in the VFO and Current Memory Area are the absolute
frequencies of  the VFOs  and the  selected memory.   The  frequencies  do  not
account for  any "increments"  that you have added to them from the transceiver
front panel with the RIT or XIT controls.

Five-Memory Window

     Upon initialization,  the Five-Memory  Window displays the frequencies and
modes stored in memories 0 through 4.  One of the memories (initially memory 0)
is highlighted  to preset easy access to it by keyboard for transceiver control
or copying.   You can easily scroll through the entire 90 non-split memories or
select by keyboard any five-memory segment of them for display.

The Command Line

     The eight  abbreviated commands  shown above  the function-key labels lead
you through  prompts to enable you to control your TS-440S transceiver and your
440 Mini-Spoiler display.  The commands and the prompts that they further offer
you are described in detail below.

440 MINI-SPOILER COMMANDS

Brief Definitions

   Source (F1)............................Select xmit and rcve vfo or memory
   Frequency (F2).........................Set frequency in any vfo or memory
   Mode (F3).........................Set any VFO or memory to LSB, USB, etc.
   Copy (F4)..............................Copy freq and mode between sources
   Window (F5).........................Set position of memory viewing window
   Files (F6)..............Load or save a Model 100/102 file of 440 memories
   TR toggle (F7)...............Toggle the XCVR between transmit and receive
   Quit (F8)...................................Return computer to MENU level

     The commands  are entered through function keys F1 through F8 just beneath
the Model 100/102 LCD display.

     All commands  other than  the Quit  Command provide  you with  prompts  to
direct your  entries.  These prompts include a prompt to return you to the main
level of  commands: a Quit Option.  Entering the first letter of an option name
evokes the option.

Memory-Window Hot Keys

     Pressing the  Down-Arrow key moves the highlight in the five-memory window
down one  memory in  the memory  to the  next-highest memory  number.   If  the
highlight is  on the  fifth memory,  the memories will scroll so that the next-
highest memory will appear highlighted at the bottom of the window.

     Similarly, pressing the Up-Arrow key moves the highlight up in the window,
and if  the highlight  is at  the top  of the  window the  key will  cause  the
memories to  scroll so  that the  next lower-numbered memory will appear at the
top of the window.

     If you  hold down the Shift key while you press the Up- or Down-Arrow key,
memories in the window scroll up or down by five.  The highlight remains in the
same position it was in before you press the key.

     You may use function key 5 to select the memories appearing in the window,
as described below.

Select (Slct) Command (F1)

     The Select  Command offers  you transceiver  control by either VFO, by the
memory currently  selected by  the  TS-440S,  by  the  memory  which  you  have
highlighted in the five-memory window, or by a memory with the number you enter
by keyboard.   The  split option  is also  available to  toggle  dual-frequency
transmit and receive by VFOs.

     The prompts  for the Source Command, which temporarily replace the Command
Line, are shown in figure 4.

                 ºA)B)VFO M)em W)in ## S)plit Q)uit ? ²    º
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                  [1]  [2]  [3]  [4]  [5]  [6]  [7]  [8]

                       Figure 4.- Source Command prompts

     Entering A,  B, or  M immediately  puts VFO  A, VFO  B, or  the  currently
selected memory  in control of the TS-440S.  Entering W puts the memory that is
highlighted in  the Five-Memory Window in control, simultaneously making it the
currently selected  memory.  Entering a number between 0 and 89 puts the memory
with that  number in  control and  makes it  the current memory.  The 440 Mini-
Spoiler will not control split memories 90 through 99.

     Entering S  toggles VFO split-frequency operation on and off.  This option
is effective  whether the transceiver is currently controlled by a memory or by
VFO.   With a  memory in  control, for example, you can toggle split on so that
when you  change to  VFO operation  the  transceiver  will  be  set  for  split
transmission and reception.

     Pressing Q  cancels the Source Command and returns the Command Line to the
bottom of  the display.  You may also cancel the command by pressing the Return
key.

Frequency (FREQ) Command (F2)

     The Frequency Command permits you to change the frequency of any source in
your transceiver (except the duplex sources, memories 90 through 99).

     The first  prompt that  replaces the  Command  Line  after  the  Frequency
Command is  entered asks you whether you to enter the source you want to change
the frequency of.  This prompt is shown in figure 5.

                 ºA)B)VFO M)em W)in ## Q)uit ? ²           º
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                  [1]  [2]  [3]  [4]  [5]  [6]  [7]  [8]

                   Figure 5.- Frequency Command first prompt

     With entering a single character, you indicate that you want to change the
frequency of VFO A, VFO B, the currently selected memory, or the memory that is
highlighted in  the Five-Memory  Window.  You may enter a number ranging from 0
to 89  to change the frequency of any memory, regardless of whether it is shown
on the  screen.   You may  enter Q  to terminate  the Frequency Command without
changing the frequency of any VFO or memory.

     The second  prompt that  replaces the  Command Line  after  the  Frequency
Command is  entered is  simply "Frequency  value or Q)uit?"; you must enter the
frequency that  you wish  to assign to your selected VFO or memory or enter the
single-character Q option (or Return) to terminate the command.

     Within useful  limits, you  may  enter  frequencies  in  KiloHertz  or  in
MegaHertz.   For frequencies  up to 9,999,999 Hertz, you have a choice of entry
methods.   You may enter them in either MegaHertz, with a decimal point, or you
may enter  them in  KiloHertz, suffixed  by a  "K" or "k" to tell the 440 Mini-
Spoiler the  difference.   An entry  of "7.12345"  is identical  to an entry of
"712345K" and "712345k."

     If you  enter a  frequency not  formatted in  these two  fashions, the 440
Mini-Spoiler will  beep and  query you again for the frequency.  If you enter a
frequency that  is outside  the range of the TS-440S transceiver, the 440 Mini-
Spoiler will also beep and query you again.

Mode (MODE) Command (F3)

     The Mode Command permits you to change the mode (LSB, USB, CW, AM, FM, and
RTTY) of  each transmission  source.  The first of two prompts that the command
brings up is shown in figure 6.

                 ºA)B)VFO M)em W)in ## Q)uit ? ²           º
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                  [1]  [2]  [3]  [4]  [5]  [6]  [7]  [8]

                     Figure 6.- Mode Command first prompt

     With entering a single character, you indicate that you want to change the
mode of  VFO A,  VFO B,  the currently  selected memory,  or the memory that is
highlighted in  the Five-Memory  Window.  You may enter a number ranging from 0
to 89  to change  the mode  of any memory, regardless of whether it is shown on
the screen.  You may enter Q to terminate the Mode Command without changing the
mode of any VFO or memory.

     The second prompt that replaces the Command Line after the Mode Command is
entered is shown in Figure 7.

                 ºL)SB U)SB C)W A)M F)M R)TTY Q)uit ? ²    º
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                  [1]  [2]  [3]  [4]  [5]  [6]  [7]  [8]

                     Figure 7.- Mode Command second prompt

     Your response to the prompt selects the mode of the VFO or memory you have
chosen or (with W for Quit) terminates the command without changing mode.

Copy (COPY) Command (F4)

     The Copy  Command permits  you to  copy the  contents of any VFO or memory
into another  VFO or  memory.   You are  first prompted for the source that you
want to copy from, and then you are prompted for the destination of the copy of
the frequency  and mode  information.  The prompt for source is shown in figure
8.

                 ºFrom: A)B)VFO M)em W)in ## Q)uit ? ²     º
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                  [1]  [2]  [3]  [4]  [5]  [6]  [7]  [8]

                     Figure 8.- Copy Command source prompt

     The prompt for destination differs only slightly, as shown in figure 9.

                 ºTo: A)B)VFO M)em W)in ## Q)uit ? ²       º
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                  [1]  [2]  [3]  [4]  [5]  [6]  [7]  [8]

                  Figure 8.- Copy Command destination prompt

     You may  terminate the  Copy Command either at the time it prompts you for
the source or at the time it prompts you for the destination.

Window (WNDW) Command (F5)

     The Window  Command  lets  you  rapidly  change  the  memories  which  are
displayed in  the five-memory  window.   You are prompted for the number of the
memory that  will be  the lowest  of the  five to appear in the window.  If you
choose memory  38, for  example, you  will cause  memories 38  through 42 to be
displayed in the five-memory window.

     The Up  and Down Arrow keys work in conjunction with the Window command to
let you  see and  select any  memory from 0 to 89.  Used without the shift key,
the arrow  keys move the inverse-video selection bar up and down in the window.
Used when  the shift key is pressed, the arrows cause the window to move up and
down on the list of memories in increments of 5, while the highlight remains in
the same  position relative  to the  top of  the window.  Pressing [SHIFT-DOWN]
when the  window is  displaying memories  5 through 9 causes the window to move
further down  the list to display memories 10 through 14.  In this instance, if
memory 5 is highlighted before you hold down Shift and press Down Arrow, memory
10 will be highlighted after your scrolling down the memories.

File (FILE) Command (F6)

     The file  command allows  you to  S)ave  current  transceiver  memories  0
through 89  to a  Model 100/102  file, and  it allows you to L)oad your TS-440S
with memories previously saved to a file.

NOTE:     The memory-file  command options  are functional  only in  registered
          copies of  the 440 Mini-Spoiler obtained on tape or diskette from the
          QSO2000 Project.   In  unregistered copies, pressing F6 will cause an
          exciting small  beep to  sound and  the command menu to return to the
          last line of the screen.

     The file may be a memory file (file name only), a cassette-tape file (file
name preceded  by CAS  as in  CAS:MEMFLE), or a disk/vidio (DVI) interface file
(with a 0 or 1 and a colon preceding a file name).

     The memory  file named MEMFLE (MEMFLE.DO) will always be loaded by the 440
Mini-Spoiler during  initialization.   This file  contains the values stored in
TS-440S memories  the last  time the  440 Mini-Spoiler  has been run and exited
with the F8 key.  Anytime the 440 Mini-Spoiler is run, the F6 key may evoke the
S)ave option  in order  to save  a file to memory, tape, or DVI disk, and a new
file of memories can be loaded with the F6 key via the L)oad option.

     The non-split  memories in  the TS-440S will be set to the frequencies and
modes set  to the  values specified  by whatever  file you  load from memory or
diskette.   They will  NOT remain as were when you initialized the program with
MEMFLE, and  they will not reflect any changes you have made since initializing
the program.

NOTE:     When you  exit the  440 Mini-Spoiler  with the  F8 key,  the  current
          memory file  (the previously  loaded file  altered by  any changes in
          frequency and mode and any memory copy operations) is saved as MEMFLE
          (MEMFLE.DO) in  order to  keep transceiver  memories and  file-stored
          memories identical.   If  you have  loaded another  memory file since
          initializing the  program, that file and any changes you have made to
          it will  be reflected  in both  your TS-440S  memories and  the  file
          MEMFLE.  If you have doubt about whether the transceiver memories are
          identical to  the file-stored  memories, press F6 and enter the S)ave
          option with  a file  name of  MEMFLE.DO to  refresh both the memories
          that  the  Spoiler  currently  recognizes  and  the  stored  file  of
          memories.

     The file  MEMFLE (MEMFLE.DO) and all other memory files that you save with
the F6 file command and S)ave option are files that you can edit with the Model
100 Text  editor.  You may alter the frequencies and modes of the memories with
TEXT, providing  that you  carefully (1)  maintain memory  sequence numbers and
frequency and  mode fields within each line and (2) use the L)oad option of the
F6 command  to enter  new frequencies  and modes  into the  TS-440S  after  you
initialize the program.

CAUTION:  If you  exit the  440 Mini-Spoiler  through any  means other  than by
          pressing F8,  the current  state of memories in your transceiver will
          not be  saved to  MEMFLE.   You then  have two options to "reconcile"
          transceiver memories  with computer  memories.   F6  with  the  S)ave
          option to the file name MEMFLE will reconcile computer-saved memories
          to those stored in the transceiver, and F6 with the L)oad option will
          reconcile transceiver memories with those stored in Model 100 RAM.

Transmit/Receive Toggle (TRtg) Command (F7)

     You can  toggle between  receive and transmit operation with the TR toggle
command.   When the transceiver is in transmit mode, a transmit sign appears to
the right  of the  current source  designation (if  non-split)  or  beside  the
receive source (if split VFO operations is in effect).

NOTE:     The transmit  command is  functional only in registered copies of the
          440 Mini-Spoiler  obtained on  tape  or  diskette  from  the  QSO2000
          Project.   In unregistered copies, pressing F7 will cause an exciting
          small beep  to sound  and the command menu to return to the last line
          of the screen.

Quit (QUIT) Command

     The Quit  Command does  exactly what  it says:  it causes  control of your
Model 100/102  to return  to the  Menu.  Whenever you want to run the 440 Mini-
Spoiler again,  simply place the inverse-video cursor over MS4200.BA again, and
press the ENTER key.

RELEASE NOTES

     Version 2.0  of the 440 Mini-Spoiler is released November 15, 1990 with no
currently known bugs.  Maintenance releases which correct inevitably discovered
bugs (as they are discovered) will be designated by incremented version numbers
(2.01, 2.02, and so on).

     Version 2.00 supersedes version 1.01, released March, 1990.

OTHER QSO2000 PROJECT SOFTWARE PACKAGES

     Please type  or print  the file  QSO2000.TXT on  this diskette  or in this
archive.

REGISTRATION AND LICENSING INFORMATION

     If you  find the 440 Mini-Spoiler to be of sufficient value for you during
your one-month  trial period,  please remit  $16.50 to the QS02000 project.  If
you would  like a  copy of  the 440  Mini-Spoiler  with  enhanced  features  in
tokenized format  to be mailed to you on cassette tape, 3-1/2 inch diskette for
the Tandy  Portable Disk Drive, or 5-1/4 inch diskette for the Tandy Disk/Video
Interface, please  include an  additional $2.50  to cover  copying and  mailing
charges (total $19.00).

     Please view  the file  RGSTR4MS for  detailed licensing  information and a
printable registration form.

                            Bill Brewer, K5KNC, Coordinator
                            QSO2000 Project
                            5518 12 Street
                            Lubbock, TX 79416