AA4RE BBS and the G8BPQ Switch.

******************************************************************************
This section is for BPQ switchs V3.23 to 3.59
******************************************************************************

From version 3.23, the switch supports the AA4RE BBS.  This has been
done by extending the PK232 host mode support, originally written to
support the G8UFQ BBS.  The system allows the first Virtual TNC port to
support up to 8 users.  The configuration I used is detailed below:

In BPQCFG.TXT:

  TYPE=PK232/AA4RE
  APPLFLAGS=6

In PARMS.BB, the recommended port settings are below

  port_type       = G8BPQ_NODE
  com             = 2                ; use the first number in TNCPORTLIST
  speed           = 4800             ; not actually used
  max_connect     = 8                ; Up to 8
  max_channel     = 9
  max_pending     = 1
  broadcast_path  = MAIL             ; is ignored - set in config.txt file

******************************************************************************
This section is for BPQ switchs V4.03 and higher
******************************************************************************

No ports are needed in the BPQCFG.TXT.  I leave one token port
for testing:


    TNCPORT
       COM=4
    ENDPORT


In PARMS.BB, the recommended port settings are below

  port_type       = BPQ-HOST-x       ; The x is the port number on the
                                     ; BPQ switch.  Each port on the BPQ switch
                                     ; can be defined if you want to control
                                     ; monitor colors or broadcast paths.

      *** AND/OR ***

  port_type       = BPQ-HOST         ; This is a generic port type for ALL
                                     ; the BPQ ports.


  com             = 127              ; Same number as HOSTINTERRUPT in the
                                     ; BPQCFG.TXT file
  speed           = 4800             ; not actually used
  max_connect     = 8                ; Up to 30??  Try 7
  max_channel     = 9                ; Up to 30 or so.. Try 9
  max_pending     = 4                ; Number of packets set to switch before
                                     ;       BBS waits
  broadcast_path  = MAIL             ;

Note:  The only commands you can issue to the BPQ-HOST port are:
   (esc)C -- Connect
   (esc)D -- Disconnect
   (esc)M -- Monitor ON
   (esc)N -- Monitor OFF

You can define both BPQ-PORT-x and BPQ-PORT types in the same PARMS.BB
if you need only partial control.  For example, you have 3 ports but only
want control over port 2.

  port_type       = BPQ-HOST-2       ; This would be port 2

  port_type       = BPQ-HOST         ; This would be all other ports

Special notes:

  1) All connects will appear on the first port defined.  This
     port will control MAXPAC, language, remote sysop, etc.

  2) The port letter used will NOT determine which radio port will
     be used.  You must use the proper switch sequence to get out
     the proper port.  Thus a terminal task (T A5) will not ensure
     that your packets will leave the radio port that is associated
     with "A".

  3) Each port will go thru its own forwarding cycle.  If you have
     two ports, A and B, each will go thru their forwarding cycle
     as per the port parameters.


******************************************************************************
This section is for all BPQ switches
******************************************************************************

In PATHS.BB

PATH GB7DAD A GB7DAD FORCE
T 0000 2359
C SWITCH                                ; note initial C SWITCH
SC LRG7
R* to *
SC G4NAD-1
R* to *

All virtual TNCs continue to run as normal.  If you are running under
Desqview, you can still run PAC2 (or even MBL/RLI!) in other windows.
However, BB needs a LOT of store - you need to use all the tricks
described in the DV manual to get a big enough window to run it
effectively.