The following programs are provided.

BPQCODE.EXE

The TSR version of the packet switch. It provides a NET/ROM compatible
packet switch, and an interface to application-level software (such as a BBS).


SWITCH.EXE

This is a foreground version of BPQCODE. It is intended to run only as
a packet switch, and not to support an application system (eg BBS). A
simple terminal program (equivalent to PAC4) is built in, as is the
SYSOP handler from the Data Engine version of the switch. The diffences
from BPQCODE are listed below:

	BPQCFG.TXT

	This can be the same as for the normal version. The code will assume
	NODE=1 and BBS=0, whatever is entered. 


	Terminal support.

	See PAC4 below for details. Ctrl/Y shuts down the whole switch.


	SYSOP Commands.

	The SYSOP feature is similar to SYSOPH, but the password protection
	works rather differently. To enter SYSOP mode, enter PASSWORD. If 
	you are using the console, the switch will respond Ok, and enter 
	SYSOP mode. If you are accessing the system remotely, it will repond 
	with 5 random numbers. You must reenter PASSWORD, this time followed 
	by the corresponding characters from the password string contained 
	in the file PASSWORD.BPQ. If these are correct the switch responds 
	OK, otherwise it ignores the message.

	So, if the password string is ABCDEFGHIJKLM the following is a
	typical sequence:

		PASSWORD
		BPQ:G8BPQ} 04 02 05 06 03
		PASSWORD DBEFC
		BPQ:GBBPQ} Ok

	Note that the password is converted to upper case before testing, so 
	PASSWORD.BPQ should contain upper case letters or digits. It should
	not contain spaces or other special characters.

	There are a number of extra SYSOP commands. These were added primarily
	for the Data Engine version, where experimenting with parameters is 
	rather more difficult, but I've left them in this version as well.
	
		Command		Corresponding BPQCFG parameter

		OBSINIT			OBSINIT
		OBSMIN			OBSMIN
		NODESINT		NODESINTERVAL
		L3TTL			L3TIMETOLIVE 
		L4RETRIES		L4RETRIES
		L4TIMEOUT		L4TIMEOUT
		T3			T3
		IDLETIME		IDLETIME
		LINKEDFLAG		ENABLE_LINKED
		IDINTERVAL		IDINTERVAL
		MINQUAL			MINQUAL
		FULLCTEXT		FULL_CTEXT
		HIDENODES		HIDENODES
		L4DELAY			L4DELAY
		L4WINDOW		L4WINDOW
		BTINTERVAL		BTINTERVAL

	There is also one commend which isnt in the DE version - SAVENODES.




BPQCFG.EXE

This program converts the configuration file BPQCFG.TXT to a binary file
(BPQCFG.BIN) for use by the switch software. It must be run after any
change to BPQCFG.TXT.



BPQNODES.COM


This program dump the ROUTES and NODES tables to a file (BPQNODES). This
file is then used to initialise the above tables when the switch is 
reloaded. It should be run before reloading the switch, and if possible
at regular intervals, so that if the system crashes, it comes back with
a reasonably up-to-date view of the network. Many BBS systems allow you
to run a program as part of the forwarding cycle, or at specified times.


It is possible to edit the BPQNODES file. This provides a way of defining
Route Qualities, etc. without changing BPQCFG.TXT, or using SYSOPH.

The file format is: ( {} indicates optional entries - don't include the{})

ROUTE ADD CALL P QUAL {!} {VIA DIGI1 {DIGI2}}

where P is the port, QUAL the Quality, and the optional ! indicates a locked
route. Up to 2 DIGIS may be specified. 

NODE ADD ALIAS:CALL CALL-1 P QUAL {!} {CALL-2 P QUAL {!} } {CALL-3 ....}

where CALL-1, CALL-2, CALL-3 are up to 3 alternate routs, which must be
defined (by ROUTES config entries or ROUTE ADD) before being used.

Although locked nodes are allowed, I strongly recommend  that they are used
only in exceptional circumstances (eg when using a digi'ed route). Note also
that a locked route to a node will be removed if the system finds 3 higher
quality routes to it.


Lines beginning with ; are treated as comments, and fields should be separated
by one (and only one) space.




BPQDUMP.COM


BPQDUMP.COM  is a simple program to dump my code to a file to aid diagnosis 
of fault conditions. It creates a file in the current directory called
BPQDUMP (about 98k).

If run without a parameter, it dumps immediately.

If a param is specified, it will loop until the free buffer count drops below
20 ( the point when the code starts to shut down), then dumps and exits. Note
this mode must only be run in a desqview window.


eg

BPQDUMP		- dumps now

BPQDUMP X	- dumps when buffers < 21



PAC2.COM


PAC2 is a small, simple terminal program, primarily for use with my switch,
but it also works with a normal TNC + COMBIOS. It has one paramter (port
number), so enter PAC2 N, where N is the (virtual) COMBIOS port you want to 
access. The program provides a buffered input line, which allows use of
the editing keys ins, del, cul, cur, etc, It allows logging to disk (CTRL/L
toggles this function on and off), and maintains a simple 'Response Time
Monitor' function - useful for seeing how badly the network is performing!

To exit from PAC2, enter CTRL/Y


PAC4.EXE


PAC4 is a simple terminal program, which uses the BPQ Host Mode to talk
to the switch. The program provides a buffered input line, which allows use 
of the editing keys ins, del, cul, cur, etc. It allows logging to disk
(CTRL/L toggles this function on and off), and maintains a simple 'Response
Time Monitor' function. A scroll-back buffer is also provided - use PageUp
and PageDown to scroll.


The program has one required paramter (port number), and a second optional
one (M for mono mode). So possible command lines are:

	PAC4 63			; to use stream 63

	PAC4 1 M		; to use stream 1, if you have a mono monitor.

Connection is made to the switch when a message is input. The ESC key 
disconnects you from the switch.

Monitoring is toggled on/off using F1. F2 toggles MCOM mode (monitoring of
control frames as well as info frames). F3 allows you to set MMASK. Press
F3, then key up to 4 hex digits, terminated with a newline. Each bit of MMASK
enables the monitoring of the corresponding radio port. Bit 0 enables port
1, bit 15 port 16. Any combination of bits may be set. The current monitor
settings are displayed on the status line.


To exit from PAC4, enter CTRL/Y


SYSOPH.COM



This program allows the manipulation of certain parameters within the switch. 
The program may be run as a normal DOS program, either in a Desqview window
or standalone, or it may run as a TSR. The TSR mode would normally be used
if you were running a BBS system that doesnt need DesqView (eg AA4RE). In
TSR mode, commands cannot be entered locally, and the SAVENODES command
is disabled. It either mode, it may be accessed over the network. 

The system has now been modifed to use BPQHOST mode rather than a virtual
TNC2 port. Program SYSOP.COM is withdrawn - the current version is SYSOPH.COM


Installation.

1. Add a suitible application name as the third APPLICATIONS Param, ie

     APPLICATIONS=BBS,,*SYSOP

   I suggest you use a name starting with a '*', as this will 'hide' the
   command from the Valid Commands display.

2® Creatå á file¬ PASSWORD.BPQ, containing a string of up to 80 characters.

3. Run program SYSOPH, with a single parameter of the stream to be used,
   either on its own, or in a DesqView window. If a second parameter of
   'RESIDENT' is specified, the program will become a TSR routine.



Commands may now be entered directly on the PC, (unless in TSR mode) or
remotely by connecting to the Node, and entering the APPL name (eg *SYSOP).
When accessed remotely, a password prompt is sent, containing 5 random numbers
in the range 1 to the length of the PASSWORD.BPQ string. The first command
entered must be the corresponding five letters from the password string, 
or the user will be disconnected.

Available Commands.

The following commands are supported:

BYE - Disconnect remote user (even if entered from console)

TXDELAY
MAXFRAME
FRACK
RESPTIME
PACLEN
RETRIES
QUALITY
PERSIST
TXTAIL
XMITOFF
DIGIFLAG
DIGIPORT
USERS
VALIDCALL
L3ONLY
BBSALIAS
SOFTDCD

   The above display or update the parameter for a specified port,

   eg   PACLEN 1 100
        PERSIST 2 50

   If the third parameter is omitted, the current value is displayed.

   Setting XMITOFF will supress all TX activity on a port (including CWID,
   beacons, etc). I put it in so I could monitor the satellites without
   causing QRM, but it could be used as a way of shutting down a port in an
   emergency.

   Setting BBSALIAS will cause connects to the port call or port alias to go
   to the BBS rather than the node.

   It is not currently possible to update VALIDCALLS, but you can display
   the current setting.


   *** Warning ***  

   At the moment the FRACK value is in 1/3sec units, and the TXDELAY is in
   50ms units for HDLC cards, and 10ms units for KISS TNCs. I'll be sorting
   this out when I get the time to rationalize the timer code, but in the 
   meantime, I suggest you make a note of the current values before you
   start fiddling. 

   Also KISS users should note that the params are only sent to the TNC every
   5 mins or so, so the updated values may not take effect for a while.


ROUTES

   To display ROUTES table, enter ROUTES

   To display entry for a particular neighbour, enter ROUTES Call Port,

   eg   ROUTES G8BPQ-2 2

   To update an entry, enter ROUTES Call Port Params

   eg   ROUTES G8BPQ-2 2 100	- Set quality to 100
        ROUTES G8BPQ-2 2 !         - Toggle 'Locked Route' flag
        ROUTES G8BPQ-2 2 100 !     - Set quality and toggle 'locked' flag

   To clear the stats counters on a route, enter:

       ROUTES G8BPQ-2 2 Z


SAVENODES (Not available in TSR mode).

   Writes the ROUTES and NODES tables to the BPQNODES file.

   The SAVENODES function may also be invoked directly from the DOS command
   line - this function replaces BPQNODES.COM

       ie.  SYSOP SAVENODES



John Wiseman, G8BPQ
31.8.92