l---+--LT1----+-T--2----T----3--T-+----4T---+---T5----+-T--6----T----7--R-+----r





                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        |          ELECTRC8
                        |          --------
                        |          Copyright 1991, by Robert J. La Capra 
                        |          All Rights Reserved 
                        |
                        |          Shareware Distribution Version
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        |          Robert J. La Capra
                        |          50 Hillside Terrace
                        |          Andover, NJ 07821
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        | 
                        |
                        |
                        |
                        |
                        |
                        |










                         -- Table Of Contents --



       Shareware ................................................ I 

       Disclaimer ............................................... II

       Included Files ........................................... II
       
       Introduction ............................................. 1

       MENUS - Main And Function ................................ 2
       
       DATA INPUT ............................................... 2

       BOX FILL & SIZING CALCULATIONS
            Device Box Fill Calculations ........................ 3
            Junction, Pull Box Calculations:
                 Straight Pull .................................. 4
                 Angle or U Pull ................................ 4
       CONDUIT SELECTOR ......................................... 5
       COST TO OPERATE .......................................... 5
       LIGHTING CALCULATIONS (Zonal Cavity Method) .............. 6
       MOTOR CALCULATIONS
            Branch Conductor Sizing ............................. 9
            Fuse or Breaker Sizing .............................. 9
            Overload Protection Sizing .......................... 9
       PIPE & WIRE SELECTOR AND COSTCOMP ........................ 10
       REFERENCE TABLES
            Equipment Grounding Conductor ....................... 11
            Grounding Electrode Conductor ....................... 11
            Killowatt - Ampere Table ............................ 11
            Underground Cover Requirements ...................... 11
            Metal Device Box Table .............................. 11
            Standard Pull & Junction Boxes ...................... 11
            Standard Fuse & Breaker Table ....................... 11
            Transformer Kva - Ampere Table ...................... 11
       SETUP
            Color Defaults ...................................... 11
       VOLTAGE DROP CALCULATOR .................................. 12
       
       Registration ............................................. 13
       Registration form ........................................ 14







                             =  Shareware  =

       Shareware is a term used to describe a software distribution or 
       marketing method. Under the shareware concept, software may be 
       freely copied and passed along to others, or distributed through 
       bulletin board systems, shareware distributors, etc...

       As a recipient of a shareware program, you may use the software 
       for a short trial period to determine if it meets your needs. If 
       it does, you must pay the registration fee to the author of the 
       program. By paying the fee, you are granted the right to retain 
       the software for your own use. If the software is not suitable, 
       then you are not obligated to pay the fee, but you must not 
       continue to use the program. 

       The shareware system provides substantial benefits to you:

       1. You get to try out the software before you buy it.
       2. Shareware is much less expensive than comparable commercial 
          packages. You don't pay for marketing and packaging.
       3. Many programs have been developed by expert programmers who 
          would never consider marketing their products commercially.
          All they ask in return is a small fee to compensate them for
          the considerable time and effort they have invested in the 
          development, testing and support of their products. 
       4. Shareware authors are much more responsive to the users' 
          requests for bug fixes, added features, special modifications, 
          etc... 
       
       
       The system is based entirely on the honor system, and usually 
       works well. Most people are honest and wouldn't violate the trust 
       placed in them by the author of the software. 

       Shareware is not free software. The author counts on your 
       integrity. If you intend to continue to use the program, please 
       register using the form at the end of this manual, or the form 
       included in the file "ELECTRC8.REG". Registration entitles you to 
       an expanded, 'Registered-User' version of this program. See the 
       end of this manual for details. 

       
       
       
       
       
       
       
       
       
       
       
       
       
       
       
       
                                   I




                        *  DISCLAIMER OF WARRANTY  *
       | 
       | THIS SOFTWARE AND DOCUMENT ARE OFFERED "AS IS" AND WITHOUT 
       | WARRANTIES AS TO PERFORMANCE OF MERCHANTABILITY OR ANY OTHER 
       | WARRANTIES WHETHER EXPRESSED OR IMPLIED. BECAUSE OF THE VARIOUS 
       | HARDWARE AND SOFTWARE ENVIRONMENTS INTO WHICH THIS PROGRAM MAY 
       | BE PUT, NO WARRANTY OF FITNESS FOR A PARTICULAR PURPOSE IS 
       | OFFERED. 
       | 
       | GOOD DATA PROCESSING PROCEDURE DICTATES THAT ANY PROGRAM BE 
       | THOROUGHLY TESTED BEFORE RELYING ON IT. THE USER MUST ASSUME 
       | THE ENTIRE RISK OF USING THIS PROGRAM. THE AUTHOR OF THIS 
       | PROGRAM ASSUMES NO LIABILITY. 
       | 
       | DUE TO THE NATURE OF THIS PROGRAM, THE USER MUST BE FAMILIAR 
       | WITH THE SAFETY CONSIDERATIONS OF DESIGNING AND SAFELY 
       | INSTALLING ELECTRICAL WIRING SYSTEMS, IN ACCORDANCE WITH THE 
       | NATIONAL ELECTRICAL CODE. THIS PROGRAM IS NOT INTENDED TO 
       | REPLACE THE NEED FOR A QUALIFIED PERSON WHO IS EXPERIENCED IN 
       | THE ELECTRICAL DESIGN, CONSTRUCTION AND MAINTENANCE OF SAID 
       | ELECTRICAL SYSTEMS IN THEIR ENTIRETY. 
       | 
       | 
       | 
       |
       | 
       | 
       | FILES INCLUDED ON ELECTRC8 DISK :
       | -------------------------------------------------------
       | Descrip.doc           Description of program
       | Update.new            Changes in this version 
       | Electrc8.reg          Registration Form
       | Electrc8.doc          This documentation file 
       | Electrc8.exe          Electrc8 program 
       | Electrc8.bug          Problem report form 
       | 
       | 
       | 
       | 
       | 
       | The importance of making a working copy of this or any other 
       | program disk cannot be too strongly stressed ! Please STOP NOW 
       | and copy all the files included on the ELECTRC8 disk to a 
       | blank formatted disk, and place the original in a secure place.
       
       
       
       




       
       
       
       
       
                                  II




       Introduction:
       -------------

       ELECTRC8 is designed to perform most common electrical contracting 
       and engineering calculations :
        
       * Device, junction and pull box calcs.

       * Conduit size selection for many combinations of different wire 
         sizes & types. 
       
       * Determine the cost to operate various loads at different 
         kwh charges. 
       
       * Lighting calculations based on zonal cavity method. 
       
       * Motor conductor, overcurrent and overload calculations.
       
       * Calculate required wire and conduit size based on allowable 
         voltage drop. 

       * Quick reference tables for:
           Grounding electrode conductor size
           Equipment grounding conductor size 
           Underground cover requirements
           KW to ampere tables 
           Transformer Kva to ampere tables
           Metal device box size and capacity
           Standard fuse & breaker ratings
           Standard pull & junction box table

       * Calculate voltage drop for various loads, voltages, wire size
         and run lengths. 
       
       * All functions operate with 'what-if' capability. You can quickly 
         and easily change only the data you wish to, without having to 
         start a new calculation and re-enter all the required data. 
         Results are calculated and displayed as you make each change.
       


       ** All functions conform to the 1990 National Electrical Code. 

       The National Electrical Code is a copyrighted document of the 
       National Fire Protection Association, Batterymarch Park, Quincy, 
       MA. 02269.









       

                                    Page 1




       MAIN MENU:
       ---------
       To run ELECTRC8, insert the program disk into the disk drive and 
       type ELECTRC8 then press ENTER or RETURN.
       
       The program starts up with an opening screen with a prompt for you 
       to input a random number as displayed. Enter the number exactly as 
       it is displayed. The main menu will follow.
       
       The main menu is a pull down type, structured as a horizontal bar 
       at the top of the screen with main titles displayed. Each of these 
       main titles represents a sub menu with one or more related program 
       functions. 
       
       To select specific program functions :
       1. Press the hilighted letter of the menu item (main or sub).
       OR,
       2. Press the DOWN ARROW key to open the first sub menu, then use 
          LEFT or RIGHT ARROW keys to move between sub menus.
       OR,
       3. Position the hilighted block over a menu selection (main or 
          sub), then press ENTER.
       

       
       DATA INPUT:
       ----------
       All functions now have 'What-If' data entry routines. This method 
       of data input and calculation allows you to instantly see the 
       results of changing one data item at a time. You will not need to 
       restart the function from the beginning and re-enter all data just 
       to see the effect of changing one parameter. 

       The data input routines are similar in all functions. Use the UP 
       and DOWN ARROW keys, or ENTER, to move between input fields, 
       entering data as you go. Some fields limit your input to certain 
       values, and if you input data that is unacceptable, you will hear 
       a beep and will not be able to move from that field until the 
       correct data has been entered (or you leave the field empty). 
       
       Some functions require that you select one data item from a list. 
       This is done by pressing a function key which pops up a menu where 
       you will select one item from a list of choices. Use the UP or 
       DOWN ARROW keys to position the hilighted bar over your choice and 
       press ENTER.
       
       After you have entered all required data, the calculation will be 
       performed and displayed. You can then change individual data items 
       and instantly see the results.

       CAUTION:
       When entering the last data item, or changing one data item which 
       was previously entered:
       Be sure to record that change by moving from that field to another 
       field, or by pressing ENTER while still on that field. 


                                     Page 2




       DEVICE BOX FILL CALCULATIONS:
       ----------------------------
       Determines cubic inch volume required for boxes, as per NEC 
       section 370-6. Conductor size range is from #18 thru #6. 
       
       Free space (cubic in.) required for each conductor is as follows:
       ----------------------------------------
       # 18 .. 1.5                  # 10 .. 2.5
       # 16 .. 1.75                 #  8 .. 3
       # 14 .. 2                    #  6 .. 5
       # 12 .. 2.25
       
       Deductions are as follows:
       -------------------------
       1 or more Fixture studs, cable clamps, hickeys  1 deduction
       Each Strap containing 1 or more devices ....... 2 deductions
       1 or more grounding conductors entering box ... 1 deduction
       1 or more Isolated Ground conductors .......... 1 deduction


       Enter the quantity of each size conductor within the box: 
       ---------------------------------------------------------
       
       A conductor running thru the box with no splices or connections 
       within the box should be counted as 1 conductor. 
       
       A conductor originating outside the box and terminating within the 
       box should be counted as 1 conductor. 
       
       Conductors, no part of which leaves the box (example ... a jumper 
       or pigtail from a splice within the box to a switch, outlet or 
       fixture mounted on the box), should not be counted. 
       
       ** One or more grounding conductors, or, a second set of grounding 
       conductors (isolated ground ), should not be included in this
       conductor count. They will be asked for later. 

       
       Answer the prompts for devices, clamps, fittings, ground 
       conductors, add'l ground conductors:
       ---------------------------------------------------------
       
       Count each mounting yoke or strap containing one or more devices
       as 1. Example... one duplex outlet - count as 1. two duplex 
       outlets - count as 2.

       The remaining prompts are self explanatory. Answer Y for yes.
       There is no need to answer N for any prompts which would be 
       answered as 'no'. A blank field is interpreted as 'no'.
       
       A quick reference table of standard metal boxes and their cubic 
       inch capacity is available for viewing at any time, by pressing 
       F2. The current screen will be saved, and the table will be shown. 
       When you wish to return to the previous screen, press any key. 



                                    Page 3



       
       JUNCTION, PULL BOX CALCULATIONS:

       Straight Pull:
       -------------

       Calculates the minimum length, in inches, of pull and junction 
       boxes where raceways enter and leave the box at opposite ends. If 
       the wiring method is cable assemblies instead of raceways, first 
       determine the trade size conduit which would be appropriate for 
       the size and quantity of conductors in the cable assembly, then 
       use that conduit size. 

       If more than one raceway or cable enters and/or leaves either end 
       of the box, always use the largest size. 

       The method used to determine minimum box length for straight pull:
       Eight times the trade diameter of the largest raceway.

       The operation of this function is straightforward. Position the 
       hilighted bar over the largest raceway size for this calculation, 
       then press ENTER. The results will be displayed.


       Angle or U Pull:
       ---------------

       Calculates the minimum distance, in inches, between each raceway 
       entry inside a junction or pull box and the opposite wall of the 
       box, where raceways enter and leave the box at angles. If the 
       wiring method is cable assemblies, see the explanation above, 
       under 'Straight Pull'. 

       The method used to determine minimum distance for angle or U Pull: 
       Six times the trade diameter of the largest raceway, PLUS,
       the sum of the diameters of all other raceway entries in any one 
       row on the same wall of the box. Use the row with the largest 
       total diameter of raceways. 
       
       A quick reference table of standard boxes and their cubic inch 
       capacity is available for viewing at any time, by pressing F2. The 
       current screen will be saved, and the table will be shown. When 
       you wish to return to the previous screen, press any key. 






       








                                    Page 4


       
       
       CONDUIT SELECTOR: 
       -----------------
       
       The Conduit Selector allows you to quickly and accurately 
       determine the conduit size required for 1 or more conductors. 
       Calculations are based on the Dimensions and Percent Area of 
       Conduit and Tubing from table 4, and from Conductor Dimensions as 
       per Table 5 of the NEC. Maximum allowable percent conduit fill is 
       53% for 1 conductor, 31% for 2 conductors and 40% for more than 2 
       conductors, as per table 4. 
       
       Use the UP, DOWN, TAB or SHIFT+TAB keys to move the cursor to the 
       desired wire size/type position, then enter the quantity of that 
       size/type conductor to include in the conduit. If you want to 
       include other size/types of conductors into the same conduit, then 
       repeat the above procedure. You can enter any combination of 
       conductors in the same conduit. 
       
       NOTE: Several fields will show an asterisk ( * ). This represents 
       the unavailability of those sizes/types of conductors. Do not 
       alter those fields. 
       
       Pressing F2 at any time will show the results of the calculation. 
       The program will list all the sizes and types of conductors you 
       chose for the calculation, their individual areas, the total area 
       extensions, the grand total area for all conductors, the minimum 
       trade size conduit required, the total area for the calculated 
       conduit, and the percent conduit fill for the calculation. If more 
       data is available than will fit on the screen, you will be able to 
       use the UP and DOWN ARROW keys to scroll through the data. 
       Pressing any key will return you to the conduit selector input 
       screen with all previous data intact. 
       
       
       
       GENERAL CALCULATIONS
 
       Cost to Operate:
       ---------------
       
       Calculates the cost to operate a certain load a number of hours 
       daily for some number of days at a certain KWH utility charge. 
       
       POWER OF LOAD is the number of WATTS the load draws. 
       DAILY USE is the number of HOURS the load is operated per day. 
       NUMBER OF DAYS is the number of days the load is operated.
       PRICE / KWH is the utility charge per killowatt hour. 
                    (Example..  10 cents/kwh, enter .10) 
       
       NOTE: A value of ten cents/Kwk initially appears in the 
             'Price/Kwh' field, as an example only. You should change 
             this value to reflect your own price/Kwh charge.
       
       After entering the above information, the program calculates and 
       displays the cost to operate the load for the number of hours 
       daily for the number of days at the chosen utility charge. 
       
                                    Page 5



       
       LIGHTING CALCULATION ( Zonal Cavity Method ):
       --------------------------------------------

       Calculates the quantity of lighting fixtures required to light any 
       room or area to any desired footcandle level. 
       
       The Illuminating Engineering Society (IES) has devised a flexible 
       and accurate method for calculating lighting requirements, called 
       the ZONAL CAVITY METHOD. This method assumes that any room or area 
       to be lighted is made up of three cavities, the CEILING CAVITY, 
       the ROOM CAVITY, and the FLOOR CAVITY. 
       
       The CEILING CAVITY extends from the ceiling surface down to the 
       lighting fixture mounting level. If the lighting fixtures are 
       recessed or surface mounted then the value of the Ceiling Cavity 
       will be zero. If they are suspended some distance below the 
       ceiling then the value of the Ceiling Cavity is the volume of 
       space between the ceiling surface and the fixture mounting level. 
       
       The ROOM CAVITY extends from the fixture mounting level down to 
       the work height level. The work height level is the distance above 
       the floor where the required quantity of footcandles is to be 
       maintained (usually desktop or work bench level). 
       
       The FLOOR CAVITY extends from the work height level down to the 
       floor. If the required footcandles is to be maintained all the way 
       to the floor, then the Floor Cavity value will be zero.
       
       Every surface exibits a certain ability to reflect light. Light 
       colored surfaces reflect more light than dark surfaces, so more 
       light will need to be provided in a dark environment. The degree 
       of a surface's reflectivity is referred to as it's Percent 
       Reflection value. Percent Reflection can be accurately measured 
       with a reflectometer, or standard reflectance tables can be 
       referred to, such as the following: 


                 TABLE FOR INTERIOR ILLUMINATION DESIGN 
                ----------------------------------------
                  COLOR                % REFLECTION   
                ----------------------------------------
                 Flat white               75 - 85       
                 Ivory                    70 - 75       
                 Buff                     60 - 70       
                 Yellow                   55 - 65       
                 Light tan                45 - 55       
                 Light green              40 - 50       
                 Gray                     30 - 50       
                 Blue                     25 - 35       
                 Red                      15 - 20       
                 Dark brown               10 - 15       
                ------------------------------------------





                                    Page 6




       
       The MAINTENANCE FACTOR is a value determined from the anticipated 
       maintenance of the fixtures and reflective surfaces in the room or 
       area. The intensity of illumination produced by a lighting
       installation will depreciate after some time due to lamp aging, 
       and dust and dirt buildup. The MAINTENANCE FACTOR is designed to 
       adjust for this. Typical values are from .5 to .8. (.5 for a 
       poorly maintained environment, .8 for well maintained).
       
       Each lighting equipment manufacturer publishes data for the 
       COEFFICIENT OF UTILIZATION (CU) for each fixture type and size in 
       it's line. The CU of a fixture is a measure of it's efficiency 
       under specific conditions of room cavity values and effective 
       reflectance values. 
       
       
       The formulas used in the ZONAL CAVITY METHOD : 
       
       CEILING CAVITY RATIO = (5 * Hc (L + W)) / (L * W) 
       
       ROOM CAVITY RATIO =  (5 * Hr (L + W)) / (L * W) 
       
       FLOOR CAVITY RATIO = (5 * Hf (L + W) / (L *  W) 
       
       WHERE: 
       Hc = distance from ceiling to fixture level (in feet).
       Hr = distance from fixture level to work height (in feet).
       Hf = distance from work height to floor (in feet).
       L = length of room in feet.
       W = width of room in feet.
       

       ROOM LENGTH and ROOM WIDTH values must be entered in FEET. 
       Decimal points are accepted (Ex. 125, 50.5, etc...).
        
       CEILING HEIGHT and FIXTURE HEIGHT must also be entered in FEET. 
       Decimal points are acceptable. 
       
       WORK HEIGHT must also be entered in FEET. Decimal points are 
       acceptable. If you want the WORK HEIGHT to be equal to the 
       floor, simply enter zero.
       
       FOOTCANDLE LEVEL is a measure of the intensity of light falling 
       upon a specific surface.













                                    Page 7




       
       Values for Percent CEILING, WALL, and FLOOR Reflectances must be 
       entered as whole numbers (50, 80, etc...) Exact values can be 
       obtained by use of a reflectometer, or a standard table for 
       interior illumination design can be referred to, such as the table 
       for interior illumination design on the previous page. 
       
       The value entered for MAINTENANCE FACTOR must be less than or 
       equal to 1. The value of between .5 and .8 will be accurate for 
       nearly all calculations. A value of 1 will exclude the MAINTENANCE 
       FACTOR from the lighting calculation. 
       NOTE: A value of .8 initially appears in the 'Maintenance Factor'
             field, as an example only. You can change this value to
             reflect your own conditions.


       To select fixture type, press F2. The menu will ask you to select 
       either 'built-in fixture type' or 'specify fixture type'. 
       
       Built-In:
       ---------
       Fixture types stored internally include Recessed Incandescent, 
       Fluorescent, and High Intensity Discharge. COEFFICIENT of 
       UTILIZATION (CU) values which have been compiled by IES are stored 
       internally for these fixtures. The internally stored fixtures are 
       representitive of their types, as are the internally stored lamp 
       types. You will get accurate results using them, but if you wish 
       to use a type of fixture not available internally, you can choose 
       to specify your own type. 

       Specify:
       --------
       If you choose to specify your own fixture type, you will be 
       prompted for the number of lamps per fixture, the quantity of 
       lumens per lamp, and, the coefficient of utilization (CU) of the 
       fixture. You will need to have the fixture manufacturer's CU 
       specs. LUMEN specs are available from various sources. Lamp 
       manufacturers will have lamp catalogs which will list LUMEN values 
       for their line of lamps. 
       
       After all data has been entered, the number of fixtures required 
       will be calculated and displayed.
       














                                    Page 8



       MOTOR CALCULATIONS:
       -------------------
       
       Branch Conductor Sizing:
       -----------------------
       Calculates motor branch circuit conductor size. NEC Article 430-
       Part B, and, 430-6. 
       
       Conductor ampacity is based on 125 percent of motor full load 
       amperage, as determined from table 430-148.
       
       Conductor types supported include THW, THWN, THHN, XHHW Copper, 
       THHN, XHHW Aluminum.
       
       
       Fuse or Breaker Sizing:
       ----------------------
       Calculates rating or setting of motor branch circuit overcurrent 
       protective device (Nontime-delay fuse, Time delay fuse, 
       Instantaneous trip circuit breaker & Inverse time circuit 
       breaker). NEC Article 430-Part D, and, 430-52. 

       Rating or setting is based on Full load amperage (from table 430-
       148) of motor, multiplied by appropriate percentage factor from 
       table 430-152 for the selected device type. Article 430-52(a).
       
       If this results in a value other than a standard size or rating of 
       overcurrent protection device, the next higher standard rating is 
       selected. Article 430-52(a), Exception 1. 


       Overload Protection Sizing:
       --------------------------
       Calculates motor overload protective device rating. Article 430, 
       Part C.

       Rating is based on motor full load amperage (from motor nameplate)
       multiplied by:
       125 % if nameplate marked service factor is not less than 1.15, or 
       125 % if nameplate marked temp. rise is not over 40 degrees C., or
       115 % for all others.
       
       Access Keys Used To Select Motor, Wire & Overcurrent Parameters:
       -----------------------------------------------------------------
       Press:    To Select:                 Press:    To Select:
       --------------------                 --------------------
       F4        Volts                      F6        Code Letter
       F5        Horsepower                 F7        Wire Type
                                            F8        Overcurrent Type
       

       At the 'Percent Motor Power Factor' field, entering 100 will 
       assume 100% power factor and exclude the motor's Power Factor from 
       the calculation. 
       
       After all data has been entered, the calculation will be performed  
       and the results will be displayed. 
       
                                    Page 9




       PIPE & WIRE SELECTOR:
       ---------------------
       Calculates the conductor size required to carry a certain load for 
       some distance while not exceeding a specific voltage drop 
       percentage, and the trade size conduit required to contain those 
       conductors.
       
       Conductor types supported include THW, THWN, THHN, XHHW Copper, 
       THHN, XHHW Aluminum. 
       
       Conductor ambient temperature derating is supported, according to 
       the ampacity correction factors at the bottom of NEC Table 310-16. 
       
       Conductor ampacity derating due to the number of current carrying 
       conductors in the raceway is supported as per NEC 310-Note 8(a).

       Six circuit types are supported:
       --------------------------------
       1 Phase 2 Wire(Phase & neutral, or 2 Phase conductors)
       1 Phase 3 Wire(2 Phase conductors & neutral)
       1 Phase 3 Wire(Above circuit from a 4 wire wye system)
       3 Phase 3 Wire(3 phase conductors)
       3 Phase 4 Wire Wye(3 phase conductors & neutral)
       3 Phase 4 Wire Wye circuit with the majority of load consisting of 
             electric discharge lighting, computers, or similar equipment.
       
       In the third circuit type above, the neutral will carry 
       substantial current, and will be considered as a current carrying 
       conductor in the pipe size selection. NEC 310-Note 10(b).

       In the last circuit type above, the neutral will carry harmonic
       currents, and will be considered as a current carrying 
       conductor in the pipe size selection. NEC 310-Note 10(c).
       
       
       Data Input:
       -----------
       The 'Maximum Percent Of Voltage Drop' field will only accept whole 
       numbers in the range of 0 to 9. This will be the maximum 
       percentage of the supply voltage which can be dropped by the 
       circuit conductors. If you enter 0 in this field, voltage drop 
       will not be considered in the selection of the wire size. 
       
       The 'Full Load Amperage Of Load' is the rated or maximum amperage.

       The 'Source Voltage' is the supply voltage for the circuit.

       The 'Length of Run In Feet' is one way length from supply to load.
       
       Press F2 to select the circuit type.
       Press F3 to select the wire type.
       Press F4 to select ambient temperature of the circuit conductors. 

       After you have entered the data, the program will calculate and 
       display the required conductor and pipe size. 


                                     Page 10




       EQUIPMENT GROUND CONDUCTOR TABLE: 
       --------------------------------
       To determine the required size equipment ground conductor,
       as per NEC Table 250-95.

       
       GROUNDING ELECTRODE CONDUCTOR TABLE: 
       -----------------------------------
       To determine the proper grounding electrode conductor size,
       as per NEC Table 250-94.
       
       
       KW TO AMPERE TABLES: 
       -------------------
       To quickly convert single and three phase KW values to ampere 
       values and vice versa. Pressing PG UP & PG DN scrolls between the 
       single phase and three phase tables. 

       
       UNDERGROUND COVER TABLE: 
       -----------------------
       To determine the minimum cover requirements of conduit,
       underground cable, and other raceways, as per NEC Table 300-5.
       

       METAL DEVICE BOX TABLE:
       ----------------------
       Table of metal device boxes and their cubic inch capacities.
       
       
       STANDARD PULL & JUNCTION BOXES:
       ------------------------------
       Table of standard pull & junction boxes and their cubic inch 
       capacities.

       
       STANDARD FUSE & BREAKER TABLE:
       -----------------------------
       Table of standard ratings of overcurrent devices.

       
       TRANSFORMER KVA TO AMPERE TABLE:
       -------------------------------
       To quickly convert single and three phase transformer Kva values 
       to ampere values and vice versa. Pressing PG UP & PG DN scrolls 
       between the single phase and three phase tables. 


       SETUP:
       Color Defaults:
       --------------
       As supplied, the program starts up in black and white. Select 
       'Setup' from the main menu. Then select either Color Display or 
       Mono Display. Your choice will be executed, and saved to a disk 
       file, which will automatically be used for future program use.


                                    Page 11




       VOLTAGE DROP CALCULATOR: 
       -----------------------

       Calculates the voltage drop on existing or proposed single phase 
       resistive AC circuits (100% power factor). Copper and aluminum 
       conductors from #14 to 2000 Kcmil are supported. The registered 
       user version supports 3 phase circuits. 
       
       The 'Length Of Run' is the length in feet of one conductor from 
       the source of power to the load terminals. 

       The 'Source Voltage' is the voltage measured at the source of 
       power. 
       
       The 'Amperage Of Load' is the current required by the load. For 
       example, if the load is a resistance heater requiring 10 amps to 
       operate as designed, then the AMPERAGE would be entered as 10. 
       
       The WIRE SIZE is in the range of #18 Awg to 2000 Kcmil. Do not 
       include the # sign or the letters Awg or Kcmil. Enter the numeric 
       size of the wire (ex. 14, 1/0, 250, 750). 
       
       The COPPER or ALUMINUM prompt is self explanatory. 
       
       After entering the above values, the program will calculate and 
       display:
       1. The VOLTAGE DROP of the circuit (the number of volts dropped).
       2. The VOLTS AT LOAD (the voltage delivered to the load terminals) 
       3. The % DROP (the percentage of the source voltage dropped) 
       


























                                    Page 12


       
       
       ================================================================
                              REGISTRATION
       ----------------------------------------------------------------


       When you register your copy of ELECTRC8, an expanded 'Registered 
       User' version of the software will be shipped to you immediately.
       That version will support these additional functions:

       * Three phase motor calculations:
            Branch conductor sizing,
            Overcurrent protection sizing, and
            Overload protection sizing.
       * Horsepower ratings not available in this version.
       * Motor types not available in this version.
       * Motor starting methods not available in this version.

       * Additional general calculations - Single & 3 Phase:
            Amperes when motor HP, PF and EFF. is known,
            Amperes when watts or VA and PF is known,
            Watts or VA when voltage, current and PF is known,
            Motor HP when voltage, current, efficiency and PF are known.

       * Short circuit calculations:
            Start at a utility transformer or service entrance and 
            perform fault current calculations at various points along 
            the distribution system using BUSSMANN's Point-To-Point 
            method. Single and three phase calcs. Wire size & length, 
            single or parallel conductors - cu/al, magnetic/non-magnetic 
            raceways.
       
       * Support of 3 phase circuits in the Voltage Drop Calculations.
       
       * Print routines for all functions:
            Print output to an ASCII disk file or to a printer.
       
       * Elimination of the program's opening screen.




















                                    Page 13




                 ELECTRC8, Copyright 1991, By Robert J. La Capra

                        ==  REGISTRATION FORM  ==

       
       SHIP TO:

       Name: _______________________________________________________
       
       Company: ____________________________________________________
 
       Address: ____________________________________________________
       
       City,State,Zip:______________________________________________
       
       
       Fee Enclosed: $__________
       
       Where did you obtain ELECTRC8 ?:
       
       _____________________________________________________________
       
       Suggestions & Comments, if you wish:
       _____________________________________________________________ 
       _____________________________________________________________
       _____________________________________________________________ 
       _____________________________________________________________ 
       _____________________________________________________________ 
       _____________________________________________________________ 
       _____________________________________________________________ 

       
       ==================================================================
       Registration fee for ELECTRC8 is $45.00 for each user.
       
       Purchase orders without payment attached cannot be accepted.

       Send this form and registration fee to:
                                            Robert J. La Capra
                                            50 Hillside Terrace 
                                            Andover, NJ 07821

       Once again, thanks for using and supporting ELECTRC8. As always, 
       any questions, comments and suggestion are welcome. 
       ==================================================================
       
                                    Page 14