- 1 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20




















           Universal Version of Geographic Clock Program

           Copyright 1988,1989,1990 (C) Joseph R. Ahlgren

           GEOCLOCK is a registered Trademark

           Version 4.2    90/06/09

           GEOCLK42.ZIP - EGA/VGA/800x600 version
           GEOMNO42.ZIP - CGA/HGC/MCGA/ATT400/PC3270 version

           Computer Bulletin Board -  703-241-7980



                              Joseph R. Ahlgren
                              2218 N. Tuckahoe St
                              Arlington, VA  22205-1946



                                        - 2 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20




                                  Table Of Contents

     A.  Introduction  . . . . . . . . . . . . . . . . . . . . . . . . . . .   3

     B.    Getting Started . . . . . . . . . . . . . . . . . . . . . . . . .   3
          B.1.  EGA/VGA/SVGA version (GEOCLK)  . . . . . . . . . . . . . . .   3
          B.2.  CGA/HGC/MCGA/ATT400/PC3270 version (GEOMNO)  . . . . . . . .   4
          B.3.  Mouse  . . . . . . . . . . . . . . . . . . . . . . . . . . .   5
          B.4.  Preparing the registered version . . . . . . . . . . . . . .   5
          B.5.  Upgrading from version 2.x . . . . . . . . . . . . . . . . .   6

     C.    Operation . . . . . . . . . . . . . . . . . . . . . . . . . . . .   6
          C.1.  Single key functions . . . . . . . . . . . . . . . . . . . .   7
          C.2.  Commands . . . . . . . . . . . . . . . . . . . . . . . . . .   7
          C.3.  Command line parameters  . . . . . . . . . . . . . . . . . .  12

     D.    Customizing . . . . . . . . . . . . . . . . . . . . . . . . . . .  12
          D.1.  Time zone data . . . . . . . . . . . . . . . . . . . . . . .  12
          D.2.  Cities in GEOCLOCK.DAT and GEO<n>.DAT  . . . . . . . . . . .  13
          D.3.  Default parameters in GECONFIG.DAT . . . . . . . . . . . . .  13

     E.    Functions for registered users only . . . . . . . . . . . . . . .  13
          E.1.  Zoom . . . . . . . . . . . . . . . . . . . . . . . . . . . .  14
          E.2.  Distance . . . . . . . . . . . . . . . . . . . . . . . . . .  14
          E.3.  Time display for cities  . . . . . . . . . . . . . . . . . .  14

     F.    Files . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  15
          F.1.  GEOCLKnn.ZIP . . . . . . . . . . . . . . . . . . . . . . . .  15
          F.2.  GEOMNOnn.ZIP . . . . . . . . . . . . . . . . . . . . . . . .  15

     G.    Technical Information . . . . . . . . . . . . . . . . . . . . . .  15
          G.1.  Ephemeris Data . . . . . . . . . . . . . . . . . . . . . . .  15
          G.2.  Use of Color . . . . . . . . . . . . . . . . . . . . . . . .  17
          G.3.  Software structure . . . . . . . . . . . . . . . . . . . . .  17
          G.4.  Map Generation System  . . . . . . . . . . . . . . . . . . .  18

     H.    HAM add-in. . . . . . . . . . . . . . . . . . . . . . . . . . . .  18

     I.    Bulletin Board  . . . . . . . . . . . . . . . . . . . . . . . . .  19

     J.    Upgrades and Enhancements for Registered Users  . . . . . . . . .  19

     K.    Registration and License  . . . . . . . . . . . . . . . . . . . .  20



                                        - 3 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


     A.  Introduction

          GEOCLOCK shows the current time (based on the system clock) with a map
     of the earth.  The current sun position is displayed and the part of the
     earth in sunlight is highlighted.  This display is automatically updated
     every 1 second (for an 8 MHz AT with an 80287) to 20 seconds (for a 5 MHz
     PC without an 8087).  Local sunrise, sunset, and the sun's azimuth and
     elevation are also displayed.  A variety of map backgrounds and other
     options are available.  A graphics adapter and a hard disk are required to
     run GEOCLOCK.  GEOCLOCK is primarily an EGA/VGA/SVGA program, although CGA,
     hercules, MCGA, AT&T 640x400, and PC3270 are supported with some
     limitations.

        GEOCLOCK is distributed as SHAREWARE.  If you use and enjoy the product,
     you must register and obtain a license for the program.  The license
     includes a few extra features and more maps.  See section K.  The
     unregistered version of the program may be distributed freely, provided
     that the entire unmodified ZIP file is included and no fee is charged other
     than a nominal amount for media and handling.  A version with special
     features for HAM operators is also available.  See section H.

     B.    Getting Started

          GEOCLOCK requires a hard disk, a minimum of 200K available RAM (up to
     250K to use VGA and 800x600 modes), and a graphics adapter and monitor.

          There are two versions of GEOCLOCK.  The first is contained in
     GEOCLK42.ZIP and is designed to support computers with a 256k EGA, VGA, or
     super VGA boards with a compatible color monitor.  The second requires both
     GEOMNO42.ZIP and GEOCLK42.ZIP and is designed to support CGA, Hercules,
     MCGA, AT&T 640x400, and PC3270 graphics, all in the highest resolution
     monochrome mode available for that card.  To get the program running, do
     the following:
          1.  Un-ZIP GEOCLK42.ZIP (and GEOMNO42.ZIP if required) to the
     directory you will run from.  It is best to have a directory dedicated to
     GEOCLOCK.
          2.  Set up the program for your graphics adapter.  Section B.1
     describes the set up procedure for the EGA, VGA, and super VGA (800x600)
     adapters.  Section B.2 describes the set up procedure for the CGA,
     Hercules, MCGA, PC3270, and AT&T 640x400 adapters.
          3.  Customize GEOCLOCK for your location.  Much customization is
     possible, and is described in detail in sections D and E.  Before you start
     running GEOCLOCK, you should edit (using any text editor) the GECONFIG.DAT
     file to specify your local time zone.  The value in the initial file
     specifies the Eastern US time zone.  You should change the PCZONE command
     at the end of GECONFIG.DAT to specify your time zone.
          4.  If you are a registered user, you need to run the REGISTER program
     to enable the special features.  You may also want to use a mouse - see
     section B.3.
          5.  Run the program.  Just enter GEOCLK (for EGA, VGA, and SVGA) or
     GEOMNO (for the other adapters) and the program will start.  Function Key 1
     will provide help, and Escape will terminate the program.

     B.1.  EGA/VGA/SVGA version (GEOCLK)



                                        - 4 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


          The EGA/VGA/SVGA version of GEOCLOCK requires an EGA, VGA, super VGA
     (800x600) or close compatible with at least 256k memory, and an EGA, VGA,
     or multiscanning color monitor.  The program uses 640x350, 640x480, and
     800x600 16 color graphics.  The distribution GEOCLK42.ZIP file contains all
     the required programs and data bases.  The main program file is named
     GEOCLK.EXE.  It will automatically determine whether or not you have a math
     co-processor (8087,80287, 80387), and use it if you do, or emulate it if
     you do not.  If you have a normal EGA, the program is already configured
     properly.  If you have a VGA or SVGA, you will need to follow one of the
     procedures below:

          1.  Set up for VGA or 640x480x16 EGA.  To enable 640x480 display, you
     must include the VGA statement in the GECONFIG.DAT file.  This statement
     tells GEOCLOCK that you have a 640x480 display and how to enter that
     display mode.  You will find a commented out VGA statement at the end of
     the GECONFIG.DAT file.  Simply use any text editor to remove the "REM " at
     the beginning of the VGA statement, so that the "V" is in column one.  If
     you have a 640x480x16 EGA, you will need to contact your adapter supplier
     to determine the appropriate parameters for the VGA statement.  See section
     C.2 for a fuller explanation.  You might also want to add the SHOWVGA
     statement to GECONFIG.DAT.  This will automatically convert EGA maps to VGA
     format.

          2.  Set up for super VGA (800x600x16).  To enable 800x600 display, you
     must include the SVGA statement in the GECONFIG.DAT file.  This statement
     tells GEOCLOCK that you have a 800x600 display and how to enter that
     display mode.  You will find several commented out SVGA statements at the
     end of the GECONFIG.DAT file, corresponding to the several adapters that
     support this graphics mode.  Simply use any text editor to remove the "REM"
     at the beginning of the appropriate SVGA statement, so that the "S" is in
     column one.  If your adapter is not listed, you will need to contact your
     adapter supplier to determine the appropriate parameters for the SVGA
     statement.  (Tell your supplier than you need the decimal values for the
     registers to enter the 800x600x16 mode using INT 10).  See section C.2 for
     a fuller explanation.  It is not necessary to include a VGA statement in
     addition to the SVGA statement unless your adapter does not use the
     standard command to enter the 640x480x16 mode.

     B.2.  CGA/HGC/MCGA/ATT400/PC3270 version (GEOMNO)

          This version of GEOCLOCK is compatible with a wide variety of graphics
     boards, including all those two color modes supported by the Turbo Pascal
     5.0 GRAPH unit.  In particular, 640x200 CGA, 720x348 HGC, 640x480 MCGA,
     640x400 ATT, and 720x350 PC3270 mode are supported.  The 640x350 EGA
     monochrome mode is NOT supported (this is a four color mode), although the
     EGA emulation of HGC is supported provided your EGA board permits this. 
     The distribution GEOMNO42.ZIP and GEOCLK42.ZIP files contain all the
     required programs and data bases.  

          After Un-ZIPping the program, the files configuring the system for
     your graphics adapter must be built.  The installation program GEOCONVT
     builds these files, installs the proper drivers, and converts the maps to
     the required format.  This program is started by:

          GEOCONVT <board type> [map file spec] [switches]



                                        - 5 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


     where board type is CGA, HGC, MCG, ATT, or 327.  The [map file spec]
     specifies which map files are to be converted to the format for your
     adapter.  If omitted, MAP*.EGA is assumed.  The switches are zero or more
     of /D (which specifies that files not required for your particular adapter
     are to be deleted) and /C (which specifies that map files are to be
     converted, but no other conversions are to be done).  By default, neither
     option is selected.  Specifying /D saves space on your disk, but be sure
     that you have kept a backup or the original ZIP file before selecting this
     option.  You should specify /C is you have already configured GEOMNO and
     only need to convert a new map file.  For the initial setup, I recommend:

          GEOCONVT CGA    (or whatever adapter is appropriate)

     without any options.  You can do a    del map*.ega     to eliminate the
     unneeded EGA map files after you are sure that everything is working
     properly.

     B.3.  Mouse

          Several GEOCLOCK functions require a graphics cursor for input.  These
     operate from both a mouse and the keyboard.  To use the mouse, the INT 33
     driver must be loaded.  This driver, which comes with most mice, is usually
     called MOUSE.COM or MOUSE.SYS.  The mouse buttons and functions are
     emulated on the keyboard as follows:

         Left Mouse Button           Control (CTRL) and Page-Up keys
         Center Mouse Button         Escape (ESC) Key
         Right Mouse Button          Alternate (ALT) and Page-Down keys
         Mouse Motion                Arrow and Shift-Arrow keys

          All the keyboard equivalents work whether or not a mouse is available. 
     In particular, the arrow keys may be used to finely position the cursor
     after the mouse has moved the cursor to the vicinity of the desired point,
     and the Escape key can be used if your mouse does not have a center button.

     B.4.  Preparing the registered version

          The registered version of GEOCLOCK includes an INSTALL batch file to
     aid in setting up GEOCLOCK on your hard disk.  The batch file un-Zips all
     the required files (include map files), converts the maps as required, and
     runs the REGISTER program which enables the special features such as Zoom,
     Distance, and city time display that are available only to registered
     users.  If you do not wish to use this batch file, follow these steps:
          a.  Create a directory for GEOCLOCK on your hard disk, and switch to
     it.  Copy the PKUNZIP.EXE program from the distribution disk to this
     directory.
          b.  Un-Zip the GEOCLOCK program by entering PKUNZIP A:GEOCLK42 .  If
     you are using the MNO version, also enter PKUNZIP A:GEOMNO42 .
          c.  Un-ZIP all the map files by entering PKUNZIP A:MAP* .  If you
     received multiple disks, you should repeat this command for every disk.
          d.  If you are using a VGA or 800x600, enter PKUNZIP A:VGA* .  If you
     are using an 800x600, also enter PKUNZIP SVGA* .
          e.  Un-Zip the GEODATA file.
          f.  If you are using the MNO version, enter GEOCONVT <code>, where
     code is CGA, HGC, MCG, ATT, or 327 as appropriate.  This converts all the
     maps to the proper MNO format.



                                        - 6 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


          g.  Copy the REGISTER.EXE file to the hard disk and enter REGISTER . 
     This enables the special features.
          h.  Finally, use the TED editor to customize the configuration.  Enter
     TED GECONFIG.DAT .  Change the PCZONE command to your time zone.  If you
     have a VGA or 800x600, add the VGA command.  If you have an 800x600, also
     add the SVGA command.

     B.5.  Upgrading from version 2.x

          Version 4.x contains many new features which require changes in some
     of the 2.x files for optimum operation.  3.x files do not require any
     conversion.  Existing 2.x data files will work but cannot take advantage of
     these new features.  The conversion process effects four types of files.
            a.  MAP<n>.EGA.  This only effects the EGA/VGA version of GEOCLOCK. 
     The map format was changed to reduce the sizes of the map files.  While
     GEOCLOCK 4.x will display both file formats, processing of the new format
     is faster.  The program CVTMAP.EXE, available on the GEOCLOCK bulletin
     board, will convert the old to new format.  To convert your existing maps,
     follow this procedure:
         DEL *.BAK
         COPY MAP*.EGA MAP*.BAK
         CVTMAP MAP*.BAK *.EGA
         DEL *.BAK
            b.  GECONFIG.DAT.  This file was required only for GEOMNO in version
     2.x.  In version 4, this file optionally contains a list of command line
     parameters (one per line).  In addition, two new commands are of particular
     interest: ZONE, which defines time zone characteristics; and PCZONE, which
     defines which time zone the PC's local clock is in.  The GECONFIG.DAT file
     provided should be used until you feel the need to change it.  GEOCONVT
     appends any existing GECONFIG.DAT file (including the one provided in
     GEOMNOnn.ZIP) to the one it produces while setting up GEOMNO.  See section
     D.
            c.  GEOCLOCK.DAT and GEO<n>.DAT.  The format of these files has been
     enhanced to take advantage of the time zone data.  The old first line,
     which specifies the displayed zone and its relationship to the PC clock, is
     now optional.  If it is omitted, it is assumed that PC local time is to be
     displayed, as specified by the PCZONE command.  If a zone code is named,
     that is the local time displayed.  On the subsequent lines, for registered
     users, the time offset (specified by +n or -n after the !) may be specified
     as <space><zone code> or <space>*<zone code>, in which case the city time
     is displayed in the time zone specified by the zone code.  If * is
     included, the time zone name is also displayed.  See section D.
            d.  *.BGI files must be replaced with new versions, since version 4
     was compiled under Turbo Pascal 5.0.  These are included in GEOMNOnn.ZIP.  

     C.    Operation

          To run GEOCLOCK, simply enter "GEOCLK" or "GEOMNO".  The initial
     display is built, and then this display is updated continuously.  The
     program recognizes a variety of functions while running.  Each of these is
     activated by pressing a letter key.  These functions are summarized below. 


     C.1.  Single key functions



                                        - 7 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


            Function Key 1 - activates the help system.  The first screen is a
     menu listing all the GEOCLOCK parameters and keys.  Select a menu item by
     pressing the indicated letter displays additional information.  You exit
     the additional information screen and display the main menu by pressing any
     key.  You exit the help system and return to GEOCLOCK display or parameter
     entry by pressing any non-letter key.

            F - speed up the rate of change of time per display update. A prompt
     asks for the number of hours (possibly fractional or negative) for the
     displayed clock to be incremented during each cycle, e.g., 0.25 for 15
     minutes every 1 to 20 second cycle.

            U - set the interval between screen updates.  A prompt asks for the
     update interval in seconds.  When this value is entered, the display is
     immediately drawn.  Subsequently, the screen in updated at the specified
     interval and synchronized with the clock.  Thus, if 15 is specified, the
     screen will be updated at 0, 15, 30, and 45 seconds past the minute.  If
     your computer is not fast enough to achieve the specified interval, the
     smallest integer multiple of this interval which works will be used.

            T - change the display time according to prompts in yy/mm/dd
     hh:mm:ss format.  This does not change the system clock.  Any missing data
     will revert to the current local time.  Thus "///12:0:0" sets the time to
     today at 12 noon, while 88 01 01 0 0 0 sets the time to midnight, January
     1, 1988.  All times in GEOCLOCK use the 24 hour format.  If you are using
     the pop-up window in the EGA version, you can use the cursor keys to edit
     the time, use ENTER to accept the new time, or escape to reject the new
     time.

            R - restore the display time to the current time, and the display
     update rate to real time.  R undoes F, T, and U.

            P - allows changes to the command line parameters.  These commands
     are listed in section C.2 below.  Entering "?" or "HELP" at the prompt will
     activate the help system.

            S - select a map.  When this key is pressed, a list of available
     maps is displayed with their coordinates, title, and North-South distance. 
     The highlighted line corresponds to the current map.  The cursor keys can
     be used to scroll through this list.  When the <ENTER> key is pressed, the
     highlighted map will be displayed.  By pressing T, the maps will be sorted
     by title, while N sorts by map number and S sorts by map size.  Some very
     early GEOCLOCK maps did not have titles.  If you have any of these maps,
     the FIXMAP program, available on the GEOCLOCK RBBS (703-241-7980) will add
     the proper titles.

            X - return to DOS.

            Escape - return to DOS.

     C.2.  Commands

            GEOCLOCK allows several command line parameters which control the
     display.  These parameters may also be entered in response to prompts from
     the "p" function above, included on the DOS command line, included in the
     GECONFIG.DAT file, or included in a GEO*.DAT file.  Some of these commands



                                        - 8 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


     take parameters.  When entered on the command line, there can be no spaces
     or commas in the command (e.g., LINE15 is OK, but LINE 15 is not).  When
     contained in a file, commas and spaces are ignored.  If you want an
     imbedded space or other mark (e.g. Washington, DC) you can enclose the
     parameter in quote marks (e.g., "Washington, DC").  Latitude and longitudes
     can be entered as decimal degrees (e.g., -14.35) or in degrees, minutes,
     seconds, heading format (e.g., 14d21mW or "14 21 00 W").  Note that S
     indicates south, not seconds.

          Below is a list of all the GEOCLOCK commands.  The DCGE column
     indicates any restrictions on the command.  "D" (default) indicates that
     this command is the initial condition of GEOCLOCK when it is started.  "C"
     (Command Line) indicates that the command may be included on the GEOCLOCK
     command line.  "G" (Global) indicates the command remains in effect until
     overridden by another command (otherwise the effect of the command is
     automatically removed when the displayed map is changed).  Finally, "E"
     (EGA or better) indicates that the command has effect only in the
     EGA/VGA/SVGA (GEOCLK) version.

     command   DCGE comments
     ?         ---- displays list of commands.
     HELP      ---- displays list of commands.
     REM       ---- remark.  The rest of the parameter is ignored.
     MAP       -C-- MAP (without a number) brings up the map selection menu,
                    similar to the "S" command.  This may be entered on the
                    command line or in the GECONFIG.DAT file, in which case the
                    map selection menu will be displayed before the program
                    starts.
     MAPn      -CG- displays appropriate map.  Map1 is the default.  The
                    GEO*.ZIP files include two maps.  MAP1 is a rectilinear
                    projection of the entire Earth.  MAP2 is a map of the 48
                    states.  MAP2000, which is a North Polar projection map. 
                    Other maps are available as detailed in section K.
     NOMAP     -CG- does not display any background map.
     SCREEN    -CGE Forces EGA maps to be handled using both screen buffers in
                    the EGA adapter.  In this mode, screen updates are smooth,
                    but the sun symbol is a dark crossed circle and the display
                    is updated less often than in the NOSCR mode.
     NOSCR     DCGE This command forces EGA maps to be handled the same way VGA
                    and SVGA maps are handled.
     SHOWVGA   -CGE This command causes all EGA maps to be automatically
                    expanded (by duplicating some rows) to VGA resolution and
                    displayed as VGA maps.  This does not change the map
                    resolution, but does change the text and sunlight
                    resolution.
     SHOWSVGA  -CGE This command causes all EGA and VGA maps to be automatically
                    expanded (by duplicating some rows and pixels within rows)
                    to SVGA resolution and displayed as SVGA maps.  This does
                    not change the map resolution, but does change the text and
                    sunlight resolution.
     VGA       -CGE This enables VGA display.  If this command is not included
                    in the GECONFIG.DAT file, VGA maps may not be displayed.  If
                    you do not have a true VGA (for example, an EGA that
                    supports 640x480x16), you may need to use the form
                    VGAa/b/c/d.  The arguments indicate decimal the values to be
                    loaded into the AX, BX, CX, and DX registers before the call



                                        - 9 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


                    to INT 10 to enter VGA mode.  Check with your display
                    adapter supplier if you are not sure of the correct
                    parameters to use.  DO NOT include this command unless you
                    have a 640x480 EGA, a VGA, or super VGA adapter and a VGA or
                    multisync monitor: your monitor may be damaged if it does
                    not support the vertical and horizontal frequencies
                    generated by the VGA.
     SVGA      -CGE SVGAa/b/c/d enables SVGA (800x600) display.  If this command
                    is not included in the GECONFIG.DAT file, SVGA maps may not
                    be displayed.  The arguments indicate the values to be
                    loaded into the AX, BX, CX, and DX registers before the call
                    to INT 10 to enter SVGA mode.  For the Paradise SVGA, the
                    parameters are optional: SVGA88/0/0/0 is assumed.  Check
                    with you display adapter supplier if you are not sure of the
                    correct parameters to use.  (Tell your supplier than you
                    need the decimal values for the registers to enter the
                    800x600x16 mode using INT 10).  DO NOT include this command
                    unless you have a super VGA adapter and a multisync monitor:
                    your monitor may be damaged if it does not support the
                    vertical and horizontal frequencies generated by the SVGA.
     MARK      -CG- displays markers for the cities in geo*.dat.  See section
                    D.3
     NOMARK    DCG- does not display city markers or city names.
     NOCITY    DCG- does not display city names for the cities in geo*.dat.
     CITY      -CG- displays city names.
     QUIET     DCG- does not beep on screen update.
     SOUND     -CG- beeps each time the screen is updated.
     NOLINE    DCG- does not display any latitude/longitude lines.
     LINEnn    -CG- displays latitude/longitude lines every nn degrees, unless
                    that would result in more than 40 lines.  If nn is 0 or
                    missing, the current latitude and longitude line intervals
                    are not changed but lines are enabled, and thus LINE undoes
                    NOLINE.
     TLINCnn   -CG- same as LINEnn, except only affects Latitude lines.
     GLINCnn   -CG- same as LINEnn, except only affects Longitude lines.
     TLSPECnn  -CG- displays one latitude line at nn.
     GLSPECnn  -CG- displays one longitude line at nn.  Up to 20 TLSPEC and
                    GLSPEC lines may be specified.

     CLINE     DCG- removes all TLSPEC and GLSPEC lines.
     HIDELL    DCG- does not label latitude/longitude lines
     SHOWLL    DCG- labels latitude/longitude lines
     DRAWLINE  ---- DRAWLINE lat1 long1 lat2 long2 color   draws a line between
                    (lat1,long1) and (lat2,long2) on the current map.  The
                    command operates only when contained in a GEO*.DAT file that
                    is processed for the map.  Color is the color in which the
                    line will be drawn.  See section G.2 for an explanation of
                    the use of color.  If omitted, color defaults to 5 (yellow).
                    Example: DRAWLINE 38.9 -77.0 34.0 -118.3 0 draws a line
                    between Washington DC and Los Angeles in color 0.
     DRAWCIRCLE---- DRAWCIRCLE latcenter longcenter latrad longrad color   
                    draws an ellipse centered at (latcenter,longcenter) and with
                    latitude (vertical) radius latrad and with longitude
                    (horizontal) radius longrad.  The command operates on when
                    contained in a GEO*.DAT file that is processed for the map. 
                    Color is the color in which the line will be drawn.  See



                                        - 10 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


                    section G.2 for an explanation of the use of color.  If
                    omitted, color defaults to 5, which is displayed as yellow. 
                    Example:  DRAWCIRCLE  38.9  -77.0  10 20 6 draws an oval
                    centered on Washington DC that is 10 degrees from the center
                    to the northernmost point, and 20 degrees from the center to
                    the easternmost point, and in color 6.
     INCLUDE   ---- When contained in a GEO*.DAT file, INCLUDE <file>  suspends
                    reading from the file being processed, and processes all
                    commands in the <file>.  When all commands in that file have
                    been processed, reading resumes from the original file. 
                    INCLUDE may be nested up to ten levels.  Include may also be
                    used in response to the "P" command.  In this case, the
                    named file will be included at the end of the GEOn.DAT file
                    for the map currently displayed.  The effect of this command
                    will be negated when a new map is selected or a new file is
                    specified with INCLUDE.
     NORM      -CG- highlights sunlit area.
     REV       -CG- highlights area not sunlit (appropriate for LCD displays)
     LIGHT     -CG- highlights entire screen, and does not show sun symbol.
     DARK      -CG- highlights no area, and does not show sun symbol.
     FLICKER   -CGE This command forces GEOCLOCK to bypass the video BIOS and
                    issue changes to the video memory start address and palette
                    directly to the video hardware.  This is necessary to
                    prevent flickering or blinking of the display on some
                    graphics adapters.
     NOBLINK   -CGE This command prevents the markers from blinking on the
                    "D"istance screen on some graphics adapters.  You may want
                    to use the MCOLOR command with NOBLINK to improve marker
                    readability.
     MCOLOR    -CGE MCOLORxxyy sets the colors of the Markers on the "D"istance
                    screen.  Marker 1 is set to xx, and Marker 2 is set to yy. 
                    For example, MCOLOR5962 sets Marker 1 to 59 (bright cyan)
                    and Marker 2 to 62 (yellow).
     SHOWCH    DCGE display screens as they are built.
     HIDECH    -CGE displays screens only after they are completed.  Not
                    compatible with SCREEN.
     PS2BUG    -CGE use if, with SHOWCH set, the display goes blank during
                    GEOCLOCK operation or after GEOCLOCK termination.  This
                    works around an error in the PS/2 VGA BIOS.
     NORAM     DCGE use if map display is trashed.  This option adds
                    approximately 25K to the memory required to execute GEOCLK.
     USERAM    -CGE use if there is insufficient RAM to run GEOCLOCK.  This
                    option moves the disk buffer to an area within the VIDEO
                    RAM.  Some EGA boards, including the ATI EGA wonder, are not
                    compatible with the DMA-s of some computers, and this option
                    will cause the display to be trashed or will cause disk
                    errors.  USERAM is also not compatible with the VGA and
                    SVGA, and may lead to map display errors.
     SHOWMN    -CG- displays the map number and name in the upper right hand
                    corner.  This data may overlap the latitude/longitude
                    display.
     HIDEMN    DCG- does not display map name and number.
     FULL      DCG- displays local location, time, and full ephemeris data.
     SUN       -CG- displays location, time, and sunrise/sunset data
     TIME      -CG- displays local date and time at bottom of screen.
     NONE      -CG- displays no text data at the bottom of the screen.



                                        - 11 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


     SUNANGLEx -CGE sets the elevation angle of the sun used to compute sunrise
                    and set.  The default is -0.8333 degree, corresponding to
                    the sun just breaking the horizon considering refraction
                    effects.  SUNANGLE-6.0 sets this angle to -6 degrees, which
                    defines civil sunrise and set.  -12 is Nautical sunrise and
                    sunset, while -18 is Astronomical sunrise and sunset.  This
                    parameter does not effect the terminator line calculations.
     SUNLIGHTn -CGE specifies the sun's elevation angle for the terminator.  The
                    default is 0, which corresponds to the geometric terminator. 
                    0.8333 corresponds to  apparent sunrise and sunset, when the
                    edge of the sun is just visible.
     TWILIGHTn -CGE specifies the  sun's  elevation angle  for  the twilight
                    terminator.  The default is 0.  -6.00 corresponds to civil
                    twilight, -12 corresponds to nautical twilight, and -18
                    corresponds to astronomical twilight.  If this angle is
                    greater than or equal to the SUNLIGHT parameter, the
                    twilight area is not displayed.  
     TLMASKn   -CGE the fraction (in 16ths) of halftoning for twilight display. 
                    8 is the default, which gives 1/2 light and 1/2 dark for the 
                    twilight area.  You may have to experiment with this value
                    to get the best display for your monitor.
     HAMDB     ---E loads the HAM call sign data base from file the named file. 
                    Only the first occurrence of this command in a GEOCLOCK
                    execution is effective (i.e., the data base will not be
                    reloaded or changed).  The HAM data base and other required
                    files are an extra cost option in GEOCLOCK.  See section H.
     HAM       -GCE activates the HAM features.  See section H.
     NOHAM     -CGE deactivates the HAM features.  See section H.
     SHOWMONTH -GC- displays the month name rather than number.  This command
                    can be followed by 12 character strings, which  specify the
                    names of the months.  The default names are the standard 3
                    character English abbreviations:
                    SHOWMONTH JAN FEB MAR APR MAY JUN JUL AUG SEP OCT NOV DEC
     NOMONTH   DGC- displays month number rather than name
     SHOWDAY   -GC- displays the day of the week.  This command can be followed
                    by 7 character strings, which specify the names of the days
                    of the week.  The default names are the standard 3 character 
                    English abbreviations:
                    SHOWDAY SUN MON TUE WED THU FRI SAT
     NODAY     DCG- does not display the day of the week.
     SHOWSEC   DCG- displays seconds.
     NOSEC     -CG- does not display seconds.
     YEAR4     -CG- displays 4 digit years (e.g., 1990)
     YEAR2     DCG- displays 2 digit years (e.g., 90)
     ZONE      --G- defines a time zone.  See section D.2.
     PCZONE    --G- defines the time zone the PC's clock is in.  See D.2.
     EQUINOX   -CG- allows the exact GMT of an equinox to be specified (e.g.,
                    EQUINOX 88/09/22 17:29).  This data is used to calibrate the
                    sun position calculation to improve the accuracy near the
                    equinoxes (while degrading it far from the equinoxes). 
                    Personally, I do not think this is a very good idea, but I
                    am tired of defending my position.  The current system
                    computes equinoxes within a few minutes.
     CSET      --GE allows the screen colors to be changed interactively.
     COLOR     -CGE COLORnxxyy changes screen color without interaction.  "n"
                    specifies the feature number (0- 7) to be changed.  Feature



                                        - 12 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


                    number n will display color xx, and feature n+8 will display
                    color yy.  Thus COLOR56262 will cause feature numbers 5 and
                    13 to display as 62 (bright yellow).  See Section G.2 for a
                    explanation of how color is used in GEOCLOCK.
     FAST      -CG- Forces GEOCLOCK to use a faster but slightly less accurate
                    algorithm for drawing the sunlit area.  This is the default
                    for systems without an 80x87.
     SLOW      -CG- Forces GEOCLOCK to use the high accuracy algorithm for
                    drawing the sunlit area.  This is the default for systems
                    with an 80x87.  On systems with an 80x87, the difference in
                    speed between SLOW and FAST is negligible, while on those
                    systems without an 80x87, FAST is approximately twice the
                    speed of SLOW.  These options do not effect polar projection
                    or azimuthal-equidistance maps.

     C.3.  Command line parameters

          Any of the commands (other than ZONE, PCZONE, CSET, DRAWLINE,
     DRAWCIRCLE, HAMDB, and INCLUDE) in section C.2 above may be entered on the
     command line that invokes GEOCLOCK.  These commands will be in effect when
     GEOCLOCK begins, and override commands placed in the GECONFIG.DAT file.

     D.    Customizing

          After the program has been extracted and is operating, you may wish to
     customize it for your computer.  The primary way to customize the program
     is through some special text files.  These files can be customized with any
     text editor.  GECONFIG.DAT describes your graphics system, defines the time
     zones, and gives the default setting for the program.  The GEOCLOCK.DAT and
     GEO<n>.DAT files specify the cities and time zones to be displayed with
     each map.  Sample GECONFIG.DAT and GEOCLOCK.DAT files are provided with the
     program, and you examine these examples to help you prepare your own custom
     versions.

     D.1.  Time zone data

          Time zones are user defined in GEOCLOCK.  Each zone (e.g., Eastern) is
     specified by giving its code name (e.g., ET), the names of summer and
     standard times (e.g., EDT and EST), the number of hours the time is ahead
     of GMT (e.g., -4 and -5), and the times between which summer time is in
     effect (e.g., ****88/04/24 8:00:00 GMT and 88/10/30 8:00:00 GMT).  The
     zones are referenced by their code names, and thus the zone data need only
     be updated once per year (sometime during the winter) and in only one place
     (where the zones are specified).  It is most convenient to include the zone
     specifications in the GECONFIG.DAT file.  If the ZONE commands are not for
     the correct year, GEOCLOCK will automatically update them by changing each
     date to the closest date in the correct year which falls on the same day of
     the week.  For example, 89/10/29 would change to 90/10/28, since both days
     fall on Sunday.  This update is not necessarily correct, and I recommend
     that the ZONE commands be kept current.

         The ZONE command takes 7 parameters: 1) a code name for the time zone
     (referenced by PCZONE, and GEO<n>.DAT files), 2) the name of the standard
     time, 3) the number of hours standard time is ahead of GMT (thus negative
     for US locations), 4) the name of the summer (daylight) time, 5) the number
     of hours summer time is ahead of GMT, 6) the date and time (GMT) to switch



                                        - 13 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


     from standard to summer time, in the format yy/mm/dd:hh:mm:ss, with
     trailing data optional (e.g., 88/10/30:8), 7) the date and time (GMT) to
     switch from summer time to standard time.  If a zone does not change during
     the year, the last four parameters may be omitted.  This command is best
     used in the GECONFIG.DAT file.

          The PCZONE command sets the relationship between the local time on the
     PC's clock and GMT, i.e., declares which time zone the PC's clock is in. 
     It takes one parameter - a time zone code, as defined in the ZONE command. 
     This command is best used in the GECONFIG.DAT file, and it must follow the
     ZONE command that it references.



     D.2.  Cities in GEOCLOCK.DAT and GEO<n>.DAT

          Cities may be overlaid on the maps.  They are specified in GEO<n>.DAT
     files.  For map number n (e.g., 2, the 48 states map), these cities are
     read from GEOn.DAT (e.g., GEO2.DAT) if that file exists.  If the file does
     not exist, cities are read from GEOCLOCK.DAT.
          The first entry in a GEO<n>.DAT file specifies the time zone code to
     be used for the standard time display.  It consists of a line with a single
     zone code.  If this line is omitted, the code for PCZONE is used. 
     Ordinarily, this code should match the time zone code for the first city in
     the file.
          Following this time zone entry, command line parameters may be
     optionally included.  The command line parameters will be processed after
     both the command line and the GECONFIG.DAT file parameters, and thus will
     override entries there.  The command REM may be used to add comments to the
     file.  
          Subsequent entries in the file specify the name and locations of
     cities to be displayed.  Each entry consists of the latitude, longitude,
     and name of the city.  Latitude and longitude may be in degrees and
     fractions (e.g., -15.35), with North and East positive, or degrees-minutes-
     seconds (e.g., 15d35S), with N S E and W specifying direction.  Most US
     locations have positive latitude and negative longitude.  The first city
     specified is used for calculating the sunrise, sunset, and the azimuth and
     elevation angles for the sun.

     D.3.  Default parameters in GECONFIG.DAT

          The GECONFIG.DAT file may be used to specify default setting and time
     information.  If you are using GEOMNO, the first four lines must be as
     written by the GEOCONVT program.  They give specification data for your
     graphics system.  Subsequent lines contain command line parameters.  There
     should be no leading spaces on these subsequent lines.  This file is
     processed BEFORE the command line parameters are executed, so the command
     line will override parameters specified here.  If you have a VGA or
     800x600, the VGA and SVGA commands should be in GECONFIG.DAT.

     E.    Functions for registered users only

          The following functions are available to registered users only.  See
     section K for details on how to register.

     E.1.  Zoom



                                        - 14 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20



          This function allows the user to change the map background using the
     cursor.  A mouse or the arrow keys can be used.  To invoke the function,
     press the letter Z.  The screen will be stabilize without any time or
     sunlight information, and an Iron-Cross type cursor will appear.  Use the
     mouse and/or arrow keys (shift-arrows move 8 times faster than non-shifted
     arrows) to locate a position on the map.  Each press of the right or left
     button on the mouse, or CONTROL or ALTERNATE keys, or Page-Up or Page-Down
     keys on the keyboard, will switch to a new map containing that point.  The
     left button "zooms in" while the right button "zooms out."  The cursor will
     remain at the specified latitude/longitude during the switch.  When the
     desired map is displayed, press the middle button or the ESCAPE key to
     return to time display.

     E.2.  Distance and Azimuth

            This function provides a display of the coordinates of three
     selected points, and the distances between them, as controlled by a mouse
     or the keyboard.  The function is invoked by pressing the letter D.  Point
     1 is selected by the left button of the mouse or the CONTROL key or Page-Up
     key on the keyboard.  Point 2 is selected by the right button or the
     ALTERNATE key or the Page-Down key.  Point 3 is the current cursor
     position.  To return to the time display, press the middle button or
     ESCAPE.  To maintain smooth cursor movement, the distance and coordinate
     displays are updated only when the cursor is not moving.  Pressing the "."
     key will display coordinates in degrees and fractions, while the "'" key
     will display coordinates is degrees, minutes, and seconds.  Pressing "A"
     will display the azimuth between the two points (the azimuth at the first
     toward the second, and the azimuth at the second toward the first, with
     North 0 and East 90) and the distance in kilometers, while pressing "D"
     will display the distance between the points in miles and kilometers.

     E.3.  Time display for cities

          For registered users only, additional control over city placement,
     color, size, and local time display is possible.  All are marked by
     characters appearing after an exclamation point (!) on a city line in
     GEO<n>.DAT.  This new data consists of an optional string of  characters as
     follows:

          A - show city name Above mark
          B - show city name Below mark
          L - show city name Left of mark
          R - show city name Right of mark (if none of above specified, use
     best)
          Y - show city name in color 5 (Yellow by default)
          E - show city name in 8x14 font (8x8 by default)
          number - show city name in color number (e.g., 6 shows city name in
     color 6).

          After these optional codes, the line may be optionally followed by a
     space and a time zone code.  If included, this specifies that the local
     time for that city is to be displayed to the right of the city name.  If a
     "*" is included, the name of the time zone will be displayed in addition to
     the time.  For example:



                                        - 15 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


                       ET
        38.90   -77.02  Washington !E
        42.65   -73.75  Albany NY !Y
        35.08  -106.65  Albuquerque NM ! *MT
        42.28   -83.75  Ann Arbor MI !A
        33.75   -84.39  Atlanta GA 
        44.30   -69.76  Augusta ME 
        33.52   -86.81  Birmingham AL ! CT
        46.80  -100.78  Bismarck ND !B *CT

     F.    Files

     F.1.  GEOCLKnn.ZIP

         GEOCLOCK.DOC   This file.
         GEOCLOCK.DAT   An example of a customization file for GEOCLOCK.  See
     section B.3 for the details of the contents of this file.
         GECONFIG.DAT   A starter for the configuration file for GEOCLOCK.  See
     section D for details.
         GEOCLK.EXE     GEOCLOCK version for EGA, VGA, and super VGA.
         MAP1.EGA       EGA database for MAP1 (world).
         MAP2.EGA       EGA database for MAP2 (48 states).
         MAP2000.EGA    EGA database for MAP2000 (North Polar Projection).
         MAILER.        Printer file to aid registration.

     Two other ZIP files are available to support GEOCLK for the VGA and SVGA. 
     VGA1-2.ZIP contains MAP4001 (VGA world) and MAP4002 (VGA 48 states). 
     SVGA1-2.ZIP contains MAP6149 (SVGA world) and MAP6002 (SVGA 48 states).

     F.2.  GEOMNOnn.ZIP

         README.MNO     Instructions for setup of GEOMNO.
         GEOMNO.EXE     GEOCLOCK version for two color graphics.
         GEOCONVT.EXE   Installation program to select drivers and font files,
     write configuration file, and convert maps to specific graphics format. 
     See section B.2 for instructions on the operation of this program.
         *.BGI          Various graphics drivers (Turbo Pascal 5.0).
         *.FON          Various font files.

     G.    Technical Information

     G.1.  Ephemeris Data and Accuracy.

         The ephemeris data in GEOCLOCK was derived by fitting two twelfth order
     polynomials to data from "Interactive Computer Ephemeris" (ICE).  One
     polynomial computes the sun's latitude, while the other computes the sun's
     longitude at noon GMT.  Both assume a 365.242199 day year.  They were made
     by a least squares fit to 400 points around 1990 data.  In this interval,
     the maximum and RMS latitude errors are 0.016845 and 0.004049 degrees,
     while the maximum and RMS longitude errors are 0.059805 and 0.016630
     degrees.  The fit has been tested against 1986 sun rise and set data, and
     with 1985 through 2000 spring equinox times, and is within a few minutes in
     time, but obviously there are no guarantees of the accuracy.  ICE is
     available on many astronomy bulletin boards, or from:

               Nautical Almanac Office



                                        - 16 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


               Code FA
               U. S. Naval Observatory
               Washington, DC 20392

         The terminator is shown as the locations where the sun's center,
     ignoring atmospheric effects, is a specified angle above the horizon.  For
     the default value of 0 degrees, the sunrise occurs earlier and the sunset
     occurs later than the terminator indicates.  The sun rise and sun set times
     are also computed as the times that the sun's center is a specified angle
     above or below the horizon.  The default value, -0.8333, corresponds to
     civil sun rise and set, where the visible edge of the sun just breaks the
     horizon.

          Some future version of GEOCLOCK may include the moon, planets, and
     artificial satellites.  This requires a few pascal routines that I just do
     not have the time to develope.  If anyone can help me with the routines
     below I will be grateful.


     {Global Variables that are set by other software }
     var
       JulianDate: real;  {Julian Date/Time, 
                           with 89/01/01 0:0:0 GMT = 16072.0000}
       SunZenithLatitude: real;  {geographic latitude of the sun at JulianDate}
       SunZenithLongitude: real; {geographic longitude of the sun at JulianDate}
     {Special Types}
     type
       ObjectType =    
     (Moon,Mercury,Venus,Mars,Jupiter,Saturn,Uranus,Neptune,Pluto);
       ElementType = record
         SatelliteName:       string;
         EpochTime:           real {JulianDate/Time};
         Inclination:         real {degrees};
         RAofNode:            real {Degrees};
         Eccentricity:        real {dimensionless};
         ArgOfPerigee:        real {degrees};
         MeanAnomaly:         real {degrees};
         MeanMotion;          real {revolutions/day};
         DecayRate:           real {revolutions/day/day};
         EpochRev:            integer {dimensionless};
         SemiMajorAxis:       real {kilometers};
         end;
     procedure SkyPosition( ObjectID: ObjectType;
                          var ZenithLatitude, ZenithLongitude: real);
     { returns the earth (not sun) latitude and longitude (not right
     ascension and declination) where the specified object is at Zenith.}

     procedure CalculateSatellitePosition( var Elements: ElementType;
                                           var Lat,Long,Alt: real);
      {Calculates the earth centered latitude, longitude, and altitude
       of the satellite described by "Elements" at time JulianDate.
       Lat" and "Long" are in degrees (East longitude positive), and "Alt"
       is in kilometers}


     G.2.  Use of Color



                                        - 17 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20



          The EGA graphics adapter provides for the simultaneous display of 16
     colors from a palette of 64.  Most programs use the default palette, which
     roughly corresponds to the colors provided by the CGA in text mode.  The
     EGA/VGA/SVGA version of GEOCLOCK does not use this standard palette.  The
     16 numbers specifying a color from the color palette are used to represent
     16 features displayed by GEOCLOCK.  The use of the 16 feature numbers is as
     follows: 

         feature       use            feature+8        use

            0    Political Bdy (dark)    8       Political Bdy (light)
            1    Water (dark)            9       Water (light)
            2    Land (dark)            10       Land (light)
            3    Land/Water Bdy (dark)  11       Land/Water Bdy (light)
            4    Text Background (dark) 12       Text Background (light)
            5    Aux Text Color (dark)  13       Aux Text and Sun (light)
            6    Lat/Long Lines (dark)  14       Lat/Long Lines (light)
            7    Frame and Text         15       Frame and Text

           The actual colors displayed are determined by the formula:
      color value = B + 2*G + 4*R + 8*b + 16*g + 32*r, where   
            B  = bright blue              b = dim blue
            G  = bright green             g = dim green
            R  = bright red               r = dim red

          Some typical colors are:
        name              RGBrgb      color value

        black             ------         0
        white             RGBrgb        63
        dark blue         -----b         8
        blue              --B---         1
        light blue        --Brgb        57
        dark green        ----g-        16
        green             -G----         2
        light green       -G-rgb        58
        brown             R---g-        20
        light yellow      RG-rgb        62      
        red               R-----         4
        bright red        R--rgb        60

     G.3.  Software structure

          GEOCLOCK is written entirely in Turbo Pascal version 5.0, except for
     the mouse interface routines and a few inline sections required for speed. 
     It has approximately 9000 lines of source code.  It uses 8 byte reals for
     most calculations, and thus relies on the 80x87 emulation package for
     systems without a math co-processor.  The EGA/VGA/SVGA version uses a
     custom graphics package which provides access to special hardware features
     (such as independent control of screen planes, disk I/O directly to the
     video memory, fast fill, and preserving the graphics memory during text
     display) that are not available in the EGAVGA.BGI driver.  The monochrome
     version uses the GRAPH unit, and builds a screen image in RAM before
     copying the image in its entirety to video memory.  The GRAPH unit
     functions other than PUTIMAGE are not used except for a few special



                                        - 18 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


     applications, such as drawing the graphics cursor, and updating the
     position and distance displays in the distance function.

     G.4.  Map Generation System

          The maps used for the GEOCLOCK program were produced by a custom data
     base and software system.  This system consists of a highly compressed
     vectorized map data base and a set of programs to convert the data into
     custom maps.  The data base is a PC conversion of World Data Bank II.  It
     contains approximately 5.7 million vectors covering coastlines, islands,
     lakes, rivers, and similar geologic features, together with political
     boundary data.  It covers the entire earth, and included features are
     accurate to approximately 600 meters.  World Data Bank II was converted to
     this custom PC format by an ad hoc program which took advantage of specific
     features of both data bases.  In its operational form, the PC data base
     uses approximately 0.84 bytes per vector, and in archival form takes
     approximately 0.5 bytes per vector.  The data base is therefore easily
     stored and manipulated on an AT class PC.

          Custom maps are generated by using two programs.  The first, MAPGEN,
     reads the appropriate parts of the map data base and produces separation
     files of the required feature data as EGA, VGA, or 800x600 raster images. 
     Rectangular, polar, azimuthal-equidistant, and Lambert projections may be
     used in forming these separation files.  Depending on complexity and scale,
     this process takes between 30 and 300 seconds on an AT with a co-processor. 
     The second, MOVIE, allows the user to process the separation files to
     select the features and colors for the final map, including filling areas. 
     This program also writes the map in a rasterized compressed format with
     headers and trailers so that it may be easily used as background data for
     other programs (for example, the GEOCLOCK program).

          Both these programs, and the converted data base, are proprietary and
     not yet available to the general public.  World Data Bank II is available
     from National Technical Information Center, Springfield, VA, for about
     $1000 on 5 reels of tape.

     H.    HAM add-in.

          An add-in package is available to provide special functions for HAM
     radio operators.  These functions include:

     Azimuthal-Equidistant (Great Circle) maps
     Twilight and terminator, or D and F layer illumination, display
     User Maintainable call sign data base.
     Remote station location
     short and long great circle path
     short and long path azimuth and range
     remote station (reciprocal) azimuth
     UTC, local, and remote station local time
     DXCC and WAE designations
     CQ and ITU zones
     Continent, area, and location names

          The package has three major components: a custom Azimuthal-Equidistant
     map centered on your HAM station; a call sign data base, and a utility



                                        - 19 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


     program to process the text call sign data base into the GEOCLOCK form.
     GEOCLOCK uses this data base to overlay HAM data on the custom map.

          The HAM package is available to registered GEOCLOCK users for $30,
     which includes your custom map.  Be sure to specify your GEOCLOCK
     registration number (or registration fee), and the latitude, longitude, and
     call sign of your station when ordering.  The HAM data base was developed
     by Eric Scace (K3NA), who was also invaluable in the design of the GEOCLOCK
     interface to the HAM functions.

     I.    Bulletin Board

         A free Remote Bulletin Board System (RBBS) provides support for users
     of the GEOCLOCK sunlight clock program.  It always has the latest and
     untainted version of GEOCLOCK available for downloading.  In addition, it
     provides a forum for all interested parties for program and information
     exchange concerning GEOCLOCK, high quality graphics for the IBM PC, high
     quality mapping for the IBM PC, and Turbo Pascal.  Information on potential
     applications and needs is as important as information on techniques and
     software.  The board is intended to help identify and solve real problems.
         Registered GEOCLOCK users have access to certain special files and
     higher access limits.  HAM package owners also have access to the latest
     version of the HAM data base.  Please have your registration number handy
     when you log on for the first time.  Except for these special files, the
     messages and files on the board are available to everyone.
         I also solicit comments and suggestions.  I am especially interested in
     including position and phase data for the moon and perhaps other planets.
         The RBBS number is 703-241-7980.  This is a Washington DC metro area
     number.

     J.    Upgrades and Enhancements for Registered Users

         The GEOCLOCK bulletin board always has the latest version of GEOCLOCK,
     and a variety of extra map files and utilities available.  In addition,
     many other bulletin boards and shareware distribution services carry the
     latest version of GEOCLOCK.  Registered users may obtain the latest version
     from any of these sources.  When a new version is released, replace the
     files you originally received with the new versions.  The REGISTER program,
     supplied on your distribution disks, must be rerun to enable the special
     features such as ZOOM and DISTANCE that are available only to registered
     users.  If you have customized any of the GE*.DAT files, you may want to
     use the old versions of these files, or to edit the new versions to reflect
     your specific requirements.

     K.    Registration and License

         The GEOCLOCK program is distributed as Shareware.  This means that
     prospective users may use the program for a short evaluation period before
     deciding whether to purchase it.  A license must be obtained to use any
     copy after this evaluation period.  By sending $30 to the address below,
     you will receive a single copy license, the latest version of the program,
     a registration program which will enable a few special features in the
     GEOCLOCK program not available in the evaluation version (see section E), a
     file with the name, latitude, and longitude of many world cities for
     building GEOCLOCK.DAT files, a "starter set" of GEO*.DAT files, and 28
     maps.



                                        - 20 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20



          The prices for the GEOCLOCK program are:

           1 copy              $30
           2-9 copies          $25/license
           10-20 copies        $20/license
           21-40 copies        $15/license
           site license        $600 for unlimited use at a single site.

          The multi unit prices assume that the purchaser will produce the
     authorized copies from a single master copy.

          GEOCLOCK is normally shipped on two 360K 5.25" floppy disks.  It is
     available on a 720K 3.5" floppy disk for an additional $5.00.  

          For an additional $20, a set of at least 15 supplemental maps will be
     included, and the next major release of the program will be mailed when it
     becomes available.  All these items are available for downloading at no
     charge from the GEOCLOCK support RBBS.  See section I.

          An add-in package for HAM operators is available for an additional
     $30.  This package includes a custom azimuthal-equidistant map centered on
     you HAM station, and a data base containing key call sign information.  Be
     sure to specify your call sign and station lat/long.  See section H for
     more details.

          Please add $5.00 for shipping and handling for destinations outside
     the US and Canada.  Cash or checks in US funds draw on US banks only.

          The file MAILER can be printed to give both a registration form and an
     envelope.

          Additional custom maps can be produced from my existing database for
     $30 per map.  Simply specify the latitude and longitude of the center
     point, and the north to south distance on the map (the map will be scaled
     so that distances and azimuths are correct in the center of the map), or
     the latitude and longitudes of the corner points.  Custom maps based on
     user supplied feature data or other projections (the GEOCLOCK program only
     uses flat rectangular, polar, and azimuthal-equidistant projections, but
     Lambert and perspective projections are available) are possible but must be
     negotiated on a case-by-case basis.



                                        - 21 -
     Joseph R. Ahlgren           GEOCLOCK version 4.2                   90/06/20


                                    Maps included with registration:

     MAP1    World                     MAP2    48 States
     MAP3    Eastern US                MAP4    SouthWestern US
     MAP5    Western Europe            MAP6    Alaska
     MAP7    New York City Area        MAP8    Finer Scale NYC
     MAP9    SouthEastern US           MAP10   NorthWestern US
     MAP11   Chicago Area              MAP12   Texas
     MAP13   Washington DC             MAP14   Carolinas
     MAP15   Pennsylvania              MAP16   New England
     MAP17   Central America           MAP18   South America
     MAP19   Africa                    MAP20   Australia
     MAP21   India                     MAP22   Middle East
     MAP23   Micronesia                MAP24   Japan
     MAP25   China                     MAP2000 North Polar Map           
     MAP2001 North Polar Map 45        MAP2002 South Polar Map
     MAP4001 VGA world                 MAP4002 VGA 48 states
     MAP6149 SVGA world                MAP6002 SVGA 48 states

                                    Maps included with optional supplemental
     disk:

     MAP26   North Central Europe      MAP27   Western Europe
     MAP28   North Central Europe      MAP30   San Francisco Area
     MAP31   USSR                      MAP32   North Atlantic
     MAP33   Scandinavia               MAP34   Highlands and Islands
     MAP35   Southern California       MAP37   Southern California
     MAP38   Sierra Nevada             MAP54   Canada
     MAP71   The Aegean Sea            MAP77   Silicon Valley
     MAP92   British Isles             MAP100  Switzerland
     MAP104  Prince William Sound      MAP131  Mexico
     MAP149  World Version 3  




                               Joseph R. Ahlgren
                              2218 N. Tuckahoe St
                              Arlington, VA  22205-1946