Chapter 1

                                  Introduction

     1.1  What is KAM-PRG?

     KAM-PRG is a terminal program that is specifically written to  support
     the  Kantronics All Mode Terminal Node Controller.   It was  developed
     using Turbo Pascal 5.0 and a set of Pascal units call Topaz.  KAM  not
     only  provides the terminal emulator but also has a full set  of  data
     base functions which allow the amateur operator to maintain his or her
     logbook and a set of NTS messages.  The data base are compatible  with
     the DBASE-III and FOXBASE products.

     KAM-PRG does not provide a WX-FAX (weather fascimili) interface.

     1.2 Flexibility
       -  KAM-PRG may be configured to function with either the COM1 or
          COM2 serial ports at speeds from 300 to 9600 baud.

       -  Fully configurable color selection, terminal screen layout, and
          file location are just a few of the adjustable parameters.

       -  Provides all of the common file handling functions of the popular
          communications programs including ASCII file transmit and re-
          ceive, screen buffer captures, and access to quick message lines
          by two key selection.

       -  Built-in help functions for the Q-signal system, the RST report
          system, and a FAST lookup database for prefix -> country conver-
          sions.

       -  Supports all modes, CW, AMTOR, RTTY, PACKET (VHF/HF).

     1.3 Ease of Use

       -  Function key <F1> help available at all times.  Direct access to
          desired functions from the help screen.

       -  Mode sensitive status and hot-key lines.  Keeps you informed as
          to the current condition of the KAM and the KAM-PRG system.

       -  Call List Database of frequently called stations for use in both
          HF and VHF packet modes.

       -  Fully scrollable receive buffer of 1000 lines.  Receive buffer
          may be written to disk file of users choice.

       -  Receive function operates independent of transmit buffer.  Create
          outgoing text while the other op' is transmitting.

       -  Dual cursor operation during transmit.  Normal cursor shows
          keyboard input, color highlight cursor shows current character




          being transmitted.  Particularly useful during CW operation.

       -  Removes operator from the cryptic TNC protocol language.  All
          change of mode transmit/receive, etc are handled by KAM-PRG.
          Operator makes selections by function key and Hot (alt) key
          combinations.

     1.4 Distribution of KAM-PRG

     KAM-PRG is public domain software.  It is intended that it serve as  a
     learning tool as well as a truly functional piece of software for the
     amateur  community.  The following conditions are place upon its  dis-
     tribution:
       -  KAM-PRG must be copied in its entirety.  That is, the distribu-
          tion must include the executable files, the documentation, and
          the Pascal source code.

       -  You may not sell or trade KAM-PRG for money or any valuable
          consideration, except for a nominal charge for postage, handling
          and reproduction.

       -  KAM-PRG may not be distributed in conjunction with any other
          product, hardware or software, without the express permission of
          Clermont Computer Consultants.

     Electronic Bulletin Board Systems, Public PC Users Groups, and Amateur
     PBBS systems may add KAM-PRG to their public domain libraries  subject
     to the conditions above.

     ShareWare  distributors may add KAM-PRG to their libraries subject  to
     the conditions above,  only after writing for and receiving my written
     consent.   It  must be prominently stated that 1)  KAM-PRG  is  Public
     Domain software, and 2) that the fee charged is for reproduction,  and
     mailing only.

     1.5  The most recent version of this software is always available from
     the author at:

               Clermont Computer Consultants
               29 N. Ravenwood Drive
               Cape May Court House, NJ  08210
               (609) 624 0076.

          A  reproduction,  distribution and small reward  for  programming
     excellence is requested.  Please send a check for $20.00 U.S. with any
     requests for updates.  If you are having trouble bringing KAM-PRG  on-
     line  I am usually available during the hours of 1700 -  2200  Eastern
     Standard  (Daylight  Savings)  Time.  Messages can be left  for  me  @
     WB2DRD.

     1.6  Disclaimer

     W1HKJ, David Freese and Clermont Computer Consultants make no  warran-
     ty, expressed or implied, concerning this program's merchantability or
     fitness for any particular use.  In no event is David Freese or  Cler-
     mont Computer Consultants liable to you for any damages resulting from
     your use of the program.




                                   Chapter 2

                          Getting Started with KAM-PRG

     2.1 System Requirements

     KAM-PRG has the following minimal requirements:

       -  IBM  PC, XT, AT, PS-2 or compatible with at least 320 K bytes  of
          memory.

       -  DOS 2.0 or later

       -  Two 360K disk drives, or a single 1.2M drive, or a single 720K  /
          1.44M drive, or a hard drive.

       -  Either COM1 or COM2 port available for serial communications.

       -  the  Kantronics All Mode Terminal Node Controller, running   ver-
          sion 2.83 or greater ROM software, or the Kantronics UTU-XT/P.

     2.2 Setting KAM-CFG up on a disk

     KAM-PRG is distributed as two self extracting ZIP files.

       1) KAMPROGS.EXE, and

       2) KAMSOURC.EXE.

     Place  a bootable system disk in drive A:, making sure that  at  least
     243K  of  free space is available on the disk.  Put  the  distribution
     diskette  (or downloaded program) in drive B:.  Log onto the  A  drive
     and type the following command:

          B:KAMPROGS

     The program will self-extract the required runtime files placing  them
     on drive A.

     2.2.1 Files include with KAM-PRG.

     The following files are included in the KAMPROGS.EXE archive:

      Length  Method   Size  Ratio   Date    Time   CRC-32  Attr  Name
      ------  ------   ----- -----   ----    ----   ------  ----  ----
      202560  Implode  93165  55%  12-09-89  20:23  df0fbeac --w  KAM.EXE
         863  Implode    422  52%  03-14-90  10:50  8efd2271 --w  KAM.CFG
       16000  Implode   2691  84%  12-02-89  14:50  6132f0f9 --w  KAM.IMG
       13849  Implode   4208  70%  11-30-89  02:08  2a14b601 --w  COUNTRY.LST
       10096  Implode   6165  39%  04-08-90  13:46  4d8b1fcc --w  KAMSETUP.EXE
      ------          ------  ---                                 -------
      243368          106651  57%                                       5

          KAM.EXE        Main KAM-PRG program file





          KAM.CFG        ASCII text file containing all configurable param-
                         eters with default values.

          KAM.IMG        Binary Image of all User and Help Screens used  by
                         the program.

          COUNTRY.LST    ASCII text file containing the Prefix/Country list
                         as found in the 1987 Call Book.  This file can  be
                         contracted or expanded as the user desires.  Place
                         new  entries in proper alpha-numeric sequence  and
                         strictly  observe  the line lengths  used  in  the
                         file.   The  On-Line prefix/country  display  will
                         automatically accommodate the new database.

          KAMSETUP.EXE   Use  this file if your KAM is brand new  from  the
                         factory,  or you have set the KAM parameter  ABAUD
                         to 0.  The KAM.EXE program expects to find the KAM
                         in a communicative mode.  That is, ABAUD has  been
                         set to agree with the baud rate parameter found in
                         KAM.CFG.   This  WILL NOT be true if ABAUD  is  0.
                         The program will lock up under this condition.

     The file KAMSOURC.EXE contains the following:

      Length  Method   Size  Ratio   Date    Time   CRC-32  Attr  Name
      ------  ------   ----- -----   ----    ----   ------  ----  ----
        2644  Implode    998  63%  11-26-89  15:39  2b04f39e --w  KAM-VID.PAS
        6854  Implode   1937  72%  11-26-89  17:13  3d2c9eda --w  KAM-RCV.PAS
        1245  Implode    443  65%  11-26-89  15:39  45d36083 --w  KAM-CLR.PAS
       18067  Implode   4195  77%  11-26-89  15:39  32907aed --w  KAM-SET.PAS
         520  Implode    227  57%  11-26-89  15:39  e3ffd06d --w  KAM-HLP.PAS
        9699  Implode   1942  80%  12-09-89  20:20  a2668ff0 --w  KAM-KBD.PAS
         965  Implode    544  44%  12-09-89  20:22  de69eaa3 --w  KAM-CON.PAS
        1865  Implode    697  63%  11-26-89  15:39  d81a41d8 --w  KAM-TYP.PAS
        4853  Implode   1738  65%  11-28-89  03:10  4338a238 --w  KAM-XMT.PAS
        3234  Implode    858  74%  11-26-89  15:39  aed37b1f --w  MAKIMAGE.PAS
       18125  Implode   4631  75%  12-09-89  20:16  bbc47022 --w  KAM-IO.PAS
        2226  Implode    666  71%  11-26-89  15:39  9b67e01a --w  KAM-DOS.PAS
       14196  Implode   4260  70%  11-26-89  18:59  48075b14 --w  KAM-LOG.PAS
       23933  Implode   6389  74%  11-26-89  19:17  dbf7a1c6 --w  KAM-NTS.PAS
        2279  Implode   1021  56%  11-26-89  15:39  6b203fda --w  KAM-VAR.PAS
        8673  Implode   2536  71%  11-26-89  17:13  eafa83e8 --w  KAM-AUX.PAS
        1743  Implode    948  46%  11-30-89  02:16  5a7e6cfb --w  KAM.PAS
         819  Implode    426  48%  11-30-89  02:21  ff54de17 --w  KAM-CLST.PAS
        1706  Implode    433  75%  11-22-89  17:26  97fe8030 --w  PRM-SCRN
        1796  Implode    734  60%  12-15-86  17:35  3607f576 --w  QSG-SCRN
        1944  Implode    531  73%  12-15-86  17:44  dcc5036f --w  RST-SCRN
        1864  Implode    733  61%  12-02-89  14:50  a8b364b7 --w  HLP-SCRN
       13849  Implode   4208  70%  11-30-89  02:08  2a14b601 --w  COUNTRY.LST
       16199  Implode   4312  74%  04-08-90  13:35  1b35cca5 --w  KAMSETUP.PAS
      ------          ------  ---                                 -------
      159298           45407  72%                                      24




     These  files  are written in Turbo Pascal version 5.0  and  use  Topaz
     units sold by

          The Research Group
          100 Valley Drive
          Brisbane, CA 94005
          (415) 571-5019

     These  units are necessary to compile and link the source code.   They
     provide the DBASE interface functions of KAM-PRG.




     2.3  First-time SetUp of KAM-PRG

     Before  executing the program, you should prepare the KAM.CFG file  to
     be  compatible with your DOS environment.  Open the KAM.CFG file  with
     your non-document editor and modify the lines as follows:

          PARAMETER           PRESET VALUE        COMMENT

          Xmt background .....    1     background color for transmit
          Xmt foreground .....   15     foreground color for transmit
          Rcv background .....    2     background color for receive
          Rcv foreground .....   14     foreground color for receive
          Status background ..    7     background color for status line
          Status foreground ..    4     foreground color for status line
          Prompt background ..    4     background color for data prompts
          Prompt foreground ..   15     foreground color for data prompts
          Aux background .....    3     background color for auxiliary
          Aux foreground .....    0     foreground color for auxiliary
          Help background ....    2     background color for help screen
          Help foreground ....   15     foreground color for help screen
          Status_line ........   18     line # for status line position
          Rcv_start_line .....    2     line # for beginning of receive
          Rcv_end_line .......   17     line # for end of receive
          Aux_line ...........    1     line # for auxiliary status info
          Xmt_start_line .....   19     line # for beginning of transmit
          Xmt_end_line .......   24     line # for end of transmit
          Transmit port ......    1     1 = COM1, 2 = COM2
          Interface baud rate. 9600     communications rate in baud
          Packet MARK freq.... 2125     MARK for HF Packet/RTTY/AMTOR
          Packet SPACE freq... 2295     SPACE for HF Packet/RTTY/AMTOR
          CW Xmt WPM .........   24     Initial CW code speed
          CW turn-off delay...    1     wait 1 second
          Xmt turn-on delay...    2     # of milliseconds between transmit
          Xmt turn-off delay..   50     on/off, used by RTTY and AMTOR
          Time Zone ..........0         GMT = 0, etc.
          Initial msg file ...normal.msg     ie: C:\HAM\BUFFERS\NORMAL.MSG
          Log Path/File.......hamlog             C:\HAM\LOG\1990LOG
          NTS database file...HAMGRAM.DBF        C:\HAM\NTS\MESSAGES
          HF switch char .....]         Packet select character for HF/VHF
          VHF switch char ....[         communications (see KAM STReamsw)

     The KAM TNC is capable of communicating with the host computer at 9600
     baud and I recommend you use that rate.  The actual on-air PACKET baud
     will  be 300 on HF and 1200 on VHF/UHF.  Bit rates for RTTY and  AMTOR
     are selectable during program operation.

     2.4 Initial Set Up of KAM TNC.

     Turn the KAM and your computer off.  Connect the two using the config-
     ured  communications  port.  Connect the KAM to your  HF/VHF  gear  in
     accordance  with  the KAM instruction manual.  I  recommend  beginning
     with  the VHF/UHF equipment.  Then proceed to bring up the HF gear  in
     the  following  modes  (increasing order of  complexity):   CW,  RTTY,
     PACKET, AMTOR.





     Turn your computer on and boot it using DOS 2.0 or later.

     Make  sure that the KAMSETUP.EXE and KAM.CFG are both in  the  default
     directory.   Execute the program KAMSETUP.EXE.  The  following  prompt
     will appear:

       This program should only be used to initialize a factory fresh KAM,
       or one which as been configured to ABAUD = 0.  This can occur by
       software reset, or internal KAM hardware reset (for example: when
       a ROM update has been installed.

       Do you wish to continue? <y/n>

     Press 'Y'

       Attempting to set KAM via com port 1  to baud rate 9600
       Operation may take several seconds to finish.
       Press any key to abort.

     If the program performs correctly it will give the final message:

       KAM has been permanently set to 9600.

     and conclude.

     2.4.1     Alternate Set Up Procedure

     Using PROCOMM, BOYAN, MIRROR or some other general purpose  communica-
     tions program.

     Turn the KAM off.

     Bring  your  communications program on-line at the desired  baud,  for
     example 9600.

     Turn  the  KAM on and wait for a readable message to  appear  on  your
     screen.  Immediately press the asterisk '*'.  The KAM will now be  set
     to the same baud as the computer.  This is only temporary however.

     Type the following commands into the KAM.

          ABAUD 9600      ( or the configured baud)
          PERM

     This sets the KAM to desired baud and makes that a permanent  setting.
     You may reset this by using ABAUD 0, or by hardware reset (internal to
     the KAM).

     2.5  On-Line Help. -  You may obtain help on the main function key and
     hot-key  usage by pressing <F1>.  Subsequent function key  or  hot-key
     may be pressed from the help screen to immediately enter that mode  or
     function.




                                   Chapter 3

                         Main Display & Operating Modes

     3.1  Main Display

     3.1.1   The  main  display consists of a transmit  window,  a  receive
     window and three information bars.  The default configuration for  the
     windows and information bars is:

          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³                 Auxiliary Status Bar                     ³
          ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
          ³                                                          ³
          ³                     Receive window                       ³
          ³                                                          ³
          ³                                                          ³
          ³                                                          ³
          ³                                                          ³
          ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
          ³                     Main Status Bar                      ³
          ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
          ³                                                          ³
          ³                                                          ³
          ³                     Transmit Window                      ³
          ³                                                          ³
          ³                                                          ³
          ³                                                          ³
          ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
          ³                    Program Usage Bar                     ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     3.1.2   Auxiliary Status Bar - This line is used to display  auxiliary
     information and prompts when required.  It normally shows the name  of
     the  file from and to which the one-line message buffers are  read  or
     written.   (see  the KAM.CFG file).  When a program  element  requires
     operator input, such as the name of a file, it will usually appear  in
     the auxiliary status bar in a unique color.

     3.1.3   Receive Window - This multi-line window will contain the  most
     recently  received  data.  It is a true window onto a 1000  line  text
     buffer.   In  the CW, AMTOR, RTTY and ASCII modes  it  performs  word-
     wrapping  so  that the incoming text is easier to  read.   The  entire
     buffer is available for review.  This may be accomplished by  pressing
     the  PAGE-UP key.  Note that doing so will change the Main Status  Bar
     information.

     3.1.4  Main Status Bar - The left hand portion of the main status  bar
     always  indicates the present mode of operation for both the  KAM  and
     KAM-PRG.   The right hand portion of the status bar shows the  present
     date  and time properly computed to Greenwich Mean Time (if  the  time
     zone parameter is set to a non-zero value in the KAM.CFG file).

     The  center portion of the main status bar shows information which  is




     dependent on the KAM-PRG operating mode.  In the HF/VHF PACKET mode it
     contains  the  signal 'Call:' possibly followed by  a  callsign.   The
     callsign  shown will be the most recently selected from  the  CALLSIGN
     list.

     In  the CW, AMTOR, RTTY and ASCII modes the center portion will  indi-
     cate  whether  the  unit is RECEIVING or  TRANSMITTING.   Whether  T/R
     switching is being performed automatically or manually, and a reminder
     that  the  control-T,  and control-R keys are used to  switch  in  the
     manual mode.

     3.1.5  Transmit Window - The transmit window is a multi-line  scrolla-
     ble  area for entering transmitted text.  When transmit data is  taken
     from  either external files or from one of the 10 transmit buffers  it
     is  shown sequentially in the area.  During low  speed  transmissions,
     such as CW and RTTY, two cursors are maintained.  The first is at  the
     place  of  next  character entry.  The second is  over  the  character
     presently  being transmitted by the KAM.  This allows the operator  to
     type  ahead  and still be aware of the outgoing data stream.   If  too
     many lines of text are entered ahead of the transmit cursor, text will
     be  lost  off the top of the window.  IT IS NOT lost to  the  transmit
     buffer  stream.  The transmit position cursor will disappear and  then
     re-appear  when the it reaches visible text.  This will probably  only
     be apparent when transmitting a long text file in the CW mode.

     3.1.6  Program Usage Bar - A one line text area which gives the opera-
     tor  some  quick hot key information relating to the current  mode  of
     operation.  Please note that this is not all inclusive and a  complete
     set of hot key combinations is always available by pressing <F1>,  the
     help key.

     3.2  Operating Modes

     3.2.1   KAM-PRG  properly interfaces with the KAM in  the  CW,  AMTOR,
     RTTY, ASCII, HF-PACKET, and VHF-PACKET operating modes.  It provides a
     layer of isolation between the operator and the KAM control  language.
     This isolation is particularly beneficial in CW, AMTOR, ASCII and RTTY
     modes as it allows the operator to concentrate on the QSO and not  the
     control  language.   It is frustrating to have to look  up  a  desired
     control  language sequence in the middle of a QSO.  Mode selection  is
     make by alternate-M activation.

     3.2.2  Changing Operating Mode.  Press the <alternate-M> key  combina-
     tion.   This brings up a window containing a list of available  modes.
     Select  the  desired mode.  It may take the program a few  seconds  to
     make the transition to the new mode.  This is due to clearing the  KAM
     buffers from the previous mode.

     3.2  VHF-PACKET Operation

     VHF-PACKET is the default mode for KAM-PRG.

     VHF-PACKET  operation  is indicated by the words "KAM PACKET"  on  the
     left  hand  side of the main status bar.  Hot key commands  which  are




     specific to the packet mode are indicated on the program usage bar:

     ALT <D>is<K>onnect  <L>calllist <H>f <V>hf <I>id <Z>cmd <X>exit <F1>help

     The  alt<K> and alt<D> commands are specific to the callsign shown  in
     the  center of the main status bar.  A packet callsign must appear  in
     that location for these commands to be effective.

     The  alt<L>  calllist command brings up a browse window  access  to  a
     dbase  III  file containing information relevant  to  commonly  called
     stations.

     Alt<H> and alt<V> all switching between the HF and VHF radios.

     Alt<I> forces an identification packet to be immediately sent.

     Alt<Z>  is  used  to return to the 'cmd:' mode when in  a  connect  or
     converse  mode.  This key combination is used as KAM-PRG captures  all
     control-C key sequences.

     Alt<X> is use to exit KAM-PRG in all modes of operation.  The operator
     is given a second chance if the alt<X> is accidentally pressed.

     Function key <F1> always brings up a help screen

     3.3 HF-PACKET Operation

     All HF packet operations are identical to VHF.

     3.4 CW Operation

     CW Operation is indicated by the following main status bar:

     CW    24 xmt,    24 rcv       RECEIVE  MAN  T/R           date  time

     The  default CW wpm given in the KAM.CFG will always be  the  starting
     transmit  and receive code speed.  The program will begin in  the  re-
     ceive  mode, and use manual switching between send and  receive  func-
     tions.

     In  both  manual and automatic mode, the operator may  type  into  the
     transmit buffer as fast as convenient.  If the CW wpm is set to 24 and
     the  operator can type at 60 wpm, he or she will easily keep ahead  of
     the  outgoing code.  The transmit buffer is 1024 characters  long,  so
     you do not need to worry about overflow.

     3.4.1  Manual Operation

     The  control-T key combination acts as transmit/receive toggle.   Type
     your outgoing text into the transmit buffer.  When ready to  transmit,
     turn the transmitter on using the control-T toggle.  You may pause the
     transmission at any time with the control-P combination.  This is also
     a  toggle.  To return to transmit, press control-P a second time.   If
     you  wish to abort the transmission before the end of text is  reached




     press the control-T combination.  Notice that the character  currently
     be  transmitted  is  highlighted by either a reverse  video  or  color
     unique cursor.

     You may continue to enter text while characters are being transmitted.

     3.4.2  Automatic Operation

     Transmit/receive switching can also be made automatic.  The alt<A> key
     combination is used as a toggle to switch between the two modes.  This
     will  be indicated by MANUAL being replace by AUTO on the main  status
     bar.

     In automatic CW operation the transmitter will be turned on immediate-
     ly upon entering new text into the transmit buffer.  It will remain on
     so long as new text is continued to be entered.  Characters will begin
     to  be sent immediately.  The "CW turn-off delay" in the KAM.CFG  file
     determines the time delay before inactivity returns the program to the
     receive mode.  The default is 1 second.  If you are not a power typist
     this may be too short.  Beware that in the automatic mode you will  be
     chased  by the 'rabbit' as my friend KB2FJ likes to say.  Its best  to
     be a good typist in this mode.

     3.4.3  CW Prosigns

     The  Program  Usage Bar shows the characters used for the  special  CW
     prosigns:

               AS  %

               AR  +

               BT  =

               SK  #

               KN  (

     3.5  Radio TeleTYpe (RTTY) Operation

     This mode is indicated by the following on the main status bar:

     RTTY   45 baud,  170 shift      RECEIVE  MAN  T/R

     Automatic  and manual switching is possible between transmit  and  re-
     ceive and is accomplished identically the same as in the CW mode.  The
     pause function is also available.

     3.5.1  Selection of new BAUD

     Alternate  <B> is used to select a new BAUD from a rotating  table  of
     entries.  As each new BAUD is selected it is so indicated by the entry
     on  the main status bar.  Changing BAUD may take a second or  two  de-
     pending on the state of the KAM at the time of change.





     3.5.2  Selection of new SHIFT

     Alternate  <S> is used to select a new SHIFT from a rotating table  of
     entries.   As  each new SHIFT is selected it is so  indicated  by  the
     entry  on  the main status bar.  This also may take a  second  or  two
     depending on the KAM state at the time of change.

     3.5.3  INVERT / NORMAL

     Most  amateur  RTTY transmissions on the HF bands with  the  following
     convention:

                         LOWER SIDEBAND SIGNAL

                    ³              ³                   :
                    ³              ³                   :
                    ³              ³                   :
                    ³              ³                   :
               ÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄ
                  SPACE          MARK              SUPPRESSED
                  2295           2125                CARRIER

     For example, the carrier might be at 14.1000 MHz, the MARK at 14.09788
     MHz  and  the SPACE at 14.09771 MHz.  NOTE that LSB is  usually  used.
     Some  stations will operate on the opposite sideband for various  rea-
     sons,  not the least of which is to avoid interference in a  congested
     band.

     You may still communicate with these stations without having to switch
     sidebands and re-tune their signal.

     Alternate  <I> is used to set the KAM to the RTTY INVERT  mode.   MARK
     and  SPACE signals are reversed before decoding in the KAM.  The  same
     reversal takes place on transmit.

     3.5.4  Tuning in RTTY signals.

     If you are new to the world of RTTY you may at first find it a  little
     difficult to get good reception.  Here are some hints.

          o    always  begin with the BAUD at 45 and the SHIFT at  170  Hz,
               put the KAM in the NORMAL position.

          o    tune across the incoming signal until the KAM LED bar  graph
               shows  a full deflection of the signal across the  MARK  and
               SPACE regions.

          o    if  proper  decoding does not take place  try  toggling  the
               INVERT/NORMAL function.

          o    next begin increasing the BAUD one at a time, repeating  the
               first three steps above for each selection.

          o    finally change the SHIFT one at a time, repeating the  first
               four steps above for each selection.

     You will soon learn to recognize a BAUD and SHIFT by its tuning  char-
     acteristics  and peculiar sound.  It won't take long before you  start
     'hearing' CQs and RYs.




     Most  RTTY operation of 40 - 10 meters is at 45 or 50 BAUD and 170  Hz
     SHIFT.   LSB (or NORMAL) is also the most common on those bands.   You
     will  most likely hear the old 850 Hz SHIFT on the 80 meter band.   It
     also seems that is where most of the mechanical RTTY'rs hang out.   My
     experience on 20 meters is that most are running a computer and a  TNC
     of some sort.

     3.5.5  RTTY Courtesies

     You  are  the proud owner of a fine IBM or Clone or  you  wouldn't  be
     using  this program.  Not all folks have your nice wide  80  character
     screen.   There  are a lot of RTTY operators  (particularly  overseas)
     that  use  C-64 computers with 64 character wide  screens.   The  last
     character  in the INVERT (or NORMAL) indicator is at the 60  character
     point  in your text.  When you reach that point, hit the ENTER key  to
     force a CR/LF pair.  That way you will keep the other OPs screen  from
     becoming cluttered.

     Operate  on RTTY the same way you would on CW.  Give  brief  exchanges
     without a lot of flourishes.  You can save some typing time by  trans-
     mitting an ASCII file or a sequence of buffers.  Use these for station
     data,  and personal particulars.  But please don't use wasteful  lines
     of  asterisks, equal signs, plus signs ad-nausium.  I'm not  interested
     in  your  artistic talents, I'm interested in you.   Spend  more  time
     telling me about yourself, about the last good book you read, or where
     your going on your next vacation.

     Most  RTTY  operators send both the other and their own  callsigns  on
     every transmission.  TOTALLY UNNECESSARY!  The 10 minute rule applies.
     If  you  really feel that you must id.  Just send the   DE  W1HKJ  for
     example.  That should suffice.

     RYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRYRY

     You  may see that appear on your screen quite often.   Some  operators
     also  think that looks very pretty on every transmission.  I  have  it
     loaded  up in one of my transmit buffers.  But only send it  when  re-
     quested to do so.  It's a carry over from the days when everyone  used
     mechanical RTTY machines.  Not all of the machines were synced to  the
     same a.c. line frequency, and the RY line gave the receiving station a
     chance to re-sync the machine.  Again in the days of computers this is
     not necessary.

     3.6  ASCII Operation

     This mode is indicated by the following on the main status bar:

     ASCII  110 baud,  170 shift     RECEIVE  MAN  T/R   NORMAL  date time

     All operations in this mode are the same as for RTTY.

     3.7  AMTOR Operation

     This mode is indicated by the following on the main status bar:

     AMTOR Listen Only            RECEIVE MAN  T/R       date time

     and the Program Usage Bar:

     ALT <K> call station  <L> listen mode  <A> A/B mode  <B> FEC mode B




     3.7.1  Receiving an AMTOR CQ.

     With the program in the AMTOR Listen mode, tune across the band  look-
     ing  for  signals in the same way your would while tuning  RTTY.   The
     AMTOR  CQ  signal is sent in FEC mode B.  This mode is  100  BAUD  and
     sounds much higher pitch and more continuous than RTTY.

     On  20 meters you will find AMTOR commonly between 14.068  and  14.080
     MHz.  RTTY between 14.080 and 14.100 MHz and HF PACKET between  14.100
     and 14.110 MHz.

     The  calling station will usually end the transmission  by  announcing
     the SELCAL (selective call) to be used in connecting to the station.

     3.7.2  Connecting to a station calling CQ.

     Press the alt<K> key combination.  A prompt will appear requesting the
     SELCAL to be use for the connect.  Enter the other stations SELCAL and
     press  ENTER.  The KAM will immediately go into a calling mode.  If  a
     connect  is  made it will be indicated by both the  CON/LOCK  and  the
     STA/VAL LEDs being lit.  Your transmitter will also be rapidly switch-
     ing  between the transmit and receive modes.  You MUST HAVE  A  MODERN
     transceiver or transmitter/receiver combination to operate AMTOR.  The
     required  switching  times are very short and this mode very  hard  on
     older equipment with slow relays.  I operate my KENWOOD 440 in all KAM
     modes with not difficulty.

     3.7.3  Calling CQ in AMTOR.

     Press the alt<B> to put the KAM in the FEC mode B.  Type several lines
     of CQ.  I suggest the following format


          CQ CQ CQ CQ DE W1HKJ CQ CQ CQ DE W1HKJ (WHKJ)
          CQ CQ CQ CQ DE W1HKJ CQ CQ CQ DE W1HKJ (WHKJ)
          CQ CQ CQ CQ DE W1HKJ CQ CQ CQ DE W1HKJ (WHKJ) KKK

     Press  alt<A>  to put the KAM in the A/B mode.  This is  the  required
     mode to allow another station to make the connect.

     3.7.4  Reversing the connect

     In  AMTOR  the  role of 'sending' and 'receiving' is made  by  a  very
     simple protocol.  When you are ready to turn the QSO over to the other
     station  you do so by typing a '+?' at the end of the line.   The  KAM
     takes care of the T/R function.

     3.7.5  AMTOR disconnect

     You may disconnect by pressing the alt<L> to put the KAM back into the
     listen mode.  Don't do so without first indicating your intent to  the
     other station (courtesies).  It is usual for the CONNECTING station to
     also be the DISCONNECTING station, but it is not necessary.




                                   Chapter 4

                                Transmit Buffers

     4.1   Ten transmit buffers are available for quick insertion into  the
     transmit data stream.  These buffers are read from and written  to the
     file NORMAL.MSG unless otherwise configured in KAM.CFG.  Function  key
     <F5> is used for all transmit buffer maintenance.

     4.2   Transmitting  a buffer - Select a transmit buffer by  using  the
     alternate key combined with a number key.  For example: buffer  number
     3 is inserted into the transmit stream by pressing alt<3>.

     4.3  Viewing and Modifying Buffers - Access to the buffers is made  by
     pressing  <F5>.   The transmit/receive screen is replaced  by  a  data
     access  screen.   The ten buffers are each 80 characters  long.   Each
     buffer  is accessed by using the up and down arrow keys.   The  buffer
     which  can be modified is highlighted.  You can type into  the  buffer
     using   wordstar   entry  keys.   Press  <ESC>  to   return   to   the
     transmit/receive screen.

     4.4  Saving the Buffers - Press alt<F5> to save the buffers to a file.
     You will be prompted for the filename.  The default will be that given
     in the KAM.CFG file.

     4.5   Reading  a Buffer File - Press shift<F5> to read  a  new  buffer
     file.   You  will be prompted for the filename.  The default  will  be
     that given in the KAM.CFG file.

     4.6  Modifying the buffer file directly - Each buffer file is a simple
     text  file  containing ten lines where each line does  not  exceed  80
     characters.   You may modify the file using a text editor.  Make  sure
     that the editor treats the file as a non-document.

                                   Chapter 5

                               File Transmission

     5.1  Plaintext (ASCII) files can be transmitted in any mode.  The file
     to  be transmitted is opened by pressing function key <F7>.  You  will
     be  prompted  for  a filename.  Use this method  to  transmit  station
     information  or other data that is too large to fit into the  transmit
     buffers areas.

                                   Chapter 6

                                 Receive Buffer

     6.1  The receive buffer in KAM-CFG consists of 1000 lines of 80  char-
     acters each.  The receive window only shows the last several lines  in
     the buffer.  Access to the entire receive buffer can be made by press-
     ing  the Page-Up key at any time.  The receive window will  then  show
     the  receive  buffer beginning with the first line of  text  received.
     Movement  through the buffer is made with the up and down arrow  keys.
     When   you  are  finished  press  <ESC>  to  return  to   the   normal
     transmit/receive screen.

     6.2  Saving the Receive Buffer - Function key <F6> is used to save the
     receive  buffer.  You will be prompted for a filename with  a  default
     given.




                                   Chapter 7

                                 Data Base Use

     7.1  KAM-PRG uses and maintains three distinct data base files:

          DEFAULT NAME             USE

          HAMLOG.DBF     DBASE-III compatible file provides full log  keep-
                         ing functions using a pop up menu.

          HAMGRAM.DBF    DBASE-III  compatible file containing  a  complete
                         message generation and storage system.

          COUNTRY.LST    ASCII text file containing cross reference data of
                         Prefix  to  Country.  Much faster than  using  the
                         callsign book.

     7.2  LOG BOOK DATA FILE

     HAMLOG.DBF  is the default log book file.  You may alter the log  name
     in the KAM.CFG configuration file.  This file is a DBASE-III  compati-
     ble file containing the following data dictionary:

          FIELD NAME     TYPE      SIZE

          CALLSIGN       CHAR      9
          NAME           CHAR      10
          DATE           DATE      10
          TIME           CHAR      5
          FREQ           NUMBER    10:5
          POWER          NUMBER    4
          MODE           CHAR      3
          RST_OUT        CHAR      3
          RST_IN         CHAR      3
          COMMENT        CHAR      30
          QSL_SENT       DATE      10
          QSL_RCVD       DATE      10

     7.2.1   HAMLOG  INDEX FILES - Two index files are  maintained  by  the
     logging  procedures.  A DATE-TIME index and a CALLSIGN  index.   These
     index files are NOT Dbase compatible.  If you modify (add, delete,  or
     sort)  the HAMLOG.DBF file using DBASE, FOXBASE or some other  general
     purpose  data  base program the INDEX files will  be  corrupted.   The
     index files have the filename HAMLOG.DTM and HAMLOG.CLL.  If the index
     files  become corrupt - DELETE the files at the DOS prompt.  The  pro-
     gram will automatically rebuild the index files the next time you  run
     it.




     7.2.2   Accessing the Data Base - Function key <F10> will bring  up  a
     pop-up window over the lower half of the screen.  The form shown is :

   Ú´Index [ callsign ] ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
   ³Record #        of          File                Last Update :            ³
   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
   ³Callsign         ³Name               ³Date             ³Time             ³
   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
   ³Freq             ³Power    |Mode     ³RSTout           ³RSTin            ³
   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
   ³Comment                              ³QSLsent          ³QSLrcvd          ³
   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
   ³Next Prev Top bOttom Go  Find Edit  Add  Del  Browse  paCk  Index  Quit  ³
   À´<F1> = HelpÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     7.2.3  A new database will always be initialized with a blank record
     as the first record.  To record your first log entry use the EDIT
     function.  For subsequent records use the ADD function.  Context
     sensitive help is available by pressing <F1>.  If you are at the
     initial data base form the help will describe each of the available
     functions.  If you are in the middle of making a field entry, the help
     will describe the keystrokes for inserting text, deleting text, over-
     laying text, etc.

     7.2.4  Pressing <I> for index will toggle the index between callsign
     and date-time.  The date-time is the default index and the last entry
     in the log book will be the one shown on initial entry via <F10>.

     7.2.5  The <F>ind function performs the search based on the index
     selected.  I usually use this to find a previously worked callsign.
     My log now has over 2000 entries covering a period of three years.
     Finding a previously worked station is instantaneous!

     7.2.6  <B>rowsing through the database.  Press <B> to bring up a
     browse window in the upper half of the screen.  Use the up and down
     arrow; or Page-Up / Page-Down keys to move through the data base.
     When a desired entry is highlighted press <ESC>.  The highlighted
     entry will now be the one which appears in the data base entry form.

     7.2.7  Return to the main transmit/receive screen by pressing <Q>uit.




     7.3  NTS MESSAGE DATA FILE

     7.3.1 KAM-PRG maintains a data base of NTS messages which have been
     transmitted.  These messages are in a DBASE-III compatible file with
     the following data dictionary:

          DATA FIELD     TYPE      SIZE

          MSG_NBR        C         4
          PRECEDENCE     C         1
          HANDLING       C         1
          HANDL_EXT      C         5
          STATION        C         10
          ORIGIN         C         15
          FILE_TIME      C         4
          FILE_MONTH     C         3
          FILE_DAY       C         2
          ADDRESSEE      C         25
          ADDR1          C         25
          ADDR2          C         25
          CITY           C         25
          STATE          C         2
          ZIP            C         5
          PHONE          C         13
          TEXT_1         C         65
          TEXT_2         C         65
          TEXT_3         C         65
          TEXT_4         C         65
          TEXT_6         C         65
          SIGN           C         25
          SIGN_ADR1      C         25
          SIGN_ADR2      C         25
          SIGN_CITY      C         25
          SIGN_ST        C         2
          SIGN_ZIP       C         5
          SIGN_PHN       C         13

     7.3  NTS Data Base Access - Press the hot key alt<N> to access the NTS
     data base.  The transmit/receive screen will be replaced with a data
     entry form which relates directly to the NTS message format.  The last
     message sent (or a blank message for a new data base) will be in the
     fields.

     7.3.1 Data entry and movement through the data base is very similar to
     making log book entries.  The main difference is that prompts and
     selectable data entries are provided.  The casual preparation of an
     NTS message does not require much of a learning curve.  The word count
     is performed automatically.




     7.3.2 Data Entry Format:

         ÚÄ´ 1 of  1 ÃÄÄ´HAMGRAM.DBFÃÄ´04/14/90ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ Nbr  P   Handling Inst  OrigSta  Place of Origin  Time Mon Day  ³
         ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
         ³            HX                                                   ³
         ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
         ³    To:                             Phone #                      ³
         ³                                                                 ³
         ³                                                                 ³
         ³                                                                 ³
         ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
         ³                                                                 ³
         ³                                                                 ³
         ³                                                                 ³
         ³                                                                 ³
         ³                                                                 ³
         ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
         ³   From:                            Phone #                      ³
         ³                                                                 ³
         ³                                          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
         ³                                          ³Word Count :          ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
      N)ext P)rev T)op b(O)t G)o S)rch E)dit A)dd D)el B)row Pa(C)k W)rite Q)uit
                                  <F1> for HELP


     7.3.3 Writing the message to an ASCII file.  Pressing the <W> select
     key will write the message in NTS format to a file name MSGnnnnn where
     nnnnn is the assigned message number in the data entry form.

     7.3.4  Return to the transmit receive screen by pressing <Q> for quit.

     7.3.5  The file MSGnnnnn may now be sent as a plain text file trans-
     mission.

     7.4 COUNTRY LIST

     7.4.1 The file COUNTRY.LST is an ASCII file with the following format:

          PREFIX         COUNTRY

          AA-AL.......United States of America
          AP..........................Pakistan
          A2..........................Botswana
          A3.............................Tonga
          A4..............................Oman

     where each line may contain no more that 36 characters.

     7.4.2  Accessing Prefix/Country list - Press function key <F9> to
     bring up a pop-up scrollable window of the prefix to country list.

     7.4.3  Quick location of a prefix can be obtained by pressing the
     first letter of the prefix.




     7.4.4 The file can be maintained using a non-document editor.  Be
     certain to observe the limitation of 36 characters per line.  You
     should also maintain the alpha-numeric sort of entries.  Adding or
     deleting lines will not effect the <F9> operation.




                                   Chapter 8

                            Capturing Incoming Text

     8.1  Two methods are available for capturing incoming text.  The
     receive buffer may be saved to a text file as previously described.
     The incoming text may also be sent to a file as it arrives.   This is
     accomplished by pressing alt<C>.  You will be prompted to enter the
     name of the capture file.

     8.2 Incoming text will continue to be sent to the named file until the
     next alt<C> is pressed.  The file will be closed.  This is particular-
     ly useful for downloading files or messages from a PBBS.


                                   Chapter 9

                          Modifying Program Parameters

     9.1  All of the parameters contained in the KAM.CFG file may be set
     from within the KAM program.  Press alt<P> to obtain a full screen
     window on the configurable parameters.  The use of the parameter
     modification screen should be self-explanatory.

     9.2  After setting the parameters you will be prompted to save the
     new parameters to a new file, the default file, or not at all.