(*****************************************************************************)
(*                                                                           *)
(*             MSATCOM(tm) - MicroSat Ground Station Terminal                *)
(*                                                                           *)
(*                              Version 1.0                                  *)
(*                                                                           *)
(*            (c) Copyright 1990 by Claudio M. Zanella LU4AEY                *)
(*                     Released For Public Distribution                      *)
(*                           ALL RIGHTS RESERVED                             *)
(*                                                                           *)
(*****************************************************************************)

    USE

    Digital communications protocol FTL0 (File Transfer Level 0)


    SOFTWARE REQUIRED

    - MSATCOM.EXE    Main program (english version)
    - README.COM     Program to read file THUNDER.DOC
    - MSATCOM.DOC    User documentation in Spanish
    - MSATENG.DOC    User documentation in English (this document)
    - MSATCOM.CNF    System configuring file

    HARDWARE REQUIRED

    MSATCOM can be used on PC, XT, AT and Compatibles. It requires for its 
    functioning TNCs with TAPR type commands and the complete connection of 
    the RS232 port, fit 1,2,3,4,5,6,7,8,20.  Take special care in fitting: 
    8 (Data Carrier Detect), 4 (Request to Send), 5 (Clear to Send). 

    With a PacComm TNC 220 & 320 set JP-C to CONN (Default is HIGH)

    The addition of the following in your CONFIG.SYS file is recommended: 

    FILES = 20
    BUFFERS = 20

    MSATCOM was tested with the following HARDWARE:

    TNC types:

    PACCOMM TINY 2
    PACCOMM TNC 200
    PACCOMM TNC 220
    PACCOMM TNC 320
    MFJ-1270/1278
    AEA PK 232
    AEA PK88

    Computer types:

    PC AT 80386   20/25 MHz
    PC AT 80286   16/20 MHz
    PC AT 80286   12/16 MHz
    PC XT 80286    8/12 MHz
    PC XT 8088     4/10 MHz       PC XT NEC V20 10/12 MHz

    SETTING THE TNC

    This programm uses Hardware Handshaking.   Set its TNC on NO PARITY and 
    WORD LENGTH OF 8 BITS. 

    CPactime OFF
    CR       ON
    SEnd     $0D
    DCD      ON  <-- External Carrier Detect in PK232

    Enable the Hardware Handshaking of your TNC as follows:

    START  0
    STOP   0
    XFLOW  OFF
    XON    0
    XOFF   0

    The following parameters are recommended:

    TXDEALY 20
    AXDELAY 20
    PRIOACK ON <-- Release TAPR 1.1.7 only
    FLOW    ON

    SUMMARY OF COMMANDS

    The following commands can be used in MSATCOM:

    F1         - Request reception of directories.
    F2         - Request reception of files (DOWNLOAD).
    F3         - Request send files (UPLOAD).
    F4         - Activate/De-activate the printer in Directory mode.
    F5         - Review downloaded directories by screens.
    F6         - Adjust time of General directories request (HIGHTIME..PG).
    F7         - Adjust time of Personal directories request (HIGHTIME.MY).
    F8         - Adjust time of Bulletin directories request (HIGHTIME.BUL).
    F9         - Change the current satellite.
    F10        - Gateway to DOS.

    Alt-B      - Send of break signal to TNC to put it into command mode.
    Alt-D      - Change level of Data Carrier Detect (DCD pin 8 v24).
    Alt-H      - Help screen (HELP).
    Alt-R      - Re-organize directory files.
    Alt-T      - Toggle modes: Terminal or Server.
    Alt-X      - End MSATCOM (Return to DOS).

    DESCRIPTION OF USE OF COMMANDS

    KEY F1 (DIRECTORY):

    By pressing F1 you get to DIRECTORY options.  There are four options 
    for the mode: 

    ALL      -  Receive the File Headers since last request.
    PERSONAL -  Receive the File Headers sent to 'mycall' since last request
    BULLETIN -  Receive the File Header sent to 'ALL' since last request
    SEARCH   -  Receive the File Header that contains the search criterion 
                specified by you taking as reference the time since the 
                last request to ALL. 

    To correct the times since the last request (hightime.xx), see options 
    F6, F7 and F8;  these are contained in files MSTIME.ALL, MSTIME.MY and 
    MSTIME.BUL in UNIX Hexadecimal format. 


    KEY F2 (DOWNLOAD):

    Through this key we DOWNLOAD.  Its use is very simple and consists of 
    indicating the HEXADECIMAL number of the file we are interested in 
    receiving. 

    This will be memorized until the DOWNLOAD concludes, satisfactorily or 
    not.  If by any chance the DOWNLOAAD of the file did not end and the 
    contact with the server is lost, the next time the satellite is in view 
    press F2 and the programm will automatically reinitiate the DOWNLOAD 
    from the offset where it lost contact. 

    ATTENTION: this will repeat as long as the program doesn't receive the 
    COMMAND DATA END or the DOWNLOAD_ERR_RESP that gets you off the PDL 
    status to the DOWNLOAD file.  If you want to abort this download 
    request, ERASE from your DOS the current DOWNLOAD file. 

    File status:

    xxxxxx.PDL   : File being downloaded (This hasn't ended).
    xxxxxx.DL    : File downloaded successfully
    xxxxxx.XDL   : Rejected file (An error occurred during the download).

    xxxxxx       : Hexadecimal number of requested file.

    KEY F3 (UPLOAD):

    By pressing this option you can UPLOAD -- sending of FTL0 format 
    files -- to the server of the Micro satelite.  As with DOWNLOADs, the 
    option UPLOAD remains memorized until it concludes satisfactorily or 
    not. 

    If the sending is incomplete because the contact with the server was 
    lost, we can reinitiate the upload from the offset where the process 
    has been interrupted the next time the satellite is in view. 

    The UPLOAD is immediate.  Once thithe programm s option is chosen, 
    initiates the connection procedureif files to be 
    sent are found, . 

    File status:

    mmmmmm.OUT   :  File in initial process of sending.
    xxxxxx.PUL   :  File in process of sending (It has been interrupted).
    xxxxxx.UP    :  File has been uploaded successfully.
    xxxxxx.XUL   :  Rejected file, an error occurred during uploading.
    mmmmmm       :  Initial name of file.
    xxxxxx       :  Hexadecimal number assigned by the server

    KEY F4 (PRINTER TOGGLE):

    This option enables to put the printer on or offline.  The same will be
    used during the DIRECTORY procedure, this means we can obtain a copy on
    paper of the directory of the server while we are receiving it, by this
    the DOWNLOAD operation is greatly speeded up.

    KEY F5 (RELOAD/REVIEW DIRECTORY):

    The function of this option is to enable to load and sort  (Reorganize)
    on memory the directories received from the current server, at the same
    time they are shown on screen from the newest to the oldest.

    By the keys PageUp and PageDwn you can skip these directories pagewise.
    By the keys UP and  DOWN we can go up  of down by lines.   The HOME key
    positions the screen at  the beginning of the  directory.  The End  key
    positions the screen at the end of the directory.  The W key enables to
    save the screen directories on a file.

    The messages directed  to our licence  will be highlighted  to indicate
    the presence of these on list.

    A subprocess  is executed  while running  this option.   It consists in
    loading the diretories on a sublist.

    This  subprocess  assures  that  the  File  Header  received during the
    DIRECTORY process are  not repeated, so  that no duplicate  directories
    are generated.  If the  presence of a duplicate directory  is detected,
    this is indicated on screen but is not saved on the master file.

    KEYS F6, F7, F8 (TIME ADJUSTMENT):

    From these options depend the times of request of directories.  MSATCOM
    performs all directory requests taking as reference the present time in
    the MSATCOM.BUL, MSATCOM.ALL or MSATCOM.MY files.

    These  files  will  be  updated  after  having  concreted  a request of
    directory, for this the time of  the last File Header in the  server is
    taken as reference.

    Once updated, this time can be  altered by these options.  It  consists
    in indicating the program the difference in hours of our GMT hour.

    The format  of these  files is  HEXADECIMAL and  corresponds to time in
    UNIX.  The  same will be  created for the  first time by  the programm,
    taking as reference the present time of the programm.

    KEY F9 (CHANGE COURRENT SATELLITE):

    This  option,  of  immediate  access,  enables  to change instantly the
    current satelite of the program.

    In this way the configuration of the program can be changed for the new
    satelite without  leaving it  to perform  changes to  the configuration
    file by loosing time and making it's use complex.

    KEY F10 (DOS GATEWAY):

    Enables  to  performa  a  DOS  shell  to  execute  external commands of
    programs to MSATCOM.

    KEY ESC (ABORT & DISCONNECT):

    This key enables to abort any operation started immediately  performing
    a total resetting of the status of variables of the program.

    KEY ALT-B (SEND BREAK):

    Enables to send a break signal of  350 ms when we are in terminal  mode
    with the target of putting the TNC in COMMAND mode.

    KEY ALT-D (DCD LEVEL):

    Enables  to  change  the  logical  state  of  the  DCD, this option was
    introduced to enable the TNC's use which use as VALID DCD a high state,
    being the Low state the commonly encountered in the TNC's.

    KEY ALT-H (HELP SCREEN):

    This option gives us access to a small onscreen help of the commands of
    the programm.

    KEY ALT-R (REBUILD DIRECTORY):

    Used to reorganize the directory file of the current satelite.

    This reorganization consists in cleaning the file directory of possible
    duplicate directories by erasing at the same time the old ones after an
    amount of days we indicate.

    KEY ALT-T (TERMINAL/SERVER MODE):

    By  this  option  we  can  switch  from  mode  SERVER  to mode TERMINAL
    instantly and quickly.

    KEY ALT-X (EXIT TO DOS):

    End the execution of MSATCOM (Return to DOS).

                                   --- ** ---

                     Configuration of file MSATCOM.CNF
                     -------------------------------------

    As we saw at the beginning,  this file is in charge of  configuring the
    system, it is  divided in four  sections (Serial SetUP,  Misc Function,
    Top_Cmd_Start/End_Cmd_Setup  y  Top_Cmd_End/End_Cmd_Setup).   The first
    and second one serve to send different commands to the proper  programm
    and the others have as mission to send commands to the TNC to set it in
    its initial and by leaving the program, the last ones can be configured
    by the user.

                              Typical configuration
                              ---------------------

    In the first  section (Serial SetUP)  we find as  start the setting  of
    speed for  communication of  the computer  to the  TNC, it is necessary
    that both coincide in this speed, the  TNC in this case must be set  on
    9600 Baud.  The length of  word, parity and the stop bit  must coincide
    with the previous setting of the TNC.  There are three options for  teh
    Handshake  and  these  are  the  following:   H (hardware, RTS/CTS) , S
    (software, XON/XOFF) y N (none).  The recommended is the Hardware.

    It is also possible  to set the communications  port to be used  in our
    computer by the option Com_Port and it is necessary to do it indicating
    an hexadecimal number, attaching in the following setting (IRQ_Com) the
    corresponding interruption number, for example:

                              Port 1 = $03f8  IRQ4
                              Port 2 = $02f8  IRQ3
                              Port 3 = $03e8  IRQ4
                              Port 4 = $02e8  IRQ3

#
#              MSATCOM version 1.0  --  Configuration FILE  --
#
# Serial SetUP
#
#
Baud_Rate   = 9600
#
Word_Lenght = 8
#
Parity      = N
#
Stop_Bit    = 1
#
Handshake   = H
#
Com_Port    = $03F8
#
IRQ_Com     = 04
#
#

    In the second section (Misc Function), we have both first  instructions
    that correspond to the  tipe of video plate  that is used normally  Not
    and Yes  are the  most used,  but sometimes  it is  necessary to change
    NOT/YES for a better functioning depending on the video plate.

    SYSOP_NAME:  as the word says, it is necessary to indicate the name  of
    the system operator.

    MYCALL: operator license.

    GMT_ZONE:  thought to be used by the program with universal coordinated
    time, taking for it the computer  hour, therefore we must take care  to
    maintain the hour of our machine  and in this case we must  indicate if
    our station is east of west of Greenwich as follows:  EST o WES

    GMT_HOURS:  this command operated parallel to the aforementioned and it
    is necessary to  indicate the time  difference that exists  between our
    QTH and the Greenwitch time allways in positive numbers.

    SATELLITE:  The  license of the  satelite to which  we want to  connect
    must be  put, without  omitting the  number that  corresponds after the
    dash  and  in  this  case  it  is  number  12,  that for all satellites
    identifies the BBS during the  execution of the program can  be changed
    of  satellite  (F9)  withouth  changing  the  configuration  DCD_LEVEL:
    logical level of the DCD L (low) or H (high)

    SORT_TYPE:  This instruction  is used by the  option F6 to perform  the
    classification of the directory, in  this case it will be  performed by
    time (TIME), this means it will be seen on screen since the most recent
    date to the oldest.  It is also possible to make the classification  by
    another parameter, for example SIZE (size).


# Misc Function
#
#
Snow_Check    = Not
#
Direct_Video  = Yes
#
#
Sysop_Name    = Ruben
#
Mycall        = LU6DYD
#
GMT_ZONE      = EST
#
GMT_HOURS     = 3
#
SATELLITE     = SIMSAT-12
#
DCD_LEVEL     = L
#
SORT_TYPE     = TIME
#
#

    In the third section we have  possibility to put the TNC parameters  we
    think adecuate to send at starting the program.  These parameters  will
    be sent automatically to the TNC and can be modified by the user for  a
    better operation with the satellite


*** Top_Cmd_Start
#
#
FULLD ON
FRAC 2
CONOK OFF
MAX 7
PAC 255
TXD 25
AXD 25
UN SIMSAT V SIMSAT-1
BT SIMSAT Earth Simulator of Micro Satellites - Buenos Aires ARGENTINA.
B E 5
M ON
CONMODE TRANS
#
*** End_Cmd_Setup
#

    In the fourth section it is  identical to the third but the  parameters
    are  sent  to  the  TNC  when  we  get  off  the  program (ALT-X) These
    parameters can also be modified by  the user mainly those that use  the
    same TNC for satellites operation and earth


#
*** Top_Cmd_End
#
#
FULLD OFF
CONMODE CONVERSE
MCOM ON
UN CQ
B E 0
BT %
CONOK ON
MON OFF
#
*** End_Cmd_Setup
#

                                   --- ** ---

    ERROR REPORT

    Due to that the programm is  still being developed, it may be  possible
    that some error occurs.  If  this happens, please pay attention to  the
    following:

    Some error in the momento of execution make that the program visualizes
    an error message and ends.

    Run time error: nnn at xxxx:yyyy

    nnn       : Number of error.
    xxxx:yyyy : Location of error (segment and displacement).

    The errors in time of running are divided in 4 types:

    Errors of D.O.S.               : Del 1 al 99.
    Errors of Entrance/Exit (I/O)  : Del 100 al 149.
    Critical Errors                : Del 150 al 199.
    Fatal Errors                   : Del 200 al 255.

    Please take note of this information and send it so as to evaluate  and
    correct the possible error.

           --------------------------------------------------------

                              *** ATENTION ***

    Ham Radio:
    -----------

    For the distribution no charge is asked.  If you are owner of  MSATCOM,
    please let me know so as to keep a statistic of use as well as any type
    of error you may detect or suggestions to improve it.

    Therefore, please mail via Packet Radio to:

    LU4AEY @ LU4AEY.#VDP.ARG.SA Claudio M. Zanella

    By satellite:

    LU4AEY @ UOSAT3, PACSAT, LUSAT

    By mail to:

    Claudio  M.  Zanella
    Av. Alvarez Jonte 3353 Piso 1 Dto  2  Villa del Parque
    CP (ZIP) 01407 Buenos Aires - ARGENTINA. TE: 001-01-567-1239.

                             * * * * * * * *

    ENJOY IT!

                      ...  Claudio