NOS PROCEDURES  for  KA9Q NOS Version 900828
(14 nov 90)


HOW TO USE FTP  (File Transfer Protocol):
  1.Start NOS with STARTNOS.BAT.  Wait for the prompt: "nos>".
  2.Type  "FTP callsign <cr>"  to initiate an FTP session.
  3.At the "Login:" prompt, enter your callsign <cr>.
    At the "Password:" prompt, enter your password <cr>.
    (Login and Password parameters are entered into the remote terminal's
     FTPUSERS file.  Typical valid Login entries may be: your callsign,
     "guest", or "anonymous".  The Password prompt typically accepts any
     entry, if so specified in the remote's FTPUSERS file.)
  4.Type  "DIR <cr>"  to display current directory.
    Type  "CD subdirname/subdirname <cr>"  to change directory.
    (Note the slash mark used for this command!!)
  5.Type  "TYPE <cr>"  to display current file transfer type.
    Type  "TYPE A <cr>"  to go into ASCII file transfer type.
    Type  "TYPE I <cr>"  to go into IMAGE (BINARY) file transfer type.
  6.Type  "GET remotefile <cr>"  to receive a file.
    Type  "GET remotefile con <cr>"  to receive a file and view its
                                     contents on my console screen.
    Type  "GET remotefile myfile <cr>"  to receive a file and rename it
                                        as "myfile".
    Type  "PUT myfile remotefile <cr>"  to send "myfile" and rename it
                                        as "remotefile"
  7.OTHER COMMANDS:
    a.Type  "ABORT <cr>"  to abort a file transfer.
    b.Type  "DELE remotefile <cr>"  to delete a file from the remote dir.
    c.Press  F10  to return to "nos>" prompt.
    d.Press  <cr> to return to current FTP session.
    e.To display session status press  F10.  Then type  "SE <cr>".
      Current session is displayed with an "*".
    f.To change to another session press  F10.  Then type  "SE number <cr>".
      Then press  <cr>  to enter new session.
    g.To close current session press  F10.  Then type  "CLOSE <cr>".
    h.To close a session after a connection has been interrupted or after
      an unsuccessful attempt to connect, press  F10.
      Then type  "RESET <cr>".
    i.To kick the remote terminal if wait time between packets becomes great:
      at the "nos>" prompt type  "REMOTE callsign KICK <cr>".



HOW TO ESTABLISH AN AX25 PACKET CONNECTION:
  1.Start NOS with STARTNOS.BAT.  Wait for the prompt: "nos>".
  2.Type  "C AX0 callsign <cr>"  to initiate ax25 Packet connection.
  3.OTHER COMMANDS:
    a.Press  F10  to return to "nos>" prompt.
    b.Press  <cr> to return to current Packet session.
    c.To display session status press  F10.  Then type  "SE <cr>".
      Current session is displayed with an "*".
    d.To change to another session press  F10.  Then type  "SE number <cr>".
      Then press  <cr>  to enter new session.
    e.To close current session press  F10.  Then type  "CLOSE <cr>".
    f.To close a session after a connection has been interrupted or after
      an unsuccessful attempt to connect, press  F10.
      Then type  "RESET <cr>".



HOW TO USE TELNET:
  1.Start NOS with STARTNOS.BAT.  Wait for the prompt: "nos>".
  2.Type  "TELNET callsign <cr>"  to initiate a TELNET session.
  3.After "connected" status is displayed, begin conversation.
  4.OTHER COMMANDS:
    a.Press  F10  to return to "nos>" prompt.
    b.Press  <cr> to return to current TELNET session.
    c.To display session status press  F10.  Then type  "SE <cr>".
      Current session is displayed with an "*".
    d.To change to another session press  F10.  Then type  "SE number <cr>".
      Then press  <cr>  to enter new session.
    e.To close current session press  F10.  Then type  "CLOSE <cr>".
    f.To close a session after a connection has been interrupted or after
      an unsuccessful attempt to connect, press  F10.
      Then type  "RESET <cr>".
    g.To upload a file to the remote console screen press  F10.
      Then type  "UPLOAD /dirname/filename <cr>".
      (Note the slash mark used for this command!!)



HOW TO USE TRACE:
  1.At the "nos>" prompt type  "TRACE AX0 nnn <cr>"  where "nnn" is the
    following:
                                      Display Display Display
                                      HEADERS HEADERS HEADERS
                                              DATA    DATA
                                                      HEX
                                     +-------+-------+-------+
            Display OFF              :   0   :   0   :   0   :
            Display INCOMING Packets :  010  :  110  :  210  :
            Display OUTGOING Packets :  001  :  101  :  201  :
            Display BOTH             :  011  :  111  :  211  :
                                     +-------+-------+-------+



NOS COMMAND SUMMARY:
  Press  F10  to return to "nos>" prompt.  Then:
    Type  "AX25 HEARD <cr>"     to display list of stations recently heard.
    Type  "AX25 FLUSH <cr>"     to clear HEARD.
    Type  "AX25 KICK <cr>"      to force Packet transmission.
    Type  "AX25 RETRY n <cr>"   to set number of Packet retries.
    Type  "EXIT <cr>"           to exit NOS.
    Type  "H C callsign <cr>"   to hopcheck a remote station.
    Type  "I S <cr>"            to display IP status.
    Type  "PARAM AX0 255 <cr>"  to force TNC out of KISS mode.
    Type  "PING callsign <cr>"  to query a station.  If an address packet
                                is displayed then that station is on freq.
    Type  "RO <cr>"             to display routes.
    Type  "SE <cr>"             to display session status.
    Type  "SO <cr>"             to display socket status.
    Type  "T S <cr>"            to display TCP status.
    Type  "T S nnnnnnnnn <cr>"  to display detailed TCP status.
                                (Note:"nnnnnnnnn" is the TCB#.)
    Type  "? <cr>"              to display commands.
    Type  "! <cr>"              to enter DOS shell.  "EXIT <cr>" to return.



==============================================================================

BM PROCEDURES  for  Bdale's Messy-DOS Mailer v.3.3.1


  HOW TO READ A MESSAGE:
    1.Start BM.EXE.
    2.Message numbers and one-line subject headers will be displayed.
      The "current" message is displayed with a ">".
      To view the current message type:  <cr>.
      To view another message type the message number followed by <cr>.
    3.OTHER COMMANDS:
      a.Type  "H <cr>"  to list message headers.
      b.Type  "1 <cr>"  to read message #1.
      c.Type  "S <cr>"  to append current message and header to \SPOOL\MBOX.
      d.Type  "S n filename <cr>"  to append message #n and its header to
                                   \SPOOL\FOLDER\filename.
      e.Type  "W <cr>"  to append current message text to \SPOOL\MBOX.
      f.Type  "W n filename <cr>"  to append message text #n to
                                   \SPOOL\filename.
      e.Type  "D <cr>"  to delete the current message.
      f.Type  "N <cr>"  to display list of Notesfiles. A different Notesfile is
                        created in \SPOOL\MAIL for each callsign that has mail
                        waiting in this NOS mailbox.
      g.Type  "N callsign <cr>"  to list messages in another Notesfile.
      h.Type  "Q <cr>"  to quit BM.EXE.



  HOW TO SEND A MESSAGE:
    1.Start BM.EXE.  Wait for the prompt: "callsign>".
    2.Type  "M <cr>"  to mail a message.
    3.At the "To:" prompt, enter the full address. (Eg. call@call)
    4.To correct mistakes type "~E"  to invoke the editor.
    5.At the end of the message text type  "CTRL-D <cr>".
      The message is now placed in \SPOOL\MQUEUE.
      A copy of the message is also appended to \SPOOL\RECORD if this option
        has been selected in BM.RC.
    6.Type  "Q <cr>"  to quit BM.EXE.
    7.Start NOS with STARTNOS.BAT. Wait for the prompt: "nos>".
    8.Send messages by any ONE of the following methods:
      a.Type  "SMTP KICK <cr>"  to send messages in \SPOOL\MQUEUE immediately.
      b.Type  "SMTP TIMER 1800 <cr>"  to send messages in \SPOOL\MQUEUE every
                                    1800 seconds. (Any time interval can be
                                    set here.)

      (Note: You can type  SMTP TIMER 1800  into AUTOEXEC.NET to send
             messages at 1800 second intervals by default.)



  HOW TO FORWARD A MESSAGE:
    1.Start BM.EXE.  Wait for the prompt:  "callsign>".
    2.Type  "N callsign <cr>"  to list messages in another Notesfile.
    3.Type the number of the message to be forwarded, followed by <cr>.
    4.Type  "F <cr>"  to forward the current message.
    5.At the "To:" prompt, enter the full address, (Eg. call@call) then <cr>.
      The message is now placed in \SPOOL\MQUEUE.
    6.Type  "Q <cr>"  to quit BM.EXE.
    7.Start NOS with STARTNOS.BAT. Wait for the prompt: "nos>".
    8.Send messages by any ONE of the following methods:
      At the  " nos> " prompt:
      a.Type  "SMTP KICK <cr>"  to send messages in \SPOOL\MQUEUE immediately.
      b.Type  "SMTP TIMER 1800 <cr>"  to send messages in \SPOOL\MQUEUE every
                                    1800 seconds. (Any time interval can be
                                    set here.)

      (Note: You can type  SMTP TIMER 1800  into AUTOEXEC.NET to send
             messages at 1800 second intervals by default.)