Article 2943 of rec.ham-radio.packet:
Path: mcdphx!asuvax!cs.utexas.edu!hellgate.utah.edu!helios.ee.lbl.gov!ucsd
		!ucsdhub!hp-sdd!hplabs!hpfcso!hpldola!hp-lsd!col!bdale
From: bdale@col.hp.com (Bdale Garbee)
Newsgroups: rec.ham-radio.packet
Subject: Re: Dial-up SLIP and NET
Message-ID: <4390091@col.hp.com>
Date: 14 Dec 89 02:31:29 GMT
References: <1298@dgbt.uucp>
Organization: HP Colorado Springs Division
Lines: 27

Ok, here's some fixed text for that section, sorry for the delay, but I've had
a few unexpected time-consumers the last week or two.

SLIP Modem Dialing

An extension to the attach command allows the syntax:

   attach <hw type> <I/O address> <vector> <mode> <label> <bufsiz> <mtu>
          [<speed>] [[optional '-' for debug] <send> <expect> <send> [...]]

for slip connections only.  The send/expect sequences allow you to dial a
modem on the slip port, and negotiate a remote login to setup a slip link.

              \d  -  delay 1 second
              \n  -  send newline
              \r  -  send carriage return
              \N  -  send NULL
              \E  -  send control-D
              \s  -  send space  (not really needed as the
                                  cmdparse routine allows quoting)
              \\  -  send backslash

Note that an expect does not have to follow the last send.  Those familiar
with UUCP will recognize the expect/send paradigm as being similar to that
used in the L.sys or Systems file.

73 - Bdale, N3EUA