ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                               ±±Ü  ±±±Ü                          º
   º                               ±±Û ±±Ûß            ±±Ü            ºÛÛ
   º          ±±±±±±Ü   ±±±±±Ü     ±±Û±±Ûß   ±±±±±Ü  ±±±±±±Ü          ºÛÛ
   º         ±±Ûßßß±±Ü    ßßß±±Ü   ±±±±Ûß   ±±Ûßß±±Ü  ß±±Ûßß          ºÛÛ
   º         ±±Û   ±±Û  ±±±±±±Ûß   ±±Û±±Ü   ±±±±±±Ûß   ±±Û            ºÛÛ
   º         ±±Û   ±±Û  ±Û   ±±Û   ±±Û ±±Ü  ±±Ûßßßß    ±±Û            ºÛÛ
   º         ±±±±±±±Ûß  ±±±±±Ü±±Ü  ±±Û  ±±±Ü ±±±±±Ü     ±±±Ü          ºÛÛ
   º         ±±Ûßßßßß    ßßßßß ßß   ßß   ßßß  ßßßßß      ßßß          ºÛÛ
   º         ±±Û                                                      ºÛÛ
   º        ±±±±Û                 Version 5                           ºÛÛ
   º         ßßßß                                                     ºÛÛ
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼ÛÛ
      ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ






              "The best Packet Radio software in the world"








                                    by









                               Tony Lonsdale

                                  VK2DHU








































                      (This page intentionally blank)




































                               TABLE OF CONTENTS




 PART I - INTRODUCTION

  Packet Radio and Digital Communications........................   1
  What is paKet? ................................................   7
  Changes in Version 5 ..........................................   8
  Other Communications Modes ....................................  11
  The paKet Documentation .......................................  12



 PART II - paKet's WINDOWS

  Overview ......................................................  13
  Binary File Transfer Window ...................................  14
  Communications Windows ........................................  15
                        - Flashback .............................  17
                        - Flashback Text Find ...................  18
                        - Write Flashback to disk ...............  18
  Configuration Windows - Overview ..............................  19
                        - System Configuration ..................  20
                        - Serial Port ...........................  21
                        - Multi User options ....................  24
                        - Communications Windows ................  26
                        - Colours ...............................  30
                        - Keyboard Macros/Auto commands .........  31
                        - REMOTE Mode options ...................  35
                        - File Transfer options .................  37
                        - File/Directories ......................  39
                        - Miscellaneous options .................  43
  Connect Window ................................................  45
  Disk Directory Window .........................................  46
  Help Window ...................................................  48
  Message Window ................................................  49
  Status Window .................................................  50
  TNC Help Window ...............................................  53
  Type Ahead Window .............................................  55



 PART III - SPECIAL KEY CODES

  Overview ......................................................  59
  Ctrl-key combinations .........................................  59
  Alt-key combinations ..........................................  59
  Function keys .................................................  60
  Other commonly used command keys ..............................  60





                                       i


 PART IV - KEYBOARD COMMANDS

  F1            Display Help Screen .............................  61
  F2            Turn Log File on/off ............................  62
  F3            Turn REMOTE Mode on/off .........................  63
  F4            Toggle Word Wrap and Single Line on/off .........  64
  F5            Send ASCII text file ............................  65
  F6            Receive ASCII text file .........................  66
  F7            Send Binary File using pP or YAPP ...............  67
  F8            Receive Binary File using pP or YAPP ............  69
  F9            DOS Gateway .....................................  70
  F10           Display TNC Help File commands ..................  71
  Alt-F1        Display Online Manual ...........................  72
  Alt-F2        Contest Mode on/off .............................  73
  Alt-F5        Send RAW Binary File ............................  74
  Alt-F6        Receive RAW Binary File .........................  75
  Alt-F7        Send Binary File to BayCom (or Digicom) .........  76
  Alt-F8        Receive Binary File from BayCom (or Digicom) ....  77
  Alt-A         Turn Alerts on/off ..............................  79
  Alt-B         Send BREAK to the TNC - return to Command Mode ..  79
  Alt-C         Connect to another station ......................  79
  Alt-D         Display a Disk Directory ........................  80
  Alt-E         Edit a data file ................................  81
  Alt-F         Find text in Flashback ..........................  81
  Alt-H         Send MHEARD command to TNC ......................  81
  Alt-I         Initialise Communications Windows ...............  82
  Alt-L         Continue Find in Flashback ......................  82
  Alt-M         Personal Message System .........................  82
  Alt-P         Turn Print Log on/off ...........................  83
  Alt-Q         Clear TNC's XOFF ................................  83
  Alt-R         Rename/Move a data file .........................  83
  Alt-S         Script Processing ...............................  84
  Alt-T         Set TNC's Time and Date .........................  84
  Alt-V         Verify TNC's Connected status ...................  84
  Alt-W         Write contents of Flashback to disk .............  85
  Alt-X         Exit the paKet program ..........................  85
  Alt-Z         Configuration ...................................  85
  Insert        Toggle Insert Mode on/off .......................  86
  Delete        Delete a character or delete a file .............  86
  Backspace     Delete the character before the cursor ..........  86
  Ctrl-Y        Delete a line ...................................  86
  Esc           Return to previous operation ....................  86
  ScrollLock    Hold all input data (pause) .....................  87
  Left-Arrow    Move the cursor left ............................  87
  Right-Arrow   Move the cursor right ...........................  87
  Up-Arrow      Type Ahead Recall or Move cursor up .............  87
  Down-Arrow    Type Ahead Recall or Move cursor down ...........  87
  Home          Move to start of text or window .................  88
  End           Move to end of text or window ...................  88
  Shift-Up      Flashback - move back a line ....................  88
  Shift-Down    Flashback - move forward a line .................  88
  PageUp        Flashback - Move back a page ....................  88
  PageDown      Flashback - Move forward a page .................  88
  Ctrl-PageUp   Flashback - Move to beginning of buffer .........  89
  Ctrl-PageDown Flashback - MOve to end of buffer ...............  89
  Shift-Left    Change to previous Communications Window ........  89
  Shift-Right   Change to next Communications Window ............  89
  Shift-Fn      Change to another Communications Window .........  89


                                      ii



 PART V - Messages in the paKet system

  Overview ......................................................  91
  Messages starting with A to C .................................  92
                         D to H .................................  95
                         I can't ................................  99
                         I to L ................................. 103
                         M to P ................................. 107
                         R to S ................................. 112
                         The .................................... 116
                         T to U ................................. 120
                         W to Z ................................. 123



 PART VI - REMOTE Mode

  Overview ...................................................... 125
  Activating REMOTE Mode ........................................ 126
  Leaving REMOTE Mode ........................................... 127
  The REMOTE Menu Commands A to L ............................... 128
                           MD to MW (BayCom commands) ........... 131
                           R to W ............................... 134
                           YD to YW (YAPP or pP commands) ....... 136
  Messages (A to L) ............................................. 138
           (M to R) ............................................. 142
           (S to Z) ............................................. 145



 PART VII - SCRIPT PROCESSING

  Overview ...................................................... 149
  Running a Script File ......................................... 149
  Script Commands ............................................... 150
  The Script File syntax ........................................ 154
  Other uses for Scripts ........................................ 154
  A sample Script ............................................... 155
  Discussion on the sample Script ............................... 156



 PART VIII - PERSONAL MESSAGE SYSTEM (PMS)

  Overview ...................................................... 157
  The Sysop PMS Menu ............................................ 158
  PMS commands in the REMOTE Menu ............................... 159
  Accessing the PMS ............................................. 160
  Messages ...................................................... 163



 PART IX - CONTEST MODE

  Overview ...................................................... 169
  Base Operation ................................................ 170
  Checkpoint Operation .......................................... 173


                                     iii





 PART X - TECHNICAL

  Hardware vs Software Handshaking .............................. 175
  Preferred TNC Settings ........................................ 177
  Kantronics TNCs ............................................... 181



 PART XI - paKet PROTOCOL (pP)

  What is pP ? .................................................. 185
  Using pP ...................................................... 186
  The Technical details of the paKet Protocol ................... 188



 PART XII - ADMINISTRATION DETAIL

  The cost of paKet ............................................. 193
  Acknowledgements and Credits .................................. 194
  Where to find the author ...................................... 195
  Registration Form ............................................. 196



































                                      iv


PART I - INTRODUCTION

Packet Radio and Digital Communications

  Packet Radio is a form of Digital Communications. It is a system of
  reliable, error free communication between two Computer equipped
  stations using Radio as the medium.

  Digital Communication is not new. Other Modes such as Morse Code, RTTY
  and AMTOR have been around for years but these modes lack one thing we
  have in Packet Radio: Error Free Communications!

  Let's have a brief look at these modes.



Morse Code.

  Morse Code is the original Digital Mode dating back to the last Century!
  Today, while the debate rages over Morse Code licensing requirements,
  more and more stations using this mode have replaced their hand key and
  their electronic keyer with a Computer keyboard and display. The
  technology is good but even today, no machine can beat the trained human
  ear for copying hand sent Morse Code under varying conditions. The
  keyboard is a more efficient Sending device though (for most people)!

  Perhaps the one advantage of Morse over Packet and the others, is that a
  human operator can decode the Morse Code transmissions by ear!



RTTY

  RTTY or RadioTeletype is a direct machine to machine communications mode
  using the Baudot (or Murray) code. This mode became popular with many
  amateurs when surplus TTY machines became available at a reasonable cost
  after World War II. These mechanical monsters provided a keyboard for
  Input and a paper roll for printed Output. Video displays were still too
  exotic and expensive in those days. It was not until the late 1970s that
  we began to see the Video Display come into more widespread use. (By the
  way, have you ever wondered why Program Languages like BASIC use the
  command PRINT to display their output?)

  When transmitting Morse Code, the transmitter is switched on and off to
  make the dits and dahs.  When sending Teletype however the transmitter
  runs continuously, sending either of two frequencies conventionally
  known as Mark and Space (a reference to paper tape reception of
  telegraphy).  When listening to a teletype signal off air, you will soon
  get to recognise the familiar warble of Mark and Space tones.

  In the amateur shack the TTY machine is usually connected to an HF
  receiver or transceiver which the operator tunes so that the received
  audio is just the right pitch or audio frequency to trigger the
  demodulator's Mark and Space resonators.

  If the receiver is slightly off the correct frequency the tones vary and
  the text becomes garbled or even lost altogether.  To help the other
  station tune the receiver correctly, a RTTY operator can send a string
  of alternate R and Y characters viz: RYRYRYRYRY.  This pattern is chosen
  as it produces the most frequent and almost symmetric alternation of
                               Page   1


  Mark and Space tones, giving the receiving operator the best chance to
  tune the receiver before the "real" message starts.  However, even if
  the signal is accurately tuned, the information can become garbled or
  completely lost due to interference, fading, or noise.  Often, it is
  possible to make sense of the message even with parts missing, but RTTY
  is by NO means an error free mode!

  I should point out that similar problems exist for other modes including
  "Packet".  While information can still fail to get through on the more
  sophisticated modes, the Error Detecting capability of some, Packet in
  particular ensure that the operator will receive either accurate
  information or nothing at all.  Usually, where "nothing at all" is
  received, the information will automatically be retransmitted when the
  radio is retuned, or the interference stops, (etc) and nothing is lost.

  Today, RTTY is still a popular mode especially on the HF bands, and the
  advent of the "Glass Terminal", firstly the Dumb Terminal and now the
  Personal Computer, has brought this mode to even more operators the
  world over. Many specialised RTTY systems were developed for the Amateur
  enthusiasts but have been superseded now by the Personal Computer with
  one of the Multi Mode TNCs which handle RTTY and many other modes
  besides.

  The latest Computerised RTTY equipment generally offers no more in terms
  of communication than the old TTY machines. Oh yes, they do it better,
  quieter, more efficiently, using less power and occupying less space,
  but the limitations of the mode remain.


AMTOR

  AMTOR is a specialised form of RTTY. The term is an acronym for AMateur
  Teleprinting Over Radio and is derived from the commercial SITOR system
  (Simplex Telex Over radio).

  AMTOR improves on RTTY by incorporating a simple Error Detection
  technique.  In ARQ mode (Automatic Repeat Query) data is sent in groups
  of 3 characters with a fixed Mark/Space proportion enabling the
  receiving system to recognise many errors received as invalid codes.
  The receiver responds to each 3 character group by sending either an ACK
  (ACKnowledge) code (if OK) or a NAK (Not AcKnowledge).

  In FEC mode, the sending station sends each character twice so this mode
  provides a means of transmitting to several stations at once.  The
  receiving station does not acknowledge the data received. If a receiving
  station matches both instances of a character, that character will be
  printed, otherwise some error symbol is printed. This mode does not
  provide for the receiver to ask for the missing data to be retransmitted.

  The Error Detection technique provides improved accuracy over the
  "vanilla" RTTY mode, but is still not entirely reliable.  It is perhaps
  better termed Error Reduction than Error Detection and has limited
  application for critical data (such as program code).







                               Page   2


Packet Radio (AX.25)

  Packet Radio offers many advantages over the other modes including
  virtually error free communications, simultaneous frequency sharing by
  several stations, multiple repeater operation ("digipeating") for longer
  distance communications, and Networking.


  Error Free Communications.

  The Error Detection (and Correction) is perhaps the major benefit of
  Packet Radio. With this mode, using HDLC and the AX.25 protocol, data is
  checked and verified before being accepted by the receiver's TNC.

  HDLC (High-level Data Link Control) is a procedure defined by ISO, the
  International Organisation for Standardisation, for the handling of
  Error Free frames of information over a communications link.

  AX.25 is a set of rules or Protocol defining the format and content of
  packets and how they are handled. It is not the only Protocol for data
  communications but is the recognised standard in the world of Amateur
  Packet Radio.

  Fortunately we don't have to know the details of either HDLC or AX.25 to
  use Packet Radio. (I read the AX.25 Protocol Specifications and am still
  not too sure what it said!)  The hard work is done in a special device
  called a TNC (Terminal Node Controller) which is a small computer in
  itself, programmed to perform the HDLC Error Handling and many AX.25
  functions to make it easy for us.

  The Error Detection is much more sophisticated than that used in AMTOR
  so the result is significantly more reliable. The chance of an
  undetected error getting through is less than one in a many millions.
  So, for all practical purposes Packet Radio is considered completely
  error free. If any data comes through the system to your computer (to
  paKet in your case) you can be sure that what you see is exactly what
  the other station sent.

 Frequency Sharing.

  Packet Radio, like the commercial X.25 Packet Switched systems, allows
  several simultaneous point to point connections to share the same
  frequency.

  In Packet Radio whenever we send a message to another station, our TNC
  builds a Packet, like an envelope, around our message adding details
  like the callsign of the station this message is addressed to. Then, if
  the frequency is clear, the Packet is transmitted into the airwaves.

  Our TNC listens to the audio coming from the radio receiver and if there
  are any other Packet Radio stations using the frequency, it waits until
  there is a lull in the transmissions before transmitting our Packet. At
  first, you might wonder how long it has to wait, thinking the other
  stations might be going for hours! However, in practice, a Packet might
  take only a fraction of a second to transmit - a relatively short burst
  of time compared to the time it takes us to type a message. Unless the
  frequency is really busy, you might not even notice the delay!

  The Packet Radio frequency in use also carries messages for many people
  at the same time. When receiving, your TNC looks at every Packet
                               Page   3


  received, checks the address on each Packet and identifies any Packets
  addressed to you.

  Any Packets not intended for you may be ignored by your TNC so you see
  on your screen only those messages addressed to you. This way you need
  not concern yourself with all the other information flowing around on
  the frequency, and are free to concentrate on your contact with the
  other station.

  If you wish, you can ask your TNC to display everything it receives.
  This is called Monitoring. Every Packet contains the AX.25 Header
  ("envelope") which identifies the station who sent it and the station it
  is addressed to. The Header contains other information too but we wont
  get into that just now.  When monitoring, your TNC will send to the
  Computer the Headers as well as the contents of the messages so you can
  see who sent what to whom. Then you will see how the AX.25 system is
  able to handle lots of different conversations on the frequency at the
  same time.  The other modes do not offer this capability.


 Multiple Repeater Operation.

  If the station you wish to communicate with is outside radio range, you
  may establish the connection via one or more intermediate stations which
  act as repeaters.

  A station providing this repeater function is commonly called a
  Digipeater ("Digital Repeater"). It is part of the AX.25 design that any
  TNC may be used as a Digipeater so, unless you deactivate this facility
  in your TNC, your system too can be used as a Digipeater.

  Say you are trying to establish a connection with a station who is out
  of radio range. (I'll call it the "Destination" to help avoid confusion
  here). There might be another station in between who can "hear" both you
  and the Destination. So, you can call the Destination "via" the
  intermediate station. Your TNC, using the AX.25 logic, will transmit a
  "Connect" message with both those callsigns; the intermediate station
  will see its callsign used as a Digipeater so it will capture the
  message, store it in its memory for the time being, and when the
  frequency is clear it will retransmit that same message. This time the
  Destination will hear it and will respond, again "via" the Digipeater
  station.

  So, you now have a point to point connection with the desired
  Destination as if it were a local contact. It just takes a little longer
  because each message is transmitted twice.

  The AX.25 Protocol provides for up to eight Digipeaters to be used for a
  single point to point connection. So for a more distant destination, you
  could call that station via two or more intermediate stations. Each of
  those Digipeaters will store your message and retransmit it as soon as
  the frequency is clear. This allows distances of hundreds, maybe
  thousands, of kilometers (even miles!) on VHF or UHF frequencies.


 Networks.

  Following on from the previous discussion on Digipeating, I should
  mention Networks.  The term "Network" is often used in different ways
  but I want to mention just two of those here.
                               Page   4



  Networking is a subject that deserves considerably more space that I
  intend to give it here in this Introductory section.

  Firstly the term is used to describe an advanced form of Digipeating
  where we can make contact with distant stations without necessarily
  knowing what intermediate stations are retransmitting our messages. The
  idea is like our telephone Network where we make a call by dialling the
  number of the person we wish to speak to. We don't know nor care how the
  call is routed, whether it goes via cable or via satellite, or how many
  telephone exchanges it goes through. We are simply interested in getting
  our call through to the other person, no matter how it gets there!

  Networking systems in use in the field of Amateur Packet Radio include
  TCP/IP, NET/ROM, and ROSE. Unlike the widespread acceptance of the AX.25
  Protocol, we do not have any one Networking system preferred over all
  others in use. There is still lots of healthy debate going on and
  developments continuing. It may be that we will have to wait for a new
  generation of Networking System before a single, global system is
  implemented.

  However, there may be at least one of these Networking systems used in
  your area, so check around with other users and see what you have to do
  to use it. It is supposed to make it easier for you but, as with all
  developing systems, there may be times when you pine for the "old,
  simple way".



  The other meaning of "Network" I want to mention is the BBS (Bulletin
  Board System) Network which provides a Global Electronic Mail Service
  for us all.

  A BBS, sometimes referred to as a PBBS (Packet Radio BBS), is a computer
  based Packet Radio system, probably run by some generous local
  enthusiast or the local club, which provides unattended (usually 24
  hours per day) access for the purpose of storing and forwarding
  messages. They are often used as a central store for data files too so
  we can transfer programs and other files to or from the BBS.

  Telephone BBS systems have been around for years, before Packet Radio
  came into being, so you might be familiar with those. The concept is the
  same, but we use radio as the medium instead of the telephone.

  This is very useful for sending messages to friends (or enemies too I
  suppose) whether they are currently in their shack or not. The BBS
  mailbox allows us to leave a message addressed to another station and
  when that other station connects to the BBS they will be able to read
  our message. This has become such a useful feature that most TNCs now
  offer a private mailbox. And so paKet has also been provided with a
  mailbox facility. Even if your TNC doesn't have one, you can still have
  messages left in your system while you are out.

  The concept was expanded when Hank Oredson (W0RLI) developed an
  automatic forwarding system between PBBS systems. Then we could leave a
  message on our local BBS system and if that message was addressed to
  someone in another area the BBS would determine where to send it and, at
  regular intervals in the day or night, it would automatically send our
  message to the next BBS system. As the "network" developed, our mail
  would hop from one BBS to another until it reached the desired
                               Page   5


  destination. The world is getting smaller! I often receive messages from
  the other side of the world, and usually find they take less time than
  an Air Mail letter.

  Next we saw the concept of Bulletins. This is a general message that is
  broadcast to anyone and everyone rather than a personal message
  addressed to one particular station. Bulletins may be "addressed" to
  some topic such as IBM or HUMOUR or HELP or MORSE... The topics help us
  to get some idea of what the Bulletin is about so we don't have to read
  every message that appears on the BBS. Bulletins are usually forwarded
  to every BBS system in the area, so if there is a Bulletin around, it
  will probably, eventually get to your local BBS for you to see.

  Personal Mail is usually addressed to a station @ (AT) some BBS address.
  For example the local BBS in this area is run by Arthur VK2ATM. So if
  you want to send a message to me you would send it to VK2DHU @ VK2ATM.
  There must be millions of Amateur Packet Radio  callsigns in use around
  the world but there are a limited number of BBS systems so it is easier
  to track down VK2ATM than it is to find VK2DHU. This problem is further
  reduced with the introduction of Hierachical Addressing which is a
  system of specifying more than just the BBS callsign, adding State,
  Country and Continent (or Region) details. For example, my full Packet
  address according to today's convention is VK2DHU @ VK2ATM.NSW.AUS.OC
  (meaning this station is in the State of New South Wales, in Australia,
  in the Oceania Region).

  Bulletins may be addressed to one particular BBS (eg to MORSE @ VK2ATM)
  but more commonly they would be issued to cover to a wider area (eg to
  MORSE @ ASIA). Then the Bulletin would be passed on from one BBS to the
  next within that area, and every BBS would have that Bulletin available
  for users to read.

  Perhaps if you are new to the world of Packet Radio, the best way to
  find out about BBS systems, Bulletins, etc is to get on the air and talk
  to the locals. They are in this hobby too and invariably will be keen to
  help the newcomers.
























                               Page   6


What is paKet?

  paKet is a communications program developed especially for use with
  Packet Radio, providing all the facilities required for Packet Radio
  communications.

  It is designed to run on an IBM compatible computer system (minimum
  384KB) and a (preferably TAPR-compatible) Terminal Node Controller (TNC).

  In addition to providing the usual Terminal Mode where you can send and
  receive data via the TNC, the program provides many features and
  facilities to enhance the operation of your Packet Radio system. Such
  features include:

    Interrupt driven communications
    Runs on COM1, COM2, COM3 or COM4
    Flashback feature
    Disk and/or printer logging
    ASCII text file transfers
    paKet-Protocol, an exciting new binary protocol
    YAPP Binary File transfer protocol
    BayCom Binary File transfers (some versions of Digicom supported too)
    There's even a RAW Binary mode (no protocol) for manual control
    Full online TNC help for your TNC commands
    Online Manual - this entire Manual is available in a pop-up window
    Both Hardware and Software Handshaking supported
    Multiple windows for up to 10 simultaneous connections
    REMOTE Mode - (unattended access)
    Personal Message System
    Contest Mode for monitoring sporting event results (eg Triathlon)
    Access to DOS, your favourite editor, and file LISTer from within paKet
    Automatic Script processing
    etc etc etc

  paKet is fully configurable so you can customise a system especially to
  suit yourself.   Setting up your system is but a matter of a few
  keystrokes - see the Configuration Windows section of this document for
  details.

  For existing paKet users, there have been many, many changes. Some quite
  small, some cosmetic, others much more significant. Most of the changes
  have been suggested by you the paKet community and reflect the wishes of
  experienced users. Some suggestions could not be implemented but I have
  tried to respond to all your ideas. When an idea is put forward by more
  than one user I have tried even harder to implement that idea. Refer to
  "Changes in Version 5" below for a summary of the major changes.

  paKet is a sophisticated communications system and it may take you a
  while to become familiar with all its features, especially if this is
  your first look at paKet, but it is designed to be "friendly" and as
  easy to use as possible.  Help is always available at the touch of the
  <F1> key if you forget what key to press. However, you really should
  read through the entire Manual to get the most from the paKet system.







                               Page   7


Changes in Version 5

  This section might not be too meaningful to you if you are seeing paket
  for the first time, but for those upgrading from an earlier version, you
  might like to have some idea of what's new in Version 5.

  Here I have indicated some of the major changes, not in any particular
  sequence, but as they occurred to me. There are lots of small things
  that have been done but not documented here. Things that I considered
  needed tidying up or improving.


  Now for a summary of the major changes:

     "PAKET" is now "paKet".  It doesn't make the program run any better,
     just makes the name a little more identifiable.

     Larger Manual - now divided into 2 separate data files because it
     wont fit on a single 360K diskette, and it may be viewed in a popup
     Window during paKet operations!

     New, improved Install program to simplify the Installation process.

     Binary Transfers now include:
        - YAPP Protocol (continued from paKet 4);

        - paKet Protocol (pP) a new YAPP compatible protocol which
          provides for automatic restart in the event of an aborted
          transfer;

        - BayCom support for its PRG (binary file) format;

        - Digicom' PRG format is also supported;

        - A RAW Binary Mode is provided for manual synchronisation using
          the TNC's Transparent Mode.

     Some added support for the Kantronics range of TNCs.

     Improved handling of Binary Transfers when STREAMDBL is OFF. This is
     mainly to allow Kantronics users to enjoy Binary Transfers with paKet.

     Alerts facility. You may specify certain strings which will trigger
     an alert bell if any of those strings appear in the Communications
     Window.

     Message level option allows the paKet operator to hide some of the
     routine messages which can sometimes become tiring for the more
     experienced operators.

     Optional Screen Blanker with variable blank time.

     When a Disk Directory is displayed a file Rename or Move option
     allows data files to be renamed or even moved to another directory
     with the <Alt-R> key.

     Additional TNC Help files have been included, thanks to some generous
     paKet users who have contributed these new data files. There are now
     5 TNC Help files supplied with this version of paKet.

                               Page   8


     Several improvements to REMOTE Mode, including:
        - optionally issuing the REMOTE Menu when another station
          connects.

        - Configurable REMOTE Trigger in case the user is having problems
          with the default <Ctrl-]> Trigger in his area.

        - full PMS accessable by REMOTE users.

        - access to multiple directories by REMOTE users (at the
          discretion of the paKet operator).

        - additional REMOTE Menu options to handle the PMS and to provide
          BayCom operators access to the paKet system for Binary File
          Transfers in both directions.

     Type Ahead Buffer handling improved.
        - Buffer capacity is now set to the number of lines configured for
          display.

        - Word Wrapping is improved.

        - Recall facility, like DOSKEY or CED, allows previously sent
          lines to be recalled and either edited or simply resent without
          retyping.

        - Full text editing facilities are now available on the Type Ahead
          data.

     The Script system has been enhanced with several new commands:

        - now there is no limit to the size of a Script process because
          this version provides for nested scripts where one Script can
          CALL another Script. In addition, the maximum size of each
          Script is doubled to 200 lines.

        - The Delay command will now wait until a specified time-of-day as
          well as an option to wait for a specified number of seconds.

        - Echo command allows you to echo a string to the system as if
          that string had been received from the other station. Provided
          mainly for documentation purposes.

        - Flags. The Script system now allows you to set, test and clear
          flags. This gives you more flexibility in programming.

        - Return command is provided, especially to allow a nested Script
          to return to the "Mainline" or calling Script.

        - A Trap facility allows you to specify one or more strings and
          tell the Script system to goto a particular label if one of
          those strings is received at any time during this Script process.

        - You can now perform any DOS command from within a Script. A
          little imagination reveals mind-boggling possibilities here.





                               Page   9


     Some keys have changed functions. (Apologies to existing paKet users,
     but the number of changes is small and, I think, for the better):

        - <F6> is now used to Send an ASCII text file.

        - <Alt-A> is now the toggle for Alerts;

        - <Alt-E> is now the System Editor key;

        - <Left-Arrow> and <Right-Arrow> are now used for Type Ahead
          buffer editing; selecting the next or previous Communications
          Window is now done with <Shift-Left-Arrow> or
          <Shift-Right-Arrow>.

        - <Up-Arrow> and <Down-Arrow> are now used for Type Ahead Recall;
          moving the Flashback display a single line is now done with the
          <Shift-Up-Arrow> and <Shift-Down-Arrow> keys.

        - <Home> and <End> are now used for Type Ahead Buffer editing.
          <Ctrl-PgUp> and <Ctrl-PgDn> are now used for Top and Bottom of
          the Flashback buffer.







































                               Page  10


Other Communications Modes

 paKet is a COMMUNICATIONS program and must be used with a TNC or Modem.
 It provides communication facilities but does not perform the decoding of
 packets - that is done in the TNC!   Neither will paKet decode any of the
 other communications modes such as Morse, RTTY or AMTOR. These modes too,
 are decoded by the TNC.

 Not all TNCs handle these modes so if this is what you want to do you
 will need one of the Multi-Mode TNCs available (such as the KAM, MFJ-1278
 or the PK-232) which decode these other modes. If you have one of those
 TNCs, you can use paKet for modes other than Packet Radio.
















































                               Page  11


The paKet Documentation.

  This documentation is supplied in two compressed files because a it is
  too large to fit on a single 360K diskette.  The two files, when
  expanded, are REF5.DOC and GUIDE5.DOC.

  These two files may be combined into a single DOC file if you have the
  space. This would be the preferred solution as you can then have the
  entire Manual available in a pop-up window during paKet operations
  (refer the <Alt-F1> key later).  The supplied INSTALL program, will
  attempt to combine these files into a single file PAKET.DOC if you had
  the space available on the output drive at the time of Installation.


  The REF5.DOC is the Reference Manual. The document explains all of
  paKet's Windows, with an example and explanation of each. Every message
  in the paKet system is listed with an explanation of what it means and
  what you have to do about it. And it contains information on all the
  keys paKet recognises plus details of all the functions available to you
  the paKet user.

  The GUIDE5.DOC is the User Guide explaining various sub systems such as
  REMOTE Mode, paKet's Personal Message System, Script Processing, the
  unique Contest Mode, plus various other sections that you may find of
  interest.



































                               Page  12


PART II - paKet's WINDOWS
paKet's Windows - Overview

  paKet uses a number of windows for all its operations.

  Do not confuse this with the popular Microsoft Windows product. You do
  not need any other software to run paKet.

  Some of paKet's windows are there permanently, others will pop up on
  demand. For example, the Communications Window is always there although
  it might be partly hidden by other windows at times.

  Some windows do not look like "windows" because they do not have a full
  box-style border. For example, the Communications Window uses all 80
  characters for its communications data, so there is no room for a border
  line down the sides. It does, however, have a border line at the top
  known as its Header Line.

  paKet uses whatever text screen is in operation when it is called.  When
  using an EGA or VGA display, if you were using 40, 52 or 60 lines and
  paKet is then called, you will find paKet now has a larger
  Communications Window where vast amounts of information can be viewed at
  once, and larger type-ahead areas (as detailed below) become practical.
  A larger monitor is desirable.

  Each of paKet's Windows is described, in alphabetic sequence, in the
  following sections. An example of the window is shown and the purpose
  and operation of each is discussed.
































                               Page  13


Binary File Transfer Window

 Example:

    ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ paKet Protocol File Transfer ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
    º Receiving File  :       VIDPARK.ARC                           º
    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
    º File Size       :    3,375        Time to complete :  00:00:04º
    º Bytes Received  :    3,036            Elapsed time :  00:00:32º
    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
    º Progress        :       89%       Bytes per second :     94   º
    º ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ>±±±±±±± º
    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
    º Last Packet Recd:  DT - Data Packet                           º
    º Current Status  :  Receiving data                             º
    ÈÍÍÍÍÍÍÍÍÍÍÍÍ Press Esc to abort the file transfer ÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


 Description.
   During the transfer of a Binary File, this window is displayed to keep
   you informed of progress. It is used for all types of Binary Transfer,
   the top line indicating the Protocol or method in use. That could be:
      paKet Protocol (as shown in this example),
      YAPP,
      BayCom (including Digicom) or
      RAW Binary (no protocol at all).

   In the example above, paKet is receiving the file VIDPARK.ARC from the
   other station; the size of that file is 3,375 bytes and the display
   shows the transfer is 89% complete with 3,036 bytes received at this
   stage. paKet has calculated the bytes per second at 94 since the
   transfer started, and as it knows how many bytes still to go, it can
   calculate the estimated time to complete (4 seconds in the example).

   The arrow under "Progress" is a "strip meter" or histograph which gives
   a proportional indication of the percentage complete.

   The "Last Packet Recd" field indicates some useful information at the
   beginning of the file transfer as you can see how the handshaking is
   progressing. During the transfer though, this does not change much.

   The "Current Status" field too, should not change much during the
   transfer, but it helps to see what is happening at the beginning and
   end.
















                               Page  14


Communications Windows

 Example:

 ÄÄÄ   50 ÄÄÄÄÄÄÄÄÄÄ Window 1 - Stream A - VK2DHU ÄÄÄÄPaused with ScrLockÄÄÄ
 cmd:echo off
 ECHO     was ON
 ECHO     now OFF
 cmd:



 Description:
   These windows, one for each connected stream, contain all
   communications information flowing to and from the TNC. All data sent
   to the TNC is displayed in a highlight colour or shade, while all data
   received from the TNC is displayed in the normal colour or shade.

   This window is 80 columns wide, so there is no border as such although
   the top line of this window is referred to as the Communications Window
   Header Line.

   Some TNCs use the term "channel" while others use "stream" but this
   Manual will use "stream" to identify the different user connections.


 The Communications Window Header Line.
   Each Communications Window's Header line identifies the current Stream
   and also the callsign of the station you are connected to (or "Not
   Connected" as appropriate).

   In the example shown above, the Header line indicates you are connected
   to VK2DHU on stream A in the first Communications Window. If the
   callsign does not appear to be correct, you can verify it with the
   <Alt-V> function, which is explained in detail in the section "Special
   Keys".

   On the left of this header line you will see a counter displaying the
   number of characters waiting in this window's input buffer (50 shown in
   the example). Usually the system will process the input characters as
   they are received so this part of the display would be blank. However,
   it is possible to have characters build up in the buffer if you are
   receiving the input characters faster than your computer can process
   them, or if processing has been suspended for any reason.

   If the data is coming in too quickly for you to read, you can pause the
   display by pressing the <ScrollLock> key.  While paused, a reminder
   message is displayed to the right of the Header Line, as illustrated in
   the example above.  To "un-pause" press <ScrollLock> again. This action
   does not stop the data coming in from the TNC - the data is captured
   and stored in paKet's input buffers until you are ready to continue.


 Multiple Communications Windows.
   You may configure paKet with up to 10 separate Communications Windows.
   When you are connected to more than one station, a separate
   Communications Window is used for each connection. Each Window is
   associated with one of the TNC's streams, and when you switch windows
   the TNC is automatically switched to the corresponding stream.

                               Page  15


   To switch from one window to another, press <Shift-Right-Arrow> or
   <Shift-Left-Arrow>, that is hold down the Shift key while pressing
   <Right-Arrow> or <Left-Arrow>. Another way to select a different window
   is to hold the Shift key while pressing a Function key (eg: press
   <Shift-F3> for the third window). The Communications Window Header Line
   will change to indicate the new window number and the TNC stream used
   with that window. Here you can make contact with the other station and
   all communications for the associated stream will appear in that Window.

   Changing streams will not change the TNC's operating Mode. So, if the
   TNC was in Command Mode and you change to another stream, the TNC will
   remain in Command Mode, regardless of whether you are connected to a
   station on that new stream or not. You will need to enter K or CONV to
   switch to Converse Mode.

   If any data is received for a Stream other than that currently
   displayed, it will be diverted to the appropriate Communications Window
   and an indicator will appear in the Status Window under "Windows". If
   that happens when you are connected to two stations, you will know the
   "other" station has sent you a message and you can switch to that
   window to see it.

   I personally can work two or three simultaneous connections without
   much problem, but any more I find rather challenging. So, it should be
   noted that although paKet allows up to 10 Communications Windows, most
   of those would not be used.  As buffers etc, have to be allocated for
   each window, it would be advisable to configure a lesser number to
   conserve memory. I think 3, or at most 4, windows would be more than
   adequate for most users.

   To avoid confusion, it would be a good idea to set your TNC's USER
   parameter to match the number of windows you configure. Then, if you
   have three windows configured and you are already connected to three
   stations, a fourth station would get a "Busy" message from the TNC
   rather than confuse things on the screen.  If your TNC has a PMS on a
   separate callsign, you could set the TNC's USER parameter to one more
   than the number of windows configured.

   paKet is almost a Multi Tasking program in that several sessions can be
   processed simultaneously, some of which may be processing in the
   background. However, I do not consider paKet to be true Multi Tasking
   and it is not promoted as such. For example, the processing for Binary
   File Transfers is NOT multi tasking and you may not conduct more than
   one simultaneous Binary File Transfer.

   It is unfortunate the original TAPR TNC (from which all modern TNCs are
   derived) did not include a Monitor stream. Consequently any data that
   is monitored on the frequency is not identified by the TNC as belonging
   to a particular stream - it comes through on whatever stream is
   currently selected. So, if you have selected window 2 and some
   monitored data is received from the TNC, it will be displayed in Window
   2.   I prefer to have the TNC's MCON set to OFF to disable monitoring
   while connected (paKet turns MCON off automatically for binary file
   transfers).






                               Page  16


Communications Windows - Flashback.

 Example:

 ÄÄÄ 1250 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄFLASHBACK - (Esc when finished)ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 CONNECT VK2ATM-1
 cmd:cmd:12-Oct-91  16:22:52  *** CONNECTED to VK2ATM-1
 [AIZ-4.20-MH$]
 G'day Tony
 VK2ATM BBS>


 Description:
   The Communications Windows will also display Flashback data.
   Flashback is a facility that allows you to redisplay earlier
   communications activity that has scrolled off the screen.

   To select Flashback Mode, press <Shift-UpArrow>, or <PageUp>.

   The Communications Window Header line will indicate FLASHBACK as shown
   in the example above. You can scroll up and down with:

      <Shift-Up-Arrow>
      <Shift-Down-Arrow>              (one line at a time)

      <PageUp>
      <PageDown>                      (one page or screenful)

      <Ctrl-PageUp>                   (top or
      <Ctrl-PageDown>                  bottom of Flashback data)


   The amount of data held in Flashback is configurable up to 64KB for
   each Communications Window.

   While you are in Flashback, any incoming data is held in the input
   buffer until you have finished (1250 characters shown in the example
   above) so be sure to return to normal communications mode when you have
   finished scanning the Flashback data.

   When scrolling forward, paket will detect the end of the Flashback
   buffer. If there is some further data waiting to be processed, pressing
   <PageDn> will display one more page of data from the buffer and paKet
   will stay in Flashback Mode. If you reach the end of the Flashback and
   there is no data further waiting in the input buffer, paKet will
   automatically return to normal communications mode.

   While in Flashback Mode you can press the <Esc> key for an immediate
   return to normal communications mode.











                               Page  17


 Communications Window - Flashback - Text Find.
   paKet has a Text FIND facility which will search backwards through the
   Flashback buffer for a user-defined string of characters.

   Press <Alt-F> to activate the Find facility.

   The Message Window will pop up where paKet will ask you for the string
   you wish to search for. It does not matter whether you enter the string
   in upper or lower case because the search is not case sensitive - both
   upper and lower case will be matched.

   The search begins with the current line in the Communications Window,
   moving back through the Flashback buffer until either a match is found
   or until the beginning of the Flashback buffer is reached. If a match
   is found, searching stops and the line containing the matching text is
   highlighted.

   If you want to continue the search, "looking" for another match of the
   same string, press <Alt-L> and the search resumes.

   Alternatively you can press <Alt-F> again to begin a search for another
   string.

   The Find facility will automatically put paKet into Flashback mode.




 Communications Window - Write Flashback buffer to disk.
   Although paKet provides a disk log facility, it is possible you have
   received something to want to keep but find the log file was not active
   at the time.

   To cover this situation, paKet has a facility to write the Flashback
   buffer to disk.

   Press <Alt-W>, and paKet will ask you for the name of the file you wish
   to use. You also have the opportunity to continue logging to this file
   if you wish. Just follow the instructions on the screen.





















                               Page  18


Configuration Windows - Overview

   As mentioned earlier, paKet is fully configurable and you can set up
   various parameters to configure the system to suit your own needs.

   With the Online Configuration facility you can call up the
   Configuration Windows at any time (with the <Alt-Z> key) and change any
   of the settings.

   Most changes will take effect immediately although there are some that
   will not become effective until the program is next started. Examples
   of these are where you change the size of the allocated buffers. These
   changes are not implemented immediately because memory is allocated at
   the beginning of the run and the buffers are already in use. The new
   buffer sizes will become effective when paKet is next started.

   The following sections describe the various Configuration Windows and
   the parameters you can change. There are two, sometimes three levels of
   Configuration Window.

   Select the desired option by either:
     1. Typing the option number; or
     2. Moving the Cursor to the desired option and pressing <Enter>; or
     3. (In many cases) typing the first letter of the option.

   For example in the following section, where the System Configuration
   Window is displayed: you could select REMOTE Mode options by
   typing "6" or "R", or you could move the cursor to that item with the
   <Down-Arrow> key,  (or press the <End> key then three <Up-Arrow>s!).

   Press the <Esc> key when finished with a Configuration Window to return
   to the previous level.




























                               Page  19


Configuration Windows - System Configuration

 Example:

                     ÉÍÍÍÍÍÍSystem ConfigurationÍÍÍÍÍ»
                     º 1. Serial Port...             º
                     º 2. Multi User options...      º
                     º 3. Comms Window settings...   º
                     º 4. Colours...                 º
                     º 5. KB Macros/Auto commands... º
                     º 6. REMOTE Mode options...     º
                     º 7. File Transfer options...   º
                     º 8. File/Directories...        º
                     º 9. Miscellaneous options...   º
                     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

 Description.
   This System Configuration window appears when you select the online
   Configuration option with the <Alt-Z> key.

   This System Configuration Window reveals a menu of various
   configuration options.  To better manage the large number of options,
   they have been subdivided into the categories shown in the above window.

   Each of the options in the System Configuration Window has its own
   Configuration Window  which will be dealt with in turn in the following
   sections of this Manual.

   When you have finished with the Configuration options, press <Esc> to
   return to normal communications mode.






























                               Page  20


Configuration Windows - Serial Port

 Example:
                     ÉÍÍÍÍÍÍÍÍ 1. Serial Port...ÍÍÍÍÍÍÍ»
                     ºCOM Port                        1º
                     ºBaud Rate                    2400º
                     ºParity                       Noneº
                     ºData bits                       8º
                     ºStop Bits                       1º
                     ºHandshaking                     Hº
                     ºDCD ON when Connected?          Yº
                     ºTNC cmd: exit               BREAKº
                     ºCommand to Initialise TNC RESTARTº
                     ÈÍÍÍÍÍÍPress ENTER to changeÍÍÍÍÍÍ¼

 Description.
   This window appears when you select option 1 from the System
   Configuration Window. It contains the parameters paKet uses for the
   computer's Serial Port parameters.

   The Serial port must be set correctly if paKet is to communicate with
   the TNC.  The aim here is to configure paKet to match your TNC settings.

   As there are a limited range of valid settings here, paKet does not
   expect you to remember the valid values. Instead you just press <Enter>
   and it will display the next valid value for that item.

 COM Port
   So, starting with the COM Port, press <Enter> to toggle from COM1 to
   COM2, COM3, COM4 and back again.  Only those COM ports actually
   recognised by your system will be offered, so if you do not have a COM3
   port installed you will not be given that option!

   If you have COM3 and/or COM4 installed but these are not being offered
   by paKet as options here, it is likely your computer system is one
   (like the original IBM PC) that does not automatically recognise these
   ports. Run the supplied COMINIT program and try paKet again. If this
   fixes the problem, I suggest you add COMINIT to your AUTOEXEC.BAT file.

   Many people do not realise that COM1 and COM3 usually share the SAME
   interrupt line - IRQ4  (COM2 and COM4 share another interrupt line -
   IRQ3).  This makes it difficult to handle the additional ports and is
   why a lot of software does not support more than COM1 and COM2.

   Let's say, for example we have a mouse on COM1 and the TNC on COM3. If
   a character is received from the TNC, an Interrupt occurs on IRQ4 which
   means the system will give paKet a nudge to go process the incoming
   character.  The trouble is, paKet gets the same nudge if you move the
   mouse because the same IRQ4 Interrupt occurs!  I have catered for this
   situation and paKet will determine if the Interrupt was caused by our
   Serial Port or the "other one", and will either process it or pass
   control over to the other driver for its own processing.

   There are a couple of considerations here if you want to use these
   additional serial ports.  Firstly, load paKet AFTER loading the other
   software (drivers, etc). Then paKet will be called first when the
   Interrupt occurs. If it is the other way around, we are depending on
   the other software to make these decisions and they may not handle the
   shared interrupts correctly.  Secondly, I suggest you choose a lower
   baud rate (say maximum 2400) for the paKet/TNC link to help reduce
                               Page  21


   conflicts. I tested it at 9600 baud and it worked satisfactorily, but
   if two interrupts occur on the same IRQ line at EXACTLY the same moment
   in time, I am not confident the system will process them both
   correctly. The lower baud rate will reduce this possibility.

   The COMINIT program developed by Dr. Paul Webster VK2BZC, includes some
   technical documentation on the use of the additional COM ports.
   (Thanks Paul - where would I be without him?).


   When the desired port is displayed, press <Down-Arrow> to move down to
   the next item, Baud Rate.

 Baud Rate
   Pressing <Enter> on the baud rate field will cycle through the valid
   values which range from 50 baud to 19200 baud.  This option sets your
   COMPUTER's serial port baud rate; the TNC also has a baud rate setting
   which must match the value chosen here.

 Parity and
 Data Bits
   You may set Parity and Data Bits to any of the displayed values but
   paKet prefers a setting of No Parity and 8 Data Bits. So unless you
   have special reason to change, please set Parity to None. You will
   notice the Data Bits parameter will automatically be set to the correct
   value.

 Stop Bits
   Stop Bits would normally be set to 1.

 Handshaking
   Handshaking is either H (for Hardware) or S (for Software).

   These options are discussed under "Hardware vs Software Handshaking" in
   the Technical Section of this Manual. If you are not sure which to use,
   try Hardware mode - paKet will tell you if it cannot see the signals it
   needs for Hardware handshaking!

   It is important to tell the TNC which mode to use too:
      for Hardware Handshaking, set XFLOW OFF;
      for Software Handshaking, set XFLOW ON.

 DCD ON when Connected?
   This is either Y(es) or N(o) and should be set to match the TNC's
   DCDCON option.

   Most TNCs have the DCDCON option which, if used, will switch on the DCD
   line in the RS-232 cable when we are connected to another station.

   paKet relies to a large extent on the "Connected" message from the TNC
   to determine whether we are currently connected to another station. If
   you are monitoring the frequency and someone sends a string of
   characters that happens to look like a "Connected" message, paKet can
   easily get confused and take that data to be a signal from the TNC that
   we have just connected to someone!  Fortunately this does not happen
   too often but if you use this DCDCON option, the risk of this problem
   occurring is greatly reduced.

   If you set this option to "Y" paKet will look at the status of the DCD
   line whenever it monitors a "Connected" message before deciding to
                               Page  22


   accept it as a new connection. If the DCD line is still low, it will
   display a warning message, ignore the "Connected" message and continue
   monitoring.

   If your TNC supports the DCDCON option and you are using Hardware
   Handshaking, it is recommended you use this feature.

 TNC cmd: exit
   This parameter has three valid values: <BREAK>, <CtrlC> or <Esc>.

   Most TNCs support the <BREAK> signal and will return to Command mode
   when this signal is received. This is the preferred option so try this
   and choose one of the others only if the <BREAK> does not work on your
   system.

   As a second choice for all TNCs except the old TNC-1, the "Command"
   code (which should be set to the default of <Ctrl-C> in your TNC) would
   be used. So, unless you have a TNC-1, choose this <Ctrl-C> option if
   <BREAK> does not work for you.

   Finally, if you have a TNC-1 which does not have a Command Mode, each
   command must be entered by sending <Esc>, then the command, followed by
   <Enter>. So you can set this option to <Esc>.  Then when you type
   <Alt-B> paKet will actually send the <Esc> code to the TNC!

 Command to Initialise TNC
   Most TNCs use the RESTART command to perform a warm start of the TNC.
   This is required to activate any changes to serial port settings so
   paKet will issue this command to the TNC after you change any of the
   Serial Port parameters (assuming you have already changed the TNC).

   However, the Kantronics TNCs use the RESET command for this so the
   option is provided here in case you have one of those TNCs.

   Please take care with this, because the RESET command, on most TNCs,
   will clear every setting you have made and return the TNC to its
   factory settings!   RESTART is the normal command here.


 Any of these parameters may be altered at any time, but of course you
 will also need to change the TNC settings to match. For example if you
 want to alter the Data Bits setting, you have to change both paKet (via
 this Configuration Window) and change the TNC with a command such as
 AWLEN. If you change one and not the other, you will probably get garbage
 on the screen and will fail to communicate correctly.


 With most TNCs, any change to its serial port settings will become
 effective after the TNC is next initialised. So, I suggest the following
 procedure to change Serial Port settings:
   1. Issue the commands to the TNC to change its settings. (They will not
      take effect until you initialise the TNC - usually with a RESTART
      command).
   2. Call up paKet's Online Configuration and enter the desired Serial
      Port parameters to match the new TNC settings.
   3. Reply "Y" when paKet asks if you would like it to initialise the TNC
      with a RESTART command.
 Then both the computer and the TNC will continue with the new settings.

 Press <Esc> when you have finished with the Serial Port parameters.
                               Page  23


Configuration Windows - Multi User options

 Example:
                ÉÍÍÍÍÍ 2. Multi User options...ÍÍÍÍÍ»
                º Maximum no. of Comms windows    3 º
                º Stream-Switch character         | º
                º STREAMDBL (CHDOUBLE) option    ON º
                º Alpha or Numeric Stream Id?     A º
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


 Description.
   This window appears when you select option 2 from the System
   Configuration Window. It contains the options you have regarding the
   use of multiple simultaneous connections with other stations.


 Maximum no. of Comms windows
   The first item specifies the number of Communications windows you would
   like to allocate. paKet uses a separate Communications window for each
   of the simultaneous connections. This field may be any value between 1
   and 10.

   You should keep the number down to a reasonable figure because they all
   take up some memory and it would be a waste to configure say, all 10
   windows when you might hardly ever use more than 2 or 3.

   As the present number of windows have already been allocated, the new
   value will not take effect until the next time you start the paKet
   program.

   To help avoid confusion, it is considered desirable to set your TNC's
   USER parameter to the same value used here, or perhaps to one extra if
   the TNC allocates a separate callsign to its PMS stream to allow one
   user to use that as well.


 Stream-Switch character
   The Stream-Switch character is the code used by paKet and by the TNC to
   signal a change of stream.

   Most TNCs use the vertical bar character ("|") as the default but you
   could change it to any other character if you wanted to. The important
   thing is to have both paKet and the TNC using the same character.

   The TNC command to change this value is probably either STREAMSW or
   CHSWITCH.

   paKet currently supports only one STREAMSW character so if your TNC has
   two ports (and two STREAMSW characters) you should set paKet's value to
   correspond to the port you mostly use.









                               Page  24


 STREAMDBL (CHDOUBLE) option
   STREAMDBL (called CHDOUBLE in some TNCs) is a TNC facility to help
   avoid confusion where the STREAMSW character is received as part of a
   data packet.

   For example, the vertical bar character ("|") that is usually used as
   the STREAMSW character is also often used as a graphic character to
   draw vertical lines or for drawing boxes. When paKet receives this
   character from the TNC it must decide whether the TNC is indicating a
   change of stream or whether this is just another data character
   received over the radio.

   If you set this STREAMDBL option ON, the TNC will generate TWO of these
   characters whenever one is received over the air - then paKet can tell
   the difference and there will be no confusion. So you can see once
   again, that both paKet and the TNC need to have this option set the
   same way.


   It is STRONGLY RECOMMENDED the facility be used so set this option ON
   in both your TNC and in this Configuration Window.


   If set OFF, paKet will assume any STREAMSW character received during
   Converse Mode is to be processed as a change of Stream; if received
   during a Binary File Transfer it will be included as a data character
   in the file. This will probably be correct in most cases but you need
   STREAMDBL to be sure.

    ************************** I REPEAT *******************************
    *  (because this has been one of the main causes of Binary File   *
    *        transfer problems in earlier versions of paKet)          *
    *                                                                 *
    * Set STREAMDBL ON in BOTH paKet's Configuration AND in your TNC. *
    *                                                                 *
    *  If this feature is not implemented in your TNC then set this   *
    *                     option in paKet OFF.                        *
    *******************************************************************

   Users of Kantronics TNCs will find their TNC does not support the
   STREAMDBL command, so you will have to set this option OFF. Please
   refer to the discussion on the Kantronics TNCs in the Technical Section
   of this Manual.


 Alpha or Numeric Stream Id?
   Although most TNCs use letters of the alphabet to identify the
   different streams, some use numeric channel numbers. This configuration
   option allows you to use paKet with either type of TNC.











                               Page  25


Configuration Windows - Communications Windows

 Example:
 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Communications Windows ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 º                 Window Number -     1   2   3   4   5   6   7   8   9  10º
 º TNC Stream Identifier               A   B   C   D   E   F   G   H   I   Jº
 º Input buffer size     (0-32K)       2   2   0   2   2   2   2   2   2   2º
 º Flashback buffer size (0-64K)      64  10   4   4   4   4   4   4   4   4º
 º Word Wrap from                     48  48  48  70  70  70  70  70  70  70º
 º Screen width (normally 79)         79  79  79  79  79  79  79  79  79  79º
 º Bells (0 - 3 or 250 - 999)          1   2   1 700 700 700 700 700 700 700º
 º Telephone style connect bell        Y   Y   Y   Y   Y   Y   Y   Y   Y   Yº
 º Process data without viewing?       Y   Y   Y   Y   Y   Y   Y   Y   Y   Yº
 º Display Status Window?              Y   Y   Y   Y   Y   Y   Y   Y   Y   Yº
 º Display Type Ahead Window?          Y   Y   Y   Y   N   N   N   N   N   Nº
 º Number of Type Ahead lines          2   2   3   2   2   3   3   3   3   2º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍ Press Tab key to move to the next Comms Window ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

 Description.
   This window appears when you select option 3 from the System
   Configuration Window. It contains parameters relating to each of the
   Communications Windows you have configured.

   Each column of values relates to the settings for that window number.
   Press <Enter> or <Up-Arrow>/<Down-Arrow> to move to different settings
   in that column. Use the <Tab> key to move across to the next column.
   Note, paKet will use only those values for the windows you have
   configured (refer "Maximum no. of Comms Windows" in the previous
   section). So if you have configured only 3 windows, the values for
   windows 4 to 10 in the Example window above are ignored by paKet.


 TNC Stream Identifier
   This is the letter or number used by the TNC to identify the different
   streams. You would normally use stream A in window 1, B in 2, and so
   on. However, paKet can handle any combination so if, for some reason,
   you wanted paKet to use TNC stream B in window 1 and stream A in window
   2, just specify these streams in the above Configuration settings.

   Some TNCs use a particular stream for their PMS. For example if your
   TNC uses stream K for your PMS, you could specify stream K for one of
   the configured windows.  Note that a programming blunder in some TNCs'
   firmware versions prevents access to stream K in the TNC, though it
   cheekily issues connect and disconnect messages on that stream!

   Of course, if your TNC uses numbers for its channel identifiers instead
   of letters, you would specify 0, 1, 2, etc instead of A, B, C, etc.


 Input buffer size (0-32K)
   Each Communications Window has an input buffer to hold the characters
   received for that stream and this option allows you to specify the size
   of that buffer.

   There is also one common 32KB System Input Buffer which is filled by
   paKet's Interrupt Handler as data is received from the TNC.  At regular
   intervals in the processing, paKet will take data from that System
   Input Buffer and distribute it to the appropriate Communications Window
   Input Buffer, according to the stream indicated by the TNC.

                               Page  26


   A large input buffer size for the Communications window should not be
   necessary; in fact you can specify 0 and not have one at all! If it is
   possible you will have multiple connections, a 2KB buffer (at least one
   screenful) could be allocated, but anything larger is unlikely to
   provide any benefits in normal circumstances.


 Flashback buffer size (0-64K)
   Flashback is a paKet facility that allows you to scroll back to view
   Communications Window information that has scrolled off the screen.

   This option allows you to specify the amount of memory to allocate to
   the Flashback buffer for this Communications Window. Of course a larger
   buffer will hold more information, but you will not be able to allocate
   64KB to all 10 windows and still hope to get all of paKet into the
   640KB allowed by DOS!

   If you are not sure how much to allocate, try setting 30KB in the first
   Communications window and 10K in the others. You can easily change
   these values later.


 Word Wrap from
 Screen width
   paKet has a Word Wrap facility that operates on data entered into the
   Type Ahead Window. If a word does not entirely fit in the "Screen
   width" specified, the whole word will be moved down to the next line.

   To paKet, a "word" is a string of characters separated by a space or
   end-of-line. So, if you are sending a line of dashes or some other
   graphic string, you will not want that "word" wrapped to the next line.
   To help avoid such problems, paKet will wrap a word only if it begins
   after a certain column, as specified in "Word Wrap from".

   For example, if the values in these two fields are 48 and 79
   respectively, paKet will wrap any word that does not fit on the line
   provided the word begins after column 48. (That is if the word is not
   longer than 32 characters).

   A Screen Width of 80 will work quite well to another paKet station, but
   will cause double-spacing when received on some lesser systems with bad
   "wrap" logic. I use a screen width of 79 on my system but you can
   specify 80 if you want to.


 Bells (0 - 3 or 250 - 999)
   This option determines the sound paKet makes when a <BEL> character is
   received from the TNC, or if paKet issues a Beep to alert the operator.

   A value of 0 means no sound, so paKet will effectively ignore any
   <BEL>s received, and will not sound any warning bells.

   1, 2 and 3 sound predefined tones. It is not easy to describe a sound
   in a print document, so change the value and try it!

   Values between 250 and 999 specify the audio frequency of the beep.




                               Page  27


 Telephone style connect bell
   This is a Y(es) or N(o) option.

   If set to 'Y', paKet will issue an Aussie telephone-style "ring" from
   the computer's speaker after a Connection is established if no
   keystrokes have been detected within 15 seconds. (It will not ring if
   you have enabled the Auto-REMOTE option where paKet automatically
   switches into REMOTE Mode on connection).

   This is to attract your attention in case you might have missed the
   fact that someone has connected to your system.

   Pressing any key-character will stop the "bell".


   If you are running multiple Communications Windows, it is possible some
   data will come into another window while you are not looking and,
   although the Status Window will display the other Window number, that
   message could go unnoticed. So, if this Telephone option is on, paKet
   will issue a "Call Waiting" (double beep) sound every 20 seconds if
   some data has some into another Communications Window and you have not
   yet selected that window to view it.



 Process data without viewing?
   When data is received from the TNC for the currently selected stream,
   it will be displayed in the Communications Window.

   However, if data is received for some other stream, paKet can either:

      - hold it in that other Communication Window's Input buffer until
        you are ready to select that window and view the data; or

      - process that data whether you have seen it or not. (It will still
        be available in that Communications Window's Flashback buffer).

   This option was originally provided for paKet's Contest Mode where a
   number of Checkpoints are constantly sending data to paKet for
   recording and automatic acknowledgement. paKet must not hold that data
   in the buffer, but allow it to be processed whether or not the paKet
   operator has actually viewed the data. While in Contest Mode, a setting
   of 'Y' will be assumed.

   If you set this option to 'N' paKet will hold the data in the buffer
   until you have selected that window to view it. However, I have found
   it is often nice to just allow the data to flow into the system - you
   can easily switch windows and use Flashback if necessary to view
   anything that may have come in.

   In either case, paKet will let you know if anything is received for any
   other stream as it will display in the Status Window the Communications
   Window number for that stream. For example, if something comes in to
   Communications Window 4, the Status Window will show "<---4->" under
   "Windows". So you will know if anything has been received, regardless
   of the setting of this option.

   Try it and see which method suits you best.


                               Page  28


 Display Status Window?
   This is a Y(es) or N(o) option.

   The Status Window occupies the top two lines of the screen and is
   continuously updated with the time and other information as things
   change during normal operations. The details on display are discussed
   in the section on Status Window in this Manual.

   I recommend this option be set to "Y" at least while you are new to the
   system, so the Status Window will appear.

   If you change this to "N" the Communications Window will start on the
   top line, effectively making that window 2 lines bigger.


 Display Type Ahead Window?
   This is a Y(es) or N(o) option.

   The Type Ahead Window appears below the Communications Window and, if
   used, may be configured to display from 1 to 9 lines.  This window
   allows you to type messages, commands, etc into paKet's Type Ahead
   buffer before they are sent to the TNC.

   There are several advantages in using this Window, so I recommend you
   set this option to "Y" at least while you are new to the system.

   Some advantages include word wrap, and a Recall facility (similar to
   the DOSKEY function in DOS 5), not to mention the ability to edit your
   typing before it goes to air!


 Number of Type Ahead lines
   The Type Ahead Window is optional (refer previous option), but if
   selected you can choose the number of lines to display.

   Valid values here are 1 to 9.

   The Type Ahead buffer capacity is limited to the number of lines
   displayed.





















                               Page  29


Configuration Windows - Colours

 Example:
                       ÉÍÍÍÍÍÍÍÍ 4. Colours...ÍÍÍÍÍÍÍÍ»
                       º 1. Message Window...         º
                       º 2. Communications Window...  º
                       º 3. Status Window...          º
                       º 4. Yapp Window...            º
                       º 5. Help Window...            º
                       º 6. TNC Help Window...        º
                       º 7. Type Ahead Window...      º
                       º 8. Configuration Windows...  º
                       º 9. Directory Window...       º
                       º A. Online Manual Window...   º
                       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

 Description.
   This window appears when you select option 4 from the System
   Configuration Window. It is a list of the various paKet windows for
   which the colours may be changed.

   If you are running a monochrome display, you might think this section
   would not apply to you, but you could try different settings to get a
   combination of highlighting and contrast that suits you best with your
   monochrome display.

   Selecting one of the items in this window will bring up yet another
   window showing three sets of colours:

                     ÉÍÍÍÍÍÍÍ 1. Message Window...ÍÍÍÍÍÍÍ»
                     ºNormal    Foreground   WHITE       º
                     ºNormal    Background   GREEN       º
                     ºHighlight Foreground   LIGHTGREEN  º
                     ºHighlight Background   BLACK       º
                     ºBorder    Foreground   WHITE       º
                     ºBorder    Background   GREEN       º
                     ÈÍÍÍÍÍÍPress ENTER to changeÍÍÍÍÍÍÍÍ¼


   As with the Serial Port options, you may change any of these settings
   by pressing <Enter> to cycle through the available options. As you
   change a colour, the new setting is displayed in the window. When you
   are happy with a particular setting, press <Down-Arrow> to move to the
   next item.

   Note that you have 16 colours available: for the foreground, the first
   8 colours are normal intensity and the second 8 are high intensity.
   Provided the display was in normal text mode, choosing a high intensity
   colour for the background will cause the display to blink.

   When you have finished changing colours, press <Esc>. You may then
   change colours for another window or by pressing <Esc> again, you are
   returned to the System Configuration Window.

   Note that in many cases, you will not see the new colours immediately.
   For example, if you change the Communications window colours, you may
   think it has not worked, but you will see the new colours coming up as
   new data is sent or received.


                               Page  30


Configuration Windows - Keyboard Macros/Auto commands

 Example:
                      ÉÍÍ 5. KB Macros/Auto commands...ÍÍ»
                      º1. Keyboard Macros...             º
                      º2. Begin Auto Commands...         º
                      º3. End Auto Commands...           º
                      º4. Alerts...                      º
                      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

 Description.
   This window appears when you select option 5 from the System
   Configuration Window.

   The Keyboard Macros facility provides up to 10 macro strings which may
   be generated and sent to the TNC at a single keystroke, well two anyway!

   Begin and End Auto Commands are some optional commands that may be sent
   to the TNC when paKet is starting up or proceeding to shut down.

   Alerts is a new facility that (again optionally) may sound the PC
   "bell" when a nominated string appears in the Communications Window.
   This feature could be used if you want to know when a particular
   callsign is on the air or if some particular topic is being discussed.

   Selecting each of the 4 options will bring up another window for the
   details, which are discussed below.


 Keyboard Macros

 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ1. Keyboard Macros...ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 1~BMAIL ON<Enter>MDC<Enter>L<Enter>                                        ³
 2~BB<Enter>MAIL OFF<Enter>                                                 ³
 3                                                                          ³
 473s from Tony in Port Macquarie<Enter>                                    ³
 5                                                                          ³
 6~BXMITOK T<Enter>                                                         ³
 7                                                                          ³
 8                                                                          ³
 9                                                                          ³
 0^CD<Enter>                                                                ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

 Description.
   There are 10 Keyboard Macros available and these are activated by
   pressing <Alt-1>, <Alt-2>, etc through to <Alt-0>. That is, the number
   keys along the top of the main keyboard (NOT the numeric keypad). The
   numbers 1 to 0 showing down the left side of the Window correspond to
   the macro key you wish to use.

   It was decided to limit the macro options to 10 number keys as most of
   the Alt-alpha key combinations are used for pre-defined paKet functions.

   Move the highlighted cursor down to the item you want to change and
   type your macro on that line. Press <Enter> to complete the entry. The
   <Enter> does not go into the string because there may be times where
   you do not want a Carriage Return at the end of the string.

                               Page  31


   If the first key you type is some data character, paKet will
   automatically blank out the line to allow you to create a new entry. If
   you want to edit the existing entry use one of the cursor movement keys
   to start (eg, <Right-Arrow>, <End>, <Home> etc) then paKet will
   retain the existing string for you to edit.

   If you have entered something on a line and change your mind, you can
   press <Esc> and paKet will ignore any changes you have made to that
   line. It is only when you press <Enter> or if you move to another line
   with <Up-Arrow> or <Down-Arrow> that paKet considers any changes to a
   line are complete.

   To delete a macro, move the cursor to that Macro and type <Ctrl-Y>.

   Many of the special keys used in paKet may be coded specifically using
   Less-Than/Greater-Than bracket pairs. These are listed under Special
   Key Codes in this Manual but as an example here, you could specify the
   <Enter> key as "<Enter>" or Function key 2 as "<F2>". Several examples
   of the <Enter> key appear in the above example macros.

   You can specify <Ctrl- > codes by entering the '^' character followed
   by the ASCII character, for example in Macro 0 above, we see
   "^CD<Enter>". The first 2 characters, "^C" will generate a single
   <Ctrl-C> code. This macro, by the way, is the macro I use to disconnect
   from another station. The <Ctrl-C> returns the TNC to Command Mode; the
   "D" followed by <Enter> issues a Disconnect command to the TNC.
   (Actually I prefer to use <Alt-B> to get the TNC into Command Mode, but
   I changed it to <Ctrl-C> for this example!)

   Those familiar with the ASCII table of control characters will see that
   specifying "^M" instead of "<Enter>" will achieve the same resuilt.

   If you wish to include <Alt- > key combinations, they may be specified
   in a similar manner to that used for the Ctrl key, but for Alt key, use
   the tilde ("~"). For example, in the example macros above you will see
   "~B" used to specify <Alt-B> which is paKet's <BREAK> key.

   Note you can use a Macro to send commands to the TNC or to send a
   string of data to another station. If sending commands it would be
   prudent to include the "~B" just to be sure the TNC is in Command Mode.

   When finished with this window press <Esc> to return to the System
   Configuration window.

















                               Page  32


 Begin-Auto Commands

  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ2. Begin Auto Commands...ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³ECHO OFF                                                               ³
  ³MAIL OFF                                                               ³
  ³CTEXT Please feel free to use the system.^V                            ³
  ³ H for Help or^V                                                       ³
  ³ S to "Send" me a message^V                                            ³
  ³   ...Tony                                                             ³
  ³                                                                       ³
  ³                                                                       ³
  ³                                                                       ³
  ³                                                                       ³
  ÀÄÄÄÄÄÄ^N to Insert a line; ^Y to Delete a line; ESC when finishedÄÄÄÄÄÄÙ

 Description.
   When paKet starts, a DAY command is sent to the TNC to initialise its
   date and time to match that in your computer.

   Then, as part of the initialisation, paKet can send up to 10 additional
   commands to the TNC. These additional commands are optional, but if you
   want to include any commands to be sent at start up time, they would be
   specified here.

   Each line contains a single command so an <Enter> is implied and will
   be generated by paKet as each line is processed.

   In the above example, I have specified a multi line CTEXT command using
   the PASS character <Ctrl-V> which will cause the following <Enter> to
   be taken by the TNC as part of the CTEXT data. Refer to your TNC Manual
   for information on the PASS character.

   Note, you may enter Special Key Codes or the <Ctrl- > or <Alt- > key
   sequences as explained in the previous section on Keyboard Macros.

   When all commands have been entered, press <Esc> to return to the
   System Configuration Window.


   There is an alternative to using these Begin Auto commands: paKet will
   check for the presence of a Script file, AUTOEXEC.SCP, and will execute
   this Script at Initialisation time if that file is found in the current
   directory. This will provide more flexibility and allow more than 10
   commands if that is necessary. It would also enable you to re-issue
   these commands (via the <Alt-S> Script command) at any time during the
   run if that might be a requirement.














                               Page  33


 End-Auto Commands

  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ3. End Auto Commands...ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³CTEXT paKet is not currently running.^V                                ³
  ³Please leave a message in the PK-232 Mailbox.^V                        ³
  ³...Tony.                                                               ³
  ³MAIL ON                                                                ³
  ³ECHO ON                                                                ³
  ³^S                                                                     ³
  ³                                                                       ³
  ³                                                                       ³
  ³                                                                       ³
  ³                                                                       ³
  ÀÄÄÄÄÄÄÄ^N to Insert a line; ^Y to Delete a line; ESC when finishedÄÄÄÄÄÙ

 Description.
   This item is almost identical to the previous option, but as you might
   guess, these commands are sent to the TNC when you exit from the
   program with the <Alt-X> command.

   Once again, these commands are optional so leave the window blank if
   you don't want any commands issued as you exit the program.

   You may wish to include a "^S" to hold monitored data in the TNC buffer
   until next session.  (paKet always sends a <Ctrl-Q> when it starts up
   just in case.) Then, when you next start, you will see as much data as
   has been held in the TNC buffer while you were "offline".

   There is an option to perform a Script file at this time. If paKet
   finds a file AUTOEND.SCP, that Script will be performed prior to
   exiting to DOS. This, like the AUTOEXEC.SCP, is optional.

 Alerts

 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ4. Alerts...ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 ³DHU                                                                     ³
 ³PAKET                                                                   ³
 ³                                                                        ³
 ³                                                                        ³
 ³                                                                        ³
 ³                                                                        ³
 ³                                                                        ³
 ³                                                                        ³
 ³                                                                        ³
 ³                                                                        ³
 ÀÄÄÄÄÄÄ^N to Insert a line; ^Y to Delete a line; ESC when finishedÄÄÄÄÄÄÄÙ

 Description.
   Up to 10 Alert strings may be recorded in this window.

   If "Alerts" is enabled with the <Alt-A> key, paKet will scan each line
   as it appears in the Communications Window for a match.  If one of
   these strings is found, paKet will sound the Bell.

   Case is not important here as paKet will match both upper and lower
   case.

   If the Bells start to annoy you, press <Alt-A> to disable the Alert
   Monitoring. The strings specified here can stay so when you toggle
   <Alt-A> again Alert Monitoring will recommence using the same strings.
                               Page  34


Configuration Windows - REMOTE Mode options

 Example:

                  ÉÍÍÍÍÍÍ 6. REMOTE Mode options...ÍÍÍÍÍ»
                  º Allow REMOTE access?              Y º
                  º Issue REMOTE Menu on connection?  Y º
                  º SEND files  to  REMOTE station?   Y º
                  º RECV files from REMOTE station?   Y º
                  º REMOTE trigger (decimal value)   29 º
                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


 Description:
   This window appears when you select option 6 from the System
   Configuration Window.

   REMOTE Mode is discussed in its own section of this Manual but briefly,
   it provides unattended access to our system by other users. It is like
   a BBS in that the other station can perform file transfers to and from
   our system, they can leave a message in our PMS, and can read any
   messages left for them, but there are NO MAIL FORWARDING facilities.


 Allow REMOTE access?
   This is a Y(es) or N(o) parameter.

   If you do NOT want other stations to use this REMOTE facility, turn
   this option off with 'N'.

   You may still activate it yourself via the <F3> key if you wish,
   temporarily overriding this Configuration option, so YOU still have a
   choice.


 Issue REMOTE Menu on connection?
   If you are happy to allow REMOTE operations, you can either wait for
   the other station to send us the REMOTE Trigger (discussed below) or
   you can choose to have paKet automatically issue the REMOTE Menu when
   the other station connects to our system.

   If you enter "Y" for this option, paKet will switch into REMOTE Mode
   and will issue the menu immediately a connection is established.

   This is intended for those times when you are not present to
   communicate with the other station. So if you have pressed a key within
   the past 60 seconds, paKet will assume you are at the keyboard and will
   NOT automatically switch into REMOTE Mode. The other station can still
   send the Trigger to get the REMOTE Menu, or you can do it with the <F3>
   key if you wish.


 SEND files to REMOTE station?
   This is a Y(es) or N(o) parameter.

   If you have decided to allow REMOTE operations, you might still want to
   prevent other stations downloading files FROM our system in REMOTE mode.

   This would normally be 'Y', but if you want to prevent REMOTE Downloads
   set this option to 'N'.
                               Page  35


 RECV files from REMOTE station?
   This is a Y(es) or N(o) parameter.

   If you have decided to allow REMOTE operations, you might still want to
   prevent other stations uploading files TO our system in REMOTE mode.
   Preventing REMOTE Uploads should reduce the risk of picking up a virus.
   Alternatively, specifying a unique Binary Receive directory should
   allow you to be suitably suspicious of whatever turns up in that
   directory. Nevertheless, if you are still concerned at this
   possibility, you may choose to set this option to 'N'.


 REMOTE trigger (decimal value)
   Another station who has connected to our system might like to switch on
   our REMOTE Mode (if it is not already on).

   This trigger code is specified here as a decimal ASCII value because
   some codes do not display well and trying to display the code itself
   could become confusing. Using a decimal value leaves no doubt as to the
   value set.

   The default value of 29 (or the ASCII GS code) is <Ctrl-]>, that is
   hold the Ctrl key while typing right-square-bracket.  So, if the other
   station sends us that code, with nothing else on the line, paKet will
   activate REMOTE Mode and send the REMOTE Menu.

   Press <Esc> to return to the System Configuration window.

































                               Page  36


Configuration Windows - File Transfer options

 Example:

                ÉÍÍÍÍÍ 7. File Transfer options...ÍÍÍÍ»
                º DWAIT  for normal operations     16 º
                º DWAIT  for binary operations     48 º
                º PACLEN for normal operations    240 º
                º PACLEN for binary operations    252 º
                º Use paKet Protocol?               Y º
                º Ctrl-Z after sending ASCII file?  Y º
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

 Description.
   This window appears when you select option 7 from the System
   Configuration Window.

   These options relate to File Transfers only.


 DWAIT  for normal operations
 DWAIT  for binary operations
   DWAIT is a TNC parameter that specifies a delay in the TNC with a view
   to minimising collisions with digipeated packets. Some operators
   recommend a setting of 48 for DWAIT during File Transfers in order to
   give other Conversational Mode contacts a better response on a crowded
   frequency. The principle here is that a file transfer should be run as
   a sort of "Background" process. So, it is considered responsible to
   give a longer DWAIT time, especially if you have to do your file
   transfers at a busy time.

   There are two values for DWAIT that you can set here: the "DWAIT for
   binary" value will be used while sending a binary file; and the TNC
   will be reset to the normal DWAIT value when the File Transfer is
   completed.

   paKet will accept any value for normal DWAIT but the value for binary
   operations must be at least 24. Recommended values are 16 for normal
   mode and at least 32 for Binary File Transfers.


 PACLEN for normal operations
 PACLEN for binary operations
   The TNC's PACLEN parameter specifies the maximum size of the packets to
   be transmitted. It has been found that in most cases a larger PACLEN
   value is more efficient for File Transfers on VHF, but perhaps smaller
   on poorer HF paths.  It is generally accepted that a large PACLEN for
   normal conversation is less important.  paKet gives you the ability to
   specify different PACLEN values for binary file transfer and
   "conversation".

   The value can be as high as 256, or 0 which in some TNCs is equivalent
   to 256.  It was found in testing that some versions of Pac-Comm and
   TAPR TNC EPROM code do not handle PACLEN 0 correctly (the TNC "crashes"
   during file transfers after 7 packets!).  A value of 255 or less
   appears to be universally reliable.  Recommended values are 240 for
   normal mode and 252 for File Transfers - certain advantages accrue from
   these settings.


                               Page  37


   The <Enter> at the end of each line determines the length of the
   packets transmitted in Converse Mode, unless you are using CPACTIME.
   Provided you are using paKet's Type Ahead buffer, the use of CPACTIME
   with a one second delay is considered more efficient in many cases than
   the older <Enter> method. For normal conversations there is little
   difference but if you are transferring an ASCII Text file (refer <F5>
   key) the CPACTIME method would use this PACLEN specified here and would
   result in more efficient transmissions. (Not all TNCs support CPACTIME
   so check your TNC manual for details).


 Use paKet Protocol?
   paKet Protocol (pP for short) is an enhanced Binary Transfer protocol
   developed especially for Packet Radio and is fully compatible with
   YAPP, the current "Standard". Refer to the section on paKet Protocol in
   the Technical section of this Manual for more details if required.

   I used the YAPP Protocol Specifications published by Jeff Jacobsen
   (WA7MBL), the author of the original YAPP program, when developing this
   pP system. Extensive testing has shown pP to be fully compatible with
   YAPP so you can use pP to exchange Binary files with any station
   equipped to handle the YAPP protocol. The pP protocol automatically
   detects the presence of another pP station and will use the enhanced
   features as required.

   However, just in case there is some other system somewhere that does
   not quite conform to the original YAPP specifications and causes some
   difficulty with the new pP, I have provided this option to allow you to
   turn off the advanced protocol, reverting to the Standard YAPP Protocol
   for Binary Transfers.

   I expect this option will always be set to "Y".


 Ctrl-Z after sending ASCII file?
   When you send an ASCII Text file with the <F5> key paKet will
   optionally generate a <Ctrl-Z> character as an End-of-File indicator.

   Most systems receiving a file or message require the <Ctrl-Z> to close
   the file or terminate the message being received. So you might find it
   convenient to set this option to "Y" and allow paKet to generate the
   code when it detects the end of the file you are sending.

   For flexibility, however, the choice is yours. If you prefer to enter
   the code manually set this option to "N".















                               Page  38


Configuration Windows - File/Directories

 Example:
        ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ 8. File/Directories...ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
        º Text   Recv directory     C:\PAKET\TEXT\                      º
        º Text   Send directory     C:\PAKET\TEXT\                      º
        º Binary Recv directory     C:\PAKET\BIN\                       º
        º Binary Send directory     C:\PAKET\BIN\                       º
        º Log File directory        C:\PAKET\                           º
        º PMS directory             C:\PAKET\                           º
        º Online Manual File        C:\DOC\PAKET.DOC                    º
        º Help File                 C:\DOC\PK-232.HLP                   º
        º System Editor             D:\EDWIN.COM                        º
        º Script File               C:\PAKET\MAILBOX.SCP                º
        º Connect File              C:\PAKET\PAKET.DIR                  º
        º Command to list a file    TYPE                                º
        ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

 Description.
   This window appears when you select option 8 from the System
   Configuration Window.

   The paKet system manages a number of files and directories and in this
   window you may specify your preferred defaults.

   Note, in the above window the first six items are DIRECTORY names so
   for these items please specify a drive and sub directory name finishing
   with a backslash character ("\"). So, if you want to specify the
   diskette in drive A: using its root directory, you would specify "A:\".

 Text Recv directory
   This is the default directory the system uses when we receive an ASCII
   text file.

   This would be when you select the Receive File function with the <F6>
   key, or it would also be used by a REMOTE user if that station sends
   us an ASCII text file.

 Text Send directory
   This is the default directory the system uses when you send an ASCII
   text file.

   So when first sending a file with the <F5> key, paKet will display this
   directory in the Disk Directory Window while you select the file to
   send. Of course, you can select a file from another directory if you
   wish.

   This directory will also be used by a REMOTE operator if that station
   wants to transfer one of our text files. A REMOTE user may access this
   directory and any sub directories below this one, so if you specify the
   Root directory here, the REMOTE user will be able to access any part of
   the specified drive for downloading.

   REMOTE operations are discussed elsewhere but it should be pointed out
   here that a REMOTE user may issue a "W" ("What") command to ask paKet
   to display a directory of our text files.  paKet will send this "Text
   Send directory".  For your protection, this directory and its sub
   directories are the only directories a REMOTE user will see.


                               Page  39


   If the Text Receive directory is not within the Text Send branch of the
   directory tree, the REMOTE operator will not know what files have been
   uploaded, so you might like to specify a directory for Text Receive
   which is the same as the Text Send (or one of its sub directories).


 Binary Recv directory
   This is the directory the system uses when we receive a Binary File.
   In paKet there are four ways to transfer a Binary file:
      paKet Protocol (pP);
      YAPP protocol;
      BayCom; and
      RAW Binary (no protocol).

   Whichever method is chosen, paKet uses this directory to receive the
   transferred file.

   It would also be used if a REMOTE user sends us a Binary File using
   one of these methods.

   You are not asked for the file name when receiving a Binary File with
   pP or YAPP: that information is expected to be in the protocol Header.
   So if you wanted the Binary File to go into a different directory or to
   have a different name, you will have to copy it or Rename/Move it
   (refer <Alt-R> key) after the transfer has completed.


 Binary Send directory
   This is the default directory the system uses when we send a Binary
   File.

   So when sending a Binary File, paKet will display this default
   directory in the Disk Directory Window while you select the file to
   send. Of course, you can select a file from another directory if you
   wish.

   This directory will also be used by a REMOTE operator if that station
   wants to transfer one of our Binary Files.

   For the same reasons discussed under the "Text Send directory" above,
   it would be helpful to REMOTE users if the Binary Receive directory is
   within the directory subtree specified for Binary Send.


 Log File directory
   This is the default directory the system uses for the disk log file.

   When you press the <F2> key to activate the log file, you will be asked
   to select the file name and, though a default is offered using the
   drive and directory specified here, you may specify a different name,
   directory or even drive if you wish.

   If you have the AUTO log option active, paKet will generate a Log File
   name based on the computer's date and will create the file in this
   directory. You don't have to do anything!





                               Page  40


 PMS Directory
   paKet has a Personal Message System which operates in a style similar
   to many of the BBS systems, and is explained in its own section of the
   Manual.

   There are two files maintained by the system for the PMS, one to
   contain the messages themselves and the other for an index into the
   message system.  The directory specified here is where these files will
   reside.

   Once you specify the directory here, there is nothing else you need to
   do. If the PMS files cannot be found, paKet will automatically create
   new ones.  Of course if you change this directory entry, next time
   paKet tries to access the PMS, the files will probably not be found in
   the new directory and it will create new files, effectively "losing"
   any messages that were in the old directory!



 The following items are FILE names although you can specify a drive
 and/or subdirectory path as well.

 Online Manual File
   paKet includes an Online version of this Manual. Actually it IS this
   Manual!

   Here you specify the path and file name so when you press <Alt-F1>
   paket knows where to look for the file. If you have sufficient disk
   space the entire paKet Manual should be combined into a single file,
   PAKET.DOC which would be the name specified here. If you prefer, you
   could leave the original DOC files separate and specify here the
   desired part, eg MANUAL1.DOC.


 Help File
   The Help File is the name of the TNC help file that you want to use.
   For example, if you have a PK-232 and you had that help file in a
   directory called C:\HELP, you could set this item to: C:\HELP\PK-232.HLP

   If you do not specify a path, paKet will assume the help file is in the
   "current" directory, which is the directory DOS was using when you
   loaded paKet.


 System Editor
   The System Editor is an external text editor you may call up with the
   <Alt-E> key.

   This item allows you to specify the name (and optionally the path) of
   your favourite text editor. Any editor may be used, even DOS's (ugh)
   EDLIN if you have nothing else!

   This editor will be run with paKet in the background, so there are a
   couple of considerations to keep in mind here:

      1. paKet will continue to capture any input from the TNC and store
         it in the System Input buffer while you are using the editor. So
         you should be able to run the editor at any time without losing
         any input data.

                               Page  41


      2. As paKet is still in the background, we will not have the full
         amount of memory available for the editor. So you may not be
         able to edit a very large file or may not even be able to load
         the editor if memory demands are high.

         For example if you have specified several Communications Windows
         each with large input and Flashback buffers, there will be less
         free memory available; and/or if your favourite editor happens to
         be one of the LARGE Word Processing packages it might not fit
         into the available memory alongside paKet anyway!

         Most of the simpler "Text" or "Programmer's" editors should work
         just fine.


 Script File
   When you execute a Script file, paKet will offer a default Script file
   name to save you unnecessary typing.   This item specifies your
   preferred default Script file name.


 Connect File
   This is the name of the file you wish to use for paKet's Connect
   facility. The Connect file contains the names and connect paths for
   our regular contacts and will be used when you select <Alt-C> to
   initiate a connection to another station.

   It is conceivable we could have more than one Connect file although
   one file will hold up to 200 entries which should be more than enough
   to satisfy most users.

   Refer to the Connect Window section for more discussion on the Connect
   facility.


 Command to list a file
   If you have pressed <Alt-D> to display a Disk Directory, you may
   highlight any file listed in the directory and press <Enter> to view
   the contents of that file.

   paKet will use this command to display the file.

   You may specify the DOS "TYPE" command (as shown in the example above),
   although I prefer to use the excellent Public Domain utility, LIST. If
   you want to use an external program (such as LIST), don't forget DOS
   will need to be able to find it, so you might specify the Drive and/or
   directory name along with the command (Eg: C:\UTILITY\LIST). Of course
   this will not be necessary if the program is it is in the current
   directory or if it is covered by the DOS PATH statement.











                               Page  42


Configuration Windows - Miscellaneous options

 Example:
          ÉÍÍÍÍÍÍÍÍÍÍÍÍ 9. Miscellaneous options...ÍÍÍÍÍÍÍÍÍÍÍÍ»
          º Station callsign                  VK2DHU           º
          º Operator's name                   Tony             º
          º Msg level (All,Warnings,Errors)   A                º
          º Eliminate SNOW? (CGA only)        N                º
          º AUTO LOG (on while Connected)     Y                º
          º Screen blanker delay (seconds)      60             º
          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

 Description.
   This window appears when you select option 9 from the System
   Configuration Window. It contains those configurable variables that did
   not seem to fit into any of the other sections.

 Station callsign
 Operator's name
   These items are used in a couple of places for display purposes. For
   example some REMOTE menu messages will show your name and/or callsign
   in order to make it appear a little more friendly.

   The callsign is also used in the PMS. If a REMOTE user leaves a
   message without specifying a callsign, paKet will assume it is for you
   and will insert your callsign as the addressee. Similarly when you
   enter a message into the PMS, there is no need to specify who it is
   from. paKet knows who you are!

 Msg level (All, Warning, Error)
   There is a complete listing of paKet's messages in its own section of
   this Manual. Each message is identified as belonging to a particular
   category.

   For example some messages are considered Information Only. They tell
   you what is going on at a particular time but are not really important
   as no action is required. Warning messages alert you to something
   unexpected but in many cases paKet can cope without your intervention,
   taking whatever action it deems necessary!  Error messages are those
   that occur in situations that are considered serious and usually
   require some action on your part.

   Most messages are left on the screen for about 3 seconds to allow time
   to read them. This can sometimes be a little tiring for experienced
   users when the system is displaying these messages, especially the
   routine Information messages which can become quite predictable.
   Experienced users might prefer to hide the simple Information Only
   messages as they will probably know what is going on anyway. And the
   real experts might choose to hide even the Warnings (at their own
   peril!).

   This option allows you to specify the level you wish to use. I
   recommend EVERYONE, regardless of experience, specify A (All) to start
   with, maybe changing the level later. I expect it would be in very
   unusual circumstances that anyone would want to hide the Warning
   messages by specifying level E.

   With level A - All messages will appear;
        level W - Warnings and Errors only will appear;
        level E - Errors only will appear.
                               Page  43


 Eliminate SNOW? (CGA only)
   This is a Y(es) or N(o) parameter.

   The SNOW parameter is used for antique CGA displays that misbehave when
   a program writes directly to the video display's RAM. The effect on
   these displays is a 'snow' effect. paKet uses direct memory writes to
   enhance performance but it will use a different (slightly slower)
   method if you set this parameter to 'Y' to minimise the 'snow'.

   Note, however, that this is for CGA displays only - it will not work
   with other types of display adapter (shouldn't be necessary anyway!).

 AUTO LOG (on while Connected)
   This is a Y(es) or N(o) parameter.

   paKet provides a disk logging facility which may be activated at any
   time with the <F2> key. However, the AUTO LOG feature (if ON) will
   automatically activate the disk log file using the default naming
   convention when a connection is established with another station and
   will turn it off when disconnected.  This allows you to keep a log of
   your communications with other stations without clogging the log file
   with other data.

   Set this field to 'Y' if you want to use the AUTO LOG feature.

 Screen blanker delay (seconds)
   The nature of Packet Radio is such that you might leave the system
   running even while you are not actually present, especially with the
   availability of paKet's REMOTE facilities.  However, prolonged display
   of unchanging information on a screen can cause a "burning-in" effect
   which may be relieved with a Screen Blanker to switch off the display
   when nothing is happening.

   paKet has its own Screen Blanker which becomes effective after a
   specified period of inactivity. This option allows you to specify the
   period.

   For example, if you specify 60 seconds here, the screen will be blanked
   if nothing is received from the TNC and if no keys have been pressed
   during the past 60 seconds. If something is received from the TNC or if
   you press a key, the 60 second countdown restarts, so in times of
   normal activity the screen might not blank at all!

   If the screen is blanked, it will be restored for normal communications
   immediately a character is received from the TNC or upon any keystroke
   from you.   Note, you can simply start typing a message because your
   keystroke will be processed by the system even if you could not see the
   paKet screen when you pressed the key.

   If you simply want to redisplay the screen without actually "typing"
   something, I suggest you press Ctrl or Alt (without any other key).
   These keys will be detected by paKet and will cause the Screen to be
   restored, but they do not actually generate any character on their own.

   A value of 0 (zero) here tells the system you do NOT want any screen
   blanking at all.




                               Page  44


Connect Window

 Example:

 ÚÄName         ->Ý Callsign to CONNECT to (including Digipeaters, etc)ÄÄÄ¿
 ³BBS             VK2ATM-1                                                ³
 ³Paul            VK2BZC                                                  ³
 ³Arthur          VK2ATM                                                  ³
 ³Col             VK2KQX                                                  ³
 ³Bill            VK2ZCV                                                  ³
 ³YDN BBS         VK2YDN-1 via VK2RCH 668900                              ³
 ³CKG Cessnock    VK2CKG via VK2RLO VK2RPW                                ³
 ³CZZ             VK2CZZ via VK2RLO VK2RPW VK2RPN                         ³
 ³Daryl           VK2DAZ v VK2RLO VK2RPW                                  ³
 ÀÄÄÄÄÄ <Enter> to CONNECT; ^N - insert a new entry; ^Y - delete entryÄÄÄÄÙ


 Description.
   The Connect Window appears when you press <Alt-C>.

   It contains a list of names and connect paths for your regular
   contacts. This feature is provided to facilitate the connection
   process. You may record up to 200 entries in the Connect Window.

   To make a connection, move the highlight bar to the desired entry and
   press <Enter>.

   At first the window will be blank but you may enter the details of your
   regular contacts to more easily establish contact with them next time.

   Some Networks require you to connect to a particular Node, then when
   that connection is established, you issue another connect request to
   the desired station.  In this case you could specify two entries in the
   Connect Window - one for the Node and another for the destination
   station.

   To create a new entry, type a name that you can easily recognise, then
   press <Tab> to move to the start of the Callsign section. Here you
   enter the details of the connect path you wish to use for this station.
   paKet will generate the TNC's CONNECT command using this "Callsign"
   information.

   If you want to insert a new entry between two existing entries, move to
   the desired location and press <Ctrl-N>.

   If you want to remove an existing entry, move to that entry and press
   <Ctrl-Y>.

   Any changes are saved automatically.











                               Page  45


Disk Directory Window

 Example:
               ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍC:\PAKET\ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
               º        (Enter file name manually)           º
               º        (Change to another drive)            º
               º ..            <Previous directory>          º
               º ALAN.LZH      14751  18-04-91  20:57        º
               º ARA            2264  11-10-91  21:13  A     º
               º AUG22.LOG      3581   1-09-91  21:45  A     º
               º AUG28.LOG       394   6-09-91  12:46  A     º
               º AUG29.LOG      6885   6-09-91  12:47  A     º
               º AUTOEXEC.SCP    144  11-09-91  21:09  A     º
               º BETA          <DIR>                         º
               º CKPT.BAK        198   3-07-91  22:34        º
               º CKPT.DAT        196  11-10-91  19:48  A     º
               º CMD              12  23-09-91  21:20  A     º
               º CONFIG.SAV     1398   1-10-91   9:50  A     º
               º CONNECT.DMP    2048  12-10-91  14:19  A     º
               º CONTEST.LOG     577   4-07-91  20:54        º
               º CONTEST.SAV   39555   1-04-91  19:54        º
               ÈÍÍÍÍÍÍÍÍÍÍ Directory - 20,480 freeÍÍÍÍÍÍÍÍÍÍÍ¼


 Description.
   This window will appear whenever you request a directory display (with
   the <Alt-D> key). It will also appear when paKet asks you to choose a
   file name (eg if you want to send a file to the other station).

   The directory is displayed in alphabetical sequence with hidden and
   system files and the volume label displayed in a different shade. (You
   can't hide from paKet!) Also shown are the file date/time and file
   attributes.

   At the top of the window is the drive\path of the displayed directory,
   and on the bottom line is the amount of free space on that drive.

   You may scroll up and down this window using the <Up-Arrow> and
   <Down-Arrow>, the <PageUp> and <PageDown> keys, or the <Home> and <End>
   keys. Or you can use paKet's hot-key typing by entering part or all of
   the file name - paKet will highlight the first filename that matches
   the characters you have typed so far. Often all you need to type is one
   or two characters to move to the file you want.

   An item may be "selected" by moving the cursor (the highlight bar) to
   that item and pressing <Enter>.

   If there is another level of subdirectory below this one, that
   subdirectory name will be listed in sequence with "<DIR>" instead of a
   file size. In the example above, there is a subdirectory named "BETA"
   shown. Selecting that item will ask paKet to display that subdirectory
   in the Window.

   Sometimes you might prefer to enter the file name yourself rather than
   go through a number of display options. This is especially so if you
   want to create a file that does not yet exist on the disk (for example
   if you are using the System Editor to create a NEW text file). In this
   case, select the option to "(Enter file name manually)" and paKet's
   Message Window will pop up for you to enter the file name.

                               Page  46


   You may display the directory of a different drive by selecting the
   "(Change to another drive)" option second from the top of the window.
   And you can select "<Previous directory>" to go back a level.

   If you used <Alt-D> to Display the directory, selecting a file will
   display the contents of that file. The command used to perform the
   display is configurable - refer to the "Configuration Windows -
   File/Directories" section for details.

   If you press the <Delete> key, paKet will delete the highlighted file
   after asking for your confirmation that you really wish to perform the
   deletion.  This is convenient if you are doing some housekeeping such
   as cleaning out unwanted log files. You can use the System Editor to
   inspect log files on the disk and to edit out unwanted data. Then
   delete any unwanted files. All without leaving paKet.

   Alternatively, a file may be renamed or indeed moved from one directory
   to another by pressing <Alt-R> whilst that file is highlighted.  You
   are then asked to type the full new path and name for the file.  If a
   new name is typed without a path, the file will remain in the current
   directory.







































                               Page  47


Help Window

 Example:
 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄpaKet 5.0 HelpÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 ³ F1  - Help                          Alt-A  - Alert bell on/off           ³
 ³ F2  - Turn Log File ON              Alt-B  - Send a BREAK signal to TNC  ³
 ³ F3  - Turn REMOTE mode ON           Alt-C  - Connect to another station  ³
 ³ F4  - Word Wrap/Single Line         Alt-D  - Disk Directory              ³
 ³ F5  - Send an ASCII text file       Alt-E  - Edit a data file            ³
 ³ F6  - Receive ASCII text file       Alt-F  - Find text in Flashback      ³
 ³ F7  - Send Binary File using pP     Alt-H  - MHEARD                      ³
 ³ F8  - Recv Binary File using pP     Alt-I  - Initialise Comms Windows    ³
 ³ F9  - DOS Gateway                   Alt-L  - Continue Find in Flashback  ³
 ³ F10 - Help with TNC Commands        Alt-M  - Personal Message System     ³
 ³ Alt-F1 - Display Online Manual      Alt-P  - Turn Print log ON           ³
 ³ Alt-F5 - Send RAW Binary file       Alt-Q  - Clear TNC's XOFF with Ctrl-Q³
 ³ Alt-F6 - Recv RAW Binary file       Alt-R  - Rename/Move data file       ³
 ³ Alt-F7 - Send File  to  BayCom      Alt-S  - Script processing           ³
 ³ Alt-F8 - Recv File from BayCom      Alt-T  - Set TNC Time and date       ³
 ³ Page Up     - Flashback             Alt-V  - Verify Connected callsign   ³
 ³ Scroll Lock - Pause                 Alt-W  - Write Flashback to disk     ³
 ³ Shift-Right - Next Comms Window     Alt-X  - Exit this program           ³
 ³ Shift-Left  - Prev Comms Window     Alt-Z  - Configuration               ³
 ³ Up/Dn Arrow - Recall Type Ahead                                          ³
 ³            Enter desired function, or Esc to leave Help Screen           ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

 Description.
   This Help Window is always available at the touch of the <F1> key.

   You may select any function by pressing the key shown in the Help
   Window - it is not necessary to remove the Window first. If you do not
   want to use any of those functions at this time, press <Esc> to remove
   the Help Window and return to normal communications.


























                               Page  48


Message Window

 Example:

  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
  º                            Log File closed                             º
  º                                                                        º
  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


 Description.
   This is a small window that will appear from time to time, mostly to
   inform you of some condition or problem. Some messages will disappear
   after a few seconds, others which are considered more serious will
   wait for you to press the <Enter> key before they disappear.

   Full details of all messages, together with an explanation of each are
   provided in the Messages Section of this Manual.

   Some of these messages may be suppressed entirely by specifying a
   higher "Message Level" in the Configuration.  But, be warned, that is
   for experienced users only!






































                               Page  49


Status Window

 Example:

 Ä Buffers Ä Windows ÄÄÄÄÄÄÄÄÄÄÄ paKet 5.0 ÄÄ Log File ÄÄÄÄ COM1(2400) ÄÄÄ
     2045 PRS<--3>       REMOTE A 14:16:41       OFF   RTS CTS DSR DCD DTR

 Description:
   This window is optional (but recommended) and displays some of paKet's
   operational settings.

   On the top line, along with the fixed headings, you have the current
   version number of the paKet program in the centre, and on the right,
   details of the serial port being used including the current baud rate.

   Most status information appears on the second line:

     Buffer: At the left is the System Input Buffer counter.

             All data received from the TNC is stored in this System Input
             Buffer temporarily while waiting for paKet to come and see
             where it belongs. If we are conducting multiple sessions,
             this data will have to be distributed to the appropriate
             Communications Window. At regular intervals in the
             processing, paKet will perform this distribution.

             The Status Window shows the number of characters in the
             buffer that have yet to be distributed.

             The count may build up if data is being received faster than
             your system can process it, or if it cannot yet be
             distributed (eg: because one of the Window input buffers has
             already filled).

             If you have started the System Editor <Alt-E> or taken the
             DOS Gateway <F9>, paKet no longer has control of your system
             and so cannot perform this data distribution. However, the
             Interrupt Handler is still operational so anything received
             from the TNC during this time will be captured and stored so
             you will not lose any input data. When you return to paKet
             you will see the System Input Buffer drain quickly into the
             Window input buffer(s) and data will flood into the
             Communications Window as paKet catches up. Just keep in mind
             that if you take TOO long and the System Input Buffer fills
             (it is 32KB), any further data data would then be lost.

             If the Status Window is displayed and the number of held
             characters reaches 25000, the counter will change colour to
             warn you it is filling up and an intermittent audible alarm
             will sound (if Bells are enabled for this Communications
             Window).

     P:      This will appear while the Print Log is active.
             (refer <Alt-P> key).

     R:      This will appear while you are Receiving an ASCII text file
             (refer <F6> key).

     S:      This will appear while you are Sending an ASCII text file
             (refer <F5> key).
                               Page  50


     <--3>   This item indicates there has been some activity on another
             Communications Window. In the example shown, there has been
             some activity in Window 3 and you should switch to that
             window (with <Shift-Right-Arrow> or <Shift-F3>) to see that
             data.

             This field will reflect the number of available windows. The
             example shown indicates three Communications Windows have
             been configured but if, for example, you had configured 6
             Communications Windows, this item would have appeared as:
             "<--3--->".

     REMOTE  This indicator field will usually be blank, but will indicate:
       or       "REMOTE" if paKet is currently in REMOTE Mode; or
     SCRIPT     "SCRIPT" if paKet is currently processing a Script file; or
       or       "INIT"   during paKet's Initialisation process; or
      INIT      "(msg)"  if a remote user has left a message for you
       or
     (msg)

     A:      Alert On.
             This indicates that paKet is scanning incoming data for
             strings that match those specified in the Alerts
             Configuration Window. If a match is detected (case is
             unimportant - both upper and lower case will be matched)
             paKet will sound the Bell.

             Perhaps you wish to know when a friend is on air and have
             specified his callsign, or you wish to see when a hot topic
             is being discussed!

             This feature may be toggled on/off with the <Alt-A> key.

     Time    In the centre is the computer's current time. This will be
             the TNC's time as well because paKet will automatically
             initialise the TNC with the computer system's time when the
             program starts or whenever you press <Alt-T>.

     OFF     This field indicates the current status of paKet's disk
      or     logging system. There are basically three different indicators:
     file
      or        - OFF   The disk log facility is not currently active so
     AUTO               nothing is written to the log file. (Press <F2>
                        to turn it on.)

                - file  When you activate the log file, you have the
                        opportunity to specify the filename. You can use
                        the default name suggested by paKet if you wish.
                        The filename chosen is displayed here in the
                        Status Window.

                - AUTO  This is a configurable option (refer to the
                        "Configuration Windows - Miscellaneous options"
                        section).

                        If the option is ON, paKet will automatically
                        activate the disk log, using the default file
                        name, when a connection is established, and will
                        automatically close the file upon disconnection.

                               Page  51


                        This field will display "AUTO" while waiting for a
                        connection; and it will change to show the default
                        file name when connected.

     RTS     This area of the Status Window is used for Handshaking
     etc     details.

             If you have specified Hardware Handshaking, the status of
             significant RS-232 lines is displayed - if the line is high,
             the indicator is shown; if the line goes low, that indicator
             disappears. For example, if the CTS (Clear to Send) "light"
             goes out you will know the TNC has asked paKet to stop
             sending for a while.

             You will see "Software Handshaking" instead of these
             indicators, if you have selected that mode. However, this
             will change to "XOFF" when the TNC sends that code to ask
             paKet to stop sending for a while. When the TNC sends the
             <XON> code, the Status Window reverts to its original
             "Software Handshaking" display.


   If you feel you do not need this Status Window display and would prefer
   to have the additional two lines available for Communications Window
   data, you can adjust the Configuration (Communications Windows option)
   so it does not appear. For new users however, it is recommended you
   keep it there at least until you are fully familiar with the paKet
   system.
































                               Page  52


TNC Help Window

 Example:

 ÉÍ COMMAND ÍÍÍÍ ARG ÍÍÍÍ DEFAULT ÍÍÍÍÍÍÍ DESCRIPTION ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 ºABaud 'n'    45-9600   110     Specify ASCII radio baud rate            º
 ºAChg         Immediate Cmd     Force AMTOR into transmit mode           º
 ºACKprior     ON|OFF    OFF     Priority Acknowledgement feature         º
 ºACRDisp 'n'  0-255     80      Set the screen or printer width.         º
 ºACRPack      ON|OFF    ON      The <SENDPAC> char is included in packetsº
 ºACRRtty 'n'  0-255     69|71   Automatically insert <CR> in output      º
 ºADelay 'n'   1-9       4       AMTOR key up delay                       º
 ºAFilter      ON|OFF    OFF     ASCII filter for all Modes               º
 ºALFDisp      ON|OFF    ON      Send <LF> to terminal after each <CR>    º
 ºALFPack      ON|OFF    OFF     Add <LF> to outgoing packets             º
 ºALFRtty      ON|OFF    ON      Add <LF> after <CR> in RTTY mode         º
 ºAList        Immediate Cmd     Switch into AMTOR's ARQ Listen mode      º
 ºAMtor        Immediate Cmd     Switch into AMTOR Mode                   º
 ºARq aaaa     Immediate Cmd     Start an ARQ SELCAL                      º
 ºARQTmo 'n'   0-250     60      Time to send ARQ before shutdown         º
 ºAScii        Immediate Cmd     Switch into ASCII RTTY mode              º
 ºAUDelay 'n'  0-120     0       Specify the delay from PTT to AFSK tones º
 ºAWlen 'n'    7|8       7       Number of data bits per word.            º
 ºAx25l2v2     ON|OFF    ON      Select level 1 or 2 of AX25 protocol.    º
 ºAXDelay 'n'  0-180     0       Extra keyup delay (n*0.1 sec).           º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

 Description.
   The TNC Help Window shows the available commands for your TNC.

   It will display each command on a single line with the valid
   abbreviation in UPPER CASE, the valid arguments, the usual default, and
   a brief description of the command.

   For example, there is an "AWLEN" command shown in the example above. AW
   is the valid abbreviation; valid arguments are 7 and 8 and the normal
   default is 7. This command is used to set the "Number of data bits per
   word" in the TNC.

   If you move the highlight bar to any of those commands and press
   <Enter>, paKet will display Detailed Help for that TNC command.

   There are several ways to move the highlight bar:
      1. use the arrow keys to move the cursor up or down - the window
         will scroll if necessary; or

      2. use the <PageUp>, <PageDown>, <Home>, or <End> keys to move
         around the available items more quickly; or

      3. use paKet's hot-key typing facility and type the command (or part
         of the command) you are interested in, either before or after
         selecting this window with the <F10> key. paKet will try to match
         what you have typed with the available commands and will move the
         cursor to the first matching item. You do not have to type the
         full command.





                               Page  53


   Once the desired item is highlighted, press <Enter> to get the Detailed
   Help description of that command, such as:

 ÉÍCOMMANDÍÍÍÍÍÍARGÍÍÍÍÍÍDEFAULTÍÍÍÍÍÍÍÍÍDESCRIPTIONÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 º AWlen 'n'    7|8       7       Number of data bits per word.          º
 ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
 º Modes:      All                                                       º
 º                                                                       º
 º Parameters:                                                           º
 º       'n' - 7 or 8 specifies the number of data bits per word.        º
 º                                                                       º
 º This value defines the word length used by the serial I/O port.       º
 º                                                                       º
 º AWLEN 8 and PARITY 0 is the required setting for paKet.               º
 º                                                                       º
 º To send and receive, retaining all 8 data bits, you should use Trans  º
 º mode (which uses all 8 data bits) or set AWLEN 8. This is for the     º
 º transmission of executable or special binary files.                   º
 º                                                                       º
 º paKet provides the several Binary protocols and automatically switchesº
 º into Transparent mode for the file transfer, so if you use the Binary º
 º File transfer facilities, you would not normally need to concern      º
 º yourself with this command.                                           º
 º                                                                       º
 ÈCommand Reference for the PK-232 (firmware to 10/89) - (PK-232.HLP v13)¼


   This information was gathered from TNC manuals but you will probably be
   aware that there can be variations between TNCs and even between
   different releases of firmware for the same TNC! So while this feature
   may prove helpful in most cases, you should refer to your TNC manual if
   in doubt or if it does not appear to be working the way this Help
   window suggests.

   As there are some differences in the commands of various TNCs it will
   be necessary to select the appropriate HLP file for your TNC. So check
   the supplied HLP files and make sure you have specified the appropriate
   file name in "Configuration Windows - File/Directories".

   There are five Help files included with the current version of paKet:

          KAM.HLP     for the Kantronics range of TNCs;
                      (thanks Col, VK2KQX for producing this Help file)
          MFJ1278.HLP for the MFJ-1278 Multi Mode TNC;
          PK-232.HLP  for the PK-232 Multi Mode TNC;
          TNC1.HLP    for the original TNC-1
                      (thanks Norm, VK2XCI for producing this Help file)
          TNC2.HLP    for just about everything else as this file covers
                      the more standard TAPR-style TNC commands.

   If there does not appear to be a HLP file for your TNC, try the
   TNC2.HLP file as it covers the basic TAPR-compatible commands that most
   TNCs use. If that does not appear to suit, let me know (via Packet to
   VK2DHU @ VK2ATM) in case another TNC Help file has been developed since
   your copy of paKet was distributed. Otherwise, I would appreciate it if
   you could let me know the details, or (preferably) if you could edit an
   existing HLP file to suit your TNC and let me have a copy of the new
   file so I can arrange to have it distributed to all users of that TNC.


                               Page  54


Type Ahead Window

 Example:

 ÄÄÄÄ Single Line ÄÄÄÄÄÄÄÄÄÄType Ahead bufferÄÄÄÄÄÄÄÄÄÄÄÄÄWord Wrap ON ÄÄÄ
 echo off


 Description.

   This window is optional (but recommended). If you choose to have a Type
   Ahead Window, you may configure the number of lines you wish to use.
   Refer to the section: "Configuration Windows - Communications Windows"
   for details.

   This window is always 80 columns wide.

   When enabled, all typed characters are displayed in this window but are
   not sent to the TNC until the <Enter> key is pressed.  This allows you
   to start typing before the other station has finished, and is sometimes
   convenient where you can start answering questions, etc and have the
   answers ready to send when your turn comes.

   If the Single Line option is ON the data will be sent to the TNC as
   each line is completed.

   The capacity of the Type Ahead buffer is limited to the number of lines
   displayed. So if you have configured 2 lines for the Type Ahead Window,
   the buffer capacity is 160 characters.

   When using this Type Ahead facility, Keyboard Macros (<Alt-1> to
   <Alt-0>) are sent and most <Alt- > functions are executed without
   affecting the partial line in the Type-Ahead.

   The following keys are effective when used in the Type Ahead buffer:
      <Enter>            - send the contents of the buffer to the TNC
                           (the entire Type Ahead buffer will be sent
                           regardless of the cursor position);
      <Backspace>        - remove the character before the cursor;
      <Delete>           - remove the character under the cursor;
      <Left-Arrow>       - move the cursor left one character;
      <Right-Arrow>      - move the cursor right one character;
      <Ctrl-Left-Arrow>  - move the cursor left one word;
      <Ctrl-Right-Arrow> - move the cursor right one word;
      <Home>             - move the cursor to the start of the buffer;
      <End>              - move the cursor to the end of the buffer;
      <Ins>              - toggle Insert mode.
                           When in Insert Mode the cursor will appear as a
                           Block character and when in overwrite mode it
                           will appear as an underscore;
      <Tab>              - will be expanded to spaces;
                           Tab "stops" are assumed to be every 8 positions.
      <Ctrl-Y>           - Clear the contents of the Type Ahead buffer
                           without sending any data to the TNC.
      <Up-Arrow> and
      <Down-Arrow>       - Recall a line from the Type Ahead "history"
                           (This will clear anything that was previously
                           in the buffer);
                           Refer to the discussion on this facility below.

                               Page  55


 Type Ahead Recall

   Each line sent from the Type Ahead buffer is saved in a Recall buffer.
   Lines may be recalled one at a time from this Recall buffer with the
   <Up-Arrow> and <Down-Arrow> keys. This facility operates in a similar
   manner to the DOSKEY or CED utilities so, if you are familiar with
   those utilities, you know what to expect here.

   A recalled line is placed into the Type Ahead buffer as if you had
   typed it again, ready for editing and/or resending.

   This could be used so "improved" versions of previously sent text can
   be sent after some editing; or the same text may be sent again. I have
   often typed a long line of text and sent it only to find the TNC was in
   Command Mode and it responds with "What?" or "Eh?" or something equally
   intelligent. So, after restoring the TNC to Converse Mode, this Recall
   facility allows me to send that line of text again, this time to the
   other station, without retyping it all!

   Similarly, if I enter a command to the TNC but find it was not in
   Command Mode at all but in Converse Mode, my "command" will go to air
   for all to see.  No problem: I just press <Alt-B> to reset the TNC to
   Command mode, then <Up-Arrow> and <Enter> to reissue the command.

   The Type Ahead buffers for each Communications Window are preserved
   between switching windows, but the Recall buffer is common.  You can
   send the same line to many connectees in quick succession!


 Word Wrap:

   paKet has a Word Wrap facility that operates on data entered in the
   Type Ahead window. If a word does not entirely fit on the current line,
   the whole word will be moved to the next line.

   You might want to turn it off (with the <F4> key) where you are typing
   a long message such as a CTEXT message and you don't want paKet to
   interfere when you reach the end of the line. However I expect most
   paKet users will have Word Wrap ON all the time. It is so much nicer to
   be on the receiving end of Word Wrapped text than the broken words we
   sometimes get from lesser systems.

   The status of the Word Wrap toggle is shown to the right of the Type
   Ahead header line. In the above example the Word Wrap option is ON.


 Single Line

   If Word Wrap is ON, you also have a Single Line option.

   Normally, the data you type will be held in the Type Ahead buffer until
   you press the <Enter> key, at which time the buffer will be transferred
   to the Communications Window and the data sent to the TNC.  If Single
   Line option is ON, the data will still be entered into the Type Ahead
   buffer, but when the line is filled (ie when the last word is wrapped
   to the next line) that full line will be sent to the TNC.

   Why have a Single Line option?  Well, sometimes you might be typing a
   lengthy reply to the other station, and with Word Wrap (as in a Word
   Processor) you do not need to concern yourself with the end of a line -
                               Page  56


   you just keep typing. In that case, the buffer could fill, or at best,
   the other station is waiting, waiting, ... until eventually you press
   <Enter> to send all that text at once! With the Single Line option ON,
   you get the benefits of the Type Ahead Window, with ability to edit or
   delete some of your text together with the freedom to be typing some
   text while the other station is sending, but without the disadvantages
   of filling the Type Ahead buffer or making the other station wait for
   the entire message.

   Anyway, try it. I was not so excited about it when a paKet user
   suggested it, but now I like it and have it ON all the time!

   Many experienced Packet Radio users do not use "over", "K", ">>" and
   such jargon from other modes because Packet is a full-duplex mode; you
   can just keep typing! Single Line mode enhances this style of
   operation. The incoming and outgoing traffic is readily distinguished
   by colour in both Communications Window and Flashback.

   The <F4> key cycles through the Word Wrap and Single Line options if
   the Type Ahead window is displayed.








































                               Page  57
































                      (This page intentionally blank)





























                               Page  58


PART III - SPECIAL KEY CODES

Overview

   Special Key Codes are expressions of keystroke-combinations which, if
   required, need to be specially coded in the various "Command Texts"
   such as a Keyboard Macro, a Script S(end) command, or the Begin-Auto or
   End-Auto commands.

   An example of a Special Key Code is the <Ctrl-C> combination. When you
   are using the keyboard this key-combination can be entered into the
   system by typing the letter C while holding the Ctrl key. Trying to
   write such a combination into one of the Command Texts requires special
   syntax, which is described in this section.

   Types of Special Key Codes include:
      Ctrl-key combinations such as <Ctrl-V>
      Alt-key combinations such as <Alt-B>
      Function-keys such as <F2>
      Many commonly used command keys such as <Enter>

   In this section, in fact in the entire Manual, I use the Less-Than and
   Greater-Than ('< >') characters as brackets to to better identify
   special key names. Let's call them "Pointer Brackets".


Ctrl-key combinations.

   Any of the <Ctrl- > key combinations from <Ctrl-A> to <Ctrl-Z> may be
   entered into a Command Text.

   The syntax is to enter two characters in the Command Text, the caret
   ('^') followed by the desired Control Letter. For example:
         ^H for <Ctrl-H> (which is the ASCII code for Backspace)
         ^M for <Ctrl-M> (which is the ASCII code for Enter)

   So a Keyboard Macro which contains the following 5 character string:
      ^CD^M
   would result in 3 bytes being sent to the TNC. The first 2 characters
   of the Macro would be combined into a single <Ctrl-C> character; the
   letter 'D' comes next; then the last 2 characters in the macro would be
   combined into a single <Ctrl-M> character (same as Enter).

   If you want to send a caret ('^') to the TNC, enter 2 of them in the
   Command Text. So, for example this Keyboard Macro:
      ABC^^XYZ
   would result in the following text being sent to the TNC:
      ABC^XYZ


Alt-key combinations.

   Any of the <Alt- > key combinations may be coded into a Command Text
   too.

   The syntax is similar to that for the <Ctrl- > key combination but here
   we use the tilde ('~') as the prefix. For example:
         ~B for <Alt-B> (which is paKet's BREAK command)
         ~6 for <Alt-6> (which is Keyboard Macro 6)

                               Page  59


   So a Keyboard Macro which contains the following 4 character string:
         ~P~H
   would send our MHEARD list to the printer. Assuming the Print Log
   function is currently OFF, the first two characters (~P) would be
   processed as <Alt-P> to turn ON the Print Log. The next two characters
   (~H) are processed as <Alt-H> which sends the MHEARD command to our
   TNC.

   If you want to send a tilde ('~') to the TNC, enter 2 of them in the
   Command Text. So this Command Text:
      ABC~~XYZ
   would result in the following text being sent to the TNC:
      ABC~XYZ


Function Keys.

   Any of the Function keys may be specified in a Command Text although
   please note paKet does not support <F11> nor <F12>.

   The syntax is to specify the letter 'F' followed by the number of the
   Function Key and surround that with Pointer Brackets. For example:
         <F2> for Function Key 2 (which paKet uses to toggle the Log File)
         <F10> for Function Key 10 (display TNC Help File)

   You can also specify an <Alt-Fkey> combination as follows:
         ~<F8> for <Alt-F8> (for Receiving a Binary File from BayCom)

   So a Keyboard Macro which contains the following string:
         YD PROG.EXE^M<F8>
   would send the string "YD PROG.EXE" to the TNC, followed by a Carriage
   Return (the equivalent of <Ctrl-M>). Then Function Key 8 is processed
   to Receive a Binary File.


Other commonly used command keys.

   The following keys may be coded for use in Command Texts and are
   written as spelt here, surrounded by Pointer Brackets:

         UP                 HOME              ENTER
         DOWN               END               ESC
         LEFT               PGUP
         RIGHT              PGDN

   Upper or lower case (or any combination) is OK.

   For example, instead of using the ^M combination as demonstrated above
   for a Carriage Return, we could specify <Enter>.  The two codes (^M and
   <Enter>) do the same thing - it is a matter of preference. I think
   "<Enter>" is more descriptive and should be preferred.

   So, the example given in Ctrl-key combinations above (^CD^M) could be
   written as:
         ~BD<Enter>

   The <Alt-B> achieves the same result as the <Ctrl-C> - they both put
   the TNC into Command Mode. The 'D' is the Disconnect command. And
   "<Enter>" generates a Carriage Return.

                               Page  60


PART IV - KEYBOARD COMMANDS

 It is intended that the operation of the paKet program should at all
 times be intuitive and as easy to use as possible. However, you still
 need to know about some of the special keys, details of which are given
 below.

F1                 Display Help Screen.

        Display a help screen showing most of paKet's special keys and
        their functions.

        You may select any function by pressing the key shown on the Help
        Screen - it is not necessary to remove the window first. If you do
        not want to use any of those functions at this time, press <Esc>
        to return to normal communications.

        This Help Screen is intended as a memory jogger. Full details are
        included here in this Manual which may be viewed by pressing
        <Alt-F1>.








































                               Page  61


F2                 Turn Log File on/off.

        Pressing this key will switch the Log File on or off.

        As explained under the description of the Status Window, the Log
        File has three possible states:

          - ON    When the log file is ON, the Status Window will display
                  the name of the file currently used as a log file and
                  all Communications Window activity will be written to
                  that log file.


          If the Log File is not ON, its state will be either:

          - OFF   The disk log facility is not currently active so
                  nothing is written to the log file.

            or

          - AUTO  (This will only occur if you set the AUTO LOG option ON).

                  In this state the disk log facility is OFF, but paKet
                  will automatically activate the disk log, using the
                  default file name, when a connection is established, and
                  will automatically close it upon disconnection.

                  The effect of this is the same as if you press <F2> on
                  connection and then press <F2> again on disconnection.


        So, if the Log File is currently OFF (or AUTO), pressing <F2> will
        turn it ON.

        A Directory window will appear, together with a suggested file
        name. The default file name will be today's date in the form
        MMMDD.LOG, for example: NOV23.LOG but you may use any name you
        like. Using the default name means you can easily keep a separate
        log for each day's activities.

        If the selected file already exists on the disk, it will be
        preserved and incoming data will be appended to that file.


        If, when you press <F2>, the Log File is currently ON, it will be
        closed and further logging activity will cease. The Log status
        will return to either OFF or AUTO, depending on the AUTO LOG
        option.

        Some operators prefer to use the log file for all captured data
        including ASCII file transfers, and use their favourite editor to
        extract desired messages, files, etc from the log file later.








                               Page  62


F3                 Turn REMOTE Mode on/off

        REMOTE Mode is discussed more fully in its own section in this
        Manual, but briefly it is a facility that allows another (remote)
        user to operate our paKet system's PMS or File Transfer systems
        even if our station is unattended.

        There are three ways to get this system into REMOTE Mode:

           1. You can configure paKet to automatically switch into REMOTE
              Mode when another station connects;

           2. The other station could send the REMOTE Trigger code.
              This code would normally be the default <Ctrl-]>, but is
              configurable via the "Configuration - REMOTE Options"
              Window;

           3. You can activate our REMOTE Mode by pressing <F3>.

        When paKet enters REMOTE Mode it will issue the REMOTE Menu to the
        other station.


        If this system is already in REMOTE Mode, there are three ways to
        switch that Mode OFF:

           1. The other station could enter B (Bye) to log off REMOTE Mode
              and Disconnect the TNC session; or he may just disconnect.

           2. The other station could enter T (Talk) to switch off REMOTE
              Mode but retain the connection continuing in normal
              communications.

           3. You could press <F3> to switch off REMOTE Mode returning to
              normal communications (same effect as if the other station
              sent "T").
























                               Page  63


F4                 Toggle Word Wrap and Single Line on/off

        Word Wrap:
           paKet has a Word Wrap facility that operates on data entered in
           the Type Ahead window. If a word does not entirely fit on the
           current line, the whole word will be moved to the next line.

           Word Wrapped text is much tidier for the receiver to read and I
           expect this option, used with Type Ahead, to be the norm.
           Perhaps you might want to turn it off where you are typing a
           long message such as a CTEXT message and you don't want paKet
           to interfere when you reach the end of the line.

           The status of the Word Wrap toggle is shown to the right of the
           Type Ahead header line.


        Single Line:
           If Word Wrap is ON, you also have a Single Line option.

           Normally, the data you type will be held in the Type Ahead
           buffer until you press the <Enter> key, at which time the
           contents of the buffer will be transferred to the
           Communications window and the data sent to the TNC.  If Single
           Line option is ON, the data will still be entered into the Type
           Ahead buffer, but when the line is filled (i.e. when the last
           word is wrapped to the next line) that full line will be
           sent to the TNC.

        The <F4> key cycles through the Word Wrap and Single Line options
        if the Type Ahead window is displayed.





























                               Page  64


F5                 Send an ASCII text file

        If you have an ASCII text file to send, this option will read the
        data from the disk file and send it to the TNC.

        An example of this might be where you want to send a lengthy
        message to someone, or if you want to send the same message to
        more than one station, you could prepare a disk file with the
        desired text before you connect to that station. Then when you are
        ready to enter the message, just press <F5> to send the file.

        Of course this option is also used to transfer a data file or
        source program file to another station, provided the file contains
        only ASCII text. While it is POSSIBLE to transmit a binary file
        using this command, it is prone to problems and NOT recommended!
        You should use one of the Binary File Transfer methods to send a
        file that contains non-ASCII data.

        When this option is selected, a Directory Window will appear and
        you can simply move the highlight bar to the desired file and
        press <Enter> to send that file. You can enter the filename
        manually if you prefer, by selecting that option at the top of the
        Directory Window.

        While the file is being sent an 'S' will appear in the Status
        Window to the left of the Windows display.

        When the entire file has been transmitted, paKet will optionally
        add a <Ctrl-Z> character indicating end-of-file to the other
        station. If you do not want this code added, you can disable the
        option via the Configuration - File Transfer options.





























                               Page  65


F6                 Receive ASCII text file

        When you press <F6>, paKet will ask you for the name of the file
        you want to open.

        From then, all data received in this Communications Window will be
        written to this file.

        If the other station sends an end-of-file character, <Ctrl-Z>, the
        file will be closed. Or you can close it yourself by pressing <F6>
        again.

        While the file is open, an 'R' will appear in the Status Window to
        the left of the Windows display.

        It should be noted that if you have more than one simultaneous
        connection, paKet will keep the data separate and will write only
        data for THIS window to this file.  You can change to another
        window and press <F6> again to create ANOTHER file for data
        received into THAT window. There is no limit to the number of
        files open at any one time, provided you have specified enough
        FILES in your CONFIG.SYS (refer to your DOS manual for details of
        the FILES parameter).





































                               Page  66


F7                 Send a Binary File using either pP or YAPP Protocol.

        To use this feature the other station must be able to handle
        either pP (paKet Protocol) or YAPP protocol.  If you have pP
        enabled and the other station is also equipped to handle pP, the
        advanced protocol is automatically selected, otherwise the
        transfer will be performed according to the original YAPP
        specifications.

        If you want to send a Binary File to a BayCom or Digicom system,
        refer to the <Alt-F7> key. And if you prefer to send a Binary File
        to the other station with no protocol at all (you will have to
        synchronise it manually), refer to the RAW Binary mode with the
        <Alt-F5> key.

        When you wish to send (or "upload") a file to the other station,
        first of all arrange for that station to be ready to receive the
        file, then press <F7>.

        paKet will ask you for the name of the file you wish to send. A
        Directory Window will pop up to help you select the file.

        Then paKet will:
              set up the necessary parameters in the TNC;
              display the Binary File Transfer Window;
              synchronise with the other station; then
              begin the transfer.

        If all goes well, you do nothing - just sit back and watch - and
        the file will be sent. The program returns to normal
        communications when the transfer is completed.

        For example, if you are logged on to a BBS system and it is waiting
        for a command, you could type:
           "YU PROG.EXE"   (This is the BBS command to upload a YAPP file)

        and it would respond with something like:
           "Ready to Receive with YAPP protocol"

        Then you press <F7> and tell it the name of your file, which is
        presumably the same as the file name you told the BBS (in this
        example, PROG.EXE).

        Of course various other systems might require a slightly different
        command and might respond with a different prompt, but you get the
        idea. If in doubt, ask the operator of the other station.

        Any problems with the file transfer could be:

          1. a problem with the other station (not in Binary Receive mode;
             not enough room on disk there; etc) in which case you need to
             try again when that station is ready to receive the Binary
             file transfer; or

          2. there could be a problem in the handshaking between your
             computer and your TNC. If you are using Hardware Handshaking
             (you will see RTS CTS etc in the right hand side of the
             Status Window), try using Software Handshaking as there could
             be a problem in the cable you are using between the computer
             and the TNC.
                               Page  67


             To change to Software Handshaking, refer to the
             "Configuration Windows - Serial Port" section of this
             manual.

             Check both the TNC and paKet's Serial Port Configuration to
             ensure the Handshaking options correspond:

                If you have specified Software Handshaking to paKet, set
                XFLOW ON in your TNC;

                If you have specified Hardware Handshaking to paKet, set
                XFLOW OFF in your TNC.

          3. There is a mismatch in your settings for STREAMDBL.

             paKet works best if STREAMDBL is ON in both the paKet
             Configuration AND in the TNC, but the important thing is to
             ensure they are BOTH set the same way!

             If your TNC does not have a STREAMDBL option, set paKet's
             option OFF.

             Refer to the section, Configuration Windows - Multi User
             options, for a full discussion on the STREAMDBL settings.

          4. Some TNCs cannot handle a PACLEN of 256 (or 0 which, to the
             TNC, is equivalent to 256).

             Reduce PACLEN for binary operations to 252 in the
             Configuration - File Transfer options.






























                               Page  68


F8                 Receive Binary file using either pP or YAPP protocol.

        This is the reverse of the Binary File Send discussed under <F7>.

        To use this feature the other station must be able to handle
        either pP (paKet Protocol) or YAPP protocol.  If you have pP
        enabled and the other station is also equipped to handle pP, the
        advanced protocol is automatically selected, otherwise the
        transfer will be performed according to the original YAPP
        specifications.

        If you want to receive a Binary File from a BayCom or Digicom
        system, use the <Alt-F8> key. And if you prefer to receive a
        Binary File from the other station with no protocol at all (you
        will have to synchronise it manually), refer to the RAW Binary
        mode with the <Alt-F6> key.

        This is even simpler than sending as you do not have to specify
        the file name here - that is sent by the other station in the
        Protocol header.

        To use this feature, prepare the other station for the file
        transfer then press <F8>. That is all!

        For example, if you are logged on to a BBS system and it is
        waiting for a command, you could type:
              "YD PROG.EXE"    (The BBS command to download a YAPP file)

        and it would respond with something like:
              "Ready to Send with YAPP protocol"

        Then you press <F8> and watch as the file PROG.EXE (or whatever
        you have specified) is transferred to your disk.

        paKet will:
              set up the necessary parameters in the TNC;
              display the Binary File Transfer Window;
              synchronise with the other station; then
              begin the transfer.

        Once again, I suggest you check with the operator of the other
        station if this command does not appear to be working on that
        system.

















                               Page  69


F9                 DOS Gateway

        Pressing this key will provide access to DOS so you can run other
        DOS jobs without leaving paKet. A Message Window will pop up
        asking you for a DOS command.

        There are two ways to perform a DOS command:

           1.  You may enter the command into the message window beside
               the ">" prompt.

               If you do this, the command will be executed (if possible)
               and you will be invited to "Press any key to continue"
               before paKet resumes where it left off.  The "Press any key
               to continue" message appears briefly over the DOS display
               to allow you time to peruse the result of the job and to
               read any messages etc that may have come from the DOS
               command.

           2. Press <Enter> instead of entering a command, and the screen
              will be cleared before control is passed over to DOS and the
              familiar DOS Prompt.

              When you have finished the DOS operations, type EXIT to
              return to paKet.  Do NOT type PAKET again as the system will
              attempt to load a second copy of paKet into memory!

        Please keep in mind that paKet is still in memory at this stage so
        you will have considerably less free memory for your other DOS
        programs. You may even find some will not run due to insufficient
        memory. The only remedy for this, I am afraid, is to return to
        paKet and exit the program (with the <Alt-X> key) so you can
        release the memory occupied by paKet.

        While you are "away" in DOS, paKet's Interrupt Handler continues
        to operate so any input from the TNC during that time will be
        captured and stored in paKet's 32KB System Input Buffer. Unless
        your DOS jobs take a long time, you should not lose any input data.






















                               Page  70


F10                Display TNC Help File commands

        This feature will load the TNC Help file and will display a window
        showing the available commands for your TNC.

        The TNC Help file that is displayed is the one specified in the
        Configuration - File/Directories Window. Several TNC Help Files
        are supplied with paKet so be sure to specify the file best suited
        to your TNC.

        The TNC Help File Window will display a list of all the commands
        for this TNC and this may be all you need to choose the desired
        command. If so, press <Esc> to return to normal communications.

        For more detail on any of these commands, highlight the desired
        command and press <Enter>. When finished with this Detail display
        press <Esc> to return to the main TNC Help file list. Then select
        another item to display or press <Esc> to return to normal
        communications.

        Further details of this display are available in the section on
        "TNC Help Window".






































                               Page  71


Alt-F1             Display the Online Manual

        Pressing this key will bring up paKet's Online Manual Window which
        reveals the entire contents of this Manual.

        The Manual is indexed and the index will appear for you to select
        a topic. Move the highlight bar with the <Up-Arrow>, <Down-Arrow>,
        <PageUp>, <PageDown>, <Home> or <End> keys to the desired topic,
        then press <Enter> to select that topic.

        Once a particular topic is selected the full text for that section
        of the Manual will be displayed and you may scroll up or down as
        desired.

        When you have finished with that section, press <Esc> to return to
        the Index to select another topic. If you have finished with the
        Online Manual, press <Esc> to return to normal communications.











































                               Page  72


Alt-F2             Contest Mode on/off

        This key combination will activate Contest Mode. If already
        active, it will cancel Contest Mode and return to normal
        communications.

        Contest Mode is a rather specialised mode designed to monitor the
        progress of a sporting event such as a Triathlon. It is a mode I
        expect would be seldom used.

        Contest Mode is described fully in its own section of this Manual.

















































                               Page  73


Alt-F5             Send a RAW Binary File

        This option is similar to the other Binary File Transfer options
        in that paKet will put the TNC into Transparent Mode and will
        display the Binary File Transfer Window while the file is being
        transferred.   The main difference here is that no protocol at all
        will be used. If there is any synchronisation required with the
        other station, you will have to do that manually.

        This facility is provided to cover those situations where you want
        to send a data file containing non-ASCII codes to another station
        (or non-ASCII commands to the TNC). If the other station cannot
        handle one of the Binary Transfer protocols supported by paKet and
        you are unable to use the standard ASCII Text file transfer (<F5>)
        because of the non-ASCII codes in the file, this might be your
        last hope!

        paKet will ask you for the name of the file you wish to send. A
        Directory Window will pop up to help you select the file.

        paKet will:
              set up the necessary parameters in the TNC;
              display the Binary File Transfer Window;
              begin the transfer.

        Remember, with this RAW method, you will have to perform any
        synchronisation required and to manually issue any commands to
        start and to end the file transfer.  paKet does nothing to help -
        this time it is your responsibility!































                               Page  74


Alt-F6             Receive a RAW Binary File

        As with the <Alt-F5> command to Send a RAW Binary File, this
        option is similar to the other Binary File Transfer options in
        that paKet will put the TNC into Transparent Mode and will display
        the Binary File Transfer Window while the file is being
        transferred.   The main difference here is that no protocol at all
        will be used. If there is any synchronisation required with the
        other station, you will have to do that manually.

        This facility is provided to cover those situations where you want
        to transfer a data file containing non-ASCII codes from another
        station which cannot handle one of the Binary Transfer protocols
        supported by paKet.

        paKet will ask you for the name of the file you wish to open to
        hold the captured data.

        paKet will:
              set up the necessary parameters in the TNC;
              display the Binary File Transfer Window;
              open the nominated file;
              write any data received into that file.

        You will have to close the file manually by pressing <Alt-F6>
        again.

        Remember, with this RAW method, you will have to perform any
        synchronisation required and to manually issue any commands to
        start and to end the file transfer.  paKet does nothing to help -
        this time it is your responsibility!





























                               Page  75


Alt-F7             Send a Binary File to a BayCom system

        The BayCom system supports Binary Transfers via its //WPRG and
        //RPRG commands but does not currently support any Binary File
        Transfer PROTOCOLS. However, with just one reservation, paKet is
        able to effect a reliable Binary File Transfer to a BayCom system.

        This paKet facility is provided primarily for Binary Transfers to
        a BayCom system although it should work into a Digicom system as
        well.

        When you press <Alt-F7> the Disk Directory window will appear for
        you to select the file to send. Then paKet will ask for the name
        (and path if that is required) this file is to have in the BayCom
        system.

        paKet will:
              set up the necessary parameters in the TNC;
              display the Binary File Transfer Window;
              send BayCom's //WPRG command;
              transfer the contents of the file;
              send BayCom's <CR>//WPRG OFF<CR> command at end-of-file.

        If all goes well, you do nothing - just sit back and watch - and
        the file will be sent. The program returns to normal
        communications when the transfer is completed.

        As the BayCom system does not have a defined File Transfer
        Protocol, the only way to indicate the end-of-file is with the
        <CR>//WPRG OFF<CR> command. The trouble is, the BayCom system will
        add this string of characters to the file BEFORE recognising it as
        the command to close the file! So the file now on the BayCom
        system will be 12 bytes longer than the one we sent. This is a
        flaw in the BayCom system and there is nothing paKet can do about
        it.

        Fortunately it is not a big problem: I have found it usually does
        not matter that the additional characters are there.  Executable
        program files and archived (compressed) files seem to ignore the
        additional characters.  And if required, the BayCom operator can
        easily edit the additional bytes from the end of the file. Small
        price to pay for the convenience of having Binary Transfer
        capability!

















                               Page  76


Alt-F8             Receive a Binary File from a BayCom system

        The BayCom system supports Binary Transfers via its //WPRG and
        //RPRG commands but does not currently support any Binary File
        Transfer PROTOCOLS. However with some operator input, paKet is
        able to effect a reliable Binary File Transfer from a BayCom
        system.

        This paKet facility is provided primarily for Binary Transfers
        from a BayCom system although it should work from a Digicom system
        as well.

        The main difficulty in transferring a Binary File from a BayCom
        system is the absence of any end-of-file indicator. The BayCom
        system will send the Binary File in response to its //RPRG command
        and will simply stop sending when it has reached its end-of-file.

        paKet needs to know when to close the file. There are four ways
        this can be done:

           1. paKet will count each byte received and, provided it knows
              the size of the file, it will close the file when that
              number of bytes has been received.

           2. If paKet receives BayCom's <CR>//WPRG OFF<CR> string it will
              assume that is the end of the file. That string will NOT be
              written to our file.

              This means the Binary File being transferred cannot have
              this string embedded in the file. If the file does happen to
              contain this string, I suggest you ask the BayCom operator
              to compress the file with LHA or similar and send the
              compressed version of the file - this should change the file
              so the string is no longer apparent.

              If the file being received was previously transferred to the
              BayCom system by some other user (or by us for that matter),
              that file will probably have the <CR>//WPRG OFF<CR> string
              on the end of the file.   paKet would recognise that and
              close the file at the right time! (Refer to the comments on
              sending a Binary File to a BayCom system, under <Alt-F7>).

              The BayCom operator could send us this "command" when that
              system has finished sending the file, although if the BayCom
              operator is present we should know the file size and will
              probably have closed the file by now.

           3. You can press <Alt-F8> during the transfer to close the file
              manually.

           4. paKet will close the file if nothing has been received for a
              period of 2 minutes.

              As the BayCom system will stop sending when it has finished
              and will wait for our next command, this option might be
              used if the BayCom system is unattended and you do not know
              the filesize.

              If the radio frequency is not busy, it should be rather
              obvious when the other system has stopped sending so you
                               Page  77


              might close the file manually with <Alt-F8> (option 3 above)
              before the 2 minutes expires.


           Before attempting the transfer, you should get the details of
           the file from the BayCom operator. You will need the filename
           of course and if it is not in the BayCom system's current
           directory you will need to know its path as well. If possible
           get the file size in bytes too.

           When you press <Alt-F8> paKet will ask you for the name of the
           file in the BayCom system. This name will form part of the
           //RPRG command paKet sends, so be sure to specify any path
           details if required.   If you are transferring a file from a
           Digicom system, it might be an unusual file name because the
           Commodore 64 can cope with longer file names including embedded
           blanks! You will have to specify the file name as it appears in
           that Digicom system. Of course the file name you choose for
           this file on our system will have to conform to the DOS
           requirements.

           Then paKet will ask you for the file size in bytes. If you do
           not know the file size, enter 0. This means the first of the
           above options will not apply and you will probably have to
           close the file manually or wait for the 2 minute timeout.

           If you are transferring a file from a Digicom system, you will
           probably not know the file size in bytes because the Commodore
           64 system displays its file sizes in blocks rather than bytes.
           In this case, enter -1 for the file size. This will tell paKet
           to expect the Digicom responses (which are a little different
           from BayCom's) as well as indicating the file is to be closed
           manually.

           Finally, paKet will ask you for the filename you wish to use
           here. As you will most likely use the same name as that on the
           BayCom system, paKet offers this name as a default. You can
           change the details if you wish or simply press <Enter> to
           accept the same name.

           Then the transfer begins.  paKet will:
              set up the necessary parameters in the TNC;
              display the Binary File Transfer Window;
              send the BayCom //RPRG command;
              begin the transfer;

           When the file is closed by one of the above methods, paKet
           removes the Binary File Transfer window and returns to normal
           communications.











                               Page  78


Alt-A              Turn Alerts on/off

        This toggle enables or disables the Alerts facility which can
        sound a Bell if one of the predefined strings is detected in the
        Communications Window.

        Refer to the Configuration - Alerts window to see how to specify
        the desired search strings.

        When the Alerts facility is enabled, an "A" will appear in the
        Status Window to the left of the Time display.


Alt-B              Send a BREAK signal to TNC - return to Command Mode

        Pressing <Alt-B> will send to the TNC either a BREAK signal, a
        <Ctrl-C>, or an <Esc> depending on the setting you have chosen in
        your Serial Port configuration.

        Most TNCs support the BREAK signal and will return to Command mode
        when this signal is received. This is the preferred option.

        If the BREAK is not supported, the TNC's "Command" character
        (usually <Ctrl-C>) must be used.

        You might need to send an <Esc> character to indicate Command
        Mode if you happen to be running a vintage TNC-1.   This
        Configuration option is available too although it should be
        specified ONLY by TNC-1 users.


Alt-C              Connect to another station

        This feature allows you to more easily make a connection to your
        regular contacts, especially where there are long path details to
        be entered.

        Pressing <Alt-C> will bring up paKet's Connect Window which is
        fully described in the section on the Connect Window.

        To make a call, simply move the cursor to the desired item and
        press <Enter>.

        You can change an existing entry by moving the cursor to the
        character to be changed, and overtyping the new data. Pressing the
        <Insert> key allows you to insert additional characters.

        Use the <Tab> key to move from the Name field to the Callsign
        field.

        To insert a new entry, move the highlight bar to the desired line
        and press <Ctrl-N>. The entry on that line and on all following
        lines will move down making room for your new entry.

        To remove an existing entry, move the highlight bar to that entry
        and press <Ctrl-Y>.




                               Page  79


Alt-D              Display a Disk Directory

        Pressing <Alt-D> will bring up the Disk Directory Window which is
        fully described in the section on the "Disk Directory Window".

        You may scroll up and down this window using the <Up-Arrow> or
        <Down-Arrow> keys, the <PageUp> or <PageDown> keys, or the <Home>
        or <End> keys. Or you can use paKet's hot-key typing by entering
        part or all of the file name - paKet will highlight the first
        filename that matches the characters you have typed so far. Often
        all you need to type is one or two characters to move to the file
        you want.

        If you press the <Enter> key, the action taken depends on the type
        of line highlighted. If the highlight bar is on:

           (Enter file name manually)
              The Message Window pops up to ask you for the desired file
              name. When you enter the file name the contents of that file
              are displayed as if you selected that file with the <Enter>
              key (see below).

           (Change to another drive)
              The Message Window pops up to ask you which drive you wish
              to change to. Then the directory display changes to show the
              root directory for that drive.

              When entering the new drive letter, the colon is optional.
              For example, you could enter either:
                 A  or
                 a:
              to select drive A:. Note upper or lower case is acceptable.

           <Previous directory>
              The directory display changes to show the contents of the
              "Parent" directory, that is the directory above this one.

           <DIR>
              If there is an entry with "<DIR>" instead of the file size,
              this represents a sub directory below this one. So pressing
              <Enter> on this line, causes that subdirectory to be
              displayed.

           (filename)
              If you press <Enter> with any file highlighted, paKet will
              display the contents of that file. The command used to
              create the display is configurable and is defined in
              Configuration Windows - File/Directories. I prefer something
              like the LIST program, but you could use the DOS "TYPE"
              command if you wish.  When the display program has finished,
              press any key to return to the Directory Window. If you
              don't want to  display any more files, press <Esc> to return
              to normal communications.

              While you are viewing the file, paKet's Interrupt Handler
              continues to operate so any input from the TNC during that
              time will be captured and stored in paKet's 32KB System
              Input Buffer.


                               Page  80


        If you press the <Delete> key while a file is highlighted, paKet
        will delete that file (after seeking your confirmation).

        If you press the <Alt-R> key while a file is highlighted, paKet
        will ask you for the new filename then will Rename that file. If
        you specify a new directory, paKet will Move the file to the new
        directory.


Alt-E              Edit a data file with your preferred System Editor

        This feature allows you to edit a file using your favourite text
        editor.

        Details of the System Editor program are defined in Configuration
        Windows - File/Directories and may be any editor or word processor
        you choose. Keep in mind however, that paKet with all its buffers
        and data is still in memory, so you will probably not be able to
        load and run one of the BIG Word Processing packages using this
        feature.

        When you press <Alt-E>, paKet will display the Disk Directory
        Window so you can identify the file you wish to edit. Then it will
        load the nominated editor program.

        When you have finished the edit and exit from that program, you
        will be returned to paKet where you left off.

        While you are using the System Editor, paKet's Interrupt Handler
        continues to operate so any input from the TNC during that time
        will be captured and stored in paKet's 32KB System Input Buffer.


Alt-F              Find text in Flashback

        Pressing <Alt-F> will commence a search backward through the
        Flashback buffer, looking for a particular string of characters.

        A Message Window will pop up asking you to enter the desired
        search string. You can enter this in either upper or lower case
        because the search is not case sensitive.

        If found, the line containing the string is highlighted and paKet
        remains in Flashback mode.

        Pressing <Alt-L> will continue the search, looking for an earlier
        occurrence of the same string.

        Further details on this option are found in the Communications
        Windows - Flashback section.


Alt-H              Send MHEARD command to the TNC

        This option simply generates and sends the MHEARD command to the
        TNC.




                               Page  81


Alt-I              Initialise Communications Windows

        This option would not be used in normal circumstances but has been
        provided mianly to "fix" problems that were discovered while
        testing with a KAM TNC. Other Kantronics TNCs were not tested but
        it is likely the problems will occur with those models as well.

        These TNCs do not behave in the same way as other TNCs when
        multiple streams are used as they do not support the STREAMDBL
        command.

        If, when monitoring the frequency, the program receives a STREAMSW
        character from the TNC, it has no way of knowing whether it is a
        data character or whether it is really a change of stream. Other
        TNCs resolve this issue with the STREAMDBL facility. If we are
        going to be able to handle multiple streams, the program cannot
        ignore this STREAMSW character - it must process it as a change of
        stream!

        The result of this is that the monitored data will suddenly start
        appearing in one of the other Communications Windows. The last of
        your configured Windows could even change to another stream id!

        If you are using one of these Kantronics TNCs and find data is
        going into some other Communications Window, you will need to
        reset the Streams, clear any responses in the other Windows and
        get everything back into order.  This is what this <Alt-I> command
        will do for you.

        If you are using some other brand of TNC this command should not
        be required although it will not cause any problems. It will
        simply clear any backlog in the other Communications Windows and
        reset the TNC to the Stream specified for the first Communications
        Window.


Alt-L              Continue Find in Flashback

        Refer to the <Alt-F> command for details.


Alt-M              Activate the Personal Message System (PMS)

        When you press this key you get the Sysop PMS menu:
           Sysop PMS menu: <B,H,K,L,R,S,?>

        While the menu is active all other communications will be held in
        the input buffers until you have finished. You don't have to do
        anything - paKet will automatically switch <ScrollLock> on and
        will switch it off again when you have finished.

        The Menu options are used as follows:

            B (Bye)  - Return to normal communications
            H (Help) - Display brief summary of menu options
            K (Kill) - Kill a message (eg K 3)
            L (List) - List available messages
            R (Read) - Read a message (eg R 3)
            S (Send) - Send a message (eg S (callsign))
            ? (Help) - Display brief summary of menu options (same as H)
                               Page  82



        If someone has left a message in the PMS via our REMOTE Mode,
        paKet will display "(msg)" in the Status Window to alert you to
        this.  Pressing <Alt-M> will remove that reminder from the Status
        Window.

        Refer to the PMS section in this Manual for more details on this
        sub system.


Alt-P              Turn Print Log on/off

        This is a toggle, meaning you press <Alt-P> to turn the Print Log
        ON and press it again to turn the Print Log OFF again.

        While the Print Log is ON, a 'P' will be displayed in the Status
        Window to the left of the Windows display and all Communications
        data will be echoed to the printer on LPT1.

        If the Print Log is OFF, no data will be sent to the Printer.


Alt-Q              Clear TNC's XOFF

        This command is mostly useful if you are using Software Handshaking.

        When the TNC wants paKet to stop sending, it will send an <XOFF>
        code. paKet will not send any further data to the TNC until an
        <XON> code is received.

        If the <XON> code is not received or appears to have been lost
        paKet will effectively be locked up waiting for that code before
        it will continue to send normally.  With this <Alt-Q> command you
        can force an <XON> to clear the way for processing to continue.

        I expect this facility would be required only on very rare
        occasions.


Alt-R              Rename/Move a data file

        <Alt-R> may be used to Rename a data file or Move it into another
        directory.

        This command may be used only while the Disk Directory is
        currently being displayed. It has no effect at other times. Refer
        to the discussion on the Disk Directory Window for more details.

        Move the Highlight bar to the file you want to rename or move
        before pressing <Alt-R>.

        The Message Window will then pop up asking you to enter the new
        filename.

        If you want to simply change the file's name, leaving the file in
        its exising directory, just type the new filename and press
        <Enter>. The filename will be changed and the Directory Window
        will be re-sorted and re-displayed.


                               Page  83


        If you want to Move the file into another directory, enter the
        full path details into the Message Window (you may also enter a
        different filename if you wish) and paKet will transfer the file
        to the new directory.  The new Directory Window will then be
        displayed, showing that file in the new directory.

        When a file is Moved into another directory, the data is not
        actually transferred, it is just the directory entry that is
        moved. DOS does not permit a "Move" to another drive, so if you
        want the file on a different drive, you'll have to COPY the file
        yourself. Refer to the <F9> DOS Command for access to DOS to
        perform the COPY.


Alt-S              Script processing - load and run a Script file

        This is the command you use to activate a paKet Script file.
        (Script Processing is discussed fully in its own section in this
        Manual).

        When you select this option, a Disk Directory Window will appear
        with the default Script file name already highlighted. If you
        decide to enter a file name manually and you type a file name
        without an extension, paKet will assume an extension of ".SCP".

        When you select the desired Script file, that file will be loaded
        and Script processing will commence.   The word "SCRIPT" will be
        displayed in the Status Window to the left of the time display
        while the Script is running.

        When the Script has completed, or is aborted by <Esc>, the
        indicator in the Status Window will disappear and you will be
        returned to normal communications.


Alt-T              Set TNC's Time and date

        If for any reason, you need to reset your TNC, you can easily
        reset the date and time with this function. paKet will generate a
        "DAY" command using the computer system's date and time as it does
        during initialisation..

        The format of the generated command includes the time in Hours,
        Minutes and Seconds. It has been brought to my notice that some
        TNCs cannot handle that format and will accept the time as Hours
        and Minutes only. So, if you hold the Ctrl key while typing this
        <Alt-T> command (i.e. <Ctrl-Alt-T>), paKet will generate the DAY
        command without the seconds.


Alt-V              Verify the TNC's Connected status

        When a Connection is established with another station, paKet will
        try to determine the callsign of that station from the TNC's
        "Connected" message when it appears in the Communications Window.
        paKet will then display that callsign in the Communication
        Window's Header line.

        Some software packages operating in Host Mode or KISS Mode can
        interrogate the TNC to get this information, but these packages
                               Page  84


        are usually more specific to certain TNCs. paKet, on the other
        hand was designed to run on all TNCs and so relies on the data
        flowing from the TNC rather than on some special TNC codes.

        paKet's method works well most of the time, but there are
        occasions where the callsign displayed is incorrect. For example,
        if you reload paKet after a TNC connection has already been
        established, the newly loaded copy of paKet will not see a
        "Connected" message and so will think there is no connection!

        This <Alt-V> command will issue a "C" (Connect) command to the TNC
        and will look at its reply to determine the connected status. A
        Message Window will pop up to advise you of the result and, if
        necessary, paKet will change the displayed callsign in the
        Communications Window Header.


Alt-W              Write contents of the Flashback buffer to disk

        If you have received some information which you wanted to save and
        is still in the Flashback buffer, but did not have the disk Log
        File on at the time, you can select this option to write the
        entire Flashback buffer to disk.

        paKet will ask you for the desired file name, via a Disk Directory
        Window.


Alt-X              Exit the paKet program

        This command returns you to the DOS operating system. Any files
        that were open will be closed automatically.

        To guard against inadvertent exits, paKet will ask for your
        confirmation that you really do want to exit.

        If you have specified any End-Auto Commands (Refer the
        Configuration section for details) they will be sent to the TNC
        and if paKet finds an AUTOEND.SCP file in the current directory
        that Script will be executed before paKet returns to DOS.


Alt-Z              Configuration

        This option allows you to configure paKet's many options to set up
        an environment especially to suit you.

        When you press <Alt-Z> the System Configuration Window will appear
        to show the major items that may be configured. Then when you
        select one of those options additional Configuration Windows will
        appear to allow you to select the desired options.

        Full details of all configurable options are shown and explained
        in the section on Configuration Windows in this Manual.  If you
        are new to this, start with the Configuration Windows - Overview
        and work your way through all the options from there.




                               Page  85


Insert             Toggle Insert Mode

    The <Insert> key toggles the Insert Mode on and off.

    When Insert Mode is on, the cursor will be a Block shape and any newly
    typed data characters will be inserted between existing data
    characters at the cursor position.

    When Insert Mode is off, (i.e. Overwrite Mode) the cursor will be an
    Underscore shape and newly typed data will overwrite any data
    previously stored at the cursor position.

    If the Type Ahead Window is not being used, you will not be able to
    "insert" characters (or move the cursor back) because in this mode
    each character you type into the Communications Window is sent to the
    TNC as you type. It is too late to insert something else!


Delete             Delete a character or delete a file

    When entering text the <Delete> key will remove the character under
    the cursor.

    If a Disk Directory Window is currently displayed, you can delete a
    file from the disk by highlighting the unwanted file then pressing the
    <Delete> key.


Backspace          Delete the character before the cursor

    When entering text the <Backspace> key will remove the character to
    the left of the cursor.


Ctrl-Y             Delete a line

    When entering text the <Ctrl-Y> key will remove all text currently in
    the Type Ahead Buffer or on the line being entered.


Esc                Return to previous operation

    The <Esc> key is used in a variety of places in paKet, each time in a
    manner of "exiting" or "returning" from the current function. It is
    your way of saying "I don't want to do this any more".

    For example, if in Flashback Mode, the <Esc> key will return the
    system to normal communications.

    And if displaying a Disk Directory Window the <Esc> key will return
    the system to normal communications.

    If there are several "levels" involved in the current function, for
    example when using the Configuration Windows you could have two or
    even three levels of Configuration Window displayed. The <Esc> key
    will take you back to the previous level. If you are already at the
    first level, it will take you back to normal communications.

    You may note the <Esc> code cannot therefore be sent to the TNC from
    the keyboard. If you need to send an <Esc> code to the TNC you could
                               Page  86


    define it in a Keyboard Macro as <Ctrl-[> (written as "^[" which is
    caret and left-square-bracket). We wont go into the details here, but
    <Ctrl-[> generates the same code as <Esc>. If you enter it this way
    paKet will process that as data, sending the code to the TNC. Refer to
    the Special Key Codes section for more information on the use of the
    '^' symbol for generating <Ctrl- > key sequences.


ScrollLock         Hold all input data in the buffers

        The <ScrollLock> key in paKet operates as a Pause key for input
        data.  Keyboard activity remains unaffected, so you may continue
        to send to the TNC.

        While the system is "ScrollLock"ed, any input data coming in from
        the TNC will be held in paKet's input buffers until the Scroll
        Lock key is pressed again to release it.  While ScrollLock is ON,
        an indicator appears to the right of the Communications Window
        Header line.

        You may have difficulty finding the <ScrollLock> function on some
       "IBM-almost-compatibles" such as the Tandy 1000.  Refer to manual!


Left-Arrow         Move the cursor left one position

    When entering text this key is used to move the cursor one character
    position to the left. The text remains unchanged.


Right-Arrow        Move the cursor right one position

    When entering text this key is used to move the cursor one character
    position to the right. The text remains unchanged.


Up-Arrow           Previous Type Ahead Recall or move up one line

    When using the Type Ahead Buffer this key is used to Recall a previous
    line from the Recall buffer.

    The Type Ahead Recall facility is discussed more fully in the Type
    Ahead Window section of this Manual.

    When viewing a Disk Directory Window, the Online Manual or the TNC
    Help File, the <Up-Arrow> key is used to move up the list of items on
    display.


Down-Arrow         Next Type Ahead Recall or move down one line

    When using the Type Ahead Buffer this key is used to Recall the next
    line from the Recall buffer.

    The Type Ahead Recall facility is discussed more fully in the Type
    Ahead Window section of this Manual.

    When viewing a Disk Directory Window, the Online Manual or the TNC
    Help File, the <Down-Arrow> key is used to move down the list of items
    on display.
                               Page  87


Home               Move to the start of the text or the window

    When entering text the <Home> key moves the cursor to the beginning of
    the text. The text remains unchanged.

    When viewing a Disk Directory Window, the Online Manual or the TNC
    Help File, the <Home> key is used to move to the first of the items on
    display.


End                Move to the end of the text or the window

    When entering text the <End> key moves the cursor to the end of the
    text. The text remains unchanged.

    When viewing a Disk Directory Window, the Online Manual or the TNC
    Help File, the <End> key is used to move to the last of the items on
    display.


Shift-Up-Arrow     Flashback - move back one line

    This key is used for Flashback operations, moving up one line at a
    time.

    Flashback Mode is a facility for redisplaying Communications Window
    information that has scrolled off the top of the screen. It is
    discussed in its own section under Communications Windows in this
    Manual.


Shift-Down-Arrow   Flashback - move down one line

    This key is used for Flashback operations, moving down one line at a
    time.

    Flashback Mode is a facility for redisplaying Communications Window
    information that has scrolled off the top of the screen. It is
    discussed in its own section under Communications Windows in this
    Manual.


PageUp             Move display up one page

    When viewing a Disk Directory Window, the Online Manual or the TNC
    Help File, the <PageUp> key is used to move up the list of items on
    display a page at a time.

    At other times this key is used for Flashback operations, moving up
    one page at a time.

    A "page" here is considered to be the size of the window being
    displayed.


PageDown           Move display down one page

    When viewing a Disk Directory Window, the Online Manual or the TNC
    Help File, the <PageDown> key is used to move down the list of items
    on display a page at a time.
                               Page  88



    At other times this key is used for Flashback operations, moving down
    one page at a time. If you reach the end of the Flashback Buffer and
    there is some Input data waiting to be displayed, paKet will display
    one page of that Input data and remain in Flashback mode. If there is
    less than a page waiting, it will return to normal communications.

    A "page" here is considered to be the size of the window being
    displayed.


Ctrl-PageUp        Move to beginning of the Flashback buffer

    This key is used for Flashback operations, scrolling to the beginning
    of the Flashback buffer. While the scrolling is in progress, pressing
    any key including <Ctrl-PageUp> again will stop it at that point.


Ctrl-PageDown      Move to end of the Flashback buffer

    This key is used for Flashback operations, moving to the end of the
    Flashback buffer. While the scrolling is in progress, pressing
    any key including <Ctrl-PageDown> again will stop it at that point.


Shift-Left-Arrow   Change to previous Communications Window

      <Shift-Left-Arrow> tells paKet to change to the previous
      Communications Window if available.

      You might prefer to use the <Shift-Fn> keys to change Communications
      Windows (eg: <Shift-F3> to change to Window 3) but whichever method
      you choose, paKet will automatically issue the change of stream
      commands to the TNC when you change Windows.


Shift-Right-Arrow  Change to next Communications Window

      <Shift-Right-Arrow> tells paKet to change to the next
      Communications Window if available.

      You might prefer to use the <Shift-Fn> keys to change Communications
      Windows (eg: <Shift-F3> to change to Window 3) but whichever method
      you choose, paKet will automatically issue the change of stream
      commands to the TNC when you change Windows.


Shift-Fn           Select another Communications window.

      You may select another Communications Window, that is select another
      Stream, by pressing Shift and a Function key.

      <Shift-F1> is the first Communications Window, <Shift-F2> the
      second, etc. For example, you can select Window 4 by pressing
      <Shift-F4>.

      Another way to change to another Communications Window is to use the
      <Shift-Left-Arrow> or <Shift-Right-Arrow> keys to move, one-by-one
      to the desired window.

                               Page  89
































                      (This page intentionally blank)





























                               Page  90