RADIO REMOTE CONTROL PROGRAM





                            By Lydia Rosa


   Copyright 1990 by Lydia Rosa










                     RADIO REMOTE CONTROL PROGRAM
     WHAT'S NEW IN THIS RELEASE




      Version 0.7
         Fixed problem that would cause occasional hang with COM2. Also
         fixed profile not recognizing COM2 in lower case.


      Version 0.6
         Documentation cleanup. No code change.


      Version 0.5
         Fixed a bug that caused garbage to display if function key pressed
         for an ANY KEY TO CONTINUE keypress.
         Fixed sort problem that caused replication of channel info.


      Version 0.4
         Fixed a bug that caused COM port not to respond.


      Version 0.3
         Added the TXADR command to allow addresses other than 8 for
         the ICOM radios.

         Fixed a bug in the SEARCH function.


      Version 0.2
         Initial Release



























WHAT'S NEW IN THIS RELEASE                                      1


                     RADIO REMOTE CONTROL PROGRAM
     DISCLAIMERS





        IBM is a trademark of IBM corporation.

        ICOM is a trademark of ICOM incorporated.

        KENWOOD is a trademark of KENWOOD corporation.

        DBASE III is a trademark of Ashton-Tate.

      The  author  takes no  responsibility for  any damages that  may
     occur due to the operation of this program.

      This program is being distributed as SHAREWARE. This means  that
     voluntary  contributions  are the  only  source  of  remuneration
     obtained  for this work. A contribution of  $20.00 gives you  the
     following:

           1.  Automatic upgrades to the program.
           2.  Fixes for any bugs.
           3.  Schematics and instructions for the interfaces.
           4.  A clear conscience.


     Please mail all contributions and problem reports to

        Lydia Rosa
        P.O. Box 414
        Marlboro, N.Y.
        12542

       Thank you for your support.
























DISCLAIMERS                                                     2


                     RADIO REMOTE CONTROL PROGRAM
     INTRODUCTION



        The  RADIO REMOTE CONTROL PROGRAM will allow  you  to  control
     your ICOM-R7000, or KENWOOD R-5000 radio from any  IBM compatible
     PC,XT or AT.  With  the  standard  interface adapters provided by
     the  manufactures of these radios, you can store and recall banks
     of  100 channels.  Using a special  interface  circuit,  you  can
     scan, search, and log  active channels.  This circuit is provided
     free of charge to all registered users.

       The program allows you to select various baud rates, as well as
     COM  port 1 or 2. Commands are buffered,  and  an interface  to a
     DBASE data file is provided.

       Although  it has not been  tested, this  program may work  with
     other radio models  produced by the manufactures of the supported
     radios.









































INTRODUCTION                                                    3


                     RADIO REMOTE CONTROL PROGRAM
     REQUIREMENTS



       In order to  run this program  you will need an IBM PC,XT or AT
     running DOS 3.0  or higher. The  program requires  about 128k  of
     available RAM to run.

       If you are controlling the R7000, you will need either the ICOM
     CI-V interface adapter, or the  modified RS232 interface.  If you
     wish  to use  the signal detection feature  of this  program, you
     will need to use the modified interface.

       For  the  R-5000,  you  will  need  the  IC-10  option  kit.  A
     modification must be made to  the R-5000  if you  wish to use the
     signal detection feature of this program.

       It  is highly recommended that the  modified interface  be used
     for all radios.  Most of the features of this program make use of
     the detection of an available  signal  (SQUELCH). These radios do
     NOT  currently  have  squelch detection as  part of  the standard
     interface.  Although  this program  will work fine  without  this
     signal detection, operations such as SCAN and SEARCH will have no
     usability.

       The interface circuit is a inexpensive, easy  to build project.
     All the parts  are readily  available  at any  electronic  store.
     Estimated cost for each interface is  $15. Plans and instructions
     for these  interfaces  are  provided to you  when  you  become  a
     registered user.






























REQUIREMENTS                                                    4


                     RADIO REMOTE CONTROL PROGRAM
     STARTUP



       To start the program,  make sure the program and data files are
     in  the  default drive. If running  the R-7000, enter ICOM at the
     DOS prompt. If running the R-5000, enter KENWOOD.

     The program will  load, and  then execute  any  existing profile.
     Once the program loads, the first page panel will be displayed.


















































STARTUP                                                         5


                     RADIO REMOTE CONTROL PROGRAM
     THE DISPLAY



       The display  panel shows you the  status of your radio, as well
     as the status of the program.  At the top left hand corner of the
     screen is displayed the current BAUD rate and COM port being used
     to talk  to the radio. At the Bottom of  the screen  is  a status
     line showing the various parameter settings. If there is a signal
     present  on  the radio, the  word "SIG" will be displayed in  the
     lower  left  hand corner. This  display  is  only  valid  if  the
     modification has been made to detect squelch.

       In  the center  of the screen, the status of memory channels is
     displayed.  These channels  reflect  the  current  setting in the
     computer's memory. They can be used  to set the radio's memory if
     so desired. There are 100 memory slots available in this program.
     Since only 20 of them can be displayed at  a time, the  PgUp  and
     PgDn  keys  are  used  to display the rest.  Information  can  be
     directly entered into most of the fields displayed.

       Toward  the bottom of  the screen  is the COMMAND line. This is
     where  commands to  the program are entered. All command  data is
     automatically  converted to upper  case.  To  the  right  of  the
     command line is  the LAST LOGGED status. This  indicates the last
     information (frequency, modulation) sent by the radio.


































THE DISPLAY                                                     6


                     RADIO REMOTE CONTROL PROGRAM
     DATA FIELDS



        Each memory channel displayed  has  several  fields associated
     with it.  Most  of these fields  can be modified just  moving the
     cursor to the field and typing.




     VALID



        The VALID field determines whether or not SCAN and SEARCH will
     use the frequency currently entered into that  channel. The field
     is set ON  by entering an "X"  while  the cursor is positioned on
     that field. The  space  bar  turns  the VALID  flag OFF. The SCAN
     operation  will  NOT scan that memory channel  on the ICOM if the
     VALID field corresponding  to that memory channel is OFF. For the
     SEARCH operation,  any frequency entered in a memory record  that
     has the VALID flag off will NOT cause the search to stop and log.

        Entering a "P" in the  valid  field  will cause the channel to
     become the current priority channel.




     DELAY



       The DELAY  field is use during the SCAN  operation. If delay is
     set  ON, scanning will continue one second  after the signal ends
     on  that  channel.  If  delay is  set  OFF,  then  scanning  will
     continue immediately  after the signal ends.  The field is set ON
     by entering an "X" while the cursor is positioned on  that field.
     Any  other key turns  the DELAY flag OFF. Delay affects only  the
     specified memory channel.




     FREQUENCY



       The FREQUENCY field is used to record or set the current memory
     channel frequency. When a SCAN  or SEARCH  stops on a  channel or
     frequency, the frequency currently set  in the ICOM  is logged in
     the appropriate display channel. If a frequency is entered into a
     specific channel, the memory channel on the ICOM corresponding to
     the  channel  on  the  display  is  set  to that  frequency.  The
     frequency  is entered by positioning the cursor to  the FREQUENCY
     field  of  the  desired channel,  and  entering  in  the  desired
     frequency.  Only number input is accepted.  The  decimal point is


DATA FIELDS                                                     7


                     RADIO REMOTE CONTROL PROGRAM
     always assumed,  and never entered.  The  LOAD  command will also
     set the frequency to correspond with the radio memory channel.




     MODE



       The  MODE  field is used to display  or set  a specified memory
     channels modulation. If a memory channel  is  logged  by the SCAN
     operation,  the  selected  modulation  of  that  channel  will be
     displayed  in this field. A channel's  modulation  can be set  by
     moving the cursor  to the MODE field and entering in the  desired
     modulation. MODE recognized by the program are as follows:

        radio                valid modulation
       ICOM                  AM, FM, FMN, SSB, CW ,LSB ,USB
       KENWOOD               AM, FM, FSK, CW, LSB, USB

     Note that the ICOM will accept  CW, LSB and USB. These modes have
     no  meaning  for  the  R-7000,  but  are  accepted  by  the  ICOM
     interface.  They are provided  for compatibility with  other ICOM
     radios.




     COUNT


        This field displays the number  of times a signal was detected
     on a  specific channel. This  field cannot be  altered.  It  can,
     however be reset. The RESET command  will cause this value  to be
     reset  to  0.  Ctl-END will also reset the COUNT, as well as  all
     other fields on the selected information line.




     DURATION


        This field  displays the  average  number  of  seconds  that a
     signal was detected on  a specific channel. This field cannot  be
     altered.  It can, however  be reset. The RESET command will cause
     this  value to  be  reset  to  0.  Ctl-END  will  also  reset the
     DURATION, as well as all other fields on the selected information
     line.










DATA FIELDS                                                     8


                     RADIO REMOTE CONTROL PROGRAM
     SERVICE



        This field is  used  to  record  the  service for  a  specific
     channel.  It is not modified by any of the commands except DBASE.
     This is a  scratch  pad  location to record information  about  a
     specific  frequency. The  DBASE  command will  fill in this field
     from  the frequency database if it  finds a  match of the current
     FREQUENCY.


















































DATA FIELDS                                                     9


                     RADIO REMOTE CONTROL PROGRAM
     COMMANDS



        All  commands  are entered from  the  COMMAND line. A  command
     stack is provided,  so that a command can  be  entered before the
     previous command  is complete. The number  of commands stacked is
     limited only by the available memory in your computer.

       When a command is stacked,  the  status line  (on the bottom of
     the screen) is updated  to  show  the number  of commands queued.
     The "Q" indicator shows  the number of stacked commands. Pressing
     ESC  will terminate  the  command in process, and cause the  next
     command in the queue to be processed.

        If a command is not valid when entered, the system will "BEEP"
     and the invalid command will be left in the COMMAND line, so that
     it  can be changed. This will also happen if there  are  too many
     commands in the command stack.




     BAUD  {value}


        The communication baud rate  between the RS232  port  and  the
     radio is set with  this command. The default  is  1200 baud.  Any
     valid baud rate can be set. However, for the program to work, the
     radio  and the computer  MUST  be set to the same baud rate.  The
     ICOM supports 9600, 1200  and 300 bauds ONLY. The  ICOM baud rate
     is selected by a jumper inside the unit. It is set at the factory
     to 1200 baud. It is recommended that 9600 be used, for efficiency
     in communications  between  the computer  and  radio. This is the
     default baud rate for the ICOM program. The KENWOOD is hard-wired
     for a 4800  baud  rate.  This is the default  baud  rate  for the
     KENWOOD program.




     CHANNEL {channel-number}


        The CHANNEL  command  sets the  radio to a  specific  channel.
     Example: CHANNEL 3 will set the selected  radio to memory channel
     3.




     CLEAR


        The  CLEAR command will clear all  memory  channels  from  the
     computer's memory. All FREQUENCY and SERVICE  fields are reset to
     blanks. The DELAY fields are set  off, and the COUNT and DURATION
     fields are  reset  to 0. The first 20  frequencies are marked  as


COMMANDS                                                       10


                     RADIO REMOTE CONTROL PROGRAM
     VALID, and the rest of the VALID fields are set off.

        This  command only affects the  COMPUTER memories.  It has  no
     affect on the radio channels.




     COM1


       This  command  sets the  communications port  for the radio  to
     COM1.  This is the default setting. After this command  executes,
     all communication  between  the computer  and  the radio will  be
     through the COM1 port.




     COM2


       This  command  sets  the  communications port  for the radio to
     COM2.  After this command executes, all communication between the
     computer and the radio will be through the COM2 port.




     DBASE


       A  sample DBASE compatible file  is provided  to  hold  details
     about  various  frequencies.  This  file  can  be  updated  using
     DBASE-III  or  any clone capable of updating  a DBASE type  file.
     The  file  is  called  FREQLIST.DBF.  The  sample  file  contains
     information on nationally allocated frequencies.

       When the DBASE command is issued, this database is searched for
     matching  frequencies. If a match  is found between the FREQUENCY
     field,  and the database, the  SERVICE  field is copied from  the
     database. This is an easy way to update the SERVICE field. Please
     note that the DBASE  command can  take  a long time  to complete,
     based on the size of the database file and the available memory.

       When  processing the DBASE command, the program will attempt to
     buffer as much information  in  free  memory  as possible.  Since
     processing from  disk  takes a  lot  longer than processing  from
     memory, this will speed  up the DBASE search. The memory for this
     buffering comes from the  free memory left over after the program
     is  loaded. The more free memory  available, the faster the DBASE
     search will finish.

       It is very  important that  the structure of the provided DBASE
     file be maintained. This program will not be able to process this
     file if certain field structures are altered. See the section  on
     data file formats for the details on this file.



COMMANDS                                                       11


                     RADIO REMOTE CONTROL PROGRAM
     DIR  {filespec}


       When  issued,  this  command  displays  files  on  the  current
     drive/directory. If issued by itself, ALL files are listed.  If a
     filespec  is included, only those  files  matching  the  spec are
     listed. This command CANNOT list files on a drive/directory other
     than the current one.




     FILENAME  {filespec}


       The  FILENAME command  will set the  current file used for SAVE
     and RECALL commands.  Please  note  that  only  the  filename and
     extension should  be entered.  Paths should NOT be included. This
     program can only save or load from the current directory.




     FKn {command}


       The FK command allows setting of function keys 1-10. "n" is the
     function  key you wish to set.  Any  valid program command can be
     set to the selected function key.  The program  comes with  a few
     of the keys already defined. These can be overridden using the FK
     command.

      Example: FK2 QUIT
      After execution  of this command,  pressing Function key  2 will
     cause the program to terminate.

      DEFAULT settings:
        F1 - HELP, F3 - QUIT, F5 - SCAN, F7 - HALT




     HALT


       If the program is SCANning, SEARCHing, or LOADing, this command
     will terminate that function. It  is  equivalent to  pressing the
     ESC key.












COMMANDS                                                       12


                     RADIO REMOTE CONTROL PROGRAM
     HELP


       The HELP command will display a list of ALL valid commands, and
     a short description of each. The current setting of function keys
     is also displayed.




     INC {value}


       The INC command sets the increment value  used for  SEARCH. The
     value  entered  will be added to the  current frequency for  each
     step of the SEARCH routine.  The increment value is assumed to be
     in kilohertz, and must be in the range of .1 to 999.9.




     LOAD


        This  command  loads  the computer memory  channels  with  the
     contents  of  the  radio's  memory  channels. All the COUNT,  and
     DURATION  values are set to 0. The SERVICE fields are clears, and
     all DELAY  flags are turned off. The first 20 channels are marked
     as  valid. This command  is  useful  initializing  the  program's
     memory channels.




     LPT1


       LPT1 sets the default printer port to LPT1. The printer port is
     used by the PRINT command. This is the  default printer  port for
     this program.




     LPT2


       LPT2 sets the default printer port to LPT2. The printer port is
     used by the PRINT command.











COMMANDS                                                       13


                     RADIO REMOTE CONTROL PROGRAM
     NOSIGNAL


       This command turns off  the signal  sensing  for the radio. The
     signal sense is the CARRIER DETECT line of the RS232 port. If the
     modified interface is not installed, this signal does not reflect
     the state of the radio's squelch.  Issuing  the NOSIGNAL  command
     tells the  program  to ignore the state of this line. When signal
     detection is off, the signal status field  displays the word  OFF
     constantly.




     PRINT


       When issued, this command prints the contents of the computer's
     memory channels to the default printer.




     PRIORITY  {channel-number}


       Any of  the 100 channels can be selected as a priority channel.
     During SCAN,  the  selected  priority channel  is  polled  once a
     second.  If there is a signal on  the priority channel,  scanning
     will stop on  the priority channel until the signal is no  longer
     present.  Scanning will then  resume with the  last  channel that
     was scanned before the priority channel activated.

       To turn  off  the priority scan, enter PRIORITY with no channel
     number.




     QUIT


       This command terminates  the program and returns to DOS (or the
     calling environment).




     RECALL {filename} {SET}


       RECALL loads the computer memories with the values specified in
     the  current file. If a channel is not included in the file, then
     it will not be set. The radio's memories are  not affected unless
     the SET option is included in command. If  a filename is included
     with  the  command, the file specified  will  be  read,  and  the
     current filename will be set to the  file  entered. If a filename
     is NOT included in the command, then the current filename will be


COMMANDS                                                       14


                     RADIO REMOTE CONTROL PROGRAM
     used.

     NOTE:If the filename you wish to recall is called SET, and you do
     NOT wish to set the  memories, you will need to first  issue  the
     FILENAME command,  then  the  RECALL  with  no  options.  This is
     because the program will not be able to tell that the SET keyword
     is a filename and NOT a command option.




     RESET


       When this command is issued, all COUNT and  DURATION values are
     reset to 0.




     RESUME {value}


       The value  entered here controls how  long SCAN or SEARCH  will
     remain on a channel after  a  signal is  detected.  A  value of 0
     causes scanning to continue ONLY after  the signal is  no  longer
     present. Any  other value will cause scanning to resume after the
     number of seconds entered have elapsed.

         For example  if the command RESUME 3  was entered, and a SCAN
     operation detected a squelch on channel 1, scanning would stop on
     channel 1 for 3 seconds, then continue on to the next channel.





     SAVE  {filename}


       This command will save the contents  of  the computer memory to
     the current filename specified. If the filename is not specified,
     the current filename will be  used. If a file already  exists, it
     is updated with the current settings.




     SCAN


       The  SCAN command starts  the radio  scanning through  selected
     memory channels. Memory channels that are flagged with  the VALID
     field will be scanned.  Channels with the VALID flag  off will be
     bypassed. When a  signal is detected, scanning will stop, and the
     memory channel being  scanned will be displayed in inverse.  When
     the signal stops, scanning will continue.



COMMANDS                                                       15


                     RADIO REMOTE CONTROL PROGRAM
       Several  parameters and  memory  channel  settings  affect  the
     operation of SCAN. Each  channel has a VALID flag associated with
     it. If this flag is set off, the  corresponding memory channel in
     the  radio  will  NOT  be  scanned.  If  the  DELAY  field of the
     corresponding  memory  channel  is set, the program will  delay 1
     second after the signal stops before resuming scan.

       The SPEED setting determines  how  fast each  channel  will  be
     scanned. In  the  event  that  a scan is  too fast to respond  to
     certain frequencies, it can be slowed with the SPEED settings.

       The  RESUME  setting determines  the  action  after the squelch
     breaks. If RESUME is set to 0, scanning  will not continue  until
     the signal  ends. If  RESUME is  any other  value,  scanning will
     resume after the number of seconds specified by RESUME.

       If  a  channel is set to be  a  PRIORITY channel,  it  will  be
     scanned  once every  second.  If  a  signal is  detected  on  the
     priority channel normal  scanning stops,  and the radio is set to
     receive the  priority channel.  Normal scanning  will resume when
     the signal is no longer present on the PRIORITY channel.

       Note  that any of the parameters or memory channel settings can
     be set either before the scan is started, or during the scan. The
     new parameters will take effect immediately in either case.




     SEARCH


        SEARCH allows you  to scan  a range of frequencies for action.
     The range is selected by the START and STOP values. The INC value
     determines the step size  for each frequency increment. The SPEED
     value determines how fast the next increment will be selected.

       During a SEARCH  operation, a frequency is set  into the radio,
     and  a check is made for a  signal.  If  no signal is found,  the
     frequency is  incriminated  by the  INC  value  and the operation
     repeated. When the  frequency reaches the  STOP value, the search
     starts again at the START value.

       If  a  signal is found  during SEARCH,  the memory channels are
     searched  for the active frequency.  If  the  active frequency is
     found in one of  the computer memory channels, and the channel is
     marked as VALID, the COUNT and  DURATION  fields will be updated.
     If the memory channel is NOT marked as VALID, searching continues
     with the next frequency.

       If a signal is found during SEARCH, and the active frequency is
     NOT found in  one of the  computer  memory  channel,  the  active
     frequency is logged in  the first  clear memory channel. If there
     are no  free  memory channels, the FULL status indicator  will be
     displayed,  and the log of the current  active  channel  will  be
     lost. You can free a memory  channel  during SEARCH by moving the
     cursor to the row of the  selected  channel and pressing CTL-END.
     Since  there are only 100  channels available,  this mean that  a


COMMANDS                                                       16


                     RADIO REMOTE CONTROL PROGRAM
     search can only locate a maximum of 100 active frequencies.

       The RESUME value controls SEARCH in the same manner as SCAN. If
     RESUME  is set to 0, searching will resume AFTER the signal is no
     longer present. If  RESUME is  set  to  a number greater  than 0,
     searching will resume  that  number  of seconds  after signal has
     been detected.



     SET


       SET causes the values in the computer memory channels to be set
     into the radio's memory channels. All 100 channels are set.  Note
     that it may take a minute or so for all the memories to be set.




     SIGNAL


       SIGNAL turns the sense for the signal detection on. This is the
     default condition for the program. It is the  opposite command of
     NOSIGNAL.




     SORT


       SORT will sort the memories by frequency in ascending order. It
     is most useful to do a sort during or after a SEARCH operation.




     SPEED {value}


       This command sets the scanning  and  searching speed. The value
     should be  a number between 0 and 32768. A Speed value  of 0 will
     result in  the  fastest  scan possible.  Higher  numbers  cause a
     slower scan. The number  is used as a countdown in the scan loop.
     The larger the number, the slower the scan/search rate.




     START {value}


       The value set in this  command controls  the starting frequency
     for  the  SEARCH  operation. The value must be  frequency  in the
     range of the radio.



COMMANDS                                                       17


                     RADIO REMOTE CONTROL PROGRAM
     STOP  {value)


       The value set in this command controls the ending frequency for
     the SEARCH operation. The value must be frequency in the range of
     the radio.




     TXADR {value)


       ICOM  radios can be set to respond to  various  addresses. This
     allows multiple radios to be connected on the ICOM C-IV bus.  The
     default  address of the R-7000  is 8. This is the default setting
     for this  program. The TXADR allows the program to talk to radios
     with a different  address.  The  value entered must be an integer
     between 1 and  255.  This command has no  affect when running the
     KENWOOD program.

     NOTE:If the program does not appear to be communicating with your
     radio, make sure that the TXADR value is  matched with the remote
     control address of  your radio. This  is  set  by a jumper inside
     ICOM radios.



































COMMANDS                                                       18


                     RADIO REMOTE CONTROL PROGRAM
     SPECIAL KEYS






     ENTER


       The ENTER key finalizes input to the program. If pressed  while
     on the COMMAND line, the entered command is  executed (if valid).
     If pressed while on the FREQUENCY field, the entered frequency is
     set  into the radio's memory, and the cursor is moved to the MODE
     field. If pressed while on the MODE field, the entered modulation
     is checked for validity.  If  the modulation  is valid, it is set
     into the radio's memory,  and  the  cursor moves  to  the SERVICE
     field.

      If the cursor  is on any other field,  ENTER will move it to the
     next field in the current row.




     ESC


       Pressing ESC terminates the current operation. It is equivalent
     to the HALT command.




     Backspace


       The destructive backspace key only works  on the command  line.
     When  entered, the current character  is deleted, and the  cursor
     moves to the previous character.




     HOME


       The  HOME key  will  move  the  cursor to the  beginning of the
     current field.











SPECIAL KEYS                                                   19


                     RADIO REMOTE CONTROL PROGRAM
     END


       If pressed while on the SERVICE field, the  cursor  is moved to
     the last entered character in that field. If pressed while on the
     command line, the  cursor is moved to the last  entered character
     in the command.




     ctl-END


       This key clears all information from  the current channel.  The
     current channel  is the line on which the cursor is currently on.
     When  pressed,  the  VALID  and  DELAY  flags  are  cleared,  the
     FREQUENCY field is set to blanks, the MODE field is set to '???',
     the COUNT and DURATION  fields are zeroed, and the  SERVICE field
     is set to blanks. This key only affects  the computer memory. The
     radio is left unaffected.




     ctl-HOME


       This key will move the cursor between  the command line and the
     memory  channel  fields. It allows  for a hot-key  switch between
     field editing and command editing.




     Cursor keys


       Cursor  keys  allow  movement  around the  screen  to  edit the
     various fields, and  contents of fields. The left and right  keys
     move within a field. The up  and  down arrows move between  rows.
     The  program will  only allow  the  cursor  to  be  placed  on  a
     changeable  field.




     PgDn/PgUp


       These keys move between the pages  of the  display. There are 5
     pages of channel displays. Each page  displays 20  channels. PgDn
     selects the next page, PgUp displays the previous page.







SPECIAL KEYS                                                   20


                     RADIO REMOTE CONTROL PROGRAM
     INS


       INS   selects  or  cancels  insert  mode.  Insert  mode  allows
     inserting of characters in a field.




     DEL


       The DEL key deletes the characters at the cursor location.




     Function keys


        Function  keys  F1-F10 can  be set  by the user  using  the FK
     command.  When one of these  keys is pressed, the current command
     assigned to  this key is  executed. Function keys that  have  not
     been set do not cause any action to be taken.




































SPECIAL KEYS                                                   21


                     RADIO REMOTE CONTROL PROGRAM
     PROFILE



       The profile  is a file named progname.PRO, where  "progname" is
     the name of the program you started. EXAMPLE: KENWOOD.PRO  is the
     profile  that would be executed when the KENWOOD program was run.
     The profile contains a collection of valid commands.  The primary
     use  of the profile  is to set up the program for  your  specific
     setup.  Any  valid command  can be  included in  the  profile.  A
     sample profile  for each  of  program  has  been included on  the
     distribution disk. If you do  not wish any profile to  be run, it
     may be deleted.















































PROFILE                                                        22


                     RADIO REMOTE CONTROL PROGRAM
     DATA FILE FORMATS




       There are several  files  that this program makes use of. These
     files are used to store and retrieve data used by the program.




     FREQLIST.DBF



       This  is  a  standard  DBASE  III+ type data file. It  contains
     frequencies and  allocations for  the  radio spectrum. There  are
     three fields that are used by this program.

       field name     allocation       description
       -----------------------------------------------------------
       FREQUENCY      decimal 9.4      holds the frequency in Mhz
       DESCRIPT       character 50     usage of the frequency
       ACTION         logical          flags the frequency in use

       If the ACTION field is not present, the  program will  use  the
     DESCRIPT field  to  determine  ACTION.  A  blank  DESCRIPT  field
     signals an inactive channel.

       The length of the DESCRIPT field can be changed, if so desired.
     This program only uses the first 38 chars of this field.

       Any other fields can be added or deleted from this file without
     affecting the  operation of the program.  However, if either  the
     FREQUENCY  or  DESCRIPT field is not present in the database, the
     DBASE function will not operate.




     frequency data files



       The  SAVE  command creates a file with the current  settings of
     memory channels, and various scan parameters. The file created is
     an  ASCII  readable  file.  Each record is terminated by  a CR/LF
     sequence. One  record represents  one memory  channel or one scan
     parameter.  Each  field  is  blank delimited.  The  file  can  be
     altered (or created) using any standard text editor.

      If  the first  non-blank character in a  record  is a  '*', that
     record is ignored. This  provides a way to imbed  comments in any
     data file.

      The format for a memory channel entry is as follows:

       field   name       value range      description


DATA FILE FORMATS                                              23


                     RADIO REMOTE CONTROL PROGRAM
       ----------------------------------------------------------------
           1   CHANNEL     0-100           channel number to set
           2   FREQUENCY   0-999.9999      frequency in Mhz
           3   MODE        3 chars         valid modulation for radio
           4   COUNT       0-999999        count of squelch breaks
           5   DURATION    0-999999        total duration of squelch
           6   VALID       VALID/NOTVALID  indicator of channel valid
           7   DELAY       DELAY/NODELAY   indicator of channel delay
           8   SERVICE     38 chars        service for channel

      The service field follows the first blank after DELAY. All chars
     up to the CR/LF are taken. If there are more then 38 chars in the
     service field, they are ignored.

      The format for a scan parameter entry is as follows:

                parm   value

      The valid parameters and there values are as follows:
       parameter          value       description
       START              0-999.999   start frequency in Mhz
       STOP               0-999.999   stop frequency in Mhz
       INC                .1-99.9     increment in Khz
       SPEED              0-32768     scanning speed
       RESUME             0-32768     resume value




     profile



       The  profile  is  a file with valid commands that gets executed
     when the program starts. The profile name is
                    progname.PRO  where  "progname" is the name of the
     program running.

      Any  command  that can be executed  on  the command  line can be
     placed in  the profile. Each record in the  profile contains  one
     command  (and  parameters)  followed  by  a CR/LF.  If the  first
     non-blank character in  a record is a '*', the record is ignored.
     This allows the user to comment the profile.

















DATA FILE FORMATS                                              24


                     RADIO REMOTE CONTROL PROGRAM
     RS232 INTERFACE




       This program is designed  to use the serial communications port
     (RS232) of the IBM  computer. In  order  to  interface a radio to
     this  port,  an  interface adapter  is  needed  designed for  the
     specific radio.  Each  radio manufacturer  makes such an adapter.
     However, none  of the  adapters  supplied from  the  manufacturer
     provide for squelch detection. Without this detection, the signal
     sensing functions of this program will not work.

       For  each  radio  supported, a  circuit  and  instructions  are
     available.  This circuit provides the squelch detection needed by
     this  program.  The interface  circuits are  easy  to build,  and
     require few parts.  All  of  the parts can be obtained cheaply at
     any electronics supply store. The schematics and instructions are
     provided to all registered users.









































RS232 INTERFACE                                                25