ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
    ³                                                                       ³
    ³                        * * *  SATAIM  * * *                           ³
    ³                                                                       ³
    ³                  Earth Station AZ/EL Chart Printer                    ³
    ³                                                          Version 2.3  ³
    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


What does it do?    SATAIM provides a printed chart listing AZ/EL aiming
                    coordinates for geosynchronous North American satellites.
                    AZ/EL bearings are TRUE (no magnetic declination computed).
                    ___________________________________________________________

What you'll need    An IBM compatible AND a printer.  No screen display of
                    coordinates is provided.  The program's two files -
                    SATAIM23.EXE and SAT.FIL - must be in the same directory.
                    ___________________________________________________________

     New to v2.3    The following enhancements have been made in version 2.3:

                    -- Satellite information updated to include the many
                    satellite "events" through mid-1992.

                    -- The "Frequency" column on the printout has been
                    expanded to accommodate user comments (examples such as
                    "Inclined Orbit" have been included).
                    ___________________________________________________________

    Using SATAIM    To print a satellite coordinate chart, follow these steps:

                    System Prompt...         Enter...

                    TERMINAL LOCATION?       Earth Station name (whatever name
                                             you may use to refer to the dish
                                             location).

                    LATITUDE?                Numbers in this format: xx,xx,xx
                    LONGITUDE?               (degrees, minutes, seconds).
                                             NOTE:  Leading zeroes, minutes
                                             and seconds are optional.

                    Hit "P" to Print,        "P" to print, F1 [enter] to quit.
                    F1 [enter] to Quit

                    Need extra copies?       Y or N.  If NO, program ends.  If
                                             YES, program asks....

                    How many (1 to 5)?       1 to 5...SATAIM will print the
                                             requested number of copies.
                    ___________________________________________________________

         SAT.FIL    SAT.FIL contains all of SATAIM's satellite information. It
                    can be easily changed if you wish to add or delete satel-
                    lites, and may contain up to 40 lines (NOTE: if SAT.FIL is
                    edited to include more than 40 lines, SATAIM will end).

                    ___________________________________________________________



  SATAIM Documentation (page 2)
_______________________________________________________________________________


    Text Editing    Any ASCII text editor may be used to modify SAT.FIL,
                    as long as it does not embed any word processing codes.
                    ___________________________________________________________

      Deleting a    When deleting a satellite from SAT.FIL, be sure to delete
      Satellite     the entire line (including carriage return/line feed).
                    ___________________________________________________________

       Adding a     To add a satellite to SAT.FIL, insert a new line contain-
       Satellite    ing the following information:

                      -- the satellite's longitudinal position

                      -- the name of the satellite (13 characters max.)

                      -- a comment line (25 characters max.)

                    EXAMPLE:

                    999.9,"BOGUSTAR 2","Ku/X - Experimental craft"
                    ___________________________________________________________

   Helpful Hints    When editing satellite information:

                      -- use commas and quotes where indicated.

                      -- make a separate line for each satellite's information.

                      -- insert new lines in proper longitudinal order (the
                         program does not sort the satellite list).

                      -- be careful when editing, since no error-checking is
                         done on the information in SAT.FIL.
                    ___________________________________________________________

  Input Problem?    Although SATAIM has been successfully tested on several
                    different machines and BIOSes, at least two users have
                    reported a strange incompatibility.  With their particular
                    systems, the program refuses to accept valid Latitude or
                    Longitude input.

                    It has been determined that if the input error-checking
                    code is disabled, the program works fine on their machines. 
                    If you experience this problem, I'll be happy to upload a
                    similarly modified program to your mailbox.
                    ___________________________________________________________

          AUTHOR    Jim Perry
                    Chief Engineer, WTIC-TV, Hartford, CT 06103
                    CompuServe 74255,1607