DgAnsi.Com
Copyright By:
    Don E. Groves, Jr.
    2915 West Ox Rd.
    Herndon, VA 22071

    CIS Number [71310,3702]

I.   Background

     When I first got DESQview, I noticed that none of my ANSI
drivers would work properly with it, and the supplied DVANSI.COM
required more memory than I was willing to sacrifice.

     DgAnsi is the result.  It requires less than 3.8 kilobytes
of memory to load, and requires as little as 1 kilobyte in a
DESQview window.  DgAnsi is a superset of the IBM PC
implementation of the ANSI X3.64-1979 specification, implementing
several extensions and enhancements to that specification.

     DgAnsi can be safely loaded in an Upper Memory Block, will
not double load, and will not load if any other ANSI driver is
loaded.  After loading it can be reconfigured, disabled, or
uninstalled.  DgAnsi can be invoked with different parameters in
different DESQview windows.

     A note of thanks should be given to:

     PC Magazine and Michael J. Mefford.  Providing and
documenting the source code of ANSI.COM gave me a big
"jump-start" in writing this program.

     Borland Turbo Assembler 2.50 and TLink.  DgAnsi is written
in TASM ideal mode.

     Mike Bessy and Edward Phillips for putting up with some of
my earlier versions.  Their willingness to try the next ones was
a great encouragement to keep trying.

DgAnsi.Com, DgAnsi18.Com, DgAnsi.Shp, and DgAnsi.Doc were written
by and are Copyright (c) 1990-91 by Don E. Groves, Jr.  All
rights reserved.


II.  Files Included In This Distribution Archive

     DgAnsi.Com   --  the basic DgAnsi program.  This version
                      will run on any computer using PC- or
                      MS-DOS 3.1 or above.

     DgAnsi18.Com --  optimized version of DgAnsi.Com using the
                      80186 instruction set.  This version will
                      run on any computer equipped with a
                      V20/V30,, 80286 or higher cpu, and using
                      PC- or MS-DOS 3.1 or above.  DgAnsi18.Com
                      is slightly smaller and slightly faster
                      than DgAnsi.Com.

                      In this document we shall refer only to the
                      command "DgAnsi;" if you are using the
                      186-optimized version make the appropriate
                      substitution.  You may prefer to delete
                      DgAnsi.Com and rename DgAnsi18.Com to
                      DgAnsi.Com.

     DgAnsi.Shp   --  "DESQview-aware" shared program module for
                      use in DESQview windows.  To use DgAnsi.Shp
                      you must load DgAnsi.Com before DESQview.
                      This enables DgAnsi.Shp to use the code of
                      DgAnsi.Com, while maintaining its own data
                      space in the DESQview window.

     DgAnsi.Doc   --  This documentation.


III. Running DgAnsi.Com

     The syntax for loading or configuring DgAnsi is as follows:

          DgAnsi [commands] [/switches]

     Entering "DgAnsi" without commands or switches will load
DgAnsi in its default configuration.

     The commands are:

     ? | /?    Displays the DgAnsi help screen.

     ON        By default, DgAnsi is loaded with all functions
               enabled.  Use this command to reenable DgAnsi
               after turning it off.

     OFF | OF  Temporarily disables DgAnsi functions.  DgAnsi OFF
               leaves DgAnsi loaded in memory, and it may be
               reenabled by issuing DgAnsi ON.

     FAST | FAS | FA | F+  Direct screen writing mode.  This is
               the default.

     SLOW | SLO | SL | F-  Screen writes via the BIOS.  If you
               are experiencing display problems, DgAnsi SLOW
               should cure them.  This mode is noticeably slower
               than the default screen writing method.

     K+        Enable keyboard reassignments.  This is the
               default.

     K-        Disable keyboard reassignments.  Disabling
               keyboard reassignments disables any key
               reassignments previously made.

     P+        Enable new key reassignments.  This is the
               default.
            
     P-        Disable new key reassignments.  Disabling further
               key reassignments retains any key reassignments
               previously made, while disabling additional
               reassignments.

     Q+        Enable Extended Unique Keys on. This is the
               default.  On enhanced keyboards, using DOS 4.0 or
               above, the gray keys generate different scan codes
               than their white key equivalents.

     Q-        Disable Extended Unique Keys on enhanced
               keyboards.  Disabling unique keys will make the
               gray keys on enhanced keyboards behave exactly as
               their white key equivalents.

     The switches are:

     /@filename  Issue ANSI commands, at initial load or after,
               contained in a file.  The entire command sequence
               must be entered in the file, including the leading
               ESCape [.

               The contents of the configuration file are typed
               to standard output, and have the same effect as

                    TYPE filename

               Very little checking for a valid filename is done.
               If the file is not found, the switch is ignored.

     /Bnnnn    Buffer size in bytes for key reassignments.  The
               value for nnnn is from 0 to approximately 61000
               bytes; the default is 200 bytes.  Specifying /b0
               will save 192 bytes in the resident load size.

               This switch may be specified only when loading
               DgAnsi; once a buffer size has been set it may not
               be changed.

               Since DgAnsi.Shp establishes it own data area, you
               may set different buffer sizes, using DgAnsi.Shp,
               in each DESQview window.

               The buffer size may also be independently set for
               any secondary shell copy of DgAnsi (/w).

     /C        Clear Reassignment Buffer.  This clears all key
               reassignments.

     /D<color>m  Set display colors from command line.  The color
               specification is a standard ANSI sequence (see
               below).  For example,

                    dgansi /d0;1;33;40m

               will load or reconfigure DgAnsi to display bright
               yellow on black.  This overcomes the command.com
               limitation of not allowing the entry of the Escape
               character from this command line.  If you are
               using 4DOS, this is equivalent to entering

                    echo e[0;1;33;40m

               from the command line.

     /T        Tests whether DgAnsi is installed.  In addition to
               displaying this information on the screen, DgAnsi
               returns the following errorlevels:

                    0    DgAnsi is loaded; will not install.
                    1    DgAnsi is not loaded; safe to install.
                    255  DgAnsi is not loaded in the current
                         DESQview window but is loaded prior to
                         DESQview.

     /U        Uninstall DgAnsi.  If DgAnsi is not the last
               loaded memory-resident program ("TSR") it cannot
               be uninstalled; instead, it will be turned off but
               will remain in memory.

     /W        Create a secondary resident copy.  This switch is
               positional and should be specified before any of
               the above options.  Its purpose is to allow the
               creation of a "shell copy" in any environment.
               This can be useful if you wish to create a
               specially defined set of ANSI sequences for a
               limited purpose, and then return easily and
               quickly to the original configuration.

               Creating a secondary copy of DgAnsi turns the
               parent copy off.  Uninstalling the shell copy does
               not automatically turn the parent copy back on; it
               must be specifically reenabled by DgAnsi ON.

  Note: DgAnsi directly supplies the KSTACK.COM functions for
  the KEYSTACK command in 4DOS version 4.0. It is therefore not
  nessecary (and will waste memory) to load both KSTACK.COM and DGANSI.COM.


IV.  DgAnsi.Shp

     DgAnsi.Shp is a "Shared Program" for DESQview.  It can be
used in place of loading DgAnsi.Com a second time in a DESQview
window.

     There are three advantages to using DgAnsi.Shp with
DESQview.  First, it loads faster.  Second, DgAnsi and a program
can be started together directly from DESQview, instead of via a
batch file which first loads DgAnsi and then loads the
application.  This avoids the overhead of loading another
instance of the command processor and occupies less memory.

     Third, DgAnsi.Shp works by utilizing the code of DgAnsi.Com,
while maintaining its own data space in the DESQview window.
This means that each DESQview window can set DgAnsi's buffer size
independently of the DgAnsi.Com's initial buffer size, or of the
buffer size in any other DESQview window.

     DgAnsi.Com must be loaded before starting DESQview if you
plan to use DgAnsi.Shp.  If DgAnsi has not been installed,
DESQview will refuse to open any window in which DgAnsi.Shp is
specified and an error message will advise you that DgAnsi.Com
must be loaded.

     Valid commands and switches for DgAnsi.Shp are the same as
for DgAnsi.Com.

     Upon shelling out of the program or upon reaching the DOS
prompt in the DESQview window, DgAnsi.Com can be used to change
the default settings in the same manner as outside DESQview.

     To specify DgAnsi.Shp in a DESQview window, open the "Change
a Program" window.  In the "Advanced Options" screen (F1 from the
opening "Change a Program" screen), specify at least 2 kilobyte
in the "System Memory" field.

     Use the tab key to advance to the "Shared Program" section
of the screen.  In the "Pathname" field, specify the full name of
DgAnsi.Shp, including the path.  Commands and switches may be
entered in the "Data" field.

     Two kilobyte of system memory is adequate for the DgAnsi.Com
default configuration.  If you install DgAnsi with a larger
keyboard reassignment buffer, you may need to specify more system
memory.  Excessively large "System Memory" values will produce
unpredictable results.


V.   Compatibility

     DgAnsi has been tested on a wide variety of computers, under
many configurations.  It should be compatible with any IBM
compatible running DOS 3.1 or above.

     DgAnsi hooks Interrupts 16h, 21h, 29h, and 2Fh.  You may
experience conflicts if other TSRs loaded on your computer hook
any of these interrupts.

      In particular, many keyboard enhancers also hook Int 16h.
In most cases this and other conflicts can be resolved simply by
assuring that DgAnsi is loaded after the conflicting program.

     4DOS, the replacement command processor, includes a KEYSTACK
command for feeding keystrokes to other applications.  Its use
requires that KSTACK.COM, a TSR which is part of the 4DOS
distribution package, be loaded in order to enable the KEYSTACK
command.  KSTACK.COM also hooks Interrupt 16h.

     DgAnsi.Com has been extensively tested with 4DOS Version
4.0, and we have found no incompatibilities.  Some systems
require that DgAnsi.Com be loaded after KSTACK.COM in order for
the key redefinitions to work properly.


VI.  DgAnsi Command Sequences

     DgAnsi includes a number of command sequences which are
neither part of the ANSI X3.64-1979 specification nor of the IBM
ANSI implementation.  In the command listing which follows the
ANSI X3.64-1979 mnemonic, if it exists, is provided in
parentheses (e.g., CUP).

Cursor Functions

  Esc[l;cH  Cursor Position                            (CUP)
  Esc[l;cV  Horizontal and Vertical Position           (HVP)
            HVP and CUP move the cursor to the position
            specified. The first parameter (l) specifies the line
            number; the second (c) specifies the column number.
            When no parameters are specified the cursor moves to
            the home position (the upper left-hand corner of the
            screen).

  Esc[nA    Cursor Up                                  (CUU)
            This sequence moves the cursor up without changing
            columns. The value of n sets the number of lines
            moved.  When no parameter is specified the cursor
            moves up one line.  It the cursor is already on the
            top line, the CUU sequence is ignored.

  Esc[nB    Cursor Down                                (CUD)
            This sequence moves the cursor down without changing
            columns.  The value of n sets the number of lines
            moved.  When no parameter is specified the cursor
            moves down one line.  It the cursor is already on the
            bottom line, the CUD sequence is ignored.

  Esc[nC    Cursor Forward                             (CUF)
            This sequence moves the cursor forward without
            changing lines.  The value of n sets the number of
            columns moved.  When no parameter is specified the
            cursor moves forward one column.  It the cursor is
            already on the far right column, the CUF sequence is
            ignored.

  Esc[nD    Cursor Backward                            (CUB)
            This sequence moves the cursor backward without
            changing lines.  The value of n sets the number of
            columns moved.  When no parameter is specified the
            cursor moves backward one column.  It the cursor is
            already on the far left column, the CUB sequence is
            ignored.

  Esc[6n    Device Status Report                       (DSR)
            The console driver outputs a Cursor Position Report
            sequence when it receives a DSR sequence.
            ANSI X3.64-1979 defines this sequence as containing
            any decimal number in the range 0 to 9, or a
            semi-colon (ASCII code 48 to 57, or 59 decimal); most
            versions of DOS specify the integer 6.  Using DgAnsi,
            any number in the range 1 to 254 will return a Cursor
            Position Report.

  Esc[255n  Device Status Report (maximum)
            Parameter 255 in a DSR sequence reports the maximum
            screen size, in line and columns, of the current
            screen mode.  The output is in the same format as the
            Cursor Position Report, except that maximum values
            instead of current values are reported.

  Esc[s     Save Cursor Position                       (SCP)
            The console driver saves the current cursor position.
            This position can be restored by the Restore Cursor
            Position sequence.

  Esc[u     Restore Cursor Position                    (RCP)
            This sequence restores the cursor position to the
            value it had when the console driver received the
            Save Cursor Position sequence.  If no SCP sequence
            was received, RCP is ignored.

  Esc[l;cR  Cursor Position Report                     (CPR)
            The console driver outputs a CPR sequence when it
            receives a Device Status Report sequence.

Erase Functions

  Esc[2J    Erase Display                              (ED)
            This sequence erases the entire screen and returns
            the cursor to the home position.

  Esc[K     Erase Line                                 (EL)
            This sequence erases everything from the current
            cursor position to the end of the line, including the
            current cursor position.

  Esc[0J    Erase Display from Cursor Forward
            This sequence erases everything from the current
            cursor position to the bottom of screen, including
            the current cursor position.  The cursor position is
            not updated.

  Esc[1J    Erase Display from Cursor Backward
            This sequence erases everything from the current
            cursor position to the top of screen, including the
            current cursor position.  The cursor position is not
            updated.

  Esc[]     Erase next Carriage Return and Line Feed
            This sequence erases the next carriage return / line
            feed pair without repositioning the cursor.  This
            makes it possible to issue an ECHO without generating
            a carriage return / line feed.

Modes of Operation

  Esc[sm    Set Graphics Rendition                     (SGR)
            This sequence invokes graphic rendition specified by
            the parameters in the following list.  These
            functions are cumulative and remain in effect until
            the next SGR sequence; multiple parameters are
            delimited by semi-colons.

            Graphics Functions

              0  All attributes off (normal, white on black)
              1  Bold on (high intensity)
              4  Underscore On (monochrome displays only)
              5  Blink on
              7  Reverse Video on
              8  Concealed on  (invisible)
              30 Black foreground
              31 Red foreground
              32 Green foreground
              33 Yellow foreground
              34 Blue foreground
              35 Magenta foreground
              36 Cyan foreground
              37 White foreground
              40 Black background
              41 Red background
              42 Green background
              43 Yellow background
              44 Blue background
              45 Magenta background
              46 Cyan background
              47 White background

  Esc[sh    Select Mode                                (SM)
            This sequence selects the screen width or type
            specified.

            Graphics Modes

              0  40 x 25 monochrome text
              1  40 x 25 color text
              2  80 x 25 monochrome text
              3  80 x 25 color text
              4  320 x 200 graphics 4-color
              5  320 x 200 graphics 2-color
              6  640 x 200 graphics 2-color
              7  wrap at end of line (word wrap)

            The following parameters were added to the IBM subset
            with DOS 4.0.  DgAnsi supports them with earlier
            versions of DOS, but they are hardware dependent:

              13 320 x 200 graphics 16-color
              14 640 x 200 graphics 16-color
              15 640 x 350 graphics 2-color
              16 640 x 350 graphics 16-color
              17 640 x 480 graphics 2-color
              18 640 x 480 graphics 16-color
              19 320 x 200 graphics 256-color

            All numbers except 7 are passed to the BIOS, Int 10h.
            Depending on your hardware and other software,
            specifying higher numbers may produce interesting
            results.  For this reason, DgAnsi makes no attempt to
            trap invalid numbers; if your hardware does not trap
            unsupported Int 10h functions, proceed at your own
            risk.


  Esc[sl    Reset Mode                                 (RM)
            This sequence resets the screen width or type
            specified; the parameters are the same as for SM.
            Setting mode 7 with an "h" command (SM) tells DgAnsi
            to wrap text to the next line when it passes the end
            of a line; setting mode 7 with an "l" (RM) command
            tells ANSI not to wrap text; the line is truncated.
            For all other modes the SM and RM commands are
            equivalent.

IBM PC Keyboard Reassignment

     Keyboard reassignment uses an undefined ANSI X3.64-1979 code
sequence to define a character or set of characters sent by the
console whenever a given key is pressed on an IBM PC compatible.
The sequence is:

     Esc[#;#p
     or Esc["string";"string"p
     or Esc[#;"string"p
     or Esc["string";#p

     The first # is the ASCII character code for the key to be
reassigned.  It is followed by a single key code or string of
codes that are to replace it.  If the first parameter is 0 or
224, then the first and second parameters make up an extended
ASCII code and the third parameter becomes the reassignment
character.

     Enclosing a string in single or double quotes permits the
entry of standard keys.  For example:

     Esc[0;32;"dir"13p

assigns the key Alt-D (0;32) to the string "dir" followed by a
carriage return (13).

     For a complete listing of ASCII key codes, see the Appendix.

To control keyboard reassignments using DgAnsi sequences:

     Esc[=1P     Turn Keyboard Reassignments On
                 Any digit other than 1 will turn keyboard
                 reassignments off.

     Esc[?1P     Enable Keyboard Reassignments
                 Any digit other than 1 will disable keyboard
                 reassignments.

     Esc[=1q     Enable Extended Keyboard support
                 Any digit other than 1 will disable extended
                 keyboard support.


VII. License and Disclaimer
     DgAnsi.Com
Copyright By:
    Don E. Groves, Jr.
    2915 West Ox Rd.
    Herndon, VA 22071

    CIS Number [71310,3702]

     DgAnsi and all files contained in this distribution archive
are copyright 1990-1992 by Don E. Groves, Jr.  Support is
available from the author via CompuServe Information Service
[71310,3702].

    If you find DgAnsi useful, your gift of $15,  or any amount,
would be greatly appreciated.

     You may distribute copies of DgAnsi to friends, computer
clubs or users' groups, and to computer bulletin boards, so long
as (1) no fee is charged (other than a nominal media fee), and
(2) all files are included without modification.  You may not
sell or charge any fee for providing DgAnsi other than a nominal
media fee not exceeding $5.00, or $10.00 if other programs are
supplied on the same distribution diskette.

     The author has taken extensive precautions to use standard,
documented programming calls and DOS functions, and to test the
software with a wide variety of hardware and software
combinations.  If you discover any bugs in the program, please
notify the author via CompuServe Mail.

     If you feel that bugs in the program have caused you any
damages, I'll sympathize with you and attempt to correct any
programming errors.  It won't do you any good to sue me, though,
because I'm just a struggling computer programmer and consultant
who doesn't have enough money to make it worth your time and
legal costs.

     The lawyers tell me I'm supposed to say it this way:

THIS PROGRAM IS PROVIDED "AS-IS" AND WITHOUT WARRANTY OF ANY
KIND.

THE AUTHOR DISCLAIMS ANY AND ALL OTHER WARRANTIES, EXPRESS OR
IMPLIED, ORAL OR WRITTEN, INCLUDING ANY IMPLIED WARRANTIES OF
MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

IN NO EVENT SHALL THE AUTHOR BE LIABLE FOR ANY INCIDENTAL,
CONSEQUENTIAL, OR PUNITIVE DAMAGES WHATSOEVER ARISING OUT OF USE
OF THE PROGRAM OR YOUR RELATIONSHIP WITH THE AUTHOR, INCLUDING
WITHOUT LIMITATION ANY OR ALL DAMAGES FOR LOSS OF PROFITS,
BUSINESS INTERRUPTION, LOSS OF INFORMATION OR ANY PECUNIARY LOSS,
EVEN IF THE AUTHOR HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH
DAMAGES.


Appendix - ASCII Key Codes

Standard Keys (All keyboards).  Codes included in parentheses
require DOS 4.0 or above.

Key                 Code       Shift      Ctrl       Alt

A                     97         65         1        0;30
B                     98         66         2        0;48
C                     99         67         3        0;46
D                     100        68         4        0;32
E                     101        69         5        0;18
F                     102        70         6        0;33
G                     103        71         7        0;34
H                     104        72         8        0;35
I                     105        73         9        0;23
J                     106        74         10       0;36
K                     107        75         11       0;37
L                     108        76         12       0;38
M                     109        77         13       0;50
N                     110        78         14       0;49
O                     111        79         15       0;24
P                     112        80         16       0;25
Q                     113        81         17       0;16
R                     114        82         18       0;19
S                     115        83         19       0;31
T                     116        84         20       0;20
U                     117        85         21       0;22
V                     118        86         22       0;47
W                     119        87         23       0;17
X                     120        88         24       0;45
Y                     121        89         25       0;21
Z                     122        90         26       0;44
1                     49         33         --       0;120
2                     50         64         0        0;121
3                     51         35         --       0;122
4                     52         36         --       0;123
5                     53         37         --       0;124
6                     54         94         30       0;125
7                     55         38         --       0;126
8                     56         42         --       0;127
9                     57         40         --       0;128
0                     48         41         --       0;129
-                     45         95         --       0;130
=                     61         43         31       0;131
[                     91         123        27       0;26
]                     93         125        29       0;27
\                     92         124        28       0;43
:                     59         58         --       0;39
'                     39         34         --       0;40
,                     44         60         --       0;51
.                     46         62         --       0;52
/                     47         63         --       0;53
`                     96         126        --      (0;41)

Enter (keypad)        13         --         10      (0;166)
/ (keypad)            47         47      (0;142)    (0;74)
* (keypad)            42      (0;144)    (0;78)       --
- (keypad)            45         45      (0;149)    (0;164)
+ (keypad)            43         43      (0;150)    (0;55)
5 (keypad)         (0;76)        53      (0;143)      --

 F1                 0;59       0;84       0;94       0;104
 F2                 0;60       0;85       0;95       0;105
 F3                 0;61       0;86       0;96       0;106
 F4                 0;62       0;87       0;97       0;107
 F5                 0;63       0;88       0;98       0;108
 F6                 0;64       0;89       0;99       0;109
 F7                 0;65       0;90       0;100      0;110
 F8                 0;66       0;91       0;101      0;111
 F9                 0;67       0;92       0;102      0;112
F10                 0;68       0;93       0;103      0;113
F11                 0;133      0;135      0;137      0;139
F12                 0;134      0;136      0;138      0;140

Home                0;71         55       0;119       --
Up                  0;72         56      (0;141)      --
PgUp                0;73         57       0;132       --
Left                0;75         52       0;115       --
Right               0;77         54       0;116       --
End                 0;79         49       0;117       --
Down                0;80         50      (0;145)      --
PgDn                0;81         51       0;118       --
Ins                 0;82         48      (0;146)      --
Del                 0;83         46      (0;147)      --

Extended Keys (Enhanced keyboards only).

Home (gray key)  (224;71)   (224;71)   (224;119)  (224;151)
Up (gray key)    (224;72)   (224;72)   (224;141)  (224;152)
PgUp (gray key)  (224;73)   (224;73)   (224;132)  (224;153)
Left (gray key)  (224;75)   (224;75)   (224;115)  (224;155)
Right (gray key) (224;77)   (224;77)   (224;116)  (224;157)
End (gray key)   (224;79)   (224;79)   (224;117)  (224;159)
Down (gray key)  (224;80)   (224;80)   (224;145)  (224;154)
PgDn (gray key)  (224;81)   (224;81)   (224;118)  (224;161)
Ins (gray key)   (224;82)   (224;82)   (224;146)  (224;162)
Del (gray key)   (224;83)   (224;83)   (224;147)  (224;163)
PrScr (gray key)     --         --        0;114       --
Pause (gray key)     --         --        0;0         --
Bksp (gray key)       8          8          127       (0)
Enter (gray key)      13        --          10        --
Tab (gray key)        9        0;15      (0;148)    (0;165)
Null (gray key)     0;3         --         --         --