*************************************›           WIRING THE ZONES›              Chapter #4›*************************************›There are as many ways to wire this ›as there are people that own ATARI  ›computers. › I will give you two examples that  ›should help you in setting up your›home security system.› The first way is simple and does not›require too many parts and most handy›people  will be able to do it with›no problems.›The second is a little harder but›still should be easy enough for most›handy people to handle.››XXX› Since this program uses the›joystick ports, You will need to buy›two joystick extension cables.›I have provided the color code for ›the RADIO SHACK joystick extension›cable.›Cables bought elsewhere may vary.›If you do use a differant cable  ›you will have to check the wiring›using a ohm meter.›XXX››*************************************›           BASIC DIAGRAM›*************************************››The first diagram is a simple one that›uses the T.V. as the output device.›I only show one port because both›are wired the same. The difference is›in the software. When plugged into›port one you get zones 1 thru 4 and›a reset. In port 2 you get zones›5 thru 8 and a bypass switch.›So, if you're going to hook up both›ports make sure they are labeled and›that you put them in the proper port›when you start the program.›XXX›Zones 1 & 2 have the two delays›assigned to them so these should be›the front or back doors. Zones 3 & 4›are just normal zones.You can put as›many doors or windows on each zone as›you want. So if you're not going to›use the internal zones (5-8) you›won't need the bypass switch because›it only works on zones 5-8.Then, you›can put the front door on zone one›the back door on zone two, and split›all the other doors and/or windows›between zones 4 & 5.›XXX›Let's use zone #1 as an example.›Using the RADIO SHACK cable, the›green wire is the one used for›zone one and the gray wire is the›return side for each zone.So you ›must run two wires to the front door›connect one to the green wire and the›other to the gray wire. As I said ›before the gray wire will be used for›all the zones so you will have a lot›of wires connected to the gray wire.›XXX›The device that you wire up at the ›door or window must have its contacts›open when the door or window is closed›so when the door opens the alarm will›go off.›If you are going to wire more than›one door or window to each zone you ›can do it in two ways;›1) By running a 2nd set of wires to›   the other door using the same›   set as the first.›2) By running two wires from the ›   first door to the 2nd door.›Either way will do the job.›XXX›*************************************›          BASIC + DIAGRAM›*************************************›The only differance with this setup›is that I have added the output device›and the exit delay switch.›The exit delay switch is the easy›part. Just put a switch in place of›a door or window  for zone #3 only›and make the proper changes using the›option menu.›XXX››The output device is also pretty ›easy. All you have to do is run wires›from the orange wire to the negative›(-) side of the sona alert and one›from the gray wire to the positive›(+) side of the sona alert.›This can be done on either or both›ports it will work either way.›So if you want you can have two›sona alerts wired up.›XXX›› In order to try and keep the cost of›this program down, I have provided›all the wiring and diagrams on the›disk itself.›I realize that it may be hard for›some of you to figure out what I've›said or how to do it.›If this is so, please send me a self-›addressed stamped envolpe With a note›saying you want the hard copy of the ›diagrams and I will send you those ›diagrams and wiring instructions.›My name and address is listed in the›summary chapter.›XXX›