›HARDWARE WAREHOUSE››Nintendo Controls on the Atari 8-bit››by John Powell››    At a recent swapmeet, one of my friends was selling a Nintendo controller that he had rewired for use with the Atari 8-bit.  I asked if he could note down the instructions.  He obliged and this article is the result.››    You can find the original Nintendo (not the Super!) controllers at any market or secondhand goods store near you.  It would probably be a good idea to make sure that the controller actually works before you spend time modifying it.››    You will also need a good Atari CX40 joystick cable.››    Once you have the correct parts you will need a small Philips screwdriver and a small 25 watt soldering iron.  Now follow these steps:››1. Remove the screws from the controller and gently separate the two halves without letting anything fall out.  Take a look at how the wire is fed into the controller and be sure to install the new wire in the same way.››2. Remove the Nintendo wiring by de-soldering the wires or simply clip them off close to the connectors.  None of these will be used.››3. De-solder and remove the large clip in the centre of the circuit board.  This chip is about 3/8" x 3/4".  The Atari cable wires will go into the holes where the chip was, so after the chip has been removed use the soldering iron and a toothpick to open up the holes to allow each wire to slip through (refer to sketch below).  You need to work on this while the circuit board is UP.››4. To prepare the Atari cable, remove about 1 1/2" of the outside wire cover and bare 1/16" of the end of each wire.››5. Be sure to feed the wire from the same side that the original wire came from; the chip side.  Insert one wire through the proper hole, flip the board side up and solder the wire in place (see sketch below).  Repeat this process for each wire.››6. While you have the controller apart, you may want to clean the contacts and buttons with a cloth and contact cleaner.  Reassemble the controller, making sure the wire is fed in properly.››                7         KEY:›    . . . . . . . .  ›                 \        1-black›    . . . . . . . .       2-brown›    1 2 3 4 5     6       3-green›                          4-blue›    There is a short      5-white›    jumper wire from      6-orange›    6 to 7.›››    I hope everyone who undertakes this conversion has fun with their new joystick.›