Assembly Language Tutorial››by Chris Crawford››LESSON TWO - NUMBER SYSTEMS››In this lecture I will take up the problem of arithmetic on the 6502. I choose this topic only because it is fairly simple to do on the 6502.› There are a couple of nerve-jangling problems associated with 6502 arithmetic, but I will breeze over those in a very cavalier fashion.› Before we can do arithmetic, though, you must know a little bit about number systems. There are three that you must know: decimal, binary, and hexadecimal.› Decimal is the standard number system that you have used since grade school. You count 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, and then you reach 0 again, so you put down a 1 in the tens place and resume counting from 0.› Binary works the same way, except that there are only two digits, not ten. The two digits are 0 and 1. You count 0, then 1, then you reach 0 again, so you put down a 1 in the twos place and resume counting from 0. Thus, counting from 0 to ten in binary like this:›› Decimal     Binary› 0              0› 1              1› 2             10› 3             11› 4            100› 5            101› 6            110› 7            111› 8           1000› 9           1001› 10          1010››In binary, instead of having ones, tens, and hundreds places, we have ones, twos, fours and eights places. It takes a lot more digits to express a number in binary, but then again, we have only the two numerals 0 and 1 to work with, so what does one expect? The hexadecimal number system is a base-16 system. In this system, you count from 0 to 16 like so 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F,10. The 10 in hexadecimal really means 16 in decimal. So 10 is 16, right? Black is white, truth is lies....stay with assembly language long enough and you'll believe anything.› Actually, it's easy to avoid confusion. We use little prefixes to tell you and the computer whether a number is expressed in decimal, binary, or hexadecimal. No prefix means decimal. A $ prefix means hexadecimal; a % means binary. Thus %10 means 2 while $10 means 16, but 10 means just plain old 10. Hexadecimal is not hard to learn at all; if you go into any store you will see that they use hexadecimal on all their signs.›*›ADDITION AND SUBTRACTION››Addition with the 6502 is very simple; it uses the ADC instruction. This instruction means "Add with Carry"; I'll get to the Carry part in just a moment. For now, let me explain the instruction. The ADC instruction has an operand, normally a location in memory. When the instruction is executed, it takes the contents of that memory location and adds that value to the value in the accumulator.› It leaves the sum of the two numbers in the accumulator. This of course destroys the old value in the accumulator. You can use the immediate mode of addressing with the ADC instruction, in which case it adds the value itself. Thus, "ADC #9" will add a 9 to the contents of the accumulator, while "ADC FISH" will add the contents of address FISH to the accumulator.› Subtraction is just like addition. The instruction to use is SBC, which means "Subtract Borrowing Carry". Again, I'll tell you about the Carry part in a moment. This instruction subtracts the operand from the contents of the accumulator, leaving the result in the accumulator. It also can be done in either immediate mode (e.g. SBC #5) or absolute mode (e.g. SBC GOAT).›*›WORD LENGTH PROBLEMS››If that were all there were to arithmetic with the 6502, programmers would be paid a lot less. The first killer problem is that the 6502 uses 8-bit words; that is, the numbers that the 6502 stores and works with are only 8 bits wide. This means that the biggest number the 6502 can comprehend is 255. Uh-oh! What happens if you want to have a checkbook balancing program and you have more than $255? What happens if you get more than 255 points in your "Decapitate the Orphans" game? In fact, what happens if you just ignore the limit and add, say, 10 to 250?› Well, believe it or not, the 6502 will give you an answer of 4. Why? The number system that the 6502 uses is like a wheel, with 0 at the top, counting clockwise 1,2,3,...all the way up to 255, which lies right next to the 0. If you go up from 255 you just wrap around past the 0 and start all over. Similarly, if you subtract 2 from 0, you'll get 254.› The solution to all this is provided by the Carry bit, discussion of which I've been putting off unitl now. The Carry bit is a flag that the 6502 uses to remember when it has done arithmetic that carried it over the boundary between 0 and 255. By using it properly, you can solve your arithmetic problems.› The first trick to using the Carry bit is to use multi-byte words. This means that, instead of using a single byte to store a number, you use several. For example, if you use two bytes to remember a number, you can store a number as large as 65,535. three bytes lets you go to 16,777,215. Four bytes lets you go to 4,294,967,295. Big enough for you?› To use multi-byte arithmetic, you set up a series of additions or subtractions. Suppose, for example, that you want to add two two-byte words. The program fragment to do this would look like this:›› LDA     LOFISH› CLC› ADC     LOGOAT› STA     LOANSR› LDA     HIFISH› ADC     HIGOAT› STA     HIANSR›› This little fragment of code assumes that the first two-byte value is called (LOGOAT, HIGOAT). The new instruction, CLC, stands for "Clear Carry" and it means that the Carry bit should be set to 0. It should always be used with all additions except chained additions like this one.› The code does the following: first it adds the two low values. If the addition resulted in a wraparound (result greater than 255), then the Carry bit was set; otherwise, it was cleared. Then it performed the second addition, adding in the value of the Carry bit (That's why we call it "Add with Carry"). Thus, if a wraparound occurred, an additional one was added into the high sum. This system insures that multi-byte addition works properly.› For subtraction, you use the SEC instruction ("Set Carry"). Otherwise, you handle subtraction the same way that you handle addition. In both addition and subraction, though, the low bytes must be handled first, then the higher bytes in the proper order (lower to higher).›*›DECIMAL & SIGNED ARITHMETIC››There are two variations on standard 6502 arithmetic. Both are so rarely used that I will not treat them here. The first is decimal arithmetic using the Decimal flag. This allows you to set up an automatic decimal adjust mode. This is useful in certain types of arithmetic, decimal adjust mode. This is useful in certain types of arithmetic, primarily BCD arithmetic.› If you don't know what this is, don't bother with the Decimal flag. Your program should always begin with the instruction CLD, which means "Clear Decimal Flag". I will tell you this just once: failure to clear the decimal flag is the source of the most frustrating and impossible-to-trace bug in the 6502. Every single program should start with the instruction CLD.› The second arcane bit of 6502 arithmetic is signed arithmetic. It uses the V flag ("oVerflow"). Signed arithmetic is always confusing and seldom useful. In 7 years of working with the 6502, I have never had need of it. Don't bother.›*›LIMITATIONS ON 6502 ARITHMETIC››There are quite a few limitations on 6502 arithmetic. There is no facility for multiplication and division; you have to write subroutines to do that. You must design your programs to make do with 8-bit words; failing in that, you must use multi-byte arithmetic, with its consequent price in speed and TAM. All in all, arithmetic is a real pain on the 6502. This is the major reason why most 6502 programs do so little arithmetic.›