FANCY FONT DISPLAY ROUTINES›---------------------------››    For so long now people have been after text display routines for graphic modes 7 & 15.  These routines have been provided,  but  they always  use a block copy technique which uses a standard 8 by 8  bit character set.››    My routines throw away these principles and allow the programmer to define the individual characters in terms of their image,  width, height and drop.››Example: The word 'Tie' might be displayed as follows››+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+›|X|X|X|X|X|X| |X| | | | | | | |›+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+›| | |X| | | | | | | | | | | | |›+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+›| | |X| | | | |X| | |X|X|X| | |›+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+›| | |X| | | | |X| |X| | | |X| |›+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+›| | |X| | | | |X| |X|X|X|X|X| |›+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+›| | |X| | | | |X| |X| | | | | |›+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+›| | |X| | | | |X| | |X|X|X|X| |›+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+››The accompanying data›to go along with the›image for the 'e' would›be as follows:››Height = 5›Width  = 6›Drop   = 2››Note that the gap should›be included in the width››    This  produces output which is more pleasing to  look  at.  It's difficult  to  do justice to this with words,  so  run  the  program "D:EGFFDR.BAS" to see what is possible.›››HOW TO USE THE ROUTINES FROM BASIC›----------------------------------››    For ease of use,  the routines are loaded upon booting the disk, the program being in an AUTORUN.SYS file. (Note: on the news-disk the program has been called FFDR.COM. It should be copied to a fresh disk and renamed AUTORUN.SYS).  The code is loaded  above DOS, then it protects itself from SYSTEM RESET by altering MEMLO and DOSINI addresses.  The routines and example font (Taken from the  ST game 'Paradroid 90' which inspired these routines) take up ^7.5K but this still leaves you with ^30K available for your BASIC program.››    There are 4 routines that you can use. In order to do this it is best that you set up the following variables within your program.››e.g.    10 MESSAGE=7459:REM Address›        of Display routine vector.›        20 SETXY=MESSAGE+3›        30 COLOUR=SETXY+3›        40 DRWLET=COLOUR+3››    Definitions for each of these routines now follow:›››SETXY›-----››Format : A=USR(SETXY,xpos,ypos)›Limits : xpos between 0 and 159›         ypos between 0 and 191›         (for graphics mode 15)›         ypos between 0 and 95›         (for graphics mode 7)››Desc.  : this moves the current›         printing position to the›         coordinates (xpos,ypos).›         Important  note - a SETXY›         must  be  executed before›         any printing is done (i.e.›         a MESSAGE or DRWLET).››COLOUR›------››Format : A=USR(COLOUR,col)›Limits : col between 0 and 3›         (Although MC routine will›         force any value of col to›         be between 0 <-> 3 )››Desc.  : Sets the output colour as›         follows -››         0 = COLOR4 (location 712)›             (Background)›         1 = COLOR0 (location 708)›         2 = COLOR1 (location 709)›         3 = COLOR2 (location 710)››DRWLET›------››Format : A=USR(DRWLET,ASC("A"))›         A=USR(DRWLET,char)›Limits : char between 0 and 127››Desc.  : Outputs the character at›         the current screen›         position (which is›         updated  accordingly).›         Spaces  are  always drawn›         in COLOR4, leaving the›         background intact.››MESSAGE›-------››Format : A=USR(MESSAGE,ADR(M$))›         A=USR(MESSAGE,ADR("An›           Example!"))›Limits : Last character of string›         must be inverse.››Desc.  : Displays the string on the›         screen at the current x,y›         position. The last›         character of the string›         must be inverse (in the›         example the '!' is›         inverse) in order to›         denote the end of string›         within the display›         routine.››ROUTINES FOR USE BY THE ASSEMBLY PROGRAMMER›-------------------------------------------››    Calling protocols are different within assembly language:››    SETXY   -> LDX xpos›               LDY ypos›               JSR POSITION››    COLOUR  -> LDA col›               JSR SETCOL››    DRWLET  -> LDA char›               JSR ONELET››    MESSAGE -> LDX # >string›               LDY # <string›               JSR DOMSG›               JMP skip›              msg›               .BYTE "An Example!"›(Remember '!' is inverse!)›              skip›               ... your code continues here››    Assembler/Editor users must remember to replace all '>' and  '<' symbols as follows:››    # >name     becomes #name/256›    # <name     becomes #name&255››    If  your including these routines in your own program  then  you can  delete all the MEMLO initialisation code (lines 1014 to  1078), otherwise assemble it to an AUTORUN.SYS file using the command:››    ASM#D:FFDR.SRC,,#D:AUTORUN.SYS›      - Ass/Ed››    ASM#D:FFDR.M65,#-,#D:AUTORUN.SYS›    - MAC/65››N.B. MAC/65 users should first load the source file using››    ENTER#D:FFDR.SRC››then save it in MAC/65 format using››    SAVE#D:FFDR.M65››The file "D:FFDR.SRC" can then be deleted, saving disk space.›››DESIGNING YOUR OWN FONTS›------------------------››    Designing  your own font is just as easy as designing  your  own 8*8 character sets. Let's go through an example - a lower case 'g'›››        |›+-+-+-+-+-+-+-+-+›| | | | | | | | |   ^  Drop = 2›+-+-+-+-+-+-+-+-+   |›| | | | | | | | |   v›+-+-+-+-+-+-+-+-+   ›| |X|X|X| | | | |   =  $3F00    ^›+-+-+-+-+-+-+-+-+               |›|X| | | |X| | | |   =  $C0C0    |›+-+-+-+-+-+-+-+-+               |›|X| | | |X| | | |   =  $C0C0    |›+-+-+-+-+-+-+-+-+               |›| |X|X|X|X| | | |   =  $3FC0    |*›+-+-+-+-+-+-+-+-+               |›| | | | |X| | | |   =  $00C0    |›+-+-+-+-+-+-+-+-+               |›|X| | | |X| | | |   =  $C0C0    |›+-+-+-+-+-+-+-+-+               |›| |X|X|X| | | | |   =  $3F00    v›+-+-+-+-+-+-+-+-+›        |››                    (*Height=7)››<--------->    Width = 6 (Remember›               to include gap!)››    Remember too that in mode 7 & 15,  each pixel is two bits  wide, giving four possible colours.  So define the character for colour 3, i.e.  both  bits set per pixel,  as the draw_letter  routine  simply AND'S  it with the current colour mask to produce the right  colour. This  is  also  why  the image is  two  bytes  wide,  to  allow  for characters with widths up to 8 pixels wide.›    The data image is stored in the source listing as follows:››1000 LG›1002    .DBYTE $3F00,$C0C0,$C0C0,$3FC0,$00C0,$C0C0,$3F00››    All  the characters are referenced in the character  table  (see CHRTAB - line 1574). This is best left alone, and you should use the same labels for your images.›    All  that's left to do is to store the height,  width  and  drop information in the correct positions in the relevant tables.  So for our example:›› Height = 7, Width = 6, Drop = 2››    These  are  stored in position 4 of lines 1656,  1686  and  1716 respectively, corresponding to the LG entry in CHRTAB.››    Hope that's enough for you to be able to do your own  thing,  if you  have any queries,  or just want to discuss programming  on  the 8-bit  Atari, then  write  to:›› Mark Keates,› 24 Hayes Mead,› Meadowcroft,› Holbury,› Southampton,› Hampshire,› S04 1JZ,› England.››Enjoy!››(This article was re-formatted and edited by Dean Garraghty.)›