- Release notes for v.8beta -››This is almost, but not quite complete.  I'm still working on some changes›to the debugger, and for now, an older version is included with the›assembler.  This version resides entirely in main system RAM, which›partially undermines the fact that the rest of the package is designed to›fit mostly in bank select memory.  Thus, this version takes up almost 5K›of system RAM, whereas the final version will only require 1-2K.››Note for non-SpartaDOS users.  The MAE.COM file does not have a DOS II run›address appended to it, and so it will not automatically run as is.›However, I have included a file called RUNAD.OBJ that you should append›onto the end of the MAE.COM file in order to make the assembler auto-run.›The RUNAD wasn't included in the file, because it can mess up the automatic›return to the program from SpartaDOS using the RUN command.  I feel it is›very important to be able to easily switch to DOS and back without losing›anything.  To return to the assembler from any non-Sparta DOS, you can run›at the address $A900.››Another note for non-Sparta users.  The assembler picks up the current›drive number from the SpartaDOS variable structure.  An attempt has been›made to bypass this step for non-Sparta DOSes, but I don't know for sure›if it will work in all cases.  Worst case, you will find the default drive›set to something other than what is stored in the configure section.  This›can easily be reset from the assembler menu.››Please report any and all bugs and suggestions.  I can be reached on GEnie›at J.HARRIS32, or on internet at jharris@cup.portal.com.  More›conventional access is available at:››John Harris›45346 Graceway Dr.›Ahwahnee, CA 93601›(209)683-3412››On to the assembler...››- STRENGTHS -››Excellent full screen editor with many features such as key macros,›automatic 'JSR' and return to subroutine labels, block moves and copies,›multiple undo.››XEP80 compatable.››High level of integration between editor-assembler-debugger.  The editor›can take you directly to lines that had assembly errors.  The debugger can›reference labels in the symbol table and assemble single program lines.››Very user friendly -- it will save you a lot of typing.  (Now, if I could›have just gotten it to type this DOC file for me.  Sigh...)››Local labels referenced between global labels.››Can assemble directly to bank select memory or bank select cartridges.››Uses very little system RAM.  Most of the code resides in bank select›memory.››Full 65816 and 24 bit support.››- WEAKNESSES -››Simple implementation of macro ability, compared with Mac/65 or other more›advanced macro assemblers.  Only expression values can be passed as›parameters.››Slower assembly speed than Mac/65 -- especially with large source files.›There are a few things that can partly offset this though.  You can start›the assembly at Pass 2 if no changes have been made that effect the symbol›table values.  This can more than double the assembly speed in these›cases.  You can also include binary files within the assembly, for›pre-assembled code or data segments.  If you program in a modular fashion,›avoiding the constant reassembly of large unchanged portions of code, you›will of course completely avoid any speed problems.››I don't know how many people I may have scared at this point.  This›assembler is not depressingly slow.  It takes 45 seconds to assemble›itself, and while Mac/65 could do it in 10 seconds, I would spend a whole›lot more than 35 seconds fighting with its inept editor.  I prefer to rate›the speed of a development system in terms of how long it would take to›write a program with it.  In this regard, I don't think this assembler can›be beat.  Enough of defending this product.  I'm proud of it the way it›is, and I hope you'll enjoy using it.››- MEMORY USAGE -››This assembler is designed to run in one bank of the extended memory›available on the 130XE or other memory expanded Atari.  This bank number›is configurable.  A portion of the assembler must reside outside of bank›select RAM, and in this version, it will occupy $A900-$BBFC.  Memory usage›for the source file and symbol table is also configurable.  In addition,›memory for the symbol table will use bank select RAM when the addresses›are within the $4000-$7FFF range, while memory for the source file will›always be in normal system RAM.  This allows memory for the source file›and symbol table to overlap, and gives you the largest possible free›memory buffer.  Having the symbol table in bank select RAM has one other›benefit.  It will usually stay intact so that the labels can be used from›the debugger.  The default values for memory usage are to place the symbol›table from $6400-$7FFF and the source buffer from LOMEM to $A8FF.  The›file ED.DOC has specific instructions about changing the memory›configurations.››Zero page memory is saved and restored from the editor and assembler, so›that they will effectively leave all of ZP available to the user.  The›debugger is using locations $F4-$FF right now, but this will change in a›future release.  For now, you should avoid using these locations.››All three modules use a $100 byte buffer in low memory that is currently›at $400-$4FF.  Please contact me if these locations conflict with your›setup, and I can assemble a version that uses a different area.››When assembling to disk files, a $100 byte buffer is used for disk I/O.›The location of this buffer is configurable, as described in ED.DOC, and›is currently set to use $500-$5FF.››- EXPRESSIONS -››Expressions can be made from decimal numbers, hex numbers by using "$",›binary numbers by using "%", single ASCII characters with a "'" (single›quote), and label names.››Any of these values can be mixed with math operators +-*/, !  (bitwise›OR), & (bitwise AND), and unary -.  The | vertical bar can be used in›place of !.››There are also special operators that refer to the low byte, high byte,›and bank byte (24 bit highest byte) of the calculated expression.  These›operators are <, >, and ^.››There is no operator precedence.  All math is evaluated left to right,›with the exception of <, >, and ^, which are done after the rest of the›expression has been evaluated.››Examples of valid expressions:››       LDA #-1        ;= $FF›       LDA #'A-$20    ;= $21›       LDA #%101&3    ;= 1›       LDA #>$1234+1  ;= $12›       LDA #^$123456  ;= $12›       LDA #>$123456  ;= $34 (mid byte)››All of these expression types can be used in .BY statements as well.›Like:››LOWS   .BY <LABEL1 <LABEL2 <LABEL3›HIGHS  .BY >LABEL1 >LABEL2 >LABEL3›       .BY 15+3!%1000›       etc...››- LABELS -››The first character of a label may be any letter, or the symbols @, \, ^,›_, or ?.  All remaining characters may also include numbers plus the›symbols ., \, :, ;, <, =, and >.  Labels may be up to 15 characters long.››Label names, and for that matter all text entered with the assembler, can›be entered in upper or lower case.  Labels are not case-sensitive.››When the first character of a label is '?', the label is a 'local label'.›Locals are defined only in the source code segment between two global›(i.e.  non-local) labels.  References to local labels cannot cross a›global label definition.››Internally, the assembler creates local labels by appending the local onto›the end of the previous global label.  Thus in the following code segment:››DELAY  LDX #100›?L     DEX›       BNE ?L››'?L' is a local label, and will be entered in the symbol table as DELAY?L.›Knowing how the label is stored, allows you to access it from the debugger›or the Esc-V expression evaluator.  You can also code a direct reference›to the label DELAY?L if you need to access the local from the other side›of the global label DELAY.››Locals are not printed in X-reference or symbol table listings, which›makes them most useful for simple loop and branch structures where you›don't want to think up unique label names for all occurances.››- ADDRESSING MODES -››All 6502 and 65816 addressing modes are supported.  Any addresses that›evaluate less than $100 will use zero page modes when possible.  Thus,›zero page labels must be defined before being used, or assembly errors›will result.››There is also a way to force 8 bit, 16 bit, or 24 bit addresses using the›operators <, !, and >.  (Yes, I know this is inconsistant with the›immediate operators for low, high and bank bytes -- I didn't write the›65816 assembler specifications).  This can be really useful for forcing›absolute 16 bit addressing on zero page labels, to add 1 cycle in time›critical applications.  For the 65816, it can force direct page addressing›for non-ZP labels, (which of course requires you to move the direct page›register to the proper page address).  All 24 bit addresses must be›preceded by the > character.››The operands for the 65816 MVP and MVN instructions should be simple bank›bytes -- not full addresses.  Ex:››       MVP $40 $80›moves memory from bank $40 to bank $80, using the addresses in X and Y.››- PSUEDO OPS -››Note that only 2 letters are required, but if additonal letters are›present they will be truncated without assembly errors.  For example, you›may use psuedo ops like '.byte' and '.org'.  Personaly, I really like›having the psuedo ops the same width as all 6502 instructions, and only›use 2 letters.››       .24›Sets the symbol table and program counter to use 24 bit addresses.›This is only useful for 65816 programs.››       .AB›The assembler will generate byte-sized values for accumulator-related›immediate constants.  (Default)››       .AW›The assembler will generate word-sized values for accumulator-related›immediate constants.  This is only useful for 65816 programs.››       .BA byte›For bank addressing, you can specify an operand to force assembler›generated object code into bank select RAM.  If the operand is >= $80,›this value will be stored into location $D301 when storing bytes of object›code into RAM.  Operands less than $80 are placed in the X register, and a›STA $D580,X is performed.  This can control certain bank select cartridge›devices.  NOTE:  For using the second method of bank addressing, the›assembler should be able to return the bank select cartridge to normal.›There is currently a 'STA $D5DC' for this purpose, but this may not be the›right address for your cartridge setup.  You should search the disk file›for this instruction, ($8D $DC $D5), and replace it with the appropriate›address.››       .BI filename›Includes the contents of a binary disk file into the assembly.  If this›file does not contain a DOS binary header, it will be assembled as in-line›data at the current PC.  Otherwise, a file that contains a header will be›loaded at its load address.››       .BY [+byte] bytes and/or ASCII›Store byte values in memory.  ASCII strings can be specified by enclosing›the string in either single or double quotes.››If the first character of the operand field is a '+', then the following›byte will be used as a constant and added to all remaining bytes of the›instruction.››Ex:›       .BY +$80 1 10 $10 'Hello' $9B››will generate:›81 8A 90 C8 E5 EC EC EF 1B››Values in .BY statements may also be separated with commas for›compatability with other assemblers.››See also .SB which creates ATASCII screen codes.››       .CL›Close output object code file.  When using the .OU psuedo op to create›object code files on disk, the file will normally be closed at the end of›assembly.  However, if you wish to close the file before that, it can be›forced closed with the .CL psuedo op.  You may use this to create multiple›output files in one assembly, or to place something in RAM in addition to›the disk file.››       .DC word byte›Define constant-filled block.  This will fill an area of size 'word' with›the constant 'byte'.››       .DS word›Define storage.  This will reserve an area of storage equal to size›'word'.››       .EC›Do not display macro generated code in the assembly listing.  Only the›macro call itself will appear.››       .EJ›Eject -- Send a form feed code to eject the page in an assembly listing.››       .EN›Mark End of assembly.  This psuedo op *must* be present to end the›assembly, or an error will result.››       .ES›Display the code resulting from Macro expansions.››       .HE hex bytes›Store hex bytes in memory.  This is a convenient method to enter strings›of hex bytes, since it does not require the use of the '$' character.  The›bytes are still separated by spaces however, which I feel makes a much›more readable layout than the 'all run together' form of hex statement›that some other assemblers use.  Example:›       .HE 0 55 AA FF››       .IB›The assembler will generate byte-sized values for index register-related›immediate constants.  (Default)››       .IW›The assembler will generate word-sized values for index register-related›immediate constants.  This is only useful for 65816 programs.››       .IN filename›Include additional files in the assembly.  Only the main source file can›contain .IN psuedo ops.  You cannot nest them.  Default drive processing›works the same here as it does when loading files from the editor, and so›you will usually not need any 'Dn:' types of filespecs.  The file name›only should be sufficient.››       .LC›Turn off (clear) the display of the assembly listing.  (Default)››       .LL›Display the assembly listing on this line only, even if the full listing›is turned off.  This can be extremely handy to display the program counter›value at important positions in the source file.››       .LO long›Stores a longword, 3 byte value in memory.  Only one operand is supported.››       .LS›Turn on (set) the display of the assembly listing.››       .MC adr›Move Code to a different address when storing object code in memory.  This›is in case the .OR assembly address conficts with something already at›that location in memory.››!!!name .MD ([label1] [label2]...)›Begin macro definition.  Described in a separate section.››       .ME›End macro definiton.››       .MG›Mark the current .IN include file as Macro Global.  This keeps this file›in memory thruought the assembly, which is required if the file contains›macros that are referenced in other .IN files.››       .OC›Turn off (clear) the storing of object code in memory.››       .OR adr›Sets the origin address for the assembly.››Note:  If there is a label on this line, it will be given the value of the›new origin.  This is not the same as in Mac/65 which could use its origin›directive to reserve space (*= *+1).  You should use the .DS psuedo op for›reserving space.››       .OS›Turn on (set) the storing of object code in memory.  (Default)››       .OU filename›Create an output disk file for the object code.  Regretfully, this file is›made up of individual 256 byte segments much like Mac/65 does.  I›apologize for the laziness here on my part, but it realy was a lot easier›to do this way.  You will need to run some type of strip program to›de-segment the file.››       .PR "text"›Print a text message to the screen on pass 1 of the assembly.  This is›generally used with the .VA psuedo op when prompting for values to be›entered from the keyboard.››       .SB [+byte] bytes and/or ASCII›This is in the same format as the .BY psuedo op, except that it will›convert all bytes into ATASCII screen codes before storing them.  The›ATASCII conversion is done before any constant is added with the '+'›modifier.››label  .VA›Will print a '?', and then accept input from the keyboard.  You may enter›any value, which will be given to the label in front of the .VA.››       .WO word›Stores a word in memory.  Only one operand is supported.››       SET label = expression›Set the specified label to a new value.  This instruction allows a label›to be redefined with different values during the assembly.  Any label can›be SET.››- CONDITIONAL ASSEMBLY -››There are four conditional instructions IFE, IFN, IFP, and IFM, that›represent conditional assembly if Equal, Not equal, Positive, and Minus.›The operand of the IF instruction will be evaluated, and if the processor›status codes match the type of IF statement, then the source code›following the IF will be assembled.  Mark the end of the conditional block›of code with the psuedo op '***'.  (*** is like an ENDIF statement).››There is no 'ELSE' instruction, and so you must use complimenting IF›statements.››Examples:››       IFN FLAG›       .              ;This block of›       .              ;code gets asm'ed›       .              ;when FLAG <> 0›       ***››       IFE FLAG›       .              ;This block does›       .              ;when FLAG=0›       ***››       IFN FLAG1!FLAG2›       .              ;asm'ed if FLAG1›       .              ;or FLAG2 <> 0››       IFE WIDTH-40›       .              ;This gets asm'ed›       .              ;when width=40›       ***››       IFM WIDTH-40›       .              ;asm'ed if WIDTH›       .              ;less than 40›       ***››       IFP WIDTH-40›       .              ;if WIDTH greater›       .              ;or equal to 40››- MACROS -››Macros must be defined before they are used in your source.  The›definition looks like this:››!!!name .MD ([label1] [label2]...)››Where 'name' is the name of the macro, and 'label1' etc.  are its›parameters.  The three exclamation marks are a special macro identifier,›and must precede the macro name.  The body of the macro definition will›follow, and should be ended with a .ME psuedo op.››The number of parameters used when calling the macro must always match the›number of labels in the definition.  When called, these parameters will be›placed into the label names, in order, where they can be used in the body›of the macro.  Parameters can only be expressions -- there is no method›for passing arbitrary text strings.››Macros can pass up to 8 parameters.››Any labels defined within a macro must use a special form.  Because macros›can be expanded multiple times, a special label type exists to avoid›errors from multiple label definitions.  These label types start with›three periods, followed by any normal label name.  These special macro›labels will be given unique numbers with each macro expansion to keep them›separate.  You can consider them local labels to each macro expansion.››Here's an example of a macro to increment a two byte value:››!!!IND .MD (LOC)›       INC LOC›       BNE ...SKP›       INC LOC+1›...SKP .ME››To call this macro, you would use:››       IND $80››- ERROR MESSAGES -››These are the error messages that can be produced by the assembler.  Error›messages are marked with an '!', and also include the source line number›that they occured on.  If you are assembling a single file, or if the›errors occurs in your main file, you will be able to use the editor ^H›command to jump directly to the errors.  For errors that occur in included›files, you will need to load in that portion, and jump to those line›numbers manually using the ^G goto line number command.››       BRANCH›Branch instruction out of range.››       OPCODE›Error in opcode field.  This can be either a bad 6502 instruction, bad›psuedo op, or an undefined macro.››       DUP›Duplicate label definiton.››       EOF›End Of File error.  All assemblies must end with a .EN psuedo op.  This›should be in the main source file, not in any included files.  This error›can also occur if a conditional or macro definition is pending at the .EN.››       UNDEF›Undefined label reference.››       NEST›Nested definition.  IF conditionals may not be nested.  .MD macro›definitions cannot contain additional definitions.››       OPERAND›Error in operand field.››       ADR MODE›Addressing mode not spported.››       BAD LABEL›Bad characters in label name.››       MACRO OV›Macro overflow in either the number of expansions, or level of nested›expansions.››       SYM OV›Symbol table overfow.››       PARMS›Number of macro parameters in the call does not match the definition.››       LABEL MISSING›Missing label on either a SET psuedo op or in an = equate definition.›