Monitor version .8 beta.››     General:››Note: 24 bit support, and the full 65816 instruction set are not completed›yet.››Filenames default to the current drive number which can be changed.›(input of 'FILE' = 'D1:FILE')  A full filespec will override the default.››Non destructive prompt character (.) for ease in full screen editing.  Also,›the prompt does not interfere with command decoding.  If the cursor is moved›up to redo a prior command, the '.' does not need to be deleted.››Upper and Lower case accepted.››Continuous memory displays can be stepped one line at a time with the space›bar.  Press 'C' to return to continuous display.  ESC, RETURN, or BREAK will›stop the display.››ALL addresses and data bytes can be entered in HEX (default), in DECIMAL with›# (#1234), in binary with % (%10011010), in ASCII with ' ('A) or as a label›currently defined in the MAE symbol table with .  (.LABEL).  Arithmetic›operators +-*/&! can also be used, and will be performed left to right.  Any›combination of these can be mixed at any time in a completely free format›scheme, with no limits on length.  (Ex:  2000-#256+'W/100) Very little will›be mentioned about this feature later on, but ALL numbers for ALL commands›accept this versatile entry system.››All commands use spaces as delimiters.  A '?' indicates a command error.›Parameter uses for commands are abbreviated to:››adr:  a 16 bit address.›by:   an 8 bit byte. ('by' with numbers indicates a string of bytes.)›bit:  a 0 or a 1.›char: an ASCII character.›Quantities in [brackets] are optional parameters.  Default values will be›used if they are not entered.  All non-bracketted values must be entered.›Any other upper case characters or symbols should be entered as stated.››'Current address' refers to the last displayed or changed address, (plus›one), and is separate from the current program counter or PC.››     COMMANDS:››          Display Memory.     M [adr] [adr][/]›Displays hex and ASCII.  Displays 24 locations if only 1 parameter.  Displays›from current adr if no parms.  '/' = to $FFFF.  The '/' can be used on all›other commands as well.  Does not display ASCII control characters when›output is being sent to an external device.››          Peek Memory.        P adr1 [adr2..] [*]›Special memory display that allows multiple addresses to be entered, and only›prints one byte per address.  * causes continuous print of list of addresses.›Push Break to abort.››          Disassemble D [adr]›Disassembles memory starting at adr, or the current adr if not entered.  If›MAE is resident, the assembly code can be modified using normal screen›editing.  Single line assembly can be started from scratch by typing,›"-adr ." followed by an assembly mnuemonic.  (The '.' is necessary).  From›the single line assembler, you may enter '*' as the first mnuemonic character›to continue disassembly from that address forward.››          Change Memory.      :adr by1 [by2..by8]›The change memory command ':' can be entered directly, or edited from the›display memory command.  Only 8 data bytes will be changed.››          ASCII Mem Change    C adr ASCII STRING›Stores ASCII string at adr.  Addresses for both change memory commands may›use * for current address.  (ex.  C 1000 COMPUTER.  :* 9B.) The second›command will put a CR after the ASCII string.››          Display Registers   R›Displays 6502 registers in this form:› ,A  X  Y  NV-BDIZC SP› ;AB 5D FA 10110001 FF 7014 LDA #$00››          Change Registers    ; register bytes›Supports screen editing of R command.  Status flags can be modified in bit›form.  When entering values directly, a comma will skip to the next register,›and you don't need to enter all the values.  EX:  ';55' will change the A›register to 55.  ';,,20' will change Y to 20.››          Goto                G[S] [adr] [*brkpt] [C by] [r by] [Pf bit]›Run program at adr, or PC if not entered.  At any time during execution, the›Break key will return to the monitor and display the current registers and›PC.  Use the 'S' option to run code that ends in an RTS.  (Note:  When using›the S option, the PC adr in the register display on return is an internal›address, not the address where the actual RTS or RTI occurred.)››A breakpoint will create a return point to the monitor whenever a particular›address or condition is reached.  *brkpt will place a 00 (BRK) at the›breakpoint address.  For this reason, breakpoints can not be used for›programs in ROM.  A '?' will be printed in this case.  The breakpoint must›also be set at an opcode rather than an operand location so that it will›execute.  The rest of the parameters add conditions to the breakpoint.››C + by Counts the number of times the breakpoint is reached.  Execution›continues until the BRK is passed the specified number of times.  Breakpoints›can also test for specific conditions by specifying (r) reg name and (by)›byte it must contain in order to BRK.  Processor flags can also be tested by›'P' + flag character + (bit) for condition.  Use the flag characters as in›the register display.››The breakpoint will be skipped over until the specific condition is reached.›When both count and condition options are used, the count will apply to the›number of times the condition is met.  Execution speed will be slightly›slower than real time in this mode.  Actual speed will depend on how often›the program is interrupted to check conditions.››NOTE:  A peculiar bug in the ATARI hardware causes breakpoints to be›intermittenly skipped over.  When the BRK interrupt occurs, the program›counter+2 is pushed on the stack, but instead of jumping through the›interrupt vector, the OS will occasionally just return to the program at›PC+2.  This is usually a very rare occurrance, but can happen more often when›using conditional breakpoints on very small and quick loops, thus BRK›interrupts are occurring very rapidly.  It took many years before I was able›to really understand what was going on, and be assured that the problem was›indeed in the computer, and not a bug in the monitor.››ADDITIONAL NOTE: This bug does not occur on the '816 processor!  Yeeeehaaa!›(Thanks John.)››     Go command examples.›G 2000          = Run program at $2000›G 4000 *4124    = Run at $4000, and break at $4124›G *3100 A'Q     = Run at current PC and break at 3100 when A register›                  equals ASCII 'Q'›G *4200 C10 PZ1 = Run at PC and break at 4200 the 16th time the zero›                  flag is set››          Remove Breakpt      *›Brkpts remove themselves, and replace what was there when the BRK is›executed.  However, in case the program stops at other than the brkpt, * will›remove it.  This can occur when the Break key is pressed, conditional or›count values are not reached, or when the BRK is set in an operand rather›than an opcode.  Setting a new brkpt with the G command will also remove an›unused BRK.››          Exit to DOS         X››          Return to Assembler A››          Fill Memory         F adr1 adr2 [by1] [by2 by3...]›Fill memory with 0 if no data bytes.  Otherwise enter 1 byte, or a sequence›of any number of bytes to fill with.››          Transfer Mem        T adr1 adr2 adr3›Move memory from adr1 through adr2 to adr3.  Handles overlapping moves.››          Hunt for chars      H adr1 adr2 by1 [by2...][!]›          Hunt for String     H adr1 adr2 'ASCII string [!]›Hunt memory for ASCII string or string of hex bytes up to length of 60.  Use›'!' for a wild card to match anything.  Realize the number entry system will›let you search for things like "A9 'A", (as in LDA #'A), but not the reverse›of this.  Entering "'A A9" will put the hunt into full ASCII form, and search›for the literal string that you typed in.  The second example can actually be›entered in the form "! 'A A9", using a wild card to avoid the initial '›identifier.  For one more example, let's say you wanted to search for a JSR›to a MAE defined label.  This can be entered as "20 .LABEL .>LABEL".››          Change wild card    % char›Change the wild card for the Hunt command to 'char'.  This is used in case a›character in the search string is '%' or HEX 25.››          Compare mem         K adr1 adr2 adr3›Compare memory from adr1 to adr2 with memory starting at adr3.  Displays all›addresses with differences.››          DEC to HEX          # decimal number [no2...]›          HEX to DEC          $ by1 [by2...]›Displays hex values of a string of decimal numbers and vice versa.››          Change Output       O [filespec]›Send output to screen and filespec.  O by itself returns to just screen›output.  Default drive processing is not done on this command.  Full›filespecs must be entered for disk files.  Because of this, other devices do›not need a ':'.  ('O P' is sufficient to send output to printer)››          Re-open Editor IOCB     E›This is useful for returning to the text screen from a graphics mode, or›80-column display, or to reset the screen after changing RAMTOP.  The other›IOCB's used are:  #3 disk reads, #4 disk writes, and #6 external output.››          Query MAE symbol table  Q adr›                                        (Sorry, I was running out of letters)›Search the current symbol table for a label that matches the value entered›for adr.  If found, the label will be printed.  This is basically the reverse›procedure for symbol table lookup, and as such will only work well when the›requested value has only one label associated to it.››          Trace Instr         I [adr]›Traces program an instruction at a time.  Automatically traces OS calls›(including jumps with implied return) as one step.  Trace normally works on›programs in ROM, except 'G' and 'R' options as noted below.  After each step,›the monitor will wait for one of the following keypresses to control the›tracing mode:››Space - Steps one instruction at a time.›C     - Continuous trace.›D     - Disassemble next instructions.  Useful for previewing code that›        you are about to step through.  The program counter will remain›        at its current location.›G     - Execute all instructions up to current 'D' command listing.  Use›        to quickly execute loops or other structures.  First use 'D' to›        find a spot past the structure, then 'G' will execute everything›        up to that point.  This command puts a Breakpoint at the end›        position, and therefore cannot be used if the program is in ROM.›S     - Execute entire subroutine as one step.›R     - Return from subroutine.  Use this command if you are already in a›        subroutine, and wish to return to the previous level.  A BRK will›        be placed at the instruction the subroutine returns to, and›        therefore cannot be used for programs in ROM.›P     - Peek the value of the operand of the current instruction.›Q     - Perform a Q monitor command on the operand of the current instruction.›        If the operand value is defined in the current MAE symbol table, the›        label name will be printed.  You can use this on JMP, JSR and branch›        intructions to get an idea where you're going, and also on any memory›        references that have you thinking, "What the heck is *that*?"›U     - Execute the user function.›X     - Ignore instruction.  Skip to the next one without executing.›ESC, RETURN, or BREAK exits trace mode.››          Change Default Drv  / 1-8›All default drive accesses change to drive number entered, including uses in›the assembler section.  The starting default drive number will be the same as›the current SpartaDOS drive.››          Binary Load         L [@adr][-adr] filename›Load DOS II binary file where it was saved, or at @adr if entered.  Prints a›'?' if the file is not DOS II format.  Loads appended files, but @adr only›works on 1st part.  -adr loads raw data with no header using a straight CIO›transfer.  Both PC and default address are set to the load address.››          Binary Save         S [-]adr1 adr2 [@adr3] [+]file›Save DOS II binary file from adr1 to adr2.  If @adr3 is entered, it will be›used as the header allowing the file to load in at a different address than›where it was saved.  Use '-' for a CIO save without header.  If + is entered,›append to existing file.››          Directory           V [name or spec]  (Sorry, I *am* out of letters)›Displays disk directory.  Default of Dn:*.*.  A filespec of D2: = D2:*.*››          Sector Read         R adr sector# [ending sector]›          Sector Write        W adr sector# [ending sector]›Direct sector I/O to default drive.  Reads single and double density disks›automatically including single density sectors 1-3 of a DD disk.››          Hex Arithmetic      ? by1(+-*/&!)[by2..]   (no spaces)›Prints hex and decimal values of expression evaluated left to right.›Can also be used for ASCII convert. (?'A)››          User Function       U [adr1] [adr2] [adr3]›Accepts up to 3 parameters, which will be stored at $F0, $F2, and $F4.  $F2›and $F4 will be 0 if not entered, while $F0 will have the current address if›not entered.  In addition, the carry flag will be set if no parms.  Then›jumps to the end address of the monitor-3.  ($BBFD in top of RAM version)›User function expects an RTS return.›