ALR22T.1

                    REAR VIEW OF FRONT PANEL

    / ------\  12 PIN   O  *  O                        /---------\
   / VOLUME  \  IC ->      !<-SOLDER BRIDGE           /           \
  / CONTROL   \         O  *  O                      /             \
 /             \                                    /     VFO       \
 \             /        O  *  O                      \  CONTROL     /
   \         /             !<-SOLDER BRIDGE           \           /
     \-----/            O  *  O                        \--------/

                        O  *  O
                           *  DO NOT SOLDER THE TOP PAD
                        O  !< O   OF THESE 3 PADS
                           * \SOLDER BRIDGE HERE

  9 RE-ASSEMBLE RADIO .
 10 RESET MICROPROCESSOR.
 11 This mod will extend the RX range as well as the TX range of the above
    unit.The display will have a range   from 29mhz to 299 mhz but this is
    just an erroneos display as the PLL on a typical radio will rx between
    130 mhz and 180mhz with a TX range that may be a little beyond these
    these frequencies.

    GOOD LUCK AND HAPPY MODING
    73 CARL
    Packet: VE3ZCO@VE3GYQ
=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=
Note: I haven't tried or verified this, proceed at your own risk.  WA2ISE

%