Alinco DR-110T

Expand Reception Range and Cross Band Repeater Enable

Procedure:

1. Remove power and antenna.
2. Remove case screws, 3 on top and 2 on botton, and open unit.
3. Locate and remove component indicated.
4. Set REPEATER/NORMAL swithc to REPEATER MODE.
5. Reset microprocessor by holding down FUNCTION button and
   turning on power.
6. Unplug two wire cross band audio repeater plug to disable audio
   "bleed" in repeater mode.
7. Re-assemble in reverse order.


                                                     Cross Band Audio
                                                     Repeater Plug--\
                                                                     |
   ---------------------------------------------------------------|  V
   |          | | | | | | |     /                             =======[]
   |          | []| | [][]|    /                                  |
   |          | | | | | | |   /                _____              |
   |                    ^cut this part         | o |  <--repeater |
   |                    ^  /                   |---|       switch |
   |                      /                                       |
   |                     /                                        |
   |--------------------------------------------------------------|