KAM

INSTALLATION of the TAPR "DCD STATE MACHINE UPGRADE" for KANTRONICS KAM


1. BROWN    Solder to the pad marked "X" near the top edge of the
           KAM'S board, near U25 by R96.


2. RED      Solder to the outer one of the pads of C53 near the top edge
           of the KAM'S board.


3. ORANGE   *** NOT USED ***


4. YELLOW    On the top of the KAM'S board inbetween U26 and R104 you will
            see the 20 pins of K8. Turn the board over and trace from pin
            21 of U26 (63B03X) to pins 7 and 8 of K8 and cut the circuit
            between 7 and 8. Then turn the board back over and solder the
            YELLOW wire to the pin of K8 that will lead back to pin 21 of U26.

5. GREEN    *** NOT USED ***


6. BLUE     Inbetween U5 and U2 solder to the end of R29 closest to U26.


7. VIOLET   Solder to the pad on the top of the KAM'S board inbetween R103
           and RLY1.


8. GRAY     You will find 2 pads on top of board inbetween U26 and U2,
           solder to the pad closest to pin 1 of U26.


 If you prefer not to view the RCV LED on the front of the KAM (which will be
on continuous) then cut the circuit that leads to L4 on the bottom of the
board.

Put the DCD Upgrade JMP across pins 2 and 3.
White and Black wires were removed, not used.

Works Great! de KA9UEX   RELAYED  BY  N0KGX...GENE