KAM.3

   ..CONNECTING THE DATA ENGINE TO YOUR COMPUTER..

Just a word of caution, when wiring the "DE, 8-pin plug, to the computer
DB-25 pins" page 5.

The DE 8 pin plug as shown, is "Reverse". It should be shown
from 8 to 1, instead of 1 to 8, top to bottom. 

    " C O R R E C T   W I R I N G"   
_________________________________________________________

DE    purpose      computer                    color
pin                DB-25 pins
8     DSR            6                         white
7     DCD            8                         brown
6     DTR            20                        yellow
5     SG             7                         green
4     RD             3                         red
3     TD             2                         black
2     CTS            5                         orange
1     RTS            4                         blue
___________________________________________________________

This applies with DATA ENGINE tnc's starting with serial no. 850
Kantronics also confirmed this, and has since rectified the problem.

When the wiring was redone, the TNC worked properly without any flaws
up to 9600 baud, TNC to COMPUTER.

Just thouth I'd tell you guys, who have intention of buying Kam's
new "BEAST" hi!!!

73's Jean, ve2ed @ve2ed ar,