th215a.2               144 - 165 TX/RX MOD

TO OPEN YOUR TH-205,215,OR 225 ALL YOU HAVE TO DO IS TAKE OUT THE SCREWS 
ON THE BACK, AND GENTLY OPEN UP THE FRONT OF THE UNIT...LOCATE THE OBVIOUS
4 JUMPER BRIDGES ON THE PC BOARD.  THE BRIDGES ARE NUMBERED J-1, J-2, J-3, 
AND J-4..JUMPER J-3 HAS ALREADY BEEN CUT...CAREFULLY SNIP JUMPERS J-1 AND 
J-2 AND EVER SO SLIGHTLY SEPERATE THE SNIPPED BRIDGES TO INSURE NO-CONTACT 
BETWEN THE POINTS.. REASSEMBLE THE UNIT..LOOK AT YOUR INSTRUCTION MANUAL 
AND RESET THE MICROPROCESSOR..THE MOD WILL NOT WORK UNTIL YOU RESET THE MPU... 
THE INFO. FOR RESET IS NEAR THE BACK OF THE MANUAL..AFTER THAT THE UNIT IS 
WIDE OPEN TO OPERATE BETWEEN 144 TO 165...GOOD LUCK ..BILL
N6WPG