TH215.4

Kenwood TH-215A / TH-215E Frequency Modification.
_____________________________________________

     I'm not quite sure why we all do this, but here's how anyway.

     In order to increase the frequency coverage of the Kenwood TH-215 
Series Handheld Transceivers, a few jumpers inside the radio need to be cut.
No retuning is necessary.  WARNING: The radio is compact internally;  if
you do not have the delicate touch of a surgeon, forget this mod or get a
radio surgeon friend to do it for you.

     Tools you will need :  #1 Phillips Screwdriver 
                            #2 Phillips Screwdriver 
                            Diagonal Cutters (Very Small!)

     Remove the Battery Pack, Antenna and Belt Clip.

     Remove the 4 small screws in the recesses near the 4 corners
        of the back of the radio. Do not separate the cases yet!

     Place radio on a clean soft work surface Face-Up.  With the
        antenna connector facing away from you.

     Lift the front case of radio STRAIT-UP.  When clear of the rear
        case, rotate the front case to the right and lay it on the
        work surface Face-Down.  Do Not Damage the Flat Cables.

     KEEP YOUR FINGERS OFF THE ELECTRONICS!

     Notice the 4 Copper colored jumpers on the surface of the circuit
        board inside of the front case cover.  These are located 1.5
        inches "NorthWest" of the center of the speaker.  They are
        numbered J1 thru J4 from the bottom to the top.  J3 is already
        cut on the TH-215A.

     Remove the jumpers as selected from the table below by cutting
        through the thin area at the center of the jumper. BE CAREFUL!

     Reassemble Radio.  All memories will be clear and the display will
        be at the lowest Transmittable Frequency (i.e. 141 or 144).

_____________________________________________________________________________

The Operating Frequencies are programmed by cutting jumpers as follows :


Jumpers.         Transmit Freqs.         Receive Freqs.          Remarks.

No Cuts         144.0 - 145.995         144.0 - 145.995         TH-215E
J3              144.0 - 147.995         141.0 - 162.995         TH-215A
J3,J1           141.0 - 150.995         141.0 - 162.995
J3,J1,J4        141.0 - 162.995         141.0 - 162.995

Note: J2 has no apparent function, leave it IN.