TS430S
 
R:890220/1252z 321@VK2EHQ [via AMTOR KULNURA]
From: VK4ALV@VK2EHQ
MODS FOR THE KENWOOD TS430S FOR AMTOR. 
ABOUT THE TS430S,,THE MODS ARE AS FOLLOWS:- 
ON THE I.F.BOARD CHANGE C-164 FROM 0.22MFD TO 10NFD..50V CHANGE C-60 
FROM 10MFD TO 4.7MFD. 16V.... 
PARALLEL A 150KOHM RESISTOR ACROSS R.109 USUING A SMALL SWITCH OR 
BY WHATEVER MEANS YOU CAN DESIGN TO SWITCH THIS RESISTOR IN AND OUT. 
IN FOR ARQ AND OUT FOR ALL OTHER MODES. SOME PEOPLE USE THE SEND/REC 
SWITCH, OTHERS HAVE USED THE NOISE BLANKER SWITCH. I HAVE USED A 
SMALL MINI SWITCH WHICH I HAVE MOUNTED IN PLACE OF THE LEFT FRONT 
RUBBER FOOT. 
IT WILL PROBALY HELP TO CUT DIODE D-50 ON THE I.F.BOARD. IF YOU USE 
A 500HZ FILTER IN THE CWN OR SSBN POSITION THEN PARALLEL A 10MFD 
CAPACITOR ACROSS C-10 OR C-8. ADD A 10MFD CAPACITOR ACROSS C-161.(ACTUALLY 
I FOUND THAT THESE LAST TWO WERE NOT NECESSARY IN MY 430S.) 
YOU WILL FIND IT BEST TO TAKE THE AUDIO FROM IN FRONT OF THE VOLUME 
CONTROL, BUT THOSE PEOPLE USUING AUDIO FROM THE SPEAKER SOCKET SEEM 
TO GET OK RESULTS. REALLY YOU CAN GET AWAY WITH JUST THE FIRST TWO 
MODS, CHANGE C-60 AND C-164. THIS ORIGINALLY CAME FROM VK2AGE. 73S 
DE LARRY IN RAVENSHOE.