TS440S.11

ACC-1  Connector                  Use a 6 Pin DIN Connector.
                                         (Radio Shack $1.29)
Pin     Signal  Comments
________________________

1       Gnd     Signal Ground
2       TXD     Serial Data from Radio to Computer
3       RXD     Serial Data from Computer to Radio
4       CTS     Computer Ready;  (Radio Input)
5       RTS     Radio Ready;    (Radio Output)
6               No Connection

Pins 4 and 5 may be left Unconnected.

***** Command Description for Kenwood Computer Interface *****
______________________________________________________________

                Auto Information
                ________________
AIn;
                The Radio Will Send the Status Info Automatically
                Whenever the Operator Manually Varies any Function
                on the Radio which is Covered in the IF; Command
                        Where   n = 0 for Auto Info OFF
                                    1 for Auto Info On

                The Status Information Will be Sent in the Form :
                        As defined in the IF; Command


                Display Memory
                ______________
DMnnnn;
                This is a Factory Diagnostic Function
                and is of no practical use to the operator
CONTINUED IN FILE TS440S.21