TS440S.13

                Memory Read
                ____________
MRnxrr;
                The Memory Channel Defined Will be Read
                        Where:  n = 0 for RX VFO
                                    1 FOR TX VFO (Split Channels Only)
                                x = Don't Care      (Use "0" or Space)
                               rr = Memory Channel No.    (00 thru 99)

                The Memory Information will be sent in the Form :
                 MRn rrggmmmkkkhhhdz    ;
                        Where:  n = 0 for RX VFO
                                    1 FOR TX VFO (Split Channels Only)
                               rr = Memory Channel No.    (00 thru 99)
                         gg~~hhh = Value as defined in FA Command
                                d = Value as defined in MD Command
                                z = "0"  (Not Used in TS-440)
                        (Note: Four trailing Spaces)


                Memory Write
                ____________
MWnxrrggmmmkkkhhhdzxxxx;
                The Memory Selected Will be Set to the Frequency Defined
                        Where:  n = 0 for RX VFO
                                    1 for TX VFO (Split Channels Only)
                                x = Don't Care  (Use "0" or Space)
                               rr = Memory Channel No.    (00 thru 99)
                          gg~~hhh = Value as defined in FA Command
                                d = Value as defined in MD Command
                                z = "0" (Not Used in TS-440)
CONTINUED IN FILE TS440S.23