TS440S.16
                Frequency VFO A / VFO B Request
                _______________________________
FA;
FB;
                The Frequency in the Selected VFO Will be Read

                The Frequency Will be Sent in the Form:
                 FAggmmmkkkhhh;   or
                 FBggmmmkkkhhh;
                        Where    gg = GHz. Value
                                mmm = MHz. Value
                                kkk = kHz. Value
                                hhh =  Hz. Value


                Frequency VFO A / VFO B Select
                ______________________________
FAggmmmkkkhhh;
FBggmmmkkkhhh;
                The VFO Selected Will be Set to the Frequency Defined
                        Where    gg = GHz. Value (May be sent As 00 or Spaces)
                               mmm = MHz. Value
                                kkk = kHz. Value
                                hhh =  Hz. Value


                Function Select
                _______________
FNn;
                The Function Defined Will be Selected
                        Where   n = 0 for VFO A
                                    1 for VFO B
                                    2 for MEMORY

                Identify Model Request
                ______________________
ID;
                The Model of the Radio Will be sent in the Form :
                 ID00n;
                        Where : n = 1 for a TS-940 (*)
                                n = 2 for a TS-811 (*)
                                n = 3 for a TS-711 (*)
                                n = 4 for a TS-440


(CONTINUED IN FILE CALLED TS440S.2 - REQUEST IT FROM THE SERVER)