TS440S.18

                Memory Read
                ____________
MRnxrr;
                The Memory Channel Defined Will be Read
                        Where:  n = 0 for RX VFO
                                    1 FOR TX VFO (Split Channels Only)
                                x = Don't Care      (Use '0' or Space)
                               rr = Memory Channel No.    (00 thru 99)

                The Memory Information will be sent in the Form :
                 MRn rrggmmmkkkhhhdz    ;
                        Where:  n = 0 for RX VFO
                                    1 FOR TX VFO (Split Channels Only)
                               rr = Memory Channel No.    (00 thru 99)
                         gghhh = Value as defined in FA Command
                                d = Value as defined in MD Command
                                z = '0' (Not Used in TS-440)


                RIT/XIT Clear
                _____________
RC;
                The RIT/XIT will be set to 0.00 kHz.


                RIT/XIT Down
                ____________
RD;
                The RIT/XIT will Decrement by 0.01 KHz. (10 Hz.)


                RIT/XIT UP
                __________
RU;
                The RIT/XIT will Increment by 0.01 KHz. (10 Hz.)