TS440S.21
                The Contents of the MPU Memory will be Read
                        Where   nnnn = MPU Address (0000 Thru FFFF (HEX))

                The Contents of the MPU Memory Will be Sent in the Form :
                 DMnnnn-aabbccddeeffgghhiijjkk;
                        Where   nnnn = MPU Address (0000 Thru FFFF (HEX))
                              aa~~kk = Hex Number Pairs Of Next 16 Locations


                Down
                ____
DN;
                The Frequency or Memory Channel
                Will Decrement One Step


                Frequency VFO A / VFO B Request
                _______________________________
FA;
FB;
                The Frequency in the Selected VFO Will be Read

                The Frequency Will be Sent in the Form:
                 FAggmmmkkkhhh;   or
                 FBggmmmkkkhhh;
                        Where    gg = GHz. Value
                                mmm = MHz. Value
                                kkk = kHz. Value
                                hhh =  Hz. Value