TS440S.30

****************** TS-440S Digital Audio Modification ******************

NOTICE:
   Please  be  very careful with your transcievers,  and  we  accept  no 
responsiablity   for  any  damage  that  may  be  incurred,   and   this 
modification  may,   and proably would be cause for any  WARENTY  to  be 
DISCONTINUED.


   This Modification allows for the Kenwood TS-440s transceiver to  have 
the data audio on PIN 11 of the 13 pin DIN connector ACC JACK 2.   Later 
models may or maynot have a correction for this,  but my PK-232, or  for 
that fact NONE of my TNC's would  drive the audio to the PIN 11 of   ACC 
JACK 2. Encountering this problem,  and having another H.F.  transceiver 
I have been using the REMOTE connector, and using an audio input to  the 
AFSK IN RCA type connector.  This would allow me to use the same   cable 
with my TS-180s also.  Anyway this modification moves the  wire's   from 
the AFSK IN to the ACC 2 connector.  This should only take about 20   to 
30 minutes to preform this change, and most of the time is used up  with 
the removal,  and  replacement of the THREE covers of the   transceivers 
cabinet.
CONTINUED IN FILE TS440S.31