TS440S.31
    The circuit boards to work with,  are called:
DISPLAY UNIT (X54-1870-00) (C/4)   This has the ACC 2 JACK.
SWITCH  UNIT (X41-1610-00) (M/14)  This has the AFSK INPUT.

    The eaiest way is to remove these two boards 4 screws hold the ACC 2 
JACK, and 2 screws hold the AFSK INPUT board in and they are located  at 
the  rear  of the transceiver. If you are interested  in  following  the 
SCEHMATIC  in your manual,  the leads you will be working with are  ANI, 
and  GROUND which is the  PURPLE  LEADS,  and the FSI lead and   GROUND, 
which are the GREEN leads.

     The  problem is that when kenwood designed this rig,  they  brought 
the DATA INPUT(ANI) from the ACC2 JACK to connector J25 of the IF  UNIT. 
This  coming in after the Processor,  and Microphone Amplifier does  not 
allow sufficent amplification of the signal, thus very low, or no  audio 
at  all. What this modification does is swap at the rear of the RIG  the 
FSI,   and ANI signals,  Which also could be done on the IF UNIT  board, 
and  for some may actually be eaiser.  In my case the leads were just  a 
bit  too short to allow this modification to be accomplished on  the  IF 
UNIT.
CONTINUED IN FILE TS440S.32