TS440S.33
Step 7.
        Remove the TWO SCREWS that HOLD the AFSK INPUT board.

Step 8.
        Remove the FOUR SCREWS that HOLD the ACC 2 JACK board.

Step 9.
        Carefully from the inside of the transceiver,  pull these TWO
        boards out.

Step 10.
        Near the Bottom edge of the ACC 2 JACK board,  is a TWO lead
        connettor,  unplug this.  The leads should be PURPLE.

Step 11.
        On the AFSK INPUT board,  there is a 6 PIN connector,  unplug
        this.  The leads you will be working with are GREEN in color.

Step 12.
        Note how the PURPLE leads are connected to the connector itself,
        and remove these two leads by inserting a very small screwdriver
        into the slot on side, and being very gental, push the leads out
        one at a time.
CONTINUED IN FILE TS440S.34