TS440S.44
Subject: TS-440s (the whole scoop)
    ed: 26 May 86 17:45:45 GMT
Organization: UCSD wombat breeding society


The TS440 is nice.  Here's what I've found out about it that isn't in
the operation manual (in some random order):

Diode options:  There are a bunch of configuration options controlled by
clipping or inserting diodes on the back of the control board.  You get
to it by taking the top and bottom covers off (a bunch of silver
screws), loosening the front panel (4 flat-head silver screws, NOT the
black ones).  Then you have:

   diode        controls                in              out (cut)
   -----        --------                ----------      ----------
   D65          mode confirmation       Morse           single beep
   D66          display resolution      100 Hz          10 Hz
   D67          memory protect          none            on
   D73          CW shift                800 Hz          400 Hz
   D78          WARC 24MHx band tx      disabled        enabled
   D79          WARC 18MHz band tx      disabled        enabled
   D80          General Coverage tx     disabled        enabled

Self-Test:  You can run a rather complete test of the control logic by
the built-in "semi-self-test", a series of 56 routines.  To run this,
turn the unit on whilst holding the AM and T-F SET switches pushed in.
It changes to the next test when you turn the VFO knob clockwise.  Turn
the power OFF to reset the unit.

   Test         What it does
   ----         ---------------------------------------------------
     0          all positions in display light
     1          all segments in display dark
     2          all positions in display light
     3          all segments in display dark
     4          one digit lighted (rightmost)
     5          next digit lighted
     6          next digit lighted
     7          next digit lighted
     8          next digit lighted
     9          next digit lighted
    10          next digit lighted
    11          next digit lighted
    12          next digit lighted
    13          next digit lighted
    14          next digit lighted
    15          next digit lighted
    16          next digit lighted (leftmost)
    17          feeper sounds
    18          feeper silent
    19          all mode LEDs ON
    20          all mode LEDs OFF
    21          receive 
    22          transmit