TS440S.45
The following tests change internal signals.  They are most useful if
you are trying to trace the circuits controlled by these signals.
You'll need a s service manual (or at least a schematic) to made reals
sense of these.

    23          Band select - all lines high
    24          BAND select - all lines low
    25          PD select - all lines high
    26          PD select - all lines low
    27          ENF select - all lines high
    28          ENF select - all lines low
    29          ENP select - a:ll lines high
    30          ENP select - all lines low
    31          RES select - all lines high
    32          RES select - all lines low
    33          CO select - all lines high
    34          CO select - all lines low
    35          AX select - all lines high
    36          AX select - all lines low

these next tests check the outputs of the 8255 parallel port interfaces,
which select several internal functions.

    37          (IC2) port A all lines high
    38          (IC2) port A all lines low
    39          (IC2) port B all lines high
    40          (IC2) port B all lines low
    41          (IC2) port C0-C3 high, C4-C7 low
    42          (IC2) port C0-C3 low, C4-C7 high
    43          (IC53) port C all lines high
    44          (IC53) port C all lines low

Following display busy lines and scan lines in the rightmost 9 digits of
the display.  You will push buttons to cause the digit to change from a
1 to a 0 indicating that the associated button has been pushed.

 test   bit8    bit7    bit6    bit5    bit4    bit3    bit2    bit1    bit0
 ----   ----    ----    ----    ----    ----    ----    ----    ----    ----
  45    LOCK            AT      Mic UP  Mic DN  PTT/AT                  VS1
  46 (none)
  47 (key scanner)
  48     1       6      V/M                     VOICE
  49     2       7      M>V     RIT             A/B
  50     3       8      SCAN    XIT             SPLIT
  51     4       9      M.IN    T-Fset          A=B     dip3    dip4    dip5
  52     5       0      CLEAR   1Mhz            dip1    dip2    dip6    dip7
  53                    ENT     DOWN            UP      dip8    dip9    dip10

(the digits 0-9 are on the front panel keyboard; dip2-dip10 are the
segments of S50, the SSB frequency response dipswitch on the rear of the
control unit printed circuit board.)

   54   not used
   55   not used
   56   END