TS440.48

TS440s Self Test

Extracted from 26 May 86 letter of Brian Kantor, WB6CYT
Ammended 19 Mar 91 by GRThompson, N6SWC
 
Self-Test:  You can run a rather complete test of the control logic by
the built-in "semi-self-test", a series of 56 routines.  To run this,
turn the unit on whilst holding the AM and T-F SET switches pushed in.
It changes to the next test when you turn the VFO knob clockwise.  Turn
the power OFF to reset the unit.

   Test         What it does
   ----         ---------------------------------------------------
     0          all positions in display light
     1          all segments in display dark
     2          all positions in display light
     3          all segments in display dark
     4          rightmost position 8 and SUB lighted
     5          next position :8 and XIT lighted
     6          next position 8 and RIT lighted
     7          next position -8 lighted
     8          next position 8. and STEP lighted
     9          next position 8. and * lighted
    10          next position 8. and SPLIT lighted
    11          next position 8. and B lighted
    12          next position 8. and VFO lighted
    13          next position 8. and A lighted
    14          next position 8. and SCAN lighted
    15          next position 8. lighted
    16          leftmost position 8 and M.CH lighted
    17          tone on
    18          tone off
    19          all mode LEDs and white noise ON
    21          all mode LEDs and white noise OFF
    21          ON AIR ON
    22          ON AIR OFF

The following tests change internal signals.  They are most useful if
you are trying to trace the circuits controlled by these signals.
You'll need a service manual (or at least a schematic) to make real
sense of these.

    23          BAND select - all lines high
    24          BAND select - all lines low
    25          PD select - all lines high
    26          PD select - all lines low
    27          ENF select - all lines high
    28          ENF select - all lines low
    29          ENP select - all lines high
    30          ENP select - all lines low
    31          RES select - all lines high
    32          RES select - all lines low
    33          CO select - all lines high
    34          CO select - all lines low
    35          AX select - all lines high
    36          AX select - all lines low
CONTINUED IN TS440S.49