TS440S.1

***** Command Description for Kenwood Computer Interface *****
______________________________________________________________

                Auto Information
               ________________

AIn;

                The Radio Will Send the Status Info Automatically
                Whenever the Operator Manually Varies any Function
                on the Radio which is Covered in the IF; Command
                        Where   n = 0 for Auto Info OFF

                                    1 for Auto Info On

                The Status Information Will be Sent in the Form :
                        As defined in the IF; Command


                Display Memory
                ______________
DMnnnn;
                This is a Factory Diagnostic Function
                and is of no practical use to the operator

                The Contents of the MPU Memory will be Read
                        Where   nnnn = MPU Address (0000 Thru FFFF (HEX))

                The Contents of the MPU Memory Will be Sent in the Form :
                        As defined in the IF; Command

CONTINUED IN FILE TS440S.35