TS520.1

TSÄ520 CW/SSB FILTER SELECT MODE
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
In the TSÄ520SE, the heater switch has been replaced with a CW WIDE/NARROW
select switch.  For those operators who desire this type feature for their
transceiver, the following information may be considered as a guideline.

TSÄ520 (series) transceivers

1.   A minature SPDT switch may be installed at the operators preference,
on the rear side or bottom panel.  Use this to switch between the CW and
SSB filters by wiring the BROWN lead, which normally is transferred to the
CW terminal on the IF unit, between the SSB filter for 'WIDE' and CW for
'NARROW'.
2.   A traditional solution has been to use the FIX CH switch, position 3
(WIDE) and 4 (NARROW) for filter switching.  This may be done by completely
rewiring the switch, or by leaving the switch wiring and the filter wiring
as for normal operation and bridging the following terminals:

     A.   FIX CH 3 terminal to IF SSB Terminal
     B.   FIX CH 4 terminal to IF CW Terminal

Placing the FIX CH switch to position 3 will operate the SSB filter in CW
mode. This is especially helpful when trying to copy a very weak signal.