ts790.2

                    OPERATING PROCEDURES

     The repeater cross band operation allows the TS790A to receive on one
     bag signals
     will automatically be switched to the sub band.The TS790A will then
     re-transmit the signals from the main band. Each band may contain
     offset and sub-audible tone information (an optional TSU-5 must be
     installed in EACH BAND for decode).


  1   Press the MAIN function swich to select the MAIN band.
  2   Select the first operating frequency and mode (fm only).Select the
      offset as required.
  3   If the CH.Q is on,press the CH.Q switch to turn the function off.
  4   Select the sub-audible tone as required .
  5   Transfer the contents of the MAIN band to the SUB band.
  6   Select the second operating frequency anf mode (FM ONLY) and turn
      the CH.Q off.
  7   Select the offset and sub-audible tone as required.
  8   Adjustd
      point.The TS790A will transmit in the repeater crossband mode if
      the squelch controls are set too low or a signal is received.

continued in ts790.3