TS830.5
========================================================================
Additional comments:

Even though the receiver low frequency end is spec'd as 150 kHZ, it will
operate down to 100 kHz. [A[BTo conveniently switch in a general purpose
receiving antenna you must use the transverter connector. When the 8 pin
DIN  plug  is  plugged  into  this  connector,  a  switch operates which
separates the coaxial antenna input from the receiver input.  These  two
connections  appear  at pins 8 and 5 resp. of the transverter connector.
(This 8 pin  DIN  plug  is  not  furnished  with  the  930).   The  most
convenient setup is to bring cables from both the REMOTE and TRANSVERTER
connectors into a junction box  which  has  appropriate  connectors  and
switches  on  it  for  interfacing  to a transverter, receiving antenna,
linear amp, etc.
CONTINUED IN FILE TS830.3