TS830.6
3. you will need a another switch, one with at least three terminals, 
with the center teminal always in contact with one or the other of the 
outside contacts. its best to use a toggle type so you can mount it in 
one of the spare holes on the back of the radio.

4. splice into the wire removed from the moeoppcich, and connect 
this wire to the center of your new switch.
o5. from one (you select) of the side terminals of the new switch, 
connect a wire and run it back to the mode switch. connect this 
wire to t  tminalon the mode switchnrom which you removed the white 
wire with the blue stripe. you did leave that 1/4 inch of wire didn't 
you? take care here, the grey wire next to the one you are working on 
carries 110 volts, so don't make any solder shorts!
CONTINUED IN FILE TS830.4