TS930.2
                                 CHANGES

1) The resolution of the main tuning digital readout  can  be  increased
from 100 Hz to 10 Hz. No digits are lost since the readout has the extra
digit for this purpose. This change is accomplished by grounding  pin  1
of connector 8 on the DIGITAL UNIT.

2) The tuning rate is 10 kHz per revolution of  the  main  tuning  knob.
The  tuning  rate  can be changed to 5 kHz per revolution by cutting one
end of diode D-13 on the DIGITAL UNIT.

(Note that the black marks on the tuning knob itself are exactly 500  Hz
apart.  The knob can be "corrected" by tuning in an exact frequency, for
example 10,000.00 kHz, pressing the DIAL LOCK switch, then  turning  the
knob  to  line  up  a black line. As long as you don't spin the dial too
fast, it will track nicely from one end to the other. With the slow rate
modification, the dial increments become 250 Hz per division).
CONTINUED IN FILE TS930.1