TS930.3

                             TS-930 MODS
                             -----------

THE EARLY 930 WILL RECEIVE BUT NOT TRANSMIT ON THE 3 NEW WARC BANDS. IF
TRANSMIT CAPABILITY IS DESIRED, A MINOR WIRING ADDITION IS REQUIRED...

1. UNPLUG THE AC POWER CABLE.

2. REMOVE THE TRANSCEIVER TOP COVER.

3. REMOVE THE 4 SCREWS FROM THE SPEAKER
   MOUNTING AND TOP PANEL ASSEMBLY.

4. SWING THE ASSEMBLY AWAY AND UNPLUG  THE RED-BLACK BATTERY BACK-UP LEADS
   FROM THE DIGITAL UNIT X54-1680-00..H5. CAREFULLY ADD A WIRE JUMPER FROM
   IC-23 (PIN 12) TO IC-24 (PIN 8)(GRD) FOR SIMPLICITY, THIS MAY BE TACK
   SOLDERED ON THE COMPONENT SIDE OF THE BOARD. DO NOT CREATE SOLDER BRIDGE
   OR DROP SOLDER OR WIRE SHARDS INTO THE RADIO.

6. THIS COMPLETES THE MOD. REASSEMBLE  THE UNIT BEING CERTAIN NOT TO PINCH
   ANY LEADS UNDER THE SPEAKER BRACKET ASSEMBLY.