TS940.2

TS-940S AMTOR SWITCHING TIME
Most stock TS-940S require 30 to 50 MS to switch back to
receive.  This can be reduced to less than 20 MS by cutting
the center lead of the digital transistor Q68 on the Control
Unit.  After the mod, a slight "cick" will be heard in the
speaker.  However, this is offset for the amtor fan by the
improved switching time.
Q68 is located on the Back of the Control Unit below IC13.

    RELAYED   BY...N0KGX...GENE