TS940.3

HUM IN RECEIVE AUDIO TS-940S
On Kenwood TS-940S's that do not have the optional voice
synthesizer VS-1 installed in unit, you may notice a hum in
the receive audio.
The already present plug-in molex connectors for the optional
voice synthesizer unit should be dressed at the top of the
shield case where the voice synthesizer mounts; however, if
they are left to hang free in the vicinity of the PLL and
Digital A units, you will notice a hum in the receive audio.
The fix, simply secure above mentioned plug-in molex
connectors to the top of the shield case where optional VS-1
should mount.  Plastic ties, trash bag ties or simple
eletrical tape works nicely.
                                RELAYED   BY..N0KGX...GENE